## Slide 1: University of Illinois at Urbana-Champaign Dept. of Electrical and Computer Engineering ECE 101: Computing Technologies and the Internet of Things
The Internet (part 1 of 2)

## Slide 2: Global Internet: One of Humanity’s Greatest Achievements
We looked at Wifi and cellular.
Now we know how our data get to the Internet.
But what is the Internet?
How does information pass through it?
In a list of human accomplishments in the last century, the Internet is probably near the top.

## Slide 3: Tradeoffs: Pros and Cons of a Design
Today, you get to be an engineer!
…
Actually,
  today we will focus on
  design tradeoffs
  as we consider different ways
  in which communication networks can be connected.

## Slide 4: View Internet Development in Terms of Tradeoffs
Organization of a network—
  which machine connects to which other machine—
  called the topology of the network.
We’ll compare benefits and disadvantages
  of different topologies
  to understand how Internet developed
  and what problems it solves.

## Slide 5: From Computation to Communication
We will talk about the Internet from the ground up.
In our first week,
  we talked about bits
  and the emergence of computing.
At the same time,
  other people were wondering
  how results could be communicated.

## Slide 6: Physical Layer (Wiring) Took Substantial Effort
A lot of research went into developing the physical wires needed to communicate.
early Ethernet cable
shared Ethernet topology

## Slide 7: Modern Ethernet Leveraged the Telephone Infrastructure
Today’s Ethernet is much easier to use.
Ethernet cable contains
  four twisted pairs of copper wire.
  Each pair carries a voltage (bits).
For decades, telephones
  used a single pair of the same type
  to connect phones throughout the home.

## Slide 8: How Do We Connect Many Computers?
Why not just connect everyone?

## Slide 9: How Many “Wires” Needed for a Clique?
Connecting everyone to everyone else produces a topology known as a clique.
How many “wires” do we need?
2 “wires”
(one in each direction)
6 “wires”
How many “wires” for
6 computers?
12 “wires”
30

## Slide 10: Requirements and Limitations for a Clique Topology
Generalize: how many “wires” for N computers?
To count,
  choose one computer (N choices), then
  choose a different computer (N – 1 choices).
Total possible choices? N(N – 1) “wires” *
Limitations of a clique?
And too many network interfaces.
*Wires usually only used in one direction, but two can be packaged in one cable, so divide by two for the number of cables.
Too many wires!

## Slide 11: Sharing Reduces Wire and Interface Count
Ethernet was originally a shared medium.
Just 1 “wire”—in yellow, labeled “The Ether” in the diagram—for all computers!

## Slide 12: The Same Six Computers on a Shared Ethernet
The Ether

## Slide 13: Which is Better? A Shared Network or a Clique?
Consider a small group (10-20 computers).
Build a clique or a shared network?
pros of sharing:
  cheaper wiring
  fewer network interfaces (one per computer instead of 9-19)
pros of a clique:
  simpler physical protocols
  no need to take turns
  simultaneous all-to-all communication
Ethernet solved these issues.

## Slide 14: Neither Technique Scales to Large Numbers
What if we have 1,000 computers?
Neither clique topologies nor shared networks scale to large numbers.
Don’t want to pay for a clique (999 wires and 999 network cards per computer!)
But sharing is also not viable:
  imagine a room with 1,000 people all speaking
  with voices amplified to be audible to all.
What has been done in other contexts?

## Slide 15: Airline Routes Must Also be Efficient
I fly from Champaign.
I need to go to many large cities.
And many smaller ones.
I want to fly directly.
Why can’t I?
Hint: everyone wants to fly directly!
Not enough passengers for flights!

## Slide 16: Hierarchy Connects All Cities More Efficiently
What do the airlines do instead?
Use a hierarchy.
Designate hub cities.
Route flights hierarchically.
Champaign to Chicago (hub) to Denver (hub) to Dallas (hub) to Columbia

## Slide 17: User of Hierarchy Permeates Natural and Human Systems
Hierarchy used ubiquitously in large systems.
Examples in nature include:
  trees (trunk, branch, smaller branch, leaf),
  roots (main root, smaller, and smaller), and
  blood vessels.
Examples in human-made systems include:
  airline routes (international, domestic, regional),
  corporate structures (CEO, VPs, directors, managers, workers) and
  power networks.

## Slide 18: One Level of Hierarchy: a Star Topology
Instead of a clique, let’s use a hierarchy.
We’ll build a “star”.
“hub”

## Slide 19: Star Topology Between Shared Network and a Clique
In a star, all data pass through the hub.
Benefits (relative to clique or shared):
  fewer wires and interfaces than a clique, but
  no sharing required.
Disadvantages (to clique):
  paths a little slower than a clique (longer, and require processing by hub), and
  hub may still be a bottleneck to communication.

## Slide 20: The “Hub” in a Computer Network is a Router
But we don’t need a monitor nor a keyboard.
router
A router forwards data packets (routes).
“hub”

## Slide 21: Hierarchies Can be Organized Hierarchically!
But why stop there?
We can use several levels of hierarchy.

## Slide 22: More Levels of Hierarchy are Possible
a second level of hierarchy

## Slide 23: Tradeoffs: One Level or Two Levels?
Why bother?
Compared with a single level of hierarchy,
  the main benefit is that
  delay gets better for close nodes.
The disadvantages include:
  more routers (more cost),
  more interfaces (routers need them, too),
  and longer paths have more delay.

## Slide 24: Can Keep Adding Layers of Hierarchy
We can do it recursively!
(over and over)

## Slide 25: Deep Hierarchies Enable Networks to Span the Globe
If we keep adding levels, the network can get really huge!

## Slide 26: What Happens When We Want to Join?
Imagine a hierarchical network here on campus.
We connect the top of our hierarchy to a router in the bigger network in Chicago.
Not just one link!
We connect to two routers instead— maybe a second node in Indianapolis.

## Slide 27: Making Connections from UIUC to the World
Chicago
Indianapolis
Build locally, then connect to someone else.
The Valley
UIUC

## Slide 28: Design Topologies to Minimize the Impact of Failures
What about failures?
Which link failures in the previous diagram disconnect groups of computers?
Lots!
But not all.
How can we connect our networks so that the network is reliable?
Real topologies are designed to reduce the impact of failures.
Notes: Nothing too technical, but students will get to play with the idea in the lab.

## Slide 29: Real Failures Can Still be Catastrophic
In practice, it’s not as reliable as one hopes.
About 15 years ago, a backhoe dug up (and broke) the optical fibers running from our campus to Chicago.
Internet traffic almost instantly shifted to route through Indianapolis.
Although we had paid for that connection, the router in Indianapolis didn’t expect any traffic.
After all, UIUC never sent any traffic that way.
The Internet was down for days at UIUC.

## Slide 30: One More Link Can Have a Huge Impact
Chicago
Indianapolis
UIUC
Now astronauts can watch Netflix!
The Valley
ISS
Netflix

## Slide 31: Plumbing: the Invisible Infrastructure
Do you care about your plumbing?
You should say, “Absolutely!”
But how often do you think about your plumbing?
Plumbing is an invisible infrastructure: you only think about it when it fails.
So we often talk about infrastructure that works well as “plumbing.”

## Slide 32: Optical Fiber and Tier 1 ISPs Form the Backbone
What about the “plumbing” in the Internet?
Governments (in the US, for example)
  own* the right-of-ways along which
  companies lay bundles of optical fiber.
Tier 1 Internet Service Providers (ISPs)
  build or lease these fibers
  to carry traffic
  across the Internet.
These form the backbone of the Internet.
*Purchased in the 19th century to lay railroads across the continent.

## Slide 33: Tier 1 ISPs Carry Transit Traffic for Lower Tiers
Tier 1 ISPs cover
  different parts of the country
  and/or world (sometimes overlapping).
They peer with one another:
  connect in several places and
  agree to carry data traffic for one another.

## Slide 34: Tier 2 and 3 ISPs Connect Directly to Customers
Tier 2 ISPs
  connect to Tier 1 ISPs and
  provide service in smaller regions,
  carrying some transit traffic, but
  not as much as Tier 1.
Tier 3 ISPs
  connect to Tier 2 ISPs and are fairly local.
  They do not carry transit traffic, only passing packets from their customers up to the Tier 2 ISPs (and back).

## Slide 35: Send Data Packets Across the Internet!
Once it’s all connected,
  you can send packets of bits
  to any machine on the Internet!
How?
You just need an IP address!
For example, here’s one for
ece.illinois.edu

## Slide 36: Every Computer Has a Unique IP Address
An Internet Protocol (IP) address
  is 4 Bytes (32 bits)
  Humans write 130.126.151.19,
  but in the computer, it’s
  1000 0010 0111 1110 1001 0111 0001 0011
  (without the spaces).
Every computer in the Internet has an IP address.*
*Sort of. Today, a household usually shares one public address.

## Slide 37: Sending is Easy: Attach an Address and Send it Off!
TO: 210.152.243.234
To send a birthday photo
  to your friend in Tokyo, your computer
  finds their computer’s IP address and
  puts it into a packet with the photo, then
  pushes the packet into the Internet.
Each router along the way
  sees the IP address
  and knows where to send it
  until it arrives at your friend’s computer!
Then their computer unpacks the photo bits.

## Slide 38: Routers Forward Data Packets Based on IP Address
When a data packet arrives at a router,
  the router must decide
  on which outgoing link/network interface
  to forward the packet.
The router looks at two things:
  destination IP address in packet,
  and its forwarding table (also called a routing table).
Which way should it go?

## Slide 39: Routers Advertise IP Addresses They Can Reach
A forwarding table maps
  IP addresses into
  interface numbers
  (1, 2, or 3, for example).
Routers periodically
  advertise IP address ranges
  that they can reach
  to their other links.
1
2
3
I can get packets to Japan (IP addresses).
I can get packets to UIUC (IP addresses).

## Slide 40: Forwarding Table Built from Advertisements
Each router
  builds its forwarding table
  based on the advertisements
  it hears from its neighbors.
1
2
3
I can get packets to Japan (IP addresses).
I can get packets to UIUC (IP addresses).
dest | interface
Japan
1
3
UIUC

## Slide 41: AS: An Independently-Operated Subnetwork
An organization’s network—including ISPs—is called an Autonomous System (AS).
AS
AS
AS
AS
peering between ASs

## Slide 42: Forwarding Between ASs Considers Only Reachability
Routing between ASs
  uses the Border Gateway Protocol (BGP),
  but each AS measures cost differently.
So BGP makes forwarding decisions
    based on reachability:
    can I get to the destination?
Full paths (hop-to-hop AS routes) are advertised to avoid loops.

## Slide 43: Let’s Try Some Forwarding Together
A packet arrives for Northwestern University (in Chicago, IL, USA).
Which interface?
A packet arrives for Tokyo University (in Tokyo, Japan).
Which interface?
A packet arrives for UIUC.
Which interface?
Usually, the more specific answer is chosen.
1
2
3
dest | interface
Japan | 1
UIUC | 3
IL state | 2
1
2
3? Or 2?
3

## Slide 44: Routing Within AS Based on Link Costs
Within an AS, each link can be assigned a cost.
Link cost may reflect
  length (delay),
  link capacity,
  congestion (queueing delay),
  any combination of those metrics,
  or just the AS’s preferences.
E
C
F
G
D
S
B
A
25
5
13
13
4
11
18
7
3
3
3
9
9
1
9
link costs

## Slide 45: Routing Within AS Based on Link Costs
To construct a forwarding table,
  a router must decide
  which path to follow
  to reach each other node.
The cost of a path is
  the sum of the costs
  of the links in the path.
And the desired path is the path with the smallest cost.
E
C
F
G
D
S
B
A
25
5
13
13
4
11
18
7
3
3
3
9
9
1
9

## Slide 46: Let’s Find Routes Together!
Complete the forwarding table for the node S.
dest | interface
D | 
M | 1
S
D
M
link cost = 1
link cost = 1
link cost = 1
1
1
1
2
2
2
S
D
M
link cost = 13
link cost = 4
link cost = 6
1
1
1
2
2
2
2
dest | interface
D | 
M | 1
1
S
D
M
link cost = 1
link cost = 4
link cost = 6
1
1
1
2
2
2
dest | interface
D | 
M | 
2
2
(by “hops”: all link costs are 1)

## Slide 47: Let’s Find Routes Together!
Complete the forwarding table for the node S.
A little trickier this time?
dest | interface
A | 2
B | 1
D | ?
7
3
1
1
1
2
2
2
S
D
1
2
A
B
5
4
8

## Slide 48: How Many Paths Must We Consider?
How many paths are possible?
7
3
1
1
1
2
2
2
S
D
1
2
A
B
5
4
8
7
3
1
1
1
2
2
2
S
D
1
2
A
B
5
4
8
7
3
1
1
1
2
2
2
S
D
1
2
A
B
5
4
8
7
3
1
1
1
2
2
2
S
D
1
2
A
B
5
4
8
4
path cost = 3 + 7 = 10
path cost = 3 + 8 + 5 = 16
path cost = 4 + 8 + 7 = 19
path cost = 4 + 5 = 9

## Slide 49: Let’s Find Routes Together!
Complete the forwarding table for the node S.
A little trickier this time?
dest | interface
A | 2
B | 
D | 
2
7
1
1
1
2
2
2
S
D
1
2
A
B
5
4
1
dest | interface
A | 2
B | 1
D | 
2
7
3
1
1
1
2
2
2
S
D
1
2
A
B
5
4
8
2
2

## Slide 50: Let’s Find Routes Together!
Complete the forwarding table for destination D from the node S.
(Prof. Roy Choudhury made it!)
dest | interface
D | ?
… | …
E
C
F
G
D
S
B
A
1
2
3
25
5
13
13
4
11
18
7
3
3
3
9
9
1
9

## Slide 51: Build a Spanning Tree for Each Destination
In practice, we build a tree starting from the destination.
What node is closest to D?
F at distance 3
And the closest to that pair?
B at distance 4
And …
1
2
3
25
5
13
13
4
11
18
7
3
3
3
9
9
1
9
3
4
7
7
11
14
19
E
C
F
G
D
S
B
A

## Slide 52: Let’s Find Routes Together!
Complete the forwarding table for destination D from the node S.
(Prof. Roy Choudhury made it!)
dest | interface
D | 
… | …
1
2
3
25
5
13
13
4
11
18
7
3
3
3
9
9
1
9
2
E
C
F
G
D
S
B
A

## Slide 53: Logically Separated Data and Control Planes
Routers forward packets.
  Packets with data are said
  to be passing through the data plane.
In addition to forwarding packets,
  routers exchange information
  about routes available to them.
  These coordination messages
  travel through the control plane.
The two planes
  use the same physical network
  (except within a single router),
  but are logically separate.

## Slide 54: Internet Plumbing: Routing and Forwarding
And have populated their forwarding tables.
Routers have established a control plane between themselves.
This is the plumbing in the Internet.

## Slide 55: Terminology You Should Know from These Slides
  design tradeoffs
  network topology
  Ethernet
  clique topology
  network interface
  shared network
  hierarchy
  star topology
  router
  Internet Service Providers (ISPs; Tier 1,2,3)
  Internet backbone
  peering
  Transit traffic
  IP address
  forwarding
  Route advertisements
  Routing (building forwarding table)
  Autonomous System (AS)
  Border Gateway Protocol (BGP)

## Slide 56: Concepts You Should Know from These Slides
  engineers must consider tradeoffs between alternative designs
  number of “wires” needed for a clique
  tradeoffs: clique vs. shared vs. hierarchy
  hierarchy appears in all large systems, both natural and human-made
  how topology affects tolerance to failures
  packets only allowed to cross Tier 1 & 2 ISPs (transit traffic)
  each computer has a 4B IP address
  how a router uses its forwarding table
  routers forward packets in data plane and send route advertisements in control plane
  how to find shortest paths in small graphs

## Slide 57: Routing within an AS: from Advertisement to Table
Within an AS,
  routers advertise distances to neighbors.
  Once in a while, each router
  uses its recorded view of costs in the network
  to compute paths to all destinations.
  and produce a forwarding table