## Slide 1
Using Computer Vision to Relieve the Crop Phenotyping Bottleneck
Researchers: Andrew Leakey, Narendra Ahuja, John M. Hart
Research Supported by the Center for Digital Agriculture and AIFARMS

## Slide 2: Develop Corn and Sorghum Plants Suited for Climate Change
Standard and Water Efficient Sorghum
These plants are being developed at the Institute for Genomic Biology and grown south of campus. Phenotype data is being collected by hand for analysis. We are working to automate this data collection using a camera set-up to collect and process images using Computer Vision.

## Slide 3: Rain Intercept Facility for Camera Installation
Digital cameras mounted to the retractable roof will enable the extraction of various phenotype data of the different plots
A set of cameras mounted on the overhead roof structure will cover the various plots growing in the field
Time-lapsed images over the growing season will be preprocessed and transmitted to a remote server for growth estimation via computer vision and comparison of the different plots being developed to find the best suited types
Future Camera Installations

## Slide 4
Design and Develop a Camera System to Collect and Transfer Images from the Field
  Program a control board (Raspberry Pi, Jetson AI module, etc.) to operate a set of cameras
  Select suitable cameras to provide time-lapse imaging of growing plants
    Acquire images multiple times a day simultaneously from all cameras per user requests
    Adjust camera parameters for the environmental conditions, sun, wind, etc.
  Determine best method for camera connectivity to the control board
  Determine best locations for mounting the cameras (FOV) over the different modified plots
  Create a user interface for remote control of camera parameters and storage options
  Design and build a battery circuit to support the system and recharge using solar panels
  Interface control board to local network to offload images to remote Computer Vision Lab
  Provide a waterproof enclosure to protect and mount the cameras overhead
  Test system at the Rain Intercept Facility (or possibly inside a greenhouse)
Potential Project for ECE445 Group

## Slide 5
Rain Intercept Facility – Retractable roof and sides close as it starts to detect rain.
Allows controlling the amount of water given to each plot during the experimentation.
Rain Intercept Facility

## Slide 6
Rain Intercept Facility – Beams for mounting cameras
Rain Intercept Facility

## Slide 7
Training of neural network, Mask-R CNN, to identify instances of early plants and leaves
Results enable plant counting in each plot as well a leaf counting on individual plants
Labeled Dataset
(Training set)
Model Training
Input Image
Output Image
Segmentation Kernel
Training Process
Future Plant/Leaf Segmentation Process

## Slide 8
Initial Plant Detection Segmentation Results
Input Image
Output Image
Mask R-CNN trained using labeled image dataset to detect whole plants in the field images
Used for counting the number of plants found growing in the field in each plot

## Slide 9
Initial Leaf Detection Segmentation Results
Input Image
Output Image
Mask R-CNN trained using labeled image dataset to detect individual leaves on plants in the field images
Each leaf assigned individual color to highlight its location in the image

## Slide 10
Please feel free to contact me with any questions:
John M. Hart
Principal Research Engineer
Coordinated Science Laboratory and
Center for Digital Agriculture
jmhart3 @ illinois.edu
Potential Project for ECE445 Group