## Slide 1: Bringing IoT to Noise Cancellation

## Slide 2
Noise is everywhere …

## Slide 3
Busy Streets in Cities
Lawn Mower in Early Morning
Coworker Chatting over Phone
Construction Site

## Slide 4
Existing Solutions

## Slide 5
This Project
Existing Solutions
Better Noise Cancellation
9dB Better

## Slide 6
This Project
Existing Solutions
Better Form Factor
(Hollow)
Better Noise Cancellation
Comparable Performance
9dB Better

## Slide 7
Wireless Networking
+
Our System: MUTE
Noise Cancellation

## Slide 8
Alice

## Slide 9
1. Sound starts
Alice

## Slide 10
1. Sound starts
2. IoT relay forwards sound over wireless
Alice

## Slide 11
1. Sound starts
2. IoT relay forwards sound over wireless
Alice
Wireless radios travel a million times faster than sound

## Slide 12
1. Sound starts
2. IoT relay forwards sound over wireless
3. Wireless arrives at ear-device earlier
Alice

## Slide 13
1. Sound starts
2. IoT relay forwards sound over wireless
3. Wireless arrives at ear-device earlier
4. Actual sound
arrives later
Alice

## Slide 14
1. Sound starts
2. IoT relay forwards sound over wireless
3. Wireless arrives at ear-device earlier
Lookahead
4. Actual sound
arrives later
Alice

## Slide 15
Lookahead allows us to cover ears in time
Analogy: Light travels much faster than sound
MUTE: Leverage lookahead for noise cancellation

## Slide 16: Talk Outline
How can MUTE leverage lookahead?
Wideband Cancellation
Non-Causal Filtering
Sound Source Profiling
Timing Gain 
Signal Processing Gain 
Application-Specific Gain 

## Slide 17: Talk Outline
How can MUTE leverage lookahead?
Wideband Cancellation
Non-Causal Filtering
Sound Source Profiling
Timing Gain 
Signal Processing Gain 
Application-Specific Gain 

## Slide 18
Noise Cancelling Headphones
-- What is inside?

## Slide 19: Noise Cancellation Primer
Ref. Mic.
DSP
Anti-Noise Speaker

## Slide 20: Noise Cancellation Primer
Ref. Mic.
DSP
Anti-Noise
Speaker

## Slide 21: Noise Cancellation Primer
Ref. Mic.
DSP
Anti-Noise
Speaker

## Slide 22: Noise Cancellation Primer
Ref. Mic.
DSP
Anti-Noise
Speaker

## Slide 23: Noise Cancellation Primer
Ref. Mic.
DSP
Anti-Noise
Speaker

## Slide 24: Noise Cancellation Primer
Ref. Mic.
DSP
Anti-Noise
Speaker
Feedback Mic.
(Error Feedback)

## Slide 25
How do they perform today?

## Slide 26
Active noise cancellation only at low frequencies
Bose QC35
Good
Bad

## Slide 27
Active noise cancellation only at low frequencies
Bose QC35
Good
Bad

## Slide 28
Active noise cancellation only at low frequencies
Bose QC35
Good
Bad
Sound absorbing material blocks high frequencies

## Slide 29
Active noise cancellation only at low frequencies
Sound absorbing material blocks high frequencies
Bose QC35
Good
Bad

## Slide 30
Why does noise cancellation not work at higher frequencies?
Let’s look into the headphone again.

## Slide 31
Ref. Mic.
Fb. Mic.
DSP
Speaker
Time

## Slide 32
Ref. Mic.
Fb. Mic.
DSP
Speaker
Noise
Time

## Slide 33
Ref. Mic.
Fb. Mic.
DSP
Speaker
Noise
Time

## Slide 34
Ref. Mic.
Fb. Mic.
DSP
Speaker
Noise
Time

## Slide 35
Ref. Mic.
Fb. Mic.
DSP
Speaker
Time budget (lookahead):
Noise
1 cm
Time

## Slide 36
Ref. Mic.
Fb. Mic.
DSP
Speaker
Noise
Anti-Noise
Time budget (lookahead):
Time

## Slide 37
Ref. Mic.
Fb. Mic.
DSP
Speaker
Noise
Anti-Noise
Time budget (lookahead):
Time
Time lag:

## Slide 38
Ref. Mic.
Fb. Mic.
DSP
Speaker
Noise
Anti-Noise
Time
High Frequency:
Anti-Noise
Noise
Residual Error
Low Frequency:
Anti-Noise
Noise
Residual Error

## Slide 39
Ref. Mic.
Fb. Mic.
DSP
Speaker
Noise
Anti-Noise
Time

## Slide 40
Let’s now look at noise cancellation in MUTE ...

## Slide 41
Ref. Mic.
Fb. Mic.
DSP
Speaker
Noise
Time

## Slide 42
Fb. Mic.
DSP
Speaker
Noise
Ref. Mic.
Time

## Slide 43
Fb. Mic.
DSP
Speaker
Noise
Ref. Mic.
Time

## Slide 44
Fb. Mic.
DSP
Speaker
Ref. Mic.
Noise
1 m
Time budget (lookahead): (100X larger)
Time

## Slide 45
Fb. Mic.
DSP
Speaker
Ref. Mic.
Noise
Time budget (lookahead): (100X larger)
Anti-Noise
Time

## Slide 46
Fb. Mic.
DSP
Speaker
Ref. Mic.
Noise
Time budget (lookahead): (100X larger)
Anti-Noise
Cancel high frequencies
Anti-Noise
Noise
Residual Error
Time

## Slide 47: Talk Outline
How can MUTE leverage lookahead?
Wideband Cancellation
Non-Causal Filtering
Sound Source Profiling
Timing Gain 
Signal Processing Gain 
Application-Specific Gain 

## Slide 48: Talk Outline
How can MUTE leverage lookahead?
Wideband Cancellation
Non-Causal Filtering
Sound Source Profiling
Timing Gain 
Signal Processing Gain 
Application-Specific Gain 

## Slide 49: Noise Cancellation Primer
Ref. Mic.
Feedback Mic.
DSP
Different

## Slide 50: Noise Cancellation Primer
Ref. Mic.
Feedback Mic.
DSP

## Slide 51: Noise Cancellation Primer
Ref. Mic.
Feedback Mic.
DSP

## Slide 52: Noise Cancellation Primer
Ref. Mic.
Feedback Mic.

## Slide 53
Future
Past
Current
Channel Impulse Response
Ref. Mic.
Feedback Mic.

## Slide 54
Future
Past
Current
Today’s Headphones (Causal)
MUTE (Non-Causal)
Channel Impulse Response
Lookahead
“Lookahead”  Non-Causal Filtering  Better Cancellation
Ref. Mic.
Feedback Mic.

## Slide 55: Talk Outline
How can MUTE leverage lookahead?
Wideband Cancellation
Non-Causal Filtering
Sound Source Profiling
Timing Gain 
Signal Processing Gain 
Application-Specific Gain 

## Slide 56: Talk Outline
How can MUTE leverage lookahead?
Wideband Cancellation
Non-Causal Filtering
Sound Source Profiling
Timing Gain 
Signal Processing Gain 
Application-Specific Gain 

## Slide 58
Alice
Bob
Alice

## Slide 59
Alice
Bob
Alice

## Slide 60
Alice
Bob
Alice

## Slide 61
With lookahead …

## Slide 62
Alice
Bob
Alice

## Slide 63
Alice
Bob
Alice

## Slide 64
Alice
Bob
Alice

## Slide 65: Talk Outline
How can MUTE leverage lookahead?
Wideband Cancellation
Non-Causal Filtering
Sound Source Profiling
Timing Gain 
Signal Processing Gain 
Application-Specific Gain 

## Slide 66
Implementation & Evaluation

## Slide 67
MUTE Platform
Noise Source

## Slide 68
MUTE Platform
IoT Relay
Noise Source

## Slide 69
MUTE Platform
Wireless Receiver
Noise Source
IoT Relay

## Slide 70
MUTE Platform
DSP Processor
Wireless Receiver
Noise Source
IoT Relay

## Slide 71
MUTE Platform
Feedback Microphone
Wireless Receiver
Noise Source
IoT Relay
DSP Processor

## Slide 72
MUTE Platform
Anti-Noise Speaker
Wireless Receiver
Noise Source
IoT Relay
DSP Processor
Feedback Microphone

## Slide 73
MUTE Platform
MUTE (Hollow)

## Slide 74
MUTE Platform
MUTE (Hollow)

## Slide 75
Evaluation
Goal: Comparable Performance
MUTE (Hollow)
Ear Blocking Headphone

## Slide 76
2. MUTE hollow design (comfort)
1. Bose headphone

## Slide 77
Evaluation
Goal: Better Performance
MUTE (Non-Hollow)
Ear Blocking Headphone

## Slide 78
2. MUTE hollow design (comfort)
3. MUTE non-hollow design (performance)
1. Bose headphone
+

## Slide 79
Zooming Out

## Slide 80
Wireless Signal

## Slide 81
MUTE Tabletop Relay
Wireless Signal

## Slide 82
DSP
MUTE Tabletop Relay
Wireless Signal

## Slide 83
DSP
MUTE Tabletop Relay
Wireless Signal
Anti-Noise over

## Slide 84
Noise Cancellation as an Edge Service
DSP

## Slide 85
Noise Cancellation as an Edge Service
DSP
Anti-Noise for Alice
Feedback

## Slide 86
MUTE Enabled Noise Sources

## Slide 87: Conclusion
Acoustic Data Plane
Wireless Control Plane
MUTE Tabletop Relay
MUTE Edge Service
MUTE Noise Source
Acoustic
Noise Cancellation

## Slide 88: Conclusion
Acoustic
Noise Cancellation
On-Ear Machine Learning
Acoustic Augmented Reality
…
MUTE Tabletop Relay
MUTE Edge Service
MUTE Noise Source
Acoustic Data Plane
Wireless Control Plane

## Slide 90
Closing Thoughts …

## Slide 91: The Wearable Market Projections
WiFore: https://www.nickhunn.com/wp-content/uploads/downloads/2014/08/The-Market-for-Smart-Wearables.pdf
https://www.nickhunn.com/wp-content/uploads/downloads/2014/08/The-Market-for-Smart-Wearables.pdf
Earphones

## Slide 92
Voice assistants
Motion tracking
In-Ear Anatomy (health, security)
Face/Jaw Activity (eating, drinking)
Spatial acoustics
Noise Cancellation
Sensor and Hardware Layer
Beamforming to Speech
We are building a
software library
for Earable Computing

## Slide 94
Thanks to my excellent
students and collaborators …
Thanks to all of you
Jay Prakash
Visiting Student

## Slide 96
Thanks and
Questions?

## Slide 97
With this level of innovation …
just natural progress will be exciting.
Many features and functions as
low hanging fruits …

## Slide 98
But are there difficult research problems … high hanging hard nuts … that must be cracked to take earables to the next level … new capabilities and applications

## Slide 99
Arguments in favor, against …
Risks, pitfalls … and together
Does it make sense
If so, engineering and research questions
In the short and long run.

## Slide 100
Bone Channel Estimation
Hollow Noise Cancellation
Binaural Acoustics
Breathing Pattern
Indoor Positioning
IMU to Speech
Multi-IMU Dead Reckoning
Gazing Direction
Ear
Infection
Voice Assistant
Ambience Synthesis
Mood Sense
Acoustic AR
Ear Fingerprint Password
Eating Analytics
Tooth
Health
Ear Impulse Response
Blind Beamforming
Sensor and Hardware Layer
Software Library and Toolkit
App Store
Inaudible Speech

## Slide 101
Bone Channel Estimation
Hollow Noise Cancellation
Binaural Acoustics
Breathing Pattern
Indoor Positioning
IMU to Speech
Multi-IMU Dead Reckoning
Gazing Direction
Ear
Infection
Voice Assistant
Ambience Synthesis
Mood Sense
Acoustic AR
Ear Fingerprint Password
Eating Analytics
Tooth
Health
Ear Impulse Response
Blind Beamforming
Sensor and Hardware Layer
Software Library and Toolkit
App Store
Inaudible Speech

## Slide 102
Bone conduction
Neural processors
Multi-touch pads
Binaural sounds
RF radios (BLE, RFID)

## Slide 103
Many others are seeing the possibilities … so many efforts are ongoing
Qualcomm and Samsung chips
Bose frames
Nura headphones
Waverly Labs
Nokia eSense
…

## Slide 105
Navigate me to my flight gate
You are looking at a Picasso original
Good job: Salads for 3 straight days
Pausing music. Someone called you
Possible upper respiratory congestion
Give me a forest sound ambience
Follow me this way

## Slide 106
Bone conduction
Neural processors
Multi-touch pads
Binaural sounds
RF radios (BLE, RFID)

## Slide 107
Reading and typing becoming burden
  Voice/hearing offers seamless HCI
  Humans Tx/Rx only in [0,20 kHz] band
2. Phones, watches, fitbits … opened up the “quantified self” era
  However, mostly for hands, legs, lower body
  Head and upper body data valuable … and missing
  Earable is at the right vantage point
3. Ear devices socially accepted … far less
  Different from Google Glass
  Alexa based voice interfaces also helping prime the pipeline

## Slide 108
2005
2015
2022
2018

## Slide 109
2005
2015
2022
2018

## Slide 110
IMU to speech
Unvoice speech
Hollow noise cancellation
Bone conduction for cancellation
Indoor localization and gazing direction
Binaural and AR
Food and drink analytics
Breathing pattern
In-ear diagnosis via radar
Ear fingerprint for authentication
Blind beamforming

## Slide 114: The Wearable Market Projections

## Slide 115
Bone Channel Estimation
Hollow Noise Cancellation
Binaural Acoustics
Breathing Pattern
Indoor Positioning
IMU to Speech
Multi-IMU Dead Reckoning
Gazing Direction
Ear
Infection
Voice Assistant
Ambience Synthesis
Mood Sense
Acoustic AR
Ear Fingerprint Password
Eating Analytics
Tooth
Health
Ear Impulse Response
Blind Beamforming
Sensor and Hardware Layer
Software Library and Toolkit
App Store
Inaudible Speech

## Slide 116
2022
2018

## Slide 117
Alexa, Navigate me to …

## Slide 118
Alexa, Navigate me to …
3D sound
scape
Active noise cancellation

## Slide 119
Alexa, Navigate me to …
3D sound
scape
Jogging detected: Play pop
Active noise cancellation

## Slide 120
Mic
IMU
Spkr.
BLE
Vibration
Neural
Arrays
Optical
Jogging,
activity
Noise
cancellation

## Slide 121
Mic
IMU
Spkr.
BLE
Vibration
Optical
Neural
Arrays
Jogging,
activity
Noise
cancellation

## Slide 122
Mic
IMU
Spkr.
BLE
Vibration
Optical
Neural
Arrays

## Slide 123
Navigate me to my flight gate
Mic
IMU
Spkr.
BLE
Vibration
Optical
Neural
Arrays
Acoustic
Health
Sense
IMU
Speech

## Slide 124
Navigate me to my flight gate
You are looking at a Picasso original
Good job: Salads for 3 straight lunches
Pausing music. Someone called your name
Possible upper respiratory congestion
Give me a forest sound ambience
Follow me this way
Mic
IMU
Spkr.
BLE
Vibration
Optical
Neural
Arrays

## Slide 125
Jogging,
activity
Noise
cancellation

## Slide 126
3D sound
scape
Jogging detected: Play pop
Active noise cancellation
Ergonomics+ PPG, ECG
Alexa, Navigate me to …

## Slide 127
Our work looking at building an
Earable Computing Library

## Slide 128
Mic
IMU
Spkr.
BLE
Vibration
Optical
Neural
Arrays
Signal Processing
Wireless Comm./nets
Embedded
Systems
Motion Tracking
Machine
Learning
Many sensors, hardware

## Slide 129
Signal Processing
Wireless Comm./nets
Embedded
Systems
Motion Tracking
Machine
Learning
Mic
IMU
Spkr.
BLE
Vibration
Optical
Neural
Arrays
Acoustic
Health
Sense
IMU
Speech
Ear
Fingerprint
Navigate me to
my flight gate

## Slide 130
Bone Channel Estimation
Hollow Noise Cancellation
Binaural Acoustics
Breathing Pattern
Jaw, Skin motion
Multi-IMU Dead Reckoning
Indoor Location + Gazing Angle
Ear
Health
Energy efficient Siri
Ambience Synthesis
Acoustic AR
Ear Fingerprint
Eating Analytics
Tooth
Health
Ear Impulse Response
Body area network
Sensor and Hardware Layer
Software Library and Toolkit
App Store
Inaudible Speech
Beam
form
Password
Offload
Sound experience (Hollow ANC, Binaural, motion-adjusted surround sound …)
Motion activities and gestures (Localization, gazing, jogging, gym, …)
Micro motion (Speech, whisper, fingerprint, emotions, …)
Health (In-ear sensing, toothbrush, breathing, eating, …)
Comm, networks (beamform to mouth, mobile off-load,

## Slide 131
Bone Channel Estimation
Hollow Noise Cancellation
Binaural Acoustics
Breathing Pattern
Jaw, Skin motion
Multi-IMU Dead Reckoning
Indoor Location + Gazing Angle
Ear
Health
Energy efficient Siri
Ambience Synthesis
Acoustic AR
Ear Fingerprint
Eating Analytics
Tooth
Health
Ear Impulse Response
Body area network
Sensor and Hardware Layer
Software Library and Toolkit
App Store
Inaudible Speech
Beam
form
Password
Offload

## Slide 132
Jogging,
activity
Noise
cancellation

## Slide 133
Jogging,
activity
Noise
cancellation
But this is only the start …

## Slide 136
Jaw, Skin motion
Energy efficient Alexa
Sensor and Hardware Layer
Inaudible Speech
Password
Emotions
Micro Vibration Analysis

## Slide 137
Mic
IMU
Spkr.
BLE
Vibration
Optical
Neural
Arrays
Acoustic
Health
Sense
IMU
Speech
Ear
Fingerprint
Navigate me to
my flight gate

## Slide 138
Bone Channel Estimation
Hollow Noise Cancellation
Jaw, Skin motion
Indoor
Location
Energy efficient Alexa
Motion adjusted 3D Sound
Acoustic AR/VR
Body area network
Sensor and Hardware Layer
Inaudible Speech
Beam
form
Offload
Motion Activities and Gestures
Gazing Direction
Jogging, Gym
New Sound Experiences
Password
Emotions
Micro Vibration Analysis
Eating, Drinking Analytics
In-Ear Sensing
Breathing
Toothbrush
for kids
Health Sensing and Analytics
Communication and Networks

## Slide 139
Bone Channel Estimation
Hollow Noise Cancellation
Motion adjusted 3D Sound
Sensor and Hardware Layer
New Sound Experiences

## Slide 140
Bone Channel Estimation
Hollow Noise Cancellation
Motion adjusted 3D Sound
Sensor and Hardware Layer
New Sound Experiences
Temporal Bone
Cochlea
Ear Drum
Noise
Anti-Noise
Bone Conduction Speaker
Noise
Cancelation

## Slide 141
Bone Channel Estimation
Hollow Noise Cancellation
Motion adjusted 3D Sound
Sensor and Hardware Layer
New Sound Experiences
Hollow Noise Cancellation Earphones
=

## Slide 142
Indoor
Location
Acoustic AR/VR
Sensor and Hardware Layer
Motion Activities and Gestures
Gazing Direction
Jogging, Gym

## Slide 143
Indoor
Location
Acoustic AR/VR
Sensor and Hardware Layer
Motion Activities and Gestures
Gazing Direction
Jogging, Gym

## Slide 144
Jaw, Skin motion
Energy efficient Alexa
Sensor and Hardware Layer
Inaudible Speech
Password
Emotions
Micro Vibration Analysis

## Slide 145
Jaw, Skin motion
Energy efficient Alexa
Sensor and Hardware Layer
Inaudible Speech
Password
Emotions
Micro Vibration Analysis

## Slide 146
Jaw, Skin motion
Energy efficient Alexa
Sensor and Hardware Layer
Inaudible Speech
Password
Emotions
Micro Vibration Analysis

## Slide 147
Sensor and Hardware Layer
Eating, Drinking Analytics
In-Ear Sensing
Breathing
Toothbrush
for kids
Health Sensing and Analytics

## Slide 148
Sensor and Hardware Layer
Eating, Drinking Analytics
In-Ear Sensing
Breathing
Toothbrush
for kids
Health Sensing and Analytics
Different eating, drinking, tooth brushing activities

## Slide 149
Sensor and Hardware Layer
Eating, Drinking Analytics
In-Ear Sensing
Breathing
Toothbrush
for kids
Health Sensing and Analytics
Tooth Localization during Brushing

## Slide 150
Body area network
Sensor and Hardware Layer
Beam
form
Offload
Communication and Networks

## Slide 151
Body area network
Sensor and Hardware Layer
Beam
form
Offload
Communication and Networks
x
hl2
hl1
hr2
hr1
y = hl2 hl1 x + hr2 hr1 x
Feedback y
Feedback y

## Slide 152
Bone Channel Estimation
Hollow Noise Cancellation
Binaural Acoustics
Breathing Pattern
Indoor Positioning
IMU to Speech
Multi-IMU Dead Reckoning
Gazing Direction
Ear
Infection
Voice Assistant
Ambience Synthesis
Mood Sense
Acoustic AR
Ear Fingerprint Password
Eating Analytics
Tooth
Health
Ear Impulse Response
Blind Beamforming
Software Library and Toolkit
App Store
Inaudible Speech
Sensor and Hardware Layer

## Slide 153
A B C …
A B C …
a b c …
a b c …
Path #2 (1st Echo)
Path #3 (2nd Echo)
Path #1 (Direct Path)
a b c …
a b c …
Pause Opportunity

## Slide 154
Iterative Align
and Cancel (IAC)
Algorithm