## Slide 1: Assertion based verification
ECE 598 SV
Shobha Vasudevan (slides from lecture co-taught with Harry Foster, Mentor Graphics)
PLEASE DO NOT DISTRIBUTE WITHOUT PERMISSION

## Slide 3: Assertion Language and Library Standards
2004
2005
2006
1993-1997
1998
1999
2000
2001
2002
2003
Assertion Languages
Assertion Libraries
Intel
FTL ForSpec
Sun -> Synopsys
OVA
v2.0
IBM
Sugar 2.0
PSL v1.1
PSL v1.01
SVA v3.1
HP
Verplex
OVL
Accellera
SMAC
OVL
OVA
SVA
v3.1a
Vera/TXP
Sugar
RCTL
SVA
IEEE Std 1800-2005
PSL IEEE Std 1850-2005
OVL
1.0 R4
OVL
1.5
OVL
1.6 1.7
SVA v3.0
Sugar 1.0
Verisity
Temporal e
Motorola
CBV
0-In/Mentor
CheckerWare
CTL (1981)
LTL (1977)
Notes: Assertion languages evolved from academic logic languages
  Key benefits are:
  Temporal (time sequence) expressions
  Compact syntax for checking
  Flexibility to express custom properties
Verification IP libraries evolved to make design checking easy
  Key benefits are:
  Easy to use
  Pre-verified
  Re-usable

## Slide 4: IEEE 1850 PSL Example
gnt[0]
req[0]
clk
gnt[1]
Arbiter
req[0]
req[1]
gnt[0]
gnt[1]
assert never ( { rose(req) ; { !gnt[0] [+] } && { gnt[1] [->2] } } ) @(posedge clk);

## Slide 5: IEEE 1800 SystemVerilog Example
error
assert property ( @(posedge clk) disable iff (~reset_n)
start |=> (!start throughout done [->1]) );
done
start
clk

## Slide 6: Accellera OVL Example
error
Semantics
  Between start_event and end_event inclusive, test_expr must not change
assert_win_unchange #(0,8) addrStbl ( clk, rst_n, we, addr, done);
severity
width
start_event
end_event
test_expr
clk
we
addr[7:0]
done
8’b0
8’b1

## Slide 7: Industry Standards Usage
Source: 2007 Far West Research and Mentor Graphics

## Slide 8: Assertions Improve Observability Reduces time-to-bug
Testbench
Reduce debugging up to 50% [CAV 2000, IBM FoCs paper]
Bugs detected closer to their source due to improved observability
=
=
Bugs missed due to poor observability

## Slide 9
Ability to Verify
Ability to Design
Ability to Fabricate
Design Gap
Verification Gap
Design Size in Millions of Gates
9
Based on data from the 2003 ITRS study and Collett International 2004 FV Survey
The Verification Gap
  Many companies still using 1990’s verification technologies
  Traditional verification techniques can’t keep up
Verification Trends
(57 % / yr))
(41 % / yr))
(25 % / yr))
Notes: 9
Design productivity Increases due to:
  Synthesis
  IP/Reuse
The verification gap. We define the verification gap as follows. Advances in manufacturing technologies has made feature sizes smaller and thus, more functionality can be incorporated to an ever shrinking die size. To leverage this, advances in HDLs, synthesis, and the availability of ready-to-use IP and/or design reuse allow large designs to be implemented rather quickly. However…
There is a big gap between what can be designed and what can be verified. Verification has become the limiting factor on what can be safely designed. The good news is that this gap can be closed. If companies move away from their comfort zone of 1990’s verification techniques, and start employing more advanced techiques that better serve complex devices, the gap can be dramatically reduced.

## Slide 10
Concurrency Challenge
Packet-Based Design
Transaction Layer Packets
Data-Link Layer Packets
Retry Buffer
Arbiter
Tx
Rx
From
Fabric
To
PHY
From Rx Channel

## Slide 11: ABV Industry Adoption

## Slide 12: Published Data on Assertions Use
Kantrowitz and Noack [DAC 1996]
Taylor et al. [DAC 1998]
Assertion Monitors 34%
Cache Coherency Checkers 9%
Register File Trace Compare 8%
Memory State Compare 7%
End-of-Run State Compare 6%
PC Trace Compare 4%
Self-Checking Test 11%
Simulation Output Inspection 7%
Simulation Hang 6%
Other 8%
Assertion Monitors 25%
Register Miscompare 22%
Simulation "No Progress” 15%
PC Miscompare 14%
Memory State Miscompare 8%
Manual Inspection 6%
Self-Checking Test 5%
Cache Coherency Check 3%
SAVES Check 2%
17% of bugs found by assertions on Cyrix M3(p1) project [Krolnik '98]
50% of bugs found by assertions on Cyrix M3(p2) project [Krolnik ‘98]
85% of bugs found using over 4000 assertions on an HP server chipset project [Foster and Coelho HDLCon 2001]
Thousands of assertions in Intel Pentium project [Bentley 2001]
10,000 OVL assertion in Cisco project [Sean Smith 2002]
© DAC Tutorial 2003

## Slide 13: Sun Assertion-Based Verification of a 32 thread SPARC™ CMT Processor [Turumella, Sharma, DAC 2008]
Category | Unique | Instantiated
Low-Level | 3912 | 132773
Interface | 5004 | 44756
High-Level | 1930 | 18618

## Slide 14: Sun Assertion-Based Verification of a 32 thread SPARC™ CMT Processor DAC 2008, Turumella, Sharma
>50%
85%
Category | Unique | Instantiated
Low-Level | 3912 | 132773
Interface | 5004 | 44756
High-Level | 1930 | 18618

## Slide 15: ABV Bus-Based Design Example Using SystemVerilog Assertions (SVA)
AHB
I/F
Datapath
FIFO
I/F
Control
Bridge
Datapath
FIFO
CPU 1
CPU 2
Memory
Controller
Graphics
Controller
Arbiter
APB
UART
Timer

## Slide 16: Assertion Building Blocks Specifying A Sequence in SVA
start
clk
transfer
start ##1 transfer
Sequence
  Temporal delay ##n (where n is an integer)

## Slide 17: Assertion Building Blocks Specifying A Sequence in SVA
start
clk
transfer
Sequence
  Temporal delay ##n
start ##2 transfer

## Slide 18: Assertion Building Blocks SVA Properties
Properties
  Overlapping sequence implication operator |->
ready ##1 start |-> go ##1 done
ready
clk
start
go
done

## Slide 19: SVA Language Structure
Properties
  Non-overlapping sequence implication operator |=>
ready ##1 start |=> go ##1 done
ready
clk
start
NOTE: start |=> go is the same as start |-> ##1 go
go
done

## Slide 20: Building Blocks SVA Properties
Properties
  Creating named properties
property p_valid_transaction;
@(posedge clk)
ready ##1 start |=> go ##1 done;
endproperty
assert property ( p_valid_transaction );

## Slide 21: Nonpipelined Bus Interface
Slave 0
clk
rst_n
sel[0]
en
write
addr
I/F
Master
I/F
wdata
rdata

## Slide 22: Non-Burst Write Cycle The Only Legal Behavior!
0 1 2 3 4
addr
Addr 1
write
sel[0]
en
wdata
Data 1
conceptual
state
INACTIVE
START
ACTIVE
INACTIVE
Notice that !(sel[0]==0 & en==1) is not a legal state of the bus!

## Slide 23: Non-Burst Read Cycle The only legal behavior!
addr
Addr 1
write
sel[0]
en
rdata
Data 1
0 1 2 3 4
conceptual
state
INACTIVE
START
ACTIVE
INACTIVE
Notice that !(sel[0]==0 & en==1) is not a legal state of the bus!

## Slide 24: Conceptual Bus State Transitions
INACTIVE
sel[0] == 0
en == 0
START
sel[0] == 1
en == 0
ACTIVE
sel[0] == 1
en == 1
transfer
no transfer
no transfer
setup
setup

## Slide 25: Bus Properties
Property Name | Description
p_valid_inactive_transition | Only INACTIVE or START states follows INACTIVE
p_valid_start_transition | Only ACTIVE state follows START
p_valid_active_transition | Only INACTIVE or START states follows ACTIVE
p_no_error_state | Bus state must be valid: !(sel[0]==0 & en==1)
INACTIVE
sel[0] == 0
en == 0
START
sel[0] == 1
en == 0
ACTIVE
sel[0] == 1
en == 1
transfer
no transfer
setup
setup

## Slide 26: Use Modeling Code to Simplify Coding
bus_inactive = ~sel[0] & ~en;
bus_start = sel[0] & ~en;
bus_active = sel[0] & en;
bus_error = ~sel[0] & en;
INACTIVE
sel[0] == 0
en == 0
START
sel[0] == 1
en == 0
ACTIVE
sel[0] == 1
en == 1
transfer
no transfer
setup
setup

## Slide 27: Formalize Properties
property p_valid_inactive_transition;
@(posedge clk) disable iff (bus_reset)
( bus_inactive) |=>
((bus_inactive) || (bus_start));
endproperty
assert property (p_valid_inactive_transition);
Property Name | Description | 
Bus legal treansitions |  | 
p_valid_inactive_transition |  | Only INACTIVE or START states follows INACTIVE
INACTIVE
sel[0] == 0
en == 0
START
sel[0] == 1
en == 0
ACTIVE
sel[0] == 1
en == 1
transfer
no transfer
setup
setup

## Slide 28: Formalize Properties
property p_valid_start_transition;
@(posedge clk) disable iff (bus_reset)
( bus_start ) |=> ( bus_active );
endproperty
assert property (p_valid_start_transition);
Property Name | Description
Bus legal treansitions | 
p_valid_start_transition | Only ACTIVE state follows START
INACTIVE
sel[0] == 0
en == 0
START
sel[0] == 1
en == 0
ACTIVE
sel[0] == 1
en == 1
transfer
no transfer
setup
setup

## Slide 29: Improved Observability
0010100101010001110101001110101010100000000011101011011011110111
Slave 0
clk
rst_n
sel[0]
en
write
addr
I/F
Master
I/F
wdata
rdata
A
A
A
A

## Slide 30: Introduction to SVA
Assertions allow us to specify design intent in a way that lends itself to automation
// Assert that the grants for our simple arbiter are mutually exclusive
Arbiter
req0
req1
clk
reset_n
grant0
grant1

## Slide 31: Introduction to SVA
For our arbiter example, we can write a Boolean expression for the error condition, as follows:
Arbiter
req0
req1
clk
reset_n
grant0
grant1
(grant0 & grant1) // error condition

## Slide 32: Introduction to SVA
module arbiter (clk, rst_n, req0, req1, grant0, grant1);
. . .
always @(posedge clk or negedge rst_n) begin
if (rst_n != 1’b0)
if (grant0 & grant1)
$display (“ERROR: Grants not mutex”);
. . .
endmodule
Error
Condition
Boolean
Expression

## Slide 33: Introduction to SVA
module arbiter (clk, rst_n, req0, req1, grant0, grant1);
. . .
assert property (@(posedge clk) disable iff (~rst_n)
!(grant0 & grant1));
. . .
endmodule

## Slide 34: SVA Language Structure
Checker packaging
assert, assume, cover
Specification of behavior; desired or undesired
How Boolean events are related over time
True or false
Boolean Expressions
Sequences (Sequential Expressions)
Properties
Directives (assert, cover)
Assertion
Units
Notes: This slide simply shows the different layers. Simply point out that booleans and sequences are used to build the properties and that these properties are used with a directive to tell the simulator what to do
with them. And both PSL and SVA have the ability to package assertions in separate files.

## Slide 35: SVA Language Structure
Boolean Expressions
Sequences (Sequential Expressions)
Properties
Directives (assert, cover)
Assertion
Units
rst_n
!(grant0 & grant1)
clk
error
assert
property (@(posedge clk) disable iff (~rst_n)
!(grant0 & grant1));
Notes: This slide simply shows the different layers. Simply point out that booleans and sequences are used to build the properties and that these properties are used with a directive to tell the simulator what to do
with them. And both PSL and SVA have the ability to package assertions in separate files.

## Slide 36: SVA Language Structure
SVA contains two types of assertions:
  Immediate and concurrent
Immediate assertions evaluate within the context of a procedural block
  Similar to an if statement
  Check to see if a conditional expression holds
    If not, the verification tool generates an error message

## Slide 37: SVA Language Structure
Immediate assertions within a procedural block
module my_arb (. . . );
. . .
always @* begin // arbiter code
. . .
if (rst_n)
assert (!(grant0 & grant1));
. . .
end
endmodule

## Slide 38: SVA Language Structure
Concurrent assertions evaluate concurrently with respect to other procedural blocks
  Unlike immediate assertions that evaluate during a particular instance in which the line of procedural code containing the assertion is executed

## Slide 39: SVA Language Structure
Concurrent assertions outside procedural blocks
module my_arb (. . . )
always @* begin // arbiter code
. . .
end
assert property ( @(posedge clk) !(grant0 & grant1) );
endmodule

## Slide 40: SVA Language Structure
SVA provides a mechanism to asynchronously disable an assertion during a reset using the SVA disable iff clause
assert property (@(posedge clk) disable iff (~rst_n)
!(grant0 & grant1));

## Slide 41: SVA Language Structure
Sequences
  So far we have examined simple assertions
    A Boolean expression must hold at every clock
  Now we introduce SVA sequences
    Multiple Boolean expressions that are valuated in a linear order of increasing time
Boolean Expressions
Sequences (Sequential Expressions)
Properties
Directives (assert, cover)
Assertion
Units

## Slide 42: SVA Language Structure
start
clk
transfer
start ##1 transfer
Sequence
  Temporal delay ##n — where n is an integer

## Slide 43: SVA Language Structure
start
clk
transfer
start ##2 transfer
Sequence
  Temporal delay ##n — where n is an integer

## Slide 44: SVA Language Structure
start
clk
transfer
Sequence
  Temporal delay ## with range [m:n]
start ##[0:2] transfer

## Slide 45: SVA Language Structure
start
clk
transfer
Sequence
  Consecutive repetition [*m] or [*m:n]
start[*2] ##1 transfer

## Slide 46: SVA Language Structure
start
clk
transfer
Sequence
  Consecutive repetition [*m] or range [*m:n]
start[*1:2] ##1 transfer

## Slide 47: SVA Language Structure
start
clk
transfer
Sequence
  Consecutive repetition [*m] or range [*m:n]
start[*1:2] ##1 transfer

## Slide 48: SVA Language Structure
start
clk
transfer
Sequence
  Non-consecutive repetition [=m] or [=m:n]
start[=2] ##1 transfer
start[=2] == !start[*0:$] ##1 start ##1 !start[*0:$] ##1 start ##1 !start[*0:$]
[*0:$] represents zero to infinity

## Slide 49: SVA Language Structure
start
clk
transfer
Sequence
  Goto non-consecutive repetition [->m] or [->m:n]
start[->2] ##1 transfer
start[->2]  !start[*0:$] ##1 start ##1 !start[*0:$] ##1 start
[*0:$] represents zero to infinity

## Slide 50: SVA Language Structure
Properties
Boolean Expressions
Sequences (Sequential Expressions)
Properties
Directives (assert, cover)
Assertion
Units

## Slide 51: SVA Language Structure
Properties
  Overlapping sequence implication operator |->
ready ##1 start |-> go ##1 done
ready
clk
start
go
done
assertion property ( @(posedge clk) ready ##1 start |-> go ##1 done );

## Slide 52: SVA Language Structure
Properties
  Non-overlapping sequence implication operator |=>
ready ##1 start |=> go ##1 done
ready
clk
start
go
done
NOTE: A |=> B is the same as A |-> ##1 B

## Slide 53: SVA Language Structure
Named properties and sequences
  To facilitate reuse, properties and sequences can be declared and then referenced by name
  Can be declared with or without parameters
sequence op_retry;
(req ##1 retry);
endsequence
sequence cache_fill(req, done, fill);
(req ##1 done [=1] ##1 fill);
endsequence

## Slide 54: SVA Language Structure
Named properties and sequences
sequence s_op_retry;
(my_req ##1 my_retry);
endsequence
sequence s_cache_fill(rdy, done, fill);
(rdy ##1 done [=1] ##1 fill);
endsequence
assert property ( @(posedge clk) disable iff (!reset_n)
s_op_retry |=> s_cache_fill (my_rdy,my_done,my_fill));

## Slide 55: SVA Language Structure
property p_en_mutex(en0, en1);
@(posedge clk) disable iff (~reset_n)
~(en0 & en1);
endproperty
assert property (p_en_mutex(en[0], en[1]));
Named properties and sequences

## Slide 56: SVA Language Structure
System functions
  $onehot (<expression>)
    Returns true if only one bit of the expression is high
  $onehot0 (<expression>)
    Returns true if at most one bit of the expression is high
  $isunknown (<expression>)
    Returns true if any bit of the expression is X or Z
    This is equivalent to ^<expression> === ’bx

## Slide 57: SVA Language Structure
System functions
$rose( expression )
$fell( expression )
$stable( expression )
$past( expression [, number_of_ticks] )

## Slide 58: Introduction to SVA
Some assertions require additional modeling code
  In addition to the assertion constructs
// Assert that the FIFO controller cannot overflow nor underflow
put
get
data_in
clk
rst_n
data_out
FIFO
full
empty
Controller
clk
rst_n

## Slide 59: Introduction to SVA
// assertion modeling code – not part of the design
`ifdef ASSERT_ON
int cnt = 0;
always @(posedge clk)
if (!rst_n)
cnt <= 0;
else
cnt <= cnt + push – pop;
// assert no overflow
assert property (@posedge clk disable iff (!rst_n)
!((cnt + push – pop) > `DEPTH));
// assert no underflow
assert property (@posedge clk disable iff (!rst_n) !((cnt + push - pop) < 0);
`endif

## Slide 60: Introduction to SVA
SVA provides local variable support within properties and sequences
  Can eliminate the need for extra modeling code
property req_gnt;
logic [3:0] lv_id; @(posedge clk) disable iff (~rst_n)
($rose(req), lv_id=req_id) |=> (gnt, gnt_id==lv_id);
endproperty

## Slide 61: Summarize SVA Structure
Boolean Expressions
Sequences (Sequential Expressions)
Properties
Directives (assert, cover)
Assertion
Units
rst_n
!(grant0 & grant1)
clk
error
assert
property (@(posedge clk) disable iff (~rst_n)
!(grant0 & grant1));
Notes: This slide simply shows the different layers. Simply point out that booleans and sequences are used to build the properties and that these properties are used with a directive to tell the simulator what to do
with them. And both PSL and SVA have the ability to package assertions in separate files.

## Slide 62: SVA Summary
Language structure
## sequence operator
Repetition operators
Overlapping |-> and non-overlapping |=> implication operator
Named properties
Directives: assert