## Slide 1: Sequential Equivalence Checking
Prof. Shobha Vasudevan

## Slide 2: Sequential circuits
What are sequential circuits?
How are they different from combinational circuits?
How do you describe/represent the functionality of sequential circuits?

## Slide 3: FSM Verification: Reminders
What’s in an FSM?
  States: unique bit pattern represents each state; FFs store state
  External inputs: inputs from the outside world
  Next state logic: from current state and external inputs, this makes the inputs to the FFs that determine the next state at the next clock tick
  Output logic: from states (and maybe inputs) makes combinational FSM outputs
  Clock: synchronizes everything; only states changes on clock tick
Next State
Logic
Output Logic
D Q

## Slide 4: Definitions
In mathematical terms, a (completely specified, deterministic) Finite State Machine (FSM) of Mealy type is a 6-tuple
⟨I, S,𝛿,S0,O,𝜆⟩
where:
I is the input alphabet i.e., a finite, non-empty set of input values;
S is the (finite, non-empty) set of states;
𝛿: 𝑆 × 𝐼 → 𝑆 is the next-state function;
𝑆0 ⊆ 𝑆 is the set of initial (reset) states;
O is the output alphabet;
𝜆 : 𝑆 × 𝐼 → 𝑂 is the output function;
How is this definition different for Moore machines?
Notes: Answer: 𝜆 : 𝑆 -> 𝑂 is the output function;

## Slide 5: Example state machine
A
D
E
B
C
F
0/0
1/1
0/0
0/0
0/0
0/0
1/0
1/1
1/0
1/1
1/0
0/0

## Slide 6: Example
Present State | Next State/Output | 
 | x = 0 | x = 1
A (Start) | E/0 | D/1
B | D/0 | F/0
C | E/0 | B/1
D | B/0 | F/0
E | C/0 | F/1
F | B/0 | C/0
Give the tuple ⟨I, S,𝛿,S0,O,𝜆⟩ and draw the state diagram for the following Flow Table:

## Slide 7: Example
Answer:
I = {0,1};
S = {A,B,C,D,E,F};
O = {0,1}
𝛿(𝐴,0)=𝐸, 𝛿(𝐴,1)=𝐷, 𝛿(𝐵,0)=𝐷,
  𝛿(𝐵,1)=𝐹, 𝛿(𝐶,0)=𝐸, 𝛿(𝐶,1)=𝐵,
  𝛿(𝐷,0)=𝐵, 𝛿(𝐷,1)=𝐹, 𝛿(𝐸,0)=𝐶,
  𝛿(𝐸,1)=𝐹, 𝛿(𝐹,0)=𝐵, 𝛿(𝐹,1)=𝐶;
S0 = {A}
𝜆(𝐴,0)=0, 𝜆(𝐴,1)=1, 𝜆(𝐵,0)=0,
  𝜆(𝐵,1)=0, 𝜆(𝐶,0)=0, 𝜆(𝐶,1)=1,
  𝜆(𝐷,0)=0, 𝜆(𝐷,1)=0, 𝜆(𝐸,0)=0,
  𝜆(𝐸,1)=1, 𝜆(𝐹,0)=0, 𝜆(𝐹,1)=0;

## Slide 8: Example
A
D
E
B
C
F
0/0
1/1
0/0
0/0
0/0
0/0
1/0
1/1
1/0
1/1
1/0
0/0

## Slide 9: Incomplete Specification
An FSM is incompletely specified if the next-state function and/or the output functions are specified only for some combinations of inputs and present states.

## Slide 10: Example
Is there any discrepancy between these representations?
I | PS | NS | O
0 | s1 | s4 | 0
1 | s1 | s3 | 0
0 | s2 | - | -
1 | s2 | s1 | -
0 | s3 | s1 | 1
1 | s3 | - | 1
0 | s4 | s2 | 1
1 | s4 | s3 | 1
s1
s3
0/0
s2
s4
1/0
1/-
0/1
0/1
1/1
Notes: Answer: See next slide

## Slide 11: FSM Verification: What’s the Problem?
Several scenarios
  You have a “trusted” implementation of the machine that you know is correct (but maybe not optimal as hardware) and a “real” implementation as gates. Are they the same?
  You have an “old” implementation in one technology, and a “new” implementation in another technology (eg, a different tech library). Is old == new?
Why is this hard?
  Because of what “same” means here
  Has to do with behavior over time -- this temporal dependence is new for us...
  We need to be more precise

## Slide 12: Equivalent FSMs
Means this:
  Start them in some known “equivalent” states; clock starts running
  For every possible combination of inputs over future clock ticks, two machines will have identical outputs
  (Doesn’t say anything about logic delays or low level stuff like that; just think about ideal clock ticks here...)
FSM 1
FSM 2

## Slide 13: FSM Equivalence: Easy Case
Sometimes this isn’t too hard: special case
  Suppose 2 FSMs have identical state encodings: same #bits, same unique bit pattern for each state, same kinds of FFs
Then this reduces to combinational equiv. checking
FSM 1
FSM 2

## Slide 14: FSM Equivalence: Hard Case
FSMs not always so easy to check. More general case:
  4 states. 2 state variables p,q. 1 input x. 1 output z. D FFs.
A/0
B/0
C/0
State: pq=00
pq=01
pq=10
D/1
pq=11
x=0
x=1
x=0
x=0,1
x=1
x=0,1
Input PS NS
x pq p+q+
0 0 0
0 1
1 0
1 1
1 0 0
0 1
1 0
1 1
pq
x
00 01 11 10
0
1
pq
x
00 01 11 10
0
1
p+ (= D input on p FF)
q+ (= D input on q FF)
p
q
0 1
0
1
z

## Slide 15: FSM1 Implementation
It looks like this...
D Q
D Q
Next State Logic
Output Logic
State
Logic

## Slide 16: FSM2: Same Behavior, Different Implementation
Let’s implement it as a 1-hot machine
  Now, 4 state variables: abcd; again D FFs, but now 4 of them
A/0
B/0
C/0
State: abcd=1000
abcd=0100
abcd = 0010
D/1
abcd=0001
x=0
x=1
x=0
x=0,1
x=1
x=0,1
Can just read off the NS logic
1 hot example transition...

## Slide 17: FSM 2 Implementation
It looks like this
D Q
D Q
Next State Logic
Output Logic
State
Logic
D Q
D Q

## Slide 18: FSM Equivalance Checking
This is why it’s hard
  Cannot just look at the logic now and state they are the same
  Need a whole new, systematic method that deals with temporal aspect of things here, and the possible differences in encodings
Next State Logic
a+ = d
b+ = ax’ + bx’
c+ = ax + c
d+ = bx
Output Logic
z = d
FSM 2 Logic
Next State Logic
p+ = pq’ + p’x
q+ = p’q + p’x’
Output Logic
z = pq
FSM 1 Logic
p
q
z
p+
q+
z
a+
b+
c+
d+
a
b
c
d
x
x

## Slide 19: FSM Formal Verification Strategy
4 Big Ideas
Sets as Boolean functions
  Use BDDs to represent sets of things
Symbolic representation of FSMs
  Represent them as sets of allowable transitions
Reachability analysis
  Represents the sets of FSM states you can get to from the start state on 0 clock ticks, 1 clock tick, 2 ticks, etc.
Cross-product FSMs
  Take 2 FSMs you want to compare for equivalence, and make 1 single new special machine, on which reachability analysis == verification

## Slide 20: State Minimization Example

## Slide 21: Distinguishing Sequences
Definition: Consider two states s and t of a given FSM, and a k-string (sequence of input symbols) x = (x0,x1,…,xk-1). Suppose the string x produces one run Run_s = (s0,s1,…,sk-1), when starting from s0 (s=s0) and another run Run_t = (t0,t1,…,tk-1), when starting from t0 (t=t0). Further, let zs = (z0s,z1s,…,zk-1s) and zt = (z0t,z1t,…,zk-1t) be the corresponding output strings.
The string x is said to be a length-k distinguishing sequence for states s and t if and only if:
zk-1s ≠ zk-1t

## Slide 23: Equivalent States
Definition: Two states s and t are k-equivalent, written s ≡k t, if and only if there does not exist a distinguishing sequence of length k or less for these states. Two states s and t are equivalent if and only if they are n-equivalent, where n = |S|.
|S| is the cardinality of S, i.e. total number of states in S.

## Slide 24: Equivalent States
Theorem: s ≡k+1 t if and only if s ≡k t and ∀𝑥∈𝑋, 𝑠𝑥 ≡𝑘 𝑡𝑥 , where sx and tx are the x-successors of s and t.
For this particular case, x can be the immediate next state of s or t
Notes: It is clearer when treating x as 1 more state after the k input string. The theorem itself is not well defined. Refer to text book p266.

## Slide 26: Equivalence
Definition: We define the binary relation 𝜉𝑘(𝑠,𝑡) ⊂ 𝑆 × 𝑆 as
𝜉𝑘={(𝑠,𝑡) | 𝑠≡𝑘 𝑡)}.
We also denote the 𝑚𝑘 equivalence classes of the relation 𝜉𝑘 by 𝐵𝑖𝑘, 𝑖=1,…,𝑚𝑘

## Slide 27: Equivalence
𝜉k is an equivalence relation
  Reflexive: A state is k-equivalent to itself
  Symmetric: s ≡k t ⇒ t ≡k s
  Transitive: s ≡k t, t ≡k u ⇒ s ≡k u

## Slide 28: Minimize this state machine
A
D
E
B
C
F
0/0
1/1
0/0
0/0
0/0
0/0
1/0
1/1
1/0
1/1
1/0
0/0

## Slide 31: Equivalence
Present State | Next State/Output | 
 | x = 0 | x = 1
A (Start) | E/0 | D/1
B | D/0 | F/0
C | E/0 | B/1
D | B/0 | F/0
E | C/0 | F/1
F | B/0 | C/0
For Example:
States in B11 = {A,C,E} are 1-equivalent
States in B21 = {B,D,F} are also 1-equivalent
  A and B are 1-distinguishable
A,C,E also 2-equivalent
  Is one equivalent
  Their successors under input 0 (E,E,C) are 1-equivalent
  Their successors under input 1 (D,B,F) are also 1-equivalent
F not 2-equivalent to B
  Input 1: F goes to C, B goes to D
    C and D are not 1-equivalent
{A,C} and {B,D} are fully equivalent

## Slide 32: Equivalence Checking

## Slide 33: Partition-Refinement
Phase 1:
Initialize P0 and P1 as partitions with one block containing all S states
Gather a vector ox of the x outputs in each state sj
Use ox to partition the vector into blocks with the same output value, Px1
Refine P1
Goal: Determine the set of all equivalent state pairs of a given FSM.

## Slide 34: Refinement
Definition: If Pa = {Bia}, and Pb = {Bjb}, then Pa ⋅ Pb, called the meet, or intersection, of partitions Pa, and Pb, is given by:
Pa ⋅ Pb =∪ij(Bia ∩ Bjb)
the meet Pc of two partitions Pa and Pb is a refinement of both Pa and Pb.
Notes: Change a and b to subscript. Explain that it is value of x.

## Slide 35: Partition-Refinement
Example (Phase 1):
Initial partition P1 = P0 = {B1}, where B1 = {A,B,C,D,E,F}.
First for loop:
  x = 0: o0 = (0,0,0,0,0,0), s = (A,B,C,D,E,F), PARTITION returns P01 = {S}, P1 = P1 ∩ P01 = {S}
  x = 1: o0 = (1,0,1,0,1,0), s = (A,B,C,D,E,F), PARTITION returns P11 = {B1x, B2x}, where B1x = {A,C,E} and B2x = {B,D,F}. P1 = P1 ∩ P11 = {{A,C,E},{B,D,F}}

## Slide 36: Partition-Refinement
Phase 2:
On each pass through the loop over k, we initialize Pk to the empty partition.
Loop through the blocks Bi of Pk-1 and compute Pik as a partition of Bi.
  Gather a vector of the x-successors of the states in Bi.
  Compute the corresponding vector of partition block indices (in partition Pk-1).
  Partition Bi into blocks with like block indices
  Refine the result with the current Pik.

## Slide 37: Partition-Refinement
Example (Phase 2):
First Pass (k = 2)
  (block B,D,F)
    x = 0: s = (B,D,F), t0 = (D,B,B), b0 = (1,1,1), Pb10 = {Bi} = {{B,D,F}}.
    x = 1: s = (B,D,F), t1 = (F,F,C), b1 = (1,1,2), Pb11 = {{B,D},{F}}.
    Set union: P2 = {{B,D},{F}}
  (block A,C,E)
    No refinement
  P2 = {{B,D},{F},{A,C,E}}
Notes: Do k = 3… on board

## Slide 38: Partition-Refinement Algorithm
:
Sort and group by like outputs
Initialize refined block partition
Return: all states are 1-equivalent
Distinguishing path lengths
Initialize Pk
Sort and group by like block indices
Phase 1
Phase 2

## Slide 39: Cross Product Machine
Given 2 FSMs to check...
  Just FSM1, FSM2, with FSM2’s states given new names (A  α, B β, etc)...
A/0
B/0
C/0
State: pq=00
pq=01
pq=10
D/1
pq=11
x=0
x=1
x=0
x=0,1
x=1
x=0,1
α/0
β/0
κ/0
State: abcd=1000
abcd=0100
abcd = 0010
Δ/1
abcd=0001
x=0
x=1
x=0
x=0,1
x=1
x=0,1

## Slide 40: Cross Product Machine: FSM1  FSM2
What are the states in FSM1  FSM2? ( == “cross”)
  All pairs of possible states (FSM1 state, FSM2 state)
FSM1  FSM2 has 4*4=16 states
A/0
B/0
C/0
State: pq=00
pq=01
pq=10
D/1
pq=11
x=0
x=1
x=0
x=0,1
x=1
x=0,1
α/0
β/0
κ/0
State: abcd=1000
abcd=0100
abcd = 0010
Δ/1
abcd=0001
x=0
x=1
x=0
x=0,1
x=1
x=0,1

## Slide 41: Cross Product Machine: FSM1  FSM2
What are the state variables for FSM1  FSM2
  Easy, just “all” the state variables from FSM1 and from FSM2
D Q
D Q
Next State Logic
???
Output Logic
???
State
Logic
D Q
D Q
D Q
D Q
p
q
a
b
c
d

## Slide 42: Cross Product Machine: FSM1  FSM2
So, what then is the next-state logic for FSM1  FSM2?
  Easy again: just the 2 separate next-state blocks from FSM1, FSM2
D Q
D Q
Next State Logic
Output Logic
???
State
Logic
D Q
D Q
D Q
D Q
p
q
a
b
c
d
FSM1 Next State
Logic
FSM2 Next State
Logic

## Slide 43: Cross Product Machine: FSM1  FSM2
FSM 1
FSM 2
inputs
clock
== ?
FSM1 outputs
FSM2 outputs
Should always
be == 1 if
FSM1 = FSM2
So, what is the output logic for FSM1  FSM2
  Now, it’s different.
  The cross-product machine is really (up to now) just the 2 separate machines FSM1 and FSM2 running side-by-side
  We want to know: if we start them both in the same “equivalent” state, will we ever reach a “combined” state (FSM1 state vars, FSM2 state vars) where the outputs of the 2 machines are different

## Slide 44: Cross Product Machine: FSM1  FSM2
So, what is the output logic for FSM1  FSM2?
D Q
D Q
Next State Logic
Output Logic
State
Logic
D Q
D Q
D Q
D Q
p
q
a
b
c
d
FSM1 Next State
Logic
FSM2 Next State
Logic
FSM1 Output Logic
FSM2 Output Logic
=?

## Slide 45: Cross Product Machine Reachability Analysis
Where are we?
  We can build, mechanically, the cross product machine
What good is this?
  FSM1 and FSM2 are equivalent if, when started in the same initial “equivalent” states, it is never possible to reach a state where the output of the cross product machine == 0
  Put another way: output of cross product machine should always be ==1, for any combined state (FSM1 state, FSM2 state) we can reach from (FSM1 start, FSM2 start)
How do we do this?
  We already know how...

## Slide 46: Cross Product Reachability Analysis
Build the cross product machine
  Means build the next state logic, and the output logic for it
Do reachability analysis on [ FSM1  FSM2 ]
  In our little example, start with A=00, α = 1000 states: R0(p+,q+,a+,b+,c+,d+) = (p+’ )(q+’)( a+)(b+’)(c+’){d+’)
  Build R1, R2, ... RK until it stops changing
  Now, you know pairs of states it is possible to reach from (A, α) start state...

## Slide 47: Cross Product Reachability Analysis
What does this tell you?
  Pairs of states you can get to from (A, α)
  Example
A/0
B/0
C/0
State: pq=00
pq=01
pq=10
D/1
pq=11
x=0
x=1
x=0
x=0,1
x=1
x=0,1
Example: 2 ticks, A B D
Example: 2 ticks, α  β β
So, in R0 we have (A, α), and in R2 we will have...
α/0
β/0
κ/0
State: abcd=1000
abcd=0100
abcd = 0010
Δ/1
abcd=0001
x=0
x=1
x=0
x=0,1
x=1
x=0,1

## Slide 48: Verification via Reachability
OK, we can build Rk for this FSM1  FSM2
Now what?
  Want to know if we can reach a combined state where cross-product output ==0; consider this logic...
Output Logic
FSM1 Output Logic
FSM2 Output Logic
=?
Rk
p+
q+
a+
b+
c+
d+
==1 if (p+ q+, a+ b+ c+ d+)
is a reachable pair
==1 if output from p+ q+
same as output from
a+ b+ c+ d+
final

## Slide 49: Verification via Reachability
Look what happens
  Build a BDD for this ckt; it has 6 inputs p+ q+ a+ b+ c+ d+, has 1 output
  If the 2 FSMs are equivalent, then this output == constant 0 BDD
  If these 2 FSMs NOT equivalent, this is some BDD with a 1 node in it
  All we have to do is see if this BDD != constant 0 BDD, and we are done!

## Slide 50: Verification via Reachability
What did we do here?
  We turned the complex temporal problem of verification of equivalence for all inputs over all subsequent clock ticks...
  ...into a series of BDD exercises, ending in a satisfiability check on a single (big, nasty) BDD; if any pattern of inputs makes this BDD ==1, then machines not equivalent
Amazingly useful result
  Doable mechanically with a good BDD package
  Definitely NOT something you want to try to do by hand.
  On the HW, you get to do it for a similar pair of machines using the KBDD package to do the nasty Boolean manipulations

## Slide 51: Simpler Example
A/0
B/1
x=0
x=1
x=0,1
C/0
D/1
x=0
x=1
x=0
x=1
FSM 1
FSM 2
State p=0
p=1
State q=0
q=1
Next state:
p+ = p+x
Output
z = p
Next state:
q+ = q  x
Output
z = q

## Slide 52: Simple Example: Cross Product Reachability
What do we expect for reachability on FSM1 X FSM2?
R0 = { (A,C) }
R1 = reachable on 0 or 1 clock tick =
R2 = reachable on 0, 1, 2 clock ticks =
R3 = reachable on 0, 1, 2, 3 clock ticks =
A/0
B/1
x=0
x=1
x=0,1
C/0
D/1
x=0
x=1
x=0
x=1
FSM 1
FSM 2

## Slide 53: Cross Product Reachability Analysis
So, we get Rk = { AC, BD, BC } ... what is Boolean func?
OK, let’s make the cross product satisfiability logic
Output Logic
FSM1: z = p
FSM2: z = q
=?
Rk
p+
q+
==1 if (p+,q+) reachable
==1 if output from p+
same as output from q+

## Slide 54: Cross Product Reachability: Satisfiable?
Well, can you get a 1 out of this...?
Output Logic
FSM1: z = p
FSM2: z = q
=?
R
p+
q+
==1 if (p+,q+)
reachable
==1 if output from p+
same as output from q+
k

## Slide 55: Product machine
Purpose: Check whether two FSM are equivalent.
Where:

## Slide 56: Product machine
How to build:

## Slide 57: Product machine

## Slide 58: Equivalence Checking between FSMs
Reachability analysis
Definition: A state t is reachable from state s if there exists a string x which produces a run s, ending in state t. A state t is simply reachable if it is reachable from any state in

## Slide 59: Reachability analysis

## Slide 60: Equivalence Checking between FSMs
Error trace algorithm:
Find an error state in the product machine.
i.e:
Perform a backtrace operation showing how the error state may be reached from the initial state.

## Slide 61: Error trace algorithm
/*