## Slide 1: Testbench architecture
Shobha Vasudevan ( Slides from lecture co-taught with Mentor Graphics)
PLEASE DO NT DISTRIBUTE WITHOUT PERMISSION

## Slide 2: Agenda
Verification Planning
Testbench Architecture
Testbench Implementation
  SystemVerilog Basics
  OOP with SystemVerilog
  OVM Introduction

## Slide 3: Evolution of HVLs
2005
Spring
2007
OVM announced: R&D teams demonstrate OVM will run on both Mentor and Cadence simulators
OVM 1.0 released as open source
OVM 2.0
OVM Users guide
Unified sequences
TLM enhancements
Other capabilities
Jan 9
eRM
URM
AVM
2002
May 7
August
2007
OVM 1.1 update
Sept
2008
More capabilities to come!!
Q1
2009
Growing volume of Ecosystem products and services
OVM 2.0.1 update
Oct
2008
Notes: 3
This is the OVM collaboration roadmap. As we mentioned earlier, URM and AVM developed in parallel and customers recognized the similarities in the base classes. They asked us to bring AVM and URM together and we accomplished a proof of that concept by Aug 16, 2007. Since then, we launch OVM world with OVM 1.0 in January 2008 and we are now about to bring OVM 2.0 to the market.
The main benefits of OVM 2.0 are that we have unified the sequence methodology with Mentor and we are jointly delivering an OVM users guide. We will also enhance the reset methodology, Transaction Level Modeling (TLM), and configuration capabilities within the OVM.
Of course, OVM 2.0 will be available as open source on OVMworld just like OVM 1.0. And that’s not the end. We have collected many ideas from the OVM community and will provide more technology in the future with the same delivery mechanism.

## Slide 4: What is OVM?
Open
  Written in IEEE 1800 SystemVerilog
  Runs on any simulator supporting the IEEE 1800 standard
  Verified on Mentor Graphics’ Questa and Cadence’s Incisive Verification Platforms
  True open-source license agreement (Apache 2.0)
Interoperable
  Ensures VIP interoperability across ecosystem & simulators
  Enables VIP ‘plug and play’ functionality for designers
  Ensures interoperability with other high level languages
Proven
  Based on Mentor’s Advanced Verification Methodology (AVM) and Cadence’s Incisive URM methodology
  Incorporates best practices from >10 years of experience
Notes: Read slide, highlight that OVM is LRM SystemVerilog, and if the customer are unable to run the examples on their simulator, it’s because the simulator don’t support SystemVerilog.
We then suggest that the customer are requesting the vendor to work with the OVM team to help them run OVM.
Notes:
OVM is available in open source form
Apache-2.0 license
  http://opensource.org/licenses/apache2.0.php
Allows user to use, modify, and distribute code
Restrictions:
  cannot modify any copyright or other ownership marks
  cannot claim ownership
  cannot redistribute under another license
Large customers choosing OVM
  Project deployment
OVM infrastructure growing rapidly
  Training
  Consulting
  IP

## Slide 5: OVM = AVM + URM
OVM is a superset of both the AVM and URM
  Cadence’s Incisive Plan-to-Closure (IPCM) URM and Mentor’s Advanced Verification Methodology (AVM)
OVM enables backward compatibility with AVM 3.0 & URM 6.2
Mentor & Cadence committed to collaborative development of OVM
Project-to-Project Reuse
Block-to-System Reuse
Coverage-Driven
Environment Configuration
Incremental Adoption
Multi-Layered Sequences
TLM Communication
Common Messaging
OVM
Open, unified class library and methodology for interoperable VIP

## Slide 6: OVM = AVM + URM AVM forms the backbone of the OVM
AVM
TLM Communication
Constrained-Random Stimulus
Functional Coverage
Modularity & Reuse
Incremental Adoption
URM
TLM Communication
Sequential Stimulus Specification
UVC Encapsulation Strategy
Environment Configuration
OVM
TLM Communication
Constrained-Random & Sequential Stimulus
Functional Coverage
Greatest Flexibility for Modularity & Reuse
Environment Configuration
Incremental Adoption
AVM
TLM Communication
Constrained-Random Stimulus
Functional Coverage
Modularity & Reuse
Incremental Adoption
URM
TLM Communication
Sequential Stimulus Specification
UVC Encapsulation Strategy
Environment Configuration

## Slide 7: What is the news?
The first truly open, interoperable, and proven verification methodology based on the SystemVerilog IEEE 1800 language
Jointly developed by Cadence and Mentor Graphics
Delivers simulator, VIP, and high level language interoperability across companies and ecosystem
Scalable to system level

## Slide 8: OVM Benefits
Open
  Written in IEEE 1800 SystemVerilog
  Runs on any simulator supporting the IEEE 1800 standard
  Verified on Cadence’s Incisive and Mentor Graphics’ Questa Verification Platform
  True open-source license agreement (Apache 2.0)
Interoperable
  Ensures VIP interoperability across ecosystem & simulators
  Enables VIP ‘plug and play’ functionality for designers
  Ensures interoperability with other high level languages
Proven
  Based on Cadence’s Incisive Plan-to-Closure URM module and Mentor’s Advanced Verification Methodology (AVM)
  Incorporates Best Practices from >10 years of experiences

## Slide 9: OVM Description
OVM Class Library uses SystemVerilog language and runs on any compliant simulator
  Provides building blocks (objects) for verification environment
  Common set of low-level utilities
OVM Methodology
  Framework to create VIP
  Guidelines for how to use the class library
OVM Class Library
OVM Methodology
(documentation,
examples, code snippets)
SystemVerilog Language
VIP and Verification
Environment
IEEE 1800 Compliant
Simulator

## Slide 10: OVM Documentation
OVM Reference Guide
  Documents all ovm classes, methods and macros in the OVM library
OVM User Guide
  OVM Overview
  Transaction Level Modeling
  Developing Reusable Verification Components
  Assembling Tests and Testbenches
  Advanced Topics
    Phasing
    Factory & Overrides
    Sequence Control & Protocol Layering
  Detailed description of Xbus example
Notes: Yes, we know the user guide is in the works, AVM books still valid, as OVM is just the natural evolution of AVM

## Slide 11: OVM Concepts: Overview
Test/Testbench Separation
  Improves reusability
  Test customizes testbench
Flexible Component Instantiation
  Test can override testbench
Configurability
  Test controls
  Structural, run-time parameters
  Allows greater topological flexibility
Hierarchical Sequential Stimulus
  Simplified Test Writer interface
  Decouple stimulus from component hierarchy
TLM Communication
  Improves component modularity
  Enables plug-n-play reuse
Test
Env(Testbench)
VC
Component2
Component
VC
VC
VC

## Slide 12: OVM: Combine SystemVerilog and TLM to build a true, reusable methodology
12
Vertical Reuse
  From block to system in a single project
Horizontal Reuse
  Reuse of modules, libraries across projects
Platform Reuse
  Reuse of testbenches, assertions etc, across the tools
A
B
Testbench
A
B
Project A
A
B
Verification IP,
Methodology
Project B
A
B
A
B
Testbench
RTL Simulation TLM Modeling
Emulation

## Slide 13: A Layered Approach to Verification
Testbench-Specific
Analysis
Design-Specific
Operational
Protocol-Specific
Transactors
Stimulus Generator
/ Master
Slave
Abstractor
Abstractor
Stimulus/ Master
Slave
Coverage
Transaction-Level interfaces
Coverage
TLM DUT
Test (Config)
Notes: Modularity helps of connect and add stuff as needed.
Basic messages:
Transactors are protocol-specific and convert between pin-level communication to the dut and transaction-level communication to the environment.
Operational layer is transaction-level that describes the behavior of the world in which the dut operates and is design-specific.
  We provide stimulus generator and other example components for you
  Masters are bi-directional components that initiate transactions
  Operational layer can be subdivided into “high-level” and “low-level” behaviors/transactions (think “frame” vs. “packet”)
Analysis layer is testbench-specific to extract information about what’s happening and whether it’s correct
  Scoreboards compare, coverage collectors count
  Information can be extracted from anywhere in the operational layer via analysis ports. Where you extract depends on what specific information you want.
  Flexibility allows you to add additional analysis with minimal impact to existing environment, even late in the project
Test controller coordinates everything.
  Starts/configures other components
  Reacts to coverage or other information to adjust/stop behavior of components
  This is the part that the “test writer” writes.
Practical tip: Picking coverage from driver etc. allows coverage development before monitor is complete. Other similar developmentat steps facilitated by TLM modularity of analysis_ports. Both coverage and scoreboards.

## Slide 14: A Layered Approach to Verification
Design-Specific
Operational
Protocol-Specific
Transactors
Testbench-Specific
Analysis
DUT
Driver
Responder
Monitor
Monitor
Stimulus Generator
/ Master
Slave
Abstractor
Abstractor
Stimulus/ Master
Slave
Coverage
Scoreboard
Coverage
Pin-Level interfaces
Transaction-Level interfaces
Assertions
Test (Config)
Notes: Modularity helps of connect and add stuff as needed.
Basic messages:
Transactors are protocol-specific and convert between pin-level communication to the dut and transaction-level communication to the environment.
Operational layer is transaction-level that describes the behavior of the world in which the dut operates and is design-specific.
  We provide stimulus generator and other example components for you
  Masters are bi-directional components that initiate transactions
  Operational layer can be subdivided into “high-level” and “low-level” behaviors/transactions (think “frame” vs. “packet”)
Analysis layer is testbench-specific to extract information about what’s happening and whether it’s correct
  Scoreboards compare, coverage collectors count
  Information can be extracted from anywhere in the operational layer via analysis ports. Where you extract depends on what specific information you want.
  Flexibility allows you to add additional analysis with minimal impact to existing environment, even late in the project
Test controller coordinates everything.
  Starts/configures other components
  Reacts to coverage or other information to adjust/stop behavior of components
  This is the part that the “test writer” writes.
Practical tip: Picking coverage from driver etc. allows coverage development before monitor is complete. Other similar developmentat steps facilitated by TLM modularity of analysis_ports. Both coverage and scoreboards.

## Slide 15: OVM Concepts: Separation
Test
Separate architectural details from end-user
Testcase customizes testbench environment
  Instantiate and configure the environment
    Components within that env.
  Tests are short, clear and descriptive
  Easy to maintain
    Changes are done in a central location
Test and environment can be derived
  Build a base classes
    Testcases
      Derivatives change stimuli kinds, negative testing etc.
    Environments
      Topology for TLM, RTL connections etc.
Testcases…
Env(Testbench)
Env1(Testbench)
Env2(Testbench)
Env3(Testbench)
Env4(Testbench)

## Slide 16: OVM Concepts: Phasing
Instantiate top-level env
Build/config components
Define connections
Resolve bindings
Configure components
Execute test (run task)
Gather information
Check results
Report results
Built-in phases handle the basics
  All phases run in-order
User can define additional phases
  Can be inserted anywhere in the list
  Automatically run in order
end_of_elaboration
start_of_simulation
run
extract
check
report
new
Construction
Elaboration
Simulation
connect
Report
build
Notes: As we are working with dynamic types we need to start it all in a controlled way

## Slide 17: Phased Build Process
class my_env extends ovm_env; A u1; B u2;
function new(string name, ovm_component parent); super.new(name, parent); endfunction
class B extends ovm_component;//u2 D u5, u6;
function void build(); super.build();
u5 = new(“u5”,this);
u6 = new(“u6”,this); u6.build();
endfunction
class A extends ovm_component;//u1 C u3, u4;
function void build(); super.build();
u3 = new(“u3”,this);
u4 = new(“u4”,this);
endfunction
function void build(); super.build();
u1 = new(“u1”,this);
u2 = new(“u2”,this);
u2.build();
endfunction
u6
u3
u4
u5
function void connect(); u1.p.connect(u2.e); endfunction
function void connect(); ...
endfunction
function void connect(); ...
endfunction
Don’t actually use “new”
Don’t actually use “new”
Don’t actually use “new” (discussed later)
Notes: [tfitz] The change from 1.0.1 to 1.1 is that now build() is a proper phase. In 1.0x it was a method that got called from the post_new() phase. You still have the option of calling it explicitly if you want. You should also call super.build() as the first line of your build() method so we can automatically keep track of whether or not it was called manually or automatically.

## Slide 18: Transaction-Level Modeling (TLM)
my_env
Target1
Target2
TLM is all about communication through interfaces
  A TLM port specifies the “API” to be used
  A TLM export supplies the implementation of the methods
Connections are between ports/exports, not components
Transactions are objects
Components with the same interfaces can be swapped transparently
  No changes to parent connect()
Analysis ports/exports support 1:many write() calls
  Write to scoreboard/collector
Initiator
ovm_put_port
ovm_get_port
class my_trans extends ovm_transaction; … endclass
ovm_put_export
ovm_get_export
Request
Response
Coverage
analysis_export
Coverage
analysis_export
ovm_analysis_port
function void connect(); i.p_port.connect(t.p_xport); i.g_port.connect(t.g_xport);
t.a_port.connect(c.analysis_export); t.a_port.connect(c2.analysis_export);
endfunction
Notes: How are blocks that communicate transactions connected?
Done through Ports/Exports (Function calls)
Analogy: Two phones, only one has a phone number
Export has the phone number
Port receives the number during the connect phase

## Slide 19: OVM Concepts: Configuration
class test;
...
set_config_int(“block”,“num_d”,2);
set_config_int(“*.d*”,“errinj”,1);
...
class block_env; bit num_d = 1; driver d[0:num_d-1];
set_config_int(“d0”,“delay”,5);
get_config_int(“num_d”,num_d);
if(num_d == 2) set_config_int(“d1”,“active”,0);
class driver; bit active = 1, errinj = 0; int delay = 2; function void build(); super.build();
get_config_int(“active”,active); get_config_int(“delay”,delay); get_config_int(“errinj”,errinj);
…
class driver;
bit active = 1; bit delay = 2;
bit errinj = 0;
Configure anything
  Modal configuration
    Change modes of operation by changing values of variables
    E.g. debug verbosity
  Topological configuration
    Changes variables to modify the topology
    E.g. Verification environment
Manual configuration
  Sets and gets the configuration manually
Automated configuration
  Set the configuration manually
  Gets the configuration via the build phases
class driver; bit active = 1, errinj = 0; int delay = 2; function void build(); super.build();
get_config_int(“active”,active); get_config_int(“delay”,delay); get_config_int(“errinj”,errinj);
…
class driver;
bit active = 0; int delay = 2;
bit errinj = 0;
class driver;
bit active = 1; int delay = 2;
bit errinj = 0;
class driver;
bit active = 1; int delay = 5;
bit errinj = 0;
class driver;
bit active = 0; int delay = 2;
bit errinj = 1;
class driver;
bit active = 1; int delay = 5;
bit errinj = 1;

## Slide 20: Running a Test
Built-in phased execution flow is launched by calling ovm_env::run_test(string test_name = “”)
  Runs test specified by function argument if provided, unless overridden by command line plusarg +OVM_TESTNAME=
  Elaboration, simulation and report (sub-)phases are executed in predefined order
  Each phase invokes a function or task with the same name
    run() is the only phase task
  Each phase is executed for every component
    Bottom-up or top-down
    run() and pre_run() for threaded components only
Notes: Controlling testcase selection
  Structural testbench top level
    run_test uses $plusargs to control factory
  Allows execution of multiple tests without recompilation
    vsim … +OVM_TESTNAME=fpu_test_add_sub
OVM testcases information stored in UCDB files

## Slide 21: Managing Shutdown
Test
Static method global_stop_request()
  Spawns stop() task in all “participating” components
  Waits for all stop() tasks to complete
Components “register” for stop management
  enable_stop_interrupt = 1;
  override stop() task
Global stop timeout
  Each component should have its own timeout as well
Global stop usually managed from base test
class my_env extends ovm_env; A u1;
B u2;
class my_env extends ovm_env; A u1;
B u2;
class B;
task run(); ...
-> st_ev;
endtask
task stop();
fork
begin @st_ev; wait(st==IDLE); end
# stop_time;
join_any disable fork;
endtask
endclass
task run(); ...
global_stop_request();
// on to extract() phase
endtask
class A;
task run(); ...
ms = 1;
endtask
task stop(); wait(ms == 1); endtask
endclass
Notes: Test normally ends when ovm_env::run() ends

## Slide 22: What are sequences?
RTL-level
Transaction-level
What are sequences
  Parallel tasks that arbitrate for access to a driver
Sequence
Task()
Sequencer
arbitration
Driver
Get(req);
Do_op
Put(rsp);
DUT
Sequence
Task()
Sequence
Task()

## Slide 23: Why Use Sequences?
Encapsulation and Modularity of Stimulus Generation
Separation of Structure from Behavior
Parallel Stimulus
Layering Protocols
  packet -> cell, multi-word -> single-word, translations
Flexible Stimulus Control
  injection of noise, gaps, errors
  control ratios of stimulus types
Reuse of Stimulus
  sequences for specific RTL blocks (i.e. configuration)
  encapsulation of functions
  ability to hand stimulus block to other project

## Slide 24: Operations
Sequences
  Create transactions (sequence_item)
  Request access, send item to driver
  Optionally get a response back
Sequencer – an arbitrating fifo
  Queue requests from sequences
  Wait for request from driver
  Arbitrate and choose sequence, send item
  Route response back to sequence
Driver
  Get request, do operation, put response

## Slide 25: Sequence Overview
A sequence requests for the driver
When granted, the sequence specifies the operation to do
The sequencer sends the operation from the sequence to the driver
The driver executes the operation
The driver optionally sends the response back to the sequence

## Slide 26: Sequential Stimulus
Sequencer
Driver
DUT
A sequence has a method that generates a stream of transactions…
trans
The sequencer provides transactions from the sequence to the driver
OVM
…or other sequences
Notes: In the AVM, the basic transaction generator is avm_random_stimulus, which randomizes individual transactions and usually puts them to a fifo, from which the driver gets them when the bus is ready. Because the stimulus generator pushes transactions, it will generate a new transaction as soon as there’s room in the fifo. Some time later, the driver will get this

## Slide 27: Sequential Stimulus
Sequencer
OVM
Sequencer
The sequencer has a default sequence that it executes
A sequence can spawn another sequence
arb
The sequencer arbitrates between multiple sequences
Each sequence attempts to execute an item in the sequence
Driver
trans
Notes: In the AVM, the basic transaction generator is avm_random_stimulus, which randomizes individual transactions and usually puts them to a fifo, from which the driver gets them when the bus is ready. Because the stimulus generator pushes transactions, it will generate a new transaction as soon as there’s room in the fifo. Some time later, the driver will get this

## Slide 28: Sequential Stimulus
OVM
Lower Sequencer
arb
Upper Sequencer
A lower-level item may request a higher-level item
A lower-level sequence processes the pkt-level item into a set of cell items
Cell Driver
Pkt
cell
cell
Notes: In the AVM, the basic transaction generator is avm_random_stimulus, which randomizes individual transactions and usually puts them to a fifo, from which the driver gets them when the bus is ready. Because the stimulus generator pushes transactions, it will generate a new transaction as soon as there’s room in the fifo. Some time later, the driver will get this

## Slide 29: Sequences
Decouple stimulus specification from structural hierarchy
  Add/remove/modify stimulus scenarios independent of testbench
  Simplify test writer API
Sequences define transaction streams
  s1.start(u1);
  fork s2.start(u1); s3.start(u1); join
Sequences can call children
  function void s5::body(); s1.start(u1,this);
  fork s2.start(u1,this); s3.start(u1,this); join
  s4.start(u1,this);
Built-in get_response() task
Sequences & transactions customizable via the factory
u1
u1
u1
s5
s1
s4
s3
s2
s1
Optional parent sequence
May start on any sequencer

## Slide 30: Sequential Stimulus
u1
Sequence calls wait_for_grant()
Sequencer waits for get()
  arbitrates and grants access
Transaction is randomized
Sequence calls send_request(req)
Sequence optionally calls get_response(rsp)
A sequence may request a transaction from another (higher-level) sequencer
  u2 just sees a “driver”
Driver does get(req)
Performs bus cycle
Driver optionally does put(rsp)
  rsp.set_id_info(req);
s1
s2
u2
s3
Sequence/Sequencer
Driver

## Slide 31: Sequences
Sequences are objects
Sequences have a virtual method body() to specify the behavior
  Executes items procedurally
  Can contain other code
  Can spawn other sequences
  Can call other sequences
  Can use all SV constructs
class my_seq extends ovm_sequence; ...
virtual task body();
logic [31:0] first_addr,next_addr;
read_count = 5;
for (int i=0; i<read_count; i++)
begin
`ovm_do_with(txn, {txn.trtype == WRITE32;})
first_addr = txn.addr;
`ovm_do_with(txn, {txn.addr == first_addr && txn.trtype == READ32;})
start(parallel_seq);
`ovm_do(sub_seq);
end
randsequence() ...
endtask
...
Notes: In the AVM, the basic transaction generator is avm_random_stimulus, which randomizes individual transactions and usually puts them to a fifo, from which the driver gets them when the bus is ready. Because the stimulus generator pushes transactions, it will generate a new transaction as soon as there’s room in the fifo. Some time later, the driver will get this

## Slide 32: Hierarchy and Elaboration
The OVM has structural base classes to aid hierarchy, elaboration and simulation
  ovm_component
    Base unit of structural hierarchy
    Provides hierarchical naming
    Provides access to the (TLM) connectivity infrastructure
      connect() method
    Provides a “run()” task
      And associated kill(), suspend() and resume() methods
    Provides reporting facilities
  ovm_env
    Derived from ovm_component to add sequence of pre-defined simulation phases
      Including connect() and run() methods
    Contains and manages all class based testbench components
    Constructs, connects and configures the testbench
  ovm_test
    Also derived from ovm_component
    Optional for encapsulating environment customizations
Notes: Actually, as of OVM 2.0 I believe ovm_env is optional too, and the sequence of pre-defined simulation phases is not reliant on having an ovm_env top

## Slide 33: OVM Component Hierarchy
ovm_test extends ovm_component;
// Customizes the environment
// Defines stop criteria
ovm_env extends ovm_component;
// Manages phasing // Encapsulates structural “testbench”
ovm_component;
// Basic unit of structural hierarchy

## Slide 34: Integrated Reporting Infrastructure
Provides utilities for consistent report handling
Features:
  Severities with one or more associated actions
    Severities: message, warning, error, fatal
    Actions: display, log, count, exit, no action, call hook
  Filtering
    By unique or common string ids
    By numeric verbosity level
    By component instance and hierarchy
  Log files
    Redirection to multiple output files

## Slide 35: Modularity + Configurability
top
test
test
env
env
The Basics: driver, monitor, stimulus & analysis
Env defines topology & configures components
  Number & type of components
  Default stimulus sequence(s)
Encapsulate components for reuse
  Packages
Reuse components in new env
  Additional stimulus & analysis
Test customizes env
  Choose env from library
  Coordinate Stimulus
  Additional tweaking
Test instantiated by top-level module
  Test chosen from library

## Slide 36: OVM Summary
True Multi-Vendor Support
  Out-of-the-box, fully tested and supported
Architected for Reuse
  Component/environment reuse
    TLM-based components use standard interfaces
    Test modifies testbench components and topology
    Components control instantiation and configuration
    Separate stimulus from testbench hierarchy
Simplified Test API
  Sequential stimulus independent of testbench
  Test defines
    Component types and configuration settings
    Stimulus to run on which components
  Test writer does not need to know full OOP details of testbench
test
testbench
d
e