## Slide 1: MP3: Multi-Source Streaming System
Instructor: Klara Nahrstedt
April 18, 2014
CS414

## Slide 2
CS414 term project contest!
Judges from industry
There will still be submission deadline and demo as usual
Finalists will be selected by Prof. Nahrstedt and TA based on performance during demo

## Slide 3
No topic limitation. Be creative!
The only requirements of this MP are
  It has to be a video streaming system that includes at least three machines: two servers and one client.
  It has to contain at least two video+audio sources, coming from different servers. These streams have to be played out simultaneously on the client side.
  The client machine has to be able to assign different priorities to contents originated from different servers. The priorities can be changed on-the-fly by the user during a session.
  All session management functionalities (MP2).

## Slide 4: Example: Multi-view Surveillance System
Window for server 1
Window for server 2
Server
  Capture Audio and Video at a fixed rate
  Video: 30 fps, Audio: 8000Hz
Client
  Requests for Video and/or Audio
  Works in Two modes: Active Mode and Passive Mode
  Active Mode:
    Media type: Audio, Video
    Video Rate: 15 to 25 fps
    Audio Rate: 8000Hz
    Video Resolution: 640X480
  Passive Mode:
    Media type: Video
    Video Rate: 10 fps
    Video Resolution: 320X240

## Slide 5: Client Behavior
Client can request active mode from Server 1 and passive mode from Server 2
Client can request active mode from Server 2 and passive mode from Server 1
Client can request active mode from both Server 1 and Server 2
Client can request passive mode from both Server 1 and Server 2

## Slide 6: Client User Interface: Example
SWITCH
SWITCH
Video window for Server 1
Connect
Edit
Video window for Server 2
Computation window for Server 2
Computation window for Server 1

## Slide 7: Resource Admission at Client
User defines streaming MODE: active or passive
Client performs resource admission
Server 1
Client
Control Channel
MODE
User

## Slide 8: Resource Admission at Client
Client
  Available Application Bandwidth ABN
  Application Frame Size, MN = ?
  Application Frame Rate, RN = ?
  Audio Bandwidth = 8000 * 16
  Request Bandwidth
    Active Mode: BN = (MN * RN) + 8000 * 16
    Passive Mode: BN = (MN * RN) = (MN * 10)
resource.txt
Optimistic Allocation
8000Hz Audio Signal
How to define RN for active mode?
fps: 10
[fps:15-25]

## Slide 9: Resource Admission at Client
Client
  Available Application Bandwidth ABN
  Application Frame Size, MN = ?
  Application Frame Rate, RN = ?
  Request Bandwidth
    Active Mode: BN = (MN * RN) + Audio Bandwidth
resource.txt
ABN = (MN*RN) + Audio Bandwidth
if RN > 25, RN = 25
if RN < 15, REJECT request
else RN

## Slide 10: Resource Admission at Server
Server
  Available Application Bandwidth ABN
  Application Frame Size, MN = ?
  Application Frame Rate, RN = [received from client]
  Audio Bandwidth = 8000 * 16
  Request Bandwidth
    Active Mode: BN = (MN * RN) + 8000 * 16
    Passive Mode: BN = (MN * RN) = (MN * 10)
  Admitted if BN <= ABN
  Else Rejected
resource.txt
Optimistic Allocation

## Slide 11: Resource Negotiation with Server
Information sent to server includes
  Requested Frame Rate (FPS) for video,
  Video Resolution, and
  Media type (audio, video)
Server 1
Client
FPS, Resolution
Media types
MODE

## Slide 12
Admission
Client admission
Server admission
Resource
requirements
Negotiation
Service Quality
Resource < lower bound
YES/NO?
HOW MUCH?
Adaptation

## Slide 13: Don’t Forget Things You Leaned from MP2
Resource Admission/Negotiation
QoS Enforcement
Data Plane Communication
Audio/Video Synchronization
Session Control
Session Adaptation
Session Monitoring

## Slide 14: Resource Reservation: Client
  Available Application Bandwidth ABN
  Used Bandwidth for Server 1 B1
  Available Bandwidth ABN = ABN –B1
  Admission is successful for B2 if B2 <= ABN
resource.txt
Server 1 | 60 Kbps
Server 2 | 35 KBps
Resource Table

## Slide 15: Evaluation of MP3
Your basic score (100pt) will depend on only the system aspects: sync, data, control, admission, etc.
Creativity and Practicality
  These contribute to the bonus part (20pt)
  These decide whether you get into the final contest

## Slide 16: Schedules
Submission deadline: May 3
Demo: 5-7pm, May 5
  You must use at least 3 PCs/ laptops for the demo, connected over the internet
Final contest: TBD