## Slide 1: Chapter 6: Wireless and Mobile Networks
Background:
# wireless (mobile) phone subscribers now exceeds # wired phone subscribers!
computer nets: laptops, palmtops, PDAs, Internet-enabled phone promise anytime untethered Internet access
two important (but different) challenges
  communication over wireless link
  handling mobile user who changes point of attachment to network

## Slide 2: Chapter 6 outline
6.1 Introduction
Wireless
6.2 Wireless links, characteristics
  CDMA
6.3 IEEE 802.11 wireless LANs (“wi-fi”)
6.4 Cellular Internet Access
  architecture
  standards (e.g., GSM)
Mobility
6.5 Principles: addressing and routing to mobile users
6.6 Mobile IP
6.7 Handling mobility in cellular networks
6.8 Mobility and higher-layer protocols
6.9 Summary

## Slide 3: Elements of a wireless network
network
infrastructure
wireless hosts
laptop, PDA, IP phone
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility

## Slide 4: Elements of a wireless network
network
infrastructure
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., cell towers 802.11 access points

## Slide 5: Elements of a wireless network
network
infrastructure
wireless link
typically used to connect mobile(s) to base station
also used as backbone link
multiple access protocol coordinates link access
various data rates, transmission distance

## Slide 7: Characteristics of selected wireless link standards
384 Kbps
56 Kbps
54 Mbps
5-11 Mbps
1 Mbps
802.15
802.11b
802.11{a,g}
IS-95 CDMA, GSM
UMTS/WCDMA, CDMA2000
.11 p-to-p link
2G
3G
Indoor
10 – 30m
Outdoor
50 – 200m
Mid range
outdoor
200m – 4Km
Long range
outdoor
5Km – 20Km

## Slide 8: Elements of a wireless network
network
infrastructure
infrastructure mode
base station connects mobiles into wired network
handoff: mobile changes base station providing connection into wired network

## Slide 9: Elements of a wireless network
Ad hoc mode
no base stations
nodes can only transmit to other nodes within link coverage
nodes organize themselves into a network: route among themselves

## Slide 10: Wireless Link Characteristics
Differences from wired link ….
  decreased signal strength: radio signal attenuates as it propagates through matter (path loss)
  interference from other sources: standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors) interfere as well
  multipath propagation: radio signal reflects off objects ground, arriving ad destination at slightly different times
…. make communication across (even a point to point) wireless link much more “difficult”

## Slide 11: Wireless network characteristics
Multiple wireless senders and receivers create additional problems (beyond multiple access):
A
B
C
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other
means A, C unaware of their interference at B
A
B
C
A’s signal
strength
space
C’s signal
strength
Signal fading:
B, A hear each other
B, C hear each other
A, C can not hear each other interferring at B

## Slide 12: Code Division Multiple Access (CDMA)
used in several wireless broadcast channels (cellular, satellite, etc) standards
unique “code” assigned to each user; i.e., code set partitioning
all users share same frequency, but each user has own “chipping” sequence (i.e., code) to encode data
encoded signal = (original data) X (chipping sequence)
decoding: inner-product of encoded signal and chipping sequence
allows multiple users to “coexist” and transmit simultaneously with minimal interference (if codes are “orthogonal”)

## Slide 13: CDMA Encode/Decode
slot 1
slot 0
d1 = -1
1
1
1
1
1
-
1
-
1
-
1
-
Zi,m= di.cm
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
channel output Zi,m
sender
code
data
bits
slot 1
slot 0
d1 = -1
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
receiver
code
received
input
Di = S Zi,m.cm
m=1
M
M

## Slide 14: CDMA: two-sender interference

## Slide 15: Chapter 6 outline
6.1 Introduction
Wireless
6.2 Wireless links, characteristics
  CDMA
6.3 IEEE 802.11 wireless LANs (“wi-fi”)
6.4 Cellular Internet Access
  architecture
  standards (e.g., GSM)
Mobility
6.5 Principles: addressing and routing to mobile users
6.6 Mobile IP
6.7 Handling mobility in cellular networks
6.8 Mobility and higher-layer protocols
6.9 Summary

## Slide 16: IEEE 802.11 Wireless LAN
802.11b
  2.4-5 GHz unlicensed radio spectrum
  up to 11 Mbps
  direct sequence spread spectrum (DSSS) in physical layer
    all hosts use same chipping code
  widely deployed, using base stations
802.11a
  5-6 GHz range
  up to 54 Mbps
802.11g
  2.4-5 GHz range
  up to 54 Mbps
All use CSMA/CA for multiple access
All have base-station and ad-hoc network versions

## Slide 17: 802.11 LAN architecture
wireless host communicates with base station
  base station = access point (AP)
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  access point (AP): base station
  ad hoc mode: hosts only
BSS 1
BSS 2
Internet
hub, switch
or router
AP
AP

## Slide 18: 802.11: Channels, association
802.11b: 2.4GHz-2.485GHz spectrum divided into 11 channels at different frequencies
  AP admin chooses frequency for AP
  interference possible: channel can be same as that chosen by neighboring AP!
host: must associate with an AP
  scans channels, listening for beacon frames containing AP’s name (SSID) and MAC address
  selects AP to associate with
  may perform authentication [Chapter 8]
  will typically run DHCP to get IP address in AP’s subnet

## Slide 19: IEEE 802.11: multiple access
avoid collisions: 2+ nodes transmitting at same time
802.11: CSMA - sense before transmitting
  don’t collide with ongoing transmission by other node
802.11: no collision detection!
  difficult to receive (sense collisions) when transmitting due to weak received signals (fading)
  can’t sense all collisions in any case: hidden terminal, fading
  goal: avoid collisions: CSMA/C(ollision)A(voidance)
A
B
C
A
B
C
A’s signal
strength
space
C’s signal
strength

## Slide 20: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 sender
1 if sense channel idle for DIFS then
  transmit entire frame (no CD)
2 if sense channel busy then
  start random backoff time
  timer counts down while channel idle
  transmit when timer expires
  if no ACK, increase random backoff interval, repeat 2
802.11 receiver
- if frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
sender
receiver
DIFS
data
SIFS
ACK

## Slide 21: Avoiding collisions (more)
idea: allow sender to “reserve” channel rather than random access of data frames: avoid collisions of long data frames
sender first transmits small request-to-send (RTS) packets to BS using CSMA
  RTSs may still collide with each other (but they’re short)
BS broadcasts clear-to-send CTS in response to RTS
RTS heard by all nodes
  sender transmits data frame
  other stations defer transmissions
Avoid data frame collisions completely
using small reservation packets!

## Slide 22: Collision Avoidance: RTS-CTS exchange
AP
A
B
time
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer

## Slide 23: 802.11 frame: addressing
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Address 2: MAC address
of wireless host or AP
transmitting this frame
Address 1: MAC address
of wireless host or AP
to receive this frame
Address 3: MAC address
of router interface to which AP is attached
Address 4: used only in ad hoc mode

## Slide 24
Internet
router
AP
H1
R1
AP MAC addr H1 MAC addr R1 MAC addr
address 1
address 2
address 3
802.11 frame
R1 MAC addr AP MAC addr
dest. address
source address
802.3 frame
802.11 frame: addressing

## Slide 25
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Type
From
AP
Subtype
To
AP
More
frag
WEP
More
data
Power
mgt
Retry
Rsvd
Protocol
version
2
2
4
1
1
1
1
1
1
1
1
802.11 frame: more
duration of reserved
transmission time (RTS/CTS)
frame seq #
(for reliable ARQ)
frame type
(RTS, CTS, ACK, data)

## Slide 26
hub or
switch
AP 2
AP 1
H1
BBS 2
BBS 1
802.11: mobility within same subnet
router
H1 remains in same IP subnet: IP address can remain same
switch: which AP is associated with H1?
  self-learning (Ch. 5): switch will see frame from H1 and “remember” which switch port can be used to reach H1

## Slide 27
M
radius of
coverage
S
S
S
P
P
P
P
M
S
Master device
Slave device
Parked device (inactive)
P
802.15: personal area network
less than 10 m diameter
replacement for cables (mouse, keyboard, headphones)
ad hoc: no infrastructure
master/slaves:
  slaves request permission to send (to master)
  master grants requests
802.15: evolved from Bluetooth specification
  2.4-2.5 GHz radio band
  up to 721 kbps

## Slide 28: Chapter 6 outline
6.1 Introduction
Wireless
6.2 Wireless links, characteristics
6.3 IEEE 802.11 wireless LANs (“wi-fi”)
6.4 Cellular Internet Access
  architecture
  standards (e.g., GSM)
Mobility
6.5 Principles: addressing and routing to mobile users
6.6 Mobile IP
6.7 Handling mobility in cellular networks
6.8 Mobility and higher-layer protocols
6.9 Summary

## Slide 29
Mobile
Switching
Center
Public telephone
network, and
Internet
Mobile
Switching
Center
Components of cellular network architecture
connects cells to wide area net
manages call setup (more later!)
handles mobility (more later!)
MSC
covers geographical region
base station (BS) analogous to 802.11 AP
mobile users attach to network through BS
air-interface: physical and link layer protocol between mobile and BS
cell
wired network

## Slide 30: Cellular networks: the first hop
Two techniques for sharing mobile-to-BS radio spectrum
combined FDMA/TDMA: divide spectrum in frequency channels, divide each channel into time slots
CDMA: code division multiple access
frequency
bands
time slots

## Slide 31: Cellular standards: brief survey
2G systems: voice channels
IS-136 TDMA: combined FDMA/TDMA (north america)
GSM (global system for mobile communications): combined FDMA/TDMA
  most widely deployed
IS-95 CDMA: code division multiple access
IS-136
GSM
IS-95
GPRS
EDGE
CDMA-2000
UMTS
TDMA/FDMA
Don’t drown in a bowl
of alphabet soup

## Slide 32: Cellular standards: brief survey
2.5 G systems: voice and data channels
for those who can’t wait for 3G service: 2G extensions
general packet radio service (GPRS)
  evolved from GSM
  data sent on multiple channels (if available)
enhanced data rates for global evolution (EDGE)
  also evolved from GSM, using enhanced modulation
  Date rates up to 384K
CDMA-2000 (phase 1)
  data rates up to 144K
  evolved from IS-95

## Slide 33: Cellular standards: brief survey
3G systems: voice/data
Universal Mobile Telecommunications Service (UMTS)
CDMA-2000
….. more (and more interesting) cellular topics due to mobility (stay tuned for details)

## Slide 35: Chapter 6 outline
6.1 Introduction
Wireless
6.2 Wireless links, characteristics
  CDMA
6.3 IEEE 802.11 wireless LANs (“wi-fi”)
6.4 Cellular Internet Access
  architecture
  standards (e.g., GSM)
Mobility
6.5 Principles: addressing and routing to mobile users
6.6 Mobile IP
6.7 Handling mobility in cellular networks
6.8 Mobility and higher-layer protocols
6.9 Summary

## Slide 36: What is mobility?
spectrum of mobility, from the network perspective:
no mobility
high mobility
mobile wireless user,
using same access
point
mobile user, passing through multiple access point while maintaining ongoing connections (like cell phone)
mobile user, connecting/ disconnecting from network using DHCP.

## Slide 37: Mobility: Vocabulary
home network: permanent “home” of mobile
(e.g., 128.119.40/24)
Permanent address: address in home network, can always be used to reach mobile
e.g., 128.119.40.186
home agent: entity that will perform mobility functions on behalf of mobile, when mobile is remote
wide area network
correspondent

## Slide 38: Mobility: more vocabulary
Care-of-address: address in visited network.
(e.g., 79,129.13.2)
wide area network
visited network: network in which mobile currently resides (e.g., 79.129.13/24)
Permanent address: remains constant (e.g., 128.119.40.186)
foreign agent: entity in visited network that performs mobility functions on behalf of mobile.
correspondent: wants to communicate with mobile

## Slide 39: How do you contact a mobile friend:
search all phone books?
call her parents?
expect her to let you know where he/she is?
I wonder where Alice moved to?
Consider friend frequently changing addresses, how do you find her?

## Slide 40: Mobility: approaches
Let routing handle it: routers advertise permanent address of mobile-nodes-in-residence via usual routing table exchange.
  routing tables indicate where each mobile located
  no changes to end-systems
Let end-systems handle it:
  indirect routing: communication from correspondent to mobile goes through home agent, then forwarded to remote
  direct routing: correspondent gets foreign address of mobile, sends directly to mobile

## Slide 41: Mobility: approaches
Let routing handle it: routers advertise permanent address of mobile-nodes-in-residence via usual routing table exchange.
  routing tables indicate where each mobile located
  no changes to end-systems
let end-systems handle it:
  indirect routing: communication from correspondent to mobile goes through home agent, then forwarded to remote
  direct routing: correspondent gets foreign address of mobile, sends directly to mobile
not
scalable
to millions of
mobiles

## Slide 42: Mobility: registration
End result:
Foreign agent knows about mobile
Home agent knows location of mobile
wide area network
home network
visited network
1
mobile contacts foreign agent on entering visited network
2
foreign agent contacts home agent home: “this mobile is resident in my network”

## Slide 43: Mobility via Indirect Routing
wide area network
home
network
visited
network
3
2
4
1
correspondent addresses packets using home address of mobile
home agent intercepts packets, forwards to foreign agent
foreign agent receives packets, forwards to mobile
mobile replies directly to correspondent

## Slide 44: Indirect Routing: comments
Mobile uses two addresses:
  permanent address: used by correspondent (hence mobile location is transparent to correspondent)
  care-of-address: used by home agent to forward datagrams to mobile
triangle routing: correspondent-home-network-mobile
  inefficient when
  correspondent, mobile
  are in same network

## Slide 45: Indirect Routing: moving between networks
suppose mobile user moves to another network
  registers with new foreign agent
  new foreign agent registers with home agent
  home agent update care-of-address for mobile
  packets continue to be forwarded to mobile (but with new care-of-address)
mobility, changing foreign networks transparent: on going connections can be maintained!

## Slide 46: Mobility via Direct Routing
wide area network
home
network
visited
network
4
2
4
1
correspondent requests, receives foreign address of mobile
correspondent forwards to foreign agent
foreign agent receives packets, forwards to mobile
mobile replies directly to correspondent
3

## Slide 47: Mobility via Direct Routing: comments
overcome triangle routing problem
non-transparent to correspondent: correspondent must get care-of-address from home agent
  what if mobile changes visited network?

## Slide 48: Accommodating mobility with direct routing
wide area network
1
foreign net visited
at session start
anchor
foreign
agent
2
4
new foreign
agent
3
5
correspondent
agent
correspondent
new
foreign
network
anchor foreign agent: FA in first visited network
data always routed first to anchor FA
when mobile moves: new FA arranges to have data forwarded from old FA (chaining)

## Slide 49: Chapter 6 outline
6.1 Introduction
Wireless
6.2 Wireless links, characteristics
  CDMA
6.3 IEEE 802.11 wireless LANs (“wi-fi”)
6.4 Cellular Internet Access
  architecture
  standards (e.g., GSM)
Mobility
6.5 Principles: addressing and routing to mobile users
6.6 Mobile IP
6.7 Handling mobility in cellular networks
6.8 Mobility and higher-layer protocols
6.9 Summary

## Slide 50: Mobile IP
RFC 3220
has many features we’ve seen:
  home agents, foreign agents, foreign-agent registration, care-of-addresses, encapsulation (packet-within-a-packet)
three components to standard:
  indirect routing of datagrams
  agent discovery
  registration with home agent

## Slide 51: Mobile IP: indirect routing
Permanent address: 128.119.40.186
Care-of address: 79.129.13.2
dest: 128.119.40.186
packet sent by correspondent
dest: 79.129.13.2
dest: 128.119.40.186
packet sent by home agent to foreign agent: a packet within a packet
dest: 128.119.40.186
foreign-agent-to-mobile packet

## Slide 52: Mobile IP: agent discovery
agent advertisement: foreign/home agents advertise service by broadcasting ICMP messages (typefield = 9)
R bit: registration required
H,F bits: home and/or foreign agent

## Slide 53: Mobile IP: registration example

## Slide 54
Components of cellular network architecture
correspondent
MSC
MSC
MSC
MSC
MSC
wired public telephone
network
different cellular networks,
operated by different providers
recall:

## Slide 55: Handling mobility in cellular networks
home network: network of cellular provider you subscribe to (e.g., Sprint PCS, Verizon)
  home location register (HLR): database in home network containing permanent cell phone #, profile information (services, preferences, billing), information about current location (could be in another network)
visited network: network in which mobile currently resides
  visitor location register (VLR): database with entry for each user currently in network
  could be home network

## Slide 56
Public switched
telephone
network
mobile
user
home
Mobile
Switching
Center
HLR
home
network
visited
network
correspondent
Mobile
Switching
Center
VLR
GSM: indirect routing to mobile
1
call routed
to home network
2
home MSC consults HLR,
gets roaming number of
mobile in visited network
3
home MSC sets up 2nd leg of call
to MSC in visited network
4
MSC in visited network completes
call through base station to mobile

## Slide 57
Mobile
Switching
Center
VLR
old BSS
new BSS
old
routing
new
routing
GSM: handoff with common MSC
Handoff goal: route call via new base station (without interruption)
reasons for handoff:
  stronger signal to/from new BSS (continuing connectivity, less battery drain)
  load balance: free up channel in current BSS
  GSM doesn’t mandate why to perform handoff (policy), only how (mechanism)
handoff initiated by old BSS

## Slide 58
Mobile
Switching
Center
VLR
old BSS
1
3
2
4
5
6
7
8
GSM: handoff with common MSC
new BSS
1. old BSS informs MSC of impending handoff, provides list of 1+ new BSSs
2. MSC sets up path (allocates resources) to new BSS
3. new BSS allocates radio channel for use by mobile
4. new BSS signals MSC, old BSS: ready
5. old BSS tells mobile: perform handoff to new BSS
6. mobile, new BSS signal to activate new channel
7. mobile signals via new BSS to MSC: handoff complete. MSC reroutes call
8 MSC-old-BSS resources released

## Slide 59
home network
Home MSC
PSTN
correspondent
MSC
anchor MSC
MSC
MSC
(a) before handoff
GSM: handoff between MSCs
anchor MSC: first MSC visited during call
  call remains routed through anchor MSC
new MSCs add on to end of MSC chain as mobile moves to new MSC
IS-41 allows optional path minimization step to shorten multi-MSC chain

## Slide 60
home network
Home MSC
PSTN
correspondent
MSC
anchor MSC
MSC
MSC
(b) after handoff
GSM: handoff between MSCs
anchor MSC: first MSC visited during cal
  call remains routed through anchor MSC
new MSCs add on to end of MSC chain as mobile moves to new MSC
IS-41 allows optional path minimization step to shorten multi-MSC chain

## Slide 61: Chapter 6 Summary
Wireless
wireless links:
  capacity, distance
  channel impairments
  CDMA
IEEE 802.11 (“wi-fi”)
  CSMA/CA reflects wireless channel characteristics
cellular access
  architecture
  standards (e.g., GSM, CDMA-2000, UMTS)
Mobility
principles: addressing, routing to mobile users
  home, visited networks
  direct, indirect routing
  care-of-addresses
case studies
  mobile IP
  mobility in GSM

## Slide 62: Questions?

## Slide 63: Mobility: GSM versus Mobile IP
GSM element |  | Comment on GSM element | Mobile IP element | 
Home system | Network to which the mobile user’s permanent phone number belongs |  |  | Home network
Gateway Mobile Switching Center, or “home MSC”. Home Location Register (HLR) | Home MSC: point of contact to obtain routable address of mobile user. HLR: database in home system containing permanent phone number, profile information, current location of mobile user, subscription information |  |  | Home agent
Visited System | Network other than home system where mobile user is currently residing |  |  | Visited network
Visited Mobile services Switching Center. Visitor Location Record (VLR) | Visited MSC: responsible for setting up calls to/from mobile nodes in cells associated with MSC. VLR: temporary database entry in visited system, containing subscription information for each visiting mobile user |  |  | Foreign agent
Mobile Station Roaming Number (MSRN), or “roaming number” | Routable address for telephone call segment between home MSC and visited MSC, visible to neither the mobile nor the correspondent. |  |  | Care-of-address

## Slide 64: Wireless, mobility: impact on higher layer protocols
logically, impact should be minimal …
  best effort service model remains unchanged
  TCP and UDP can (and do) run over wireless, mobile
… but performance-wise:
  packet loss/delay due to bit-errors (discarded packets, delays for link-layer retransmissions), and handoff
  TCP interprets loss as congestion, will decrease congestion window un-necessarily
  delay impairments for real-time traffic
  limited bandwidth of wireless links