## Slide 1: Layering
CS 438: Spring 2014
Instructor: Matthew Caesar
http://courses.engr.illinois.edu/cs438/

## Slide 2: Outline
Last time: low-level plumbing
Today: top-down architecting of the Internet
  Goals
  Layering
  Protocols
  The end-to-end principle

## Slide 3: Recall from Lecture #1
Architecture is not the implementation itself
Architecture is how we structure implementations
  what functions?, where?, what interfaces?
Architecture is the modular design of the network

## Slide 4: How would you go about designing the Internet?
Sit down and…
  List your goals
  Prioritize them
  Hence define the service you will offer
  Architect a solution that implements the service
Of course, the original designers of the Internet didn’t do anything of the sort…

## Slide 5: Reality
The lessons accrued over time; many contributors
  1961: packet switching (Baran and Kleinrock)
  1967: vision of a robust network (ARPANET)
  1972: “best effort inter-networking” proposed (Kahn)
  1974: TCP/IP paper (Cerf/Kahn)

## Slide 6: Reality
The lessons accrued over time; many contributors
Many of the lessons were learnt “on the job”
  E.g., TCP’s congestion control algorithms were developed in response to the Internet meltdowns of the early 1980s

## Slide 7: Reality
The lessons accrued over time; many contributors
Many of the lessons were learnt “on the job”
Consensus didn’t come easy
  1961: packet switching is proposed
  1972: best-effort communication is advocated
  1980: IP adopted as the defense standard
  1985: NSFnet picks IP
  199x: Circuit switching rises (and falls) in the form of ATM
  199x: `Quality of Service’ (QoS) rises and falls

## Slide 8: Reality
The lessons accrued over time; many contributors
Many of the lessons were learnt “on the job”
Consensus didn’t come easy
And progress was ad-hoc
  “rough consensus and running code.”

## Slide 9: Reality
The lessons accrued over time; many contributors
Many of the lessons were learnt “on the job”
Consensus didn’t come easy
And progress was ad-hoc
Yet, there was also
  constant dialogue
  constant introspection
  constant experimentation, leading to…
A strong consistency of vision emerging by the ‘80s, driven by D. Clark, chair of the Internet Arch. Board

## Slide 10: Internet Design Goals (from Clark’s SIGCOMM 1988 paper)
Connect existing networks
Robust in face of failures
Support multiple types of delivery services
Accommodate a variety of networks
Allow distributed management
Cost effective
Easy host attachment
Allow resource accountability

## Slide 11: Connect Existing Networks
Wanted a single unifying interface that could be used to connect any pair of (existing) networks
Interface to be compatible with existing networks
  couldn’t demand performance capabilities not supported by existing networks
  had to support existing packet switched networks
Led to focus on an inter-networking service based on the best-effort delivery of packets

## Slide 12: How would you go about designing the Internet?
Sit down and…
  List your goals
  Prioritize them
  Hence define the service you will offer
  Architect a solution that implements the service

## Slide 13: Three steps
Decompose the problem into tasks
Organize these tasks
Assign tasks to entities (who does what)

## Slide 14: Decomposition
What does it take to send packets across the globe?
Bits on wire
Packets on wire
Delivery packets within a single physical network
Deliver packets across multiple networks
Ensure the destination received the data
Do something with the data
This is decomposition…
Now, how do we organize these tasks?
Datalink
Network
Transport
Application
Physical

## Slide 15: Inspiration…
Dear John,
Your days are numbered.
--Pat
CEO A writes letter to CEO B
  Folds letter and hands it to administrative aide
Aide:
  Puts letter in envelope with CEO B’s full name
  Takes to FedEx
FedEx Office
  Puts letter in larger envelope
  Puts name and street address on FedEx envelope
  Puts package on FedEx delivery truck
FedEx delivers to other company

## Slide 16: The Path of the Letter
CEO
Aide
FedEx
CEO
Aide
FedEx
Location
Fedex Envelope (FE)
Letter
Envelope
Semantic Content
Identity
“Peers” on each side understand the same things
No one else needs to
Lowest level has most packaging

## Slide 17: The Path Through FedEx
Truck
Sorting
Office
Airport
FE
Sorting
Office
Airport
Truck
Sorting
Office
Airport
Crate
Crate
FE
New
Crate
Crate
FE
Deepest Packaging (Envelope+FE+Crate)
at the Lowest Level of Transport

## Slide 18: The Path Through FedEx
Truck
Sorting
Office
Airport
FE
Sorting
Office
Airport
Truck
Sorting
Office
Airport
Crate
Crate
FE
New
Crate
Crate
FE
Higher “Stack”
at Ends
Partial “Stack”
During Transit
Deepest Packaging (Envelope+FE+Crate)
at the Lowest Level of Transport
Highest Level of
“Transit Stack”
is Routing

## Slide 19: In the context of the Internet
Applications
…built on…
…built on…
…built on…
…built on…
Reliable (or unreliable) transport
Best-effort global packet delivery
Best-effort local packet delivery
Physical transfer of bits
Application
Transport
Network
Data link
Physical
L1
L2
L3
L4
L7
This is
not a typo
nope, not a typo

## Slide 20: In the context of the Internet
Application
Presentation
Session
Transport
Network
Data link
Physical
1
2
3
4
5
6
7
The Open Systems Interconnect (OSI) model developed by the ISO included two additional layers that are often implemented as part of the application

## Slide 21: Protocols and Layers
Communication between peer layers on different systems is defined by protocols
Application
Transport
Network
Data link
Physical
L1
L2
L3
L4
L7
Application
Transport
Network
Data link
Physical
L1
L2
L3
L4
L7

## Slide 22: What is a Protocol?
Friendly greeting
Time?
2pm
Friendly greeting
Thank you

## Slide 23: What is a Protocol?
E.g., the destination address is in the 1st four bytes of the packet
When A sends B a packet of type X…
…B should return a packet of type Y to A
… then A should respond with Z
….

## Slide 24: What is a Protocol?
An agreement between parties on how to communicate
Include syntax and semantics
  how a communication is specified and structured
  what a communication means
Protocols exist at many hardware, software, all levels!
Defined by a variety of standards bodies
  IETF (ietf.org), IEEE, ITU, …

## Slide 25: So we have decomposition and organization
Next: what gets implemented where?
Application
Transport
Network
Data link
Physical
L1
L2
L3
L4
L7
Application
Transport
Network
Data link
Physical
L1
L2
L3
L4
L7

## Slide 26: Distributing Layers Across Network
Layers are simple if only on a single machine
  Just stack of modules interacting with those above/below
But we need to implement layers across machines
  Hosts
  Routers (switches)
What gets implemented where?

## Slide 27: What gets implemented at the end host
Bits arrive on wire, must make it up to application
Therefore, all layers must exist at host!

## Slide 28: What gets implemented in the network?
Bits arrive on wire
  Physical layer necessary
Packets must be delivered to next-hop and across local networks
  Datalink layer necessary
Packets must be delivered between networks for global delivery
  Network layer necessary
The network doesn’t support reliable delivery
  Transport layer (and above) not supported

## Slide 29: Switches vs. Routers
Switches do what routers do, except they don’t participate in global delivery, just local delivery
Switches only need to support Physical and Datalink
  Don’t need to support Network layer
Routers support Physical, Datalink and Network layers
Won’t focus on the router/switch distinction
  When I say switch, I almost always mean router
  Almost all boxes support network layer these days

## Slide 30: Simple diagram
Lower three layers implemented everywhere
Top two layers implemented only at hosts
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router
Notes: Why go up? Why not stay down in the lower levels?

## Slide 31: Looking a little closer
Application
Transport
Network
Data link
Physical
At the end host
Application
  user space: web server, browser, mail, game
Transport and network.
  Typically part of the operating system
Datalink
  Often written by vendor of the network interface hardware
Physical
  Hardware: network interface card and link

## Slide 32: Logical Communication
Layers interacts with peer’s corresponding layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 33: Physical Communication
Communication goes down to physical network
Then from network peer to peer
Then up to relevant layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 34: Layer Encapsulation
Trans: Connection ID
Net: Source/Dest
Link: Src/Dest
Appl: Get index.html
User A
User B
Notes: Deepest level most header

## Slide 35: Protocols at different layers
There is just one network-layer protocol, IP
The “narrow waist” of the Internet hourglass
Application
Transport
Network
Data link
Physical
L1
L2
L3
L4
L7
SMTP
HTTP
DNS
NTP
TCP
UDP
IP
Ethernet
FDDI
PPP
optical
copper
radio
PSTN

## Slide 36: Implications of Hourglass
Single network-layer protocol (IP)
Allows arbitrary networks to interoperate
  Any network that supports IP can exchange packets
Decouples applications from low-level networking technologies
  applications to function on all networks
Supports simultaneous innovations above and below IP
But changing IP itself is hard (e.g., IPv4  IPv6)

## Slide 37: A Protocol-Centric Diagram
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet

## Slide 38: What are some of the benefits of protocols and layering?

## Slide 39: Interoperability
Many implementations of many technologies
  Hosts running FreeBSD, Linux, Windows, MacOS, …
  People using Mozilla, Explorer, Opera, …
  Routers made by cisco, juniper, …
  Hardware made by IBM, Dell, Apple, …
And it changes all the time.
Phew!
But they can all talk together because they use the same protocol(s)

## Slide 40: Abstraction & Reuse
Multiple choices of protocol at many layers
  Physical: copper, fiber, air, carrier pigeon
  Link: ethernet, token ring, SONET, FDDI
  Transport: TCP, UDP, SCTP
But we don’t want to have to write “a web (HTTP) browser for TCP networks running IP over Ethernet on Copper” and another for the fiber version…
  Protocols provide a standard interface to write to
  Layers hide the details of the protocols below

## Slide 41: Decoupling aids innovation
Technologies at each layer pursued by very different communities
Innovation at each layer can proceed in parallel

## Slide 42: What are some of the drawbacks of protocols and layering?

## Slide 43: Drawbacks of Layering
Layer N may duplicate lower layer functionality
  e.g., error recovery to retransmit lost data
Information hiding may hurt performance
  e.g., packet loss due to corruption vs. congestion
Headers start to get really big
  e.g., typical TCP+IP+Ethernet is 54 bytes
Layer violations when the gains too great to resist
  e.g., TCP-over-wireless
Layer violations when network doesn’t trust ends
  e.g., firewalls

## Slide 44: Where to place network functionality?
Hugely influential paper: “End-to-End Arguments in System Design” by Saltzer, Reed, and Clark (‘84)
  articulated the “End-to-End Principle” (E2E)
Endless debate over what it means
Everyone cites it as supporting their position
Notes: Contrary to wisdom of the day!
Talmud

## Slide 45: Basic Observation
Some application requirements can only be correctly implemented end-to-end
  reliability, security, etc.
Implementing these in the network is hard
  every step along the way must be fail proof
Hosts
  Can satisfy the requirement without network’s help
  Will/must do so, since they can’t rely on the network
Notes: Contrary to wisdom of the day!
Talmud

## Slide 46: Example: Reliable File Transfer
Solution 1: make each step reliable, and string them together to make reliable end-to-end process
Solution 2: end-to-end check and retry
OS
Appl.
OS
Appl.
Host A
Host B
OK

## Slide 47: Discussion
Solution 1 (make each step reliable) is incomplete
  What happens if any network element misbehaves?
  Receiver has to do the check anyway!
Solution 2 (end to end check) is complete
  Full functionality can be entirely implemented at application layer with no need for reliability from lower layers
Is there any need to implement reliability at lower layers?
Notes: Contrary to wisdom of the day!
Talmud

## Slide 48: Summary of End-to-End Principle
Implementing functionality (e.g., reliability) in the network
  Doesn’t reduce host implementation complexity
  Does increase network complexity
  Probably increases delay and overhead on all applications even if they don’t need the functionality (e.g. VoIP)
However, implementing in the network can improve performance in some cases
  e.g., consider a very lossy link
Notes: Contrary to wisdom of the day!
Talmud

## Slide 49: “Only if sufficient” interpretation
Don’t implement a function at the lower levels of the system unless it can be completely implemented at this level
Unless you can relieve the burden from hosts, don’t bother

## Slide 50: “Only if necessary” interpretation
Don’t implement anything in the network that can be implemented correctly by the hosts
Make network layer absolutely minimal
  This E2E interpretation trumps performance issues
  Increases flexibility, since lower layers stay simple
Notes: One make hosts as simple as possible. The other makes the network as simple as possible. Which do you prefer?

## Slide 51: “Only if useful” interpretation
If hosts can implement functionality correctly, implement it in a lower layer only as a performance enhancement
But do so only if it does not impose burden on applications that do not require that functionality

## Slide 52: Taking stock of where we’re at…

## Slide 53: First Step: Basic Concepts and Decisions
Plumbing: links, switches
Packet Switching winner over circuit switching
Best-effort service model

## Slide 54: Second Step: Architectural Principles
Protocols and Layering
End-to-End Principle

## Slide 55: Third Step: Design Challenges and Solutions
Let’s go layer by layer
  Physical
  Datalink
  Network
  Transport
  Application

## Slide 56: Two Layers We’ll Worry About Less
Physical:
  Technology dependent
  Lots of possible solutions
  Not specific to the Internet
Application:
  Application-dependent
  Lots of possible solutions

## Slide 57: Datalink and Network Layers
Both support best-effort delivery
  Datalink over local scope
  Network over global scope
Key challenge: scalable, robust routing
  How do we address destinations
  How to direct packets to destination

## Slide 58: Transport Layer
Provide reliable delivery over unreliable network