## Slide 1: Pixels and Image Filtering
Computational Photography
Derek Hoiem
08/27/15
Graphic: http://www.notcot.org/post/4068/

## Slide 2: Administrative stuff
Any questions?
Office hours: times will be set Friday, so be sure to fill out poll http://doodle.com/8cqbis4qx52wm5fs
Tutorial:
  Looks like Sept 2 at 5pm, but will finalize later today --- vote soon http://doodle.com/6drhrg3kdedu892x

## Slide 3: Today’s Class: Pixels and Linear Filters
What is a pixel? How is an image represented?
What is image filtering and how do we do it?
Introduce Project 1: Hybrid Images

## Slide 4: Next three classes
Image filters in spatial domain
  Smoothing, sharpening, measuring texture
Image filters in the frequency domain
  Denoising, sampling, image compression
Templates and Image Pyramids
  Detection, coarse-to-fine registration

## Slide 5: Image Formation

## Slide 6: Digital camera
A digital camera replaces film with a sensor array
Each cell in the array is light-sensitive diode that converts photons to electrons
Two common types:
  Charge Coupled Device (CCD): larger yet slower, better quality
  Complementary Metal Oxide Semiconductor (CMOS): high bandwidth, lower quality
http://electronics.howstuffworks.com/digital-camera.htm
Slide by Steve Seitz

## Slide 7: Sensor Array
CMOS sensor
CCD sensor

## Slide 8: The raster image (pixel matrix)

## Slide 9: The raster image (pixel matrix)
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93

## Slide 10: Perception of Intensity
from Ted Adelson

## Slide 11: Perception of Intensity
from Ted Adelson

## Slide 12: Digital Color Images

## Slide 13: Color Image
R
G
B

## Slide 14: Images in Matlab
Images represented as a matrix
Suppose we have a NxM RGB image called “im”
  im(1,1,1) = top-left pixel value in R-channel
  im(y, x, b) = y pixels down, x pixels to right in the bth channel
  im(N, M, 3) = bottom-right pixel in B-channel
imread(filename) returns a uint8 image (values 0 to 255)
  Convert to double format (values 0 to 1) with im2double
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
R
G
B
row
column

## Slide 15: Image filtering
Image filtering: compute function of local neighborhood at each position
Really important!
  Enhance images
    Denoise, resize, increase contrast, etc.
  Extract information from images
    Texture, edges, distinctive points, etc.
  Detect patterns
    Template matching

## Slide 16
1
1
1
1
1
1
1
1
1
Slide credit: David Lowe (UBC)
Example: box filter

## Slide 17
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Credit: S. Seitz
Image filtering
1
1
1
1
1
1
1
1
1
Notes: ones, divide by 9

## Slide 18
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 19
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 20
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 | 30 |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 21
 | 0 | 10 | 20 | 30 | 30 |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 22
 | 0 | 10 | 20 | 30 | 30 |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
?
Notes: ones, divide by 9

## Slide 23
 | 0 | 10 | 20 | 30 | 30 |  |  |  | 
 |  |  |  | 50 |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
?
Notes: ones, divide by 9

## Slide 24
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 | 30 | 30 | 30 | 20 | 10 | 
 | 0 | 20 | 40 | 60 | 60 | 60 | 40 | 20 | 
 | 0 | 30 | 60 | 90 | 90 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 20 | 30 | 50 | 50 | 60 | 40 | 20 | 
 | 10 | 20 | 30 | 30 | 30 | 30 | 20 | 10 | 
 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 0 | 
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz

## Slide 25
 | 0 | 10 | 20 | 30 | 30 | 30 | 20 | 10 | 
 | 0 | 20 | 40 | 60 | 60 | 60 | 40 | 20 | 
 | 0 | 30 | 60 | 90 | 90 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 20 | 30 | 50 | 50 | 60 | 40 | 20 | 
 | 10 | 20 | 30 | 30 | 30 | 30 | 20 | 10 | 
 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 0 | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Informally, what does the filter do?

## Slide 26
What does it do?
Replaces each pixel with an average of its neighborhood
Achieve smoothing effect (remove sharp features)
1
1
1
1
1
1
1
1
1
Slide credit: David Lowe (UBC)
Box Filter

## Slide 27
Smoothing with box filter

## Slide 28: One more on board…

## Slide 29: Practice with linear filters
0
0
0
0
1
0
0
0
0
Original
?
Source: D. Lowe

## Slide 30: Practice with linear filters
0
0
0
0
1
0
0
0
0
Original
Filtered
(no change)
Source: D. Lowe

## Slide 31: Practice with linear filters
0
0
0
1
0
0
0
0
0
Original
?
Source: D. Lowe

## Slide 32: Practice with linear filters
0
0
0
1
0
0
0
0
0
Original
Shifted left
By 1 pixel
Source: D. Lowe

## Slide 33: Practice with linear filters
Original
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
?
(Note that filter sums to 1)
Source: D. Lowe

## Slide 34: Practice with linear filters
Original
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
Sharpening filter
  Accentuates differences with local average
Source: D. Lowe

## Slide 35: Sharpening
Source: D. Lowe

## Slide 36: Other filters
-1
0
1
-2
0
2
-1
0
1
Vertical Edge
(absolute value)
Sobel

## Slide 37: Other filters
-1
-2
-1
0
0
0
1
2
1
Horizontal Edge
(absolute value)
Sobel
Q?
Notes: Questions at this point?

## Slide 38: How could we synthesize motion blur?
theta = 30; len = 20;
fil = imrotate(ones(1, len), theta, 'bilinear');
fil = fil / sum(fil(:));
figure(2), imshow(imfilter(im, fil));

## Slide 39: Filtering vs. Convolution
2d filtering
  h=filter2(g,f); or h=imfilter(f,g);
2d convolution
  h=conv2(g,f);
f=image
g=filter

## Slide 40: Key properties of linear filters
Linearity:
filter(f1 + f2) = filter(f1) + filter(f2)
Shift invariance: same behavior regardless of pixel location
filter(shift(f)) = shift(filter(f))
Any linear, shift-invariant operator can be represented as a convolution
Source: S. Lazebnik

## Slide 41: More properties
Commutative: a * b = b * a
  Conceptually no difference between filter and signal (image)
Associative: a * (b * c) = (a * b) * c
  Often apply several filters one after another: (((a * b1) * b2) * b3)
  This is equivalent to applying one filter: a * (b1 * b2 * b3)
Distributes over addition: a * (b + c) = (a * b) + (a * c)
Scalars factor out: ka * b = a * kb = k (a * b)
Identity: unit impulse e = [0, 0, 1, 0, 0], a * e = a
Source: S. Lazebnik

## Slide 42
Weight contributions of neighboring pixels by nearness
0.003 0.013 0.022 0.013 0.003
0.013 0.059 0.097 0.059 0.013
0.022 0.097 0.159 0.097 0.022
0.013 0.059 0.097 0.059 0.013
0.003 0.013 0.022 0.013 0.003
5 x 5,  = 1
Slide credit: Christopher Rasmussen
Important filter: Gaussian

## Slide 43
Smoothing with Gaussian filter

## Slide 44
Smoothing with box filter

## Slide 45: Gaussian filters
Remove “high-frequency” components from the image (low-pass filter)
  Images become more smooth
Convolution with self is another Gaussian
  So can smooth with small-width kernel, repeat, and get same result as larger-width kernel would have
  Convolving two times with Gaussian kernel of width σ is same as convolving once with kernel of width
Separable kernel
  Factors into product of two 1D Gaussians
Source: K. Grauman
Notes: Linear vs. quadratic in mask size

## Slide 46: Separability of the Gaussian filter
Source: D. Lowe

## Slide 47: Separability example
*
*
=
=
2D filtering (center location only)
Source: K. Grauman
The filter factors into a product of 1D filters:
Perform filtering along rows:
Followed by filtering along the remaining column:

## Slide 48: Separability
Why is separability useful in practice?

## Slide 49: Some practical matters

## Slide 50: Practical matters
How big should the filter be?
Values at edges should be near zero
Rule of thumb for Gaussian: set filter half-width to about 3 σ

## Slide 51: Practical matters
What about near the edge?
  the filter window falls off the edge of the image
  need to extrapolate
  methods:
    clip filter (black)
    wrap around
    copy edge
    reflect across edge
Source: S. Marschner

## Slide 52: Practical matters
  methods (MATLAB):
    clip filter (black): imfilter(f, g, 0)
    wrap around: imfilter(f, g, ‘circular’)
    copy edge: imfilter(f, g, ‘replicate’)
    reflect across edge: imfilter(f, g, ‘symmetric’)
Source: S. Marschner

## Slide 53: Practical matters
What is the size of the output?
MATLAB: filter2(g, f, shape)
  shape = ‘full’: output size is sum of sizes of f and g
  shape = ‘same’: output size is same as f
  shape = ‘valid’: output size is difference of sizes of f and g
f
g
g
g
g
f
g
g
g
g
f
g
g
g
g
full
same
valid
Source: S. Lazebnik
Q?

## Slide 54: Application: Representing Texture
Source: Forsyth

## Slide 55: Texture and Material
http://www-cvr.ai.uiuc.edu/ponce_grp/data/texture_database/samples/

## Slide 56: Texture and Orientation
http://www-cvr.ai.uiuc.edu/ponce_grp/data/texture_database/samples/

## Slide 57: Texture and Scale
http://www-cvr.ai.uiuc.edu/ponce_grp/data/texture_database/samples/

## Slide 58: What is texture?
Regular or stochastic patterns caused by bumps, grooves, and/or markings

## Slide 59: How can we represent texture?
Compute responses of blobs and edges at various orientations and scales

## Slide 60: Overcomplete representation: filter banks
LM Filter Bank
Code for filter banks: www.robots.ox.ac.uk/~vgg/research/texclass/filters.html

## Slide 61: Filter banks
Process image with each filter and keep responses (or squared/abs responses)

## Slide 62: How can we represent texture?
Measure responses of blobs and edges at various orientations and scales
Record simple statistics (e.g., mean, std.) of absolute filter responses

## Slide 63: Can you match the texture to the response?
Mean abs responses
Filters
A
B
C
1
2
3

## Slide 64: Representing texture by mean abs response
Mean abs responses
Filters

## Slide 65: Project 1: Hybrid Images
http://courses.engr.illinois.edu/cs498dh3/projects/hybrid/ComputationalPhotography_ProjectHybrid.html
Gaussian Filter!
Laplacian Filter!
Project Instructions:
A. Oliva, A. Torralba, P.G. Schyns, “Hybrid Images,” SIGGRAPH 2006
Gaussian
unit impulse
Laplacian of Gaussian

## Slide 67: Take-home messages
Image is a matrix of numbers
Linear filtering is a dot product at each position
  Can smooth, sharpen, translate (among many other uses)
Be aware of details for filter size, extrapolation, cropping
Start thinking about project (read the paper, create a test project page)
1
1
1
1
1
1
1
1
1
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
=

## Slide 68: Take-home questions
Write down a 3x3 filter that returns a positive value if the average value of the 4-adjacent neighbors is less than the center and a negative value otherwise
Write down a filter that will compute the gradient in the x-direction:
gradx(y,x) = im(y,x+1)-im(y,x) for each x, y

## Slide 69: Take-home questions
3. Fill in the blanks:
a) _ = D * B
b) A = _ * _
c) F = D * _
d) _ = D * D
A
B
C
D
E
F
G
H
I
Filtering Operator

## Slide 70: Next class: Thinking in Frequency