## Slide 1
11/16/17
Computational Approaches to Cameras
Computational Photography
Derek Hoiem, University of Illinois
Magritte , The False Mirror (1935)

## Slide 2: Announcements
Final project proposal due Monday (see links on webpage)

## Slide 3: Conventional cameras
Conventional cameras are designed to capture light in a medium that is directly viewable
Light
Lens
Sensor
Display
Scene
Eye

## Slide 4: Computational cameras
With a computational approach, we can capture light and then figure out what to do with it
Light
Displays
Scene
Eyes
Captured Light
Computation

## Slide 5: Questions for today
How can we represent all of the information contained in light?
What are the fundamental limitations of cameras?
What sacrifices have we made in conventional cameras? For what benefits?
How else can we design cameras for better focus, deblurring, multiple views, depth, etc.?

## Slide 6
How can we represent all of the information contained in light?

## Slide 7: Representing Light: The Plenoptic Function
Q: What is the set of all things that we can ever see?
A: The Plenoptic Function (Adelson & Bergen)
Let’s start with a stationary person and try to parameterize everything that he can see…
Figure by Leonard McMillan
Slides from Efros

## Slide 8: Grayscale snapshot
is intensity of light
  Seen from a single view point
  At a single time
  Averaged over the wavelengths of the visible spectrum
(can also do P(x,y), but spherical coordinate are nicer)
P(q,f)

## Slide 9: Color snapshot
is intensity of light
  Seen from a single view point
  At a single time
  As a function of wavelength
P(q,f,l)

## Slide 10: A movie
is intensity of light
  Seen from a single view point
  Over time
  As a function of wavelength
P(q,f,l,t)

## Slide 11: Holographic movie
is intensity of light
  Seen from ANY viewpoint
  Over time
  As a function of wavelength
P(q,f,l,t,VX,VY,VZ)

## Slide 12: The Plenoptic Function
  Can reconstruct every possible view, at every moment, from every position, at every wavelength
  Contains every photograph, every movie, everything that anyone has ever seen!
P(q,f,l,t,VX,VY,VZ)

## Slide 13: Full Plenoptic Camera
Records position and orientation of each ray at each time and wavelength
P(VX,VY,VZ,q,f,t,l)

## Slide 14
What fundamentally limits cameras?

## Slide 15: Representing light
  The atomic element of light: a pixel a ray

## Slide 16: Fundamental limitations and trade-offs
Only so much light in a given area to capture
Basic sensor accumulates light at a set of positions from all orientations, over all time
We want intensity of light at a given time at one position for a set of orientations
Solutions:
  funnel, constrain, redirect light
  change the sensor
CCD inside camera

## Slide 17
What sacrifices does the conventional camera make? For what gains?

## Slide 18: Trade-offs of conventional camera
Add a pinhole
  Pixels correspond to small range of orientations at the camera center, instead of all gathered light at one position
  Much less light hits sensor
Add a lens
  More light hits sensor
  Limited depth of field
  Chromatic aberration
Add a shutter
  Capture average intensity at a particular range of times
Increase sensor resolution
  Each pixel represents a smaller range of orientations
  Less light per pixel
Controls: aperture size, focal length, shutter time

## Slide 19
How else can we design cameras?
What do they sacrifice/gain?

## Slide 20: 1. Light Field Photography with “Plenoptic Camera”
Ng et al. Stanford TR, 2005
Adelson and Wang 1992
Conventional Camera
“Plenoptic Camera”

## Slide 21: Light field photography
Like replacing the human retina with an insect compound eye
Records where light ray hits the lens

## Slide 22: Stanford Plenoptic Camera [Ng et al 2005]
4000 × 4000 pixels ÷ 292 × 292 lenses = 14 × 14 pixels per lens
Contax medium format camera
Kodak 16-megapixel sensor
Adaptive Optics microlens array
125μ square-sided microlenses

## Slide 23: Light field photography: applications

## Slide 24: Light field photography: applications
Change in viewpoint

## Slide 25: Light field photography: applications
Change in viewpoint
Lateral
Along Optical Axis

## Slide 26: Digital Refocusing

## Slide 27: Light field photography w/ microlenses
We gain
  Ability to refocus or increase depth of field
  Ability for small viewpoint shifts
What do we lose (vs. conventional camera)?
Notes: Lose resolution and/or light

## Slide 28: 2. Coded apertures

## Slide 29: Image and Depth from a Conventional Camera with a Coded Aperture
Anat Levin, Rob Fergus, Frédo Durand, William Freeman
MIT CSAIL
Slides from SIGGRAPH Presentation

## Slide 30
Single input image:
Output #1: Depth map
Notes: In this work we infer depth from a single image by analyzing the local defocus patterns.

## Slide 31
Single input image:
Output #1: Depth map
Output #2: All-focused image
Notes: We also undo the defocus blur and recover an all focused image.

## Slide 32: Lens and defocus
Lens
Camera sensor
Point spread function
Image of a point light source
Focal plane
Lens’ aperture
Notes: before we modify lenses, let’s start with a brief review of conventional lenses.
When we capture an object at the focus distance of a lens all light rays which emerge from an object point will be mapped by the lens onto a single point on the sensor plane.

## Slide 33: Lens and defocus
Lens
Object
Camera sensor
Point spread function
Image of a defocused point light source
Lens’ aperture
Focal plane
Notes: when the object is moved from the focus distance, the rays will spread over multiple sensor points and the captured image will be blurry.

## Slide 34: Lens and defocus
Lens
Camera sensor
Point spread function
Image of a defocused point light source
Object
Lens’ aperture
Focal plane
Notes: If the object is moved further away the blur will be even larger

## Slide 35: Lens and defocus
Lens
Camera sensor
Point spread function
Image of a defocused point light source
Lens’ aperture
Object
Focal plane

## Slide 36: Lens and defocus
Lens
Camera sensor
Point spread function
Image of a defocused point light source
Lens’ aperture
Object
Focal plane

## Slide 37: Depth and defocus
Depth from defocus:
Infer depth by analyzing local scale of defocus blur
Out of focus
In focus
ill posed
Notes: Therefore, if we could measure the exact amount of defocus blur at every image location, we could infer the depth of the scene.
Unfortunately, despite many years of research there is no good way to measure defocus from a single input image.

## Slide 38: Challenges
Hard to discriminate a smooth scene from defocus blur
Hard to undo defocus blur
Input
Ringing with conventional deblurring algorithm
Out of focus
?
Notes: The reason the problem is hard is that when observing a blurry image window it’s very hard to know: do we observe the blurry image of a sharp object or the sharp image of a blurry scene.
The second challenge involved with the project is that even if we could infer the depth, undoing the defocus blur is not strait forward.

## Slide 39: Key ideas
Exploit prior on natural images
- Improve deconvolution
- Improve depth discrimination
Coded aperture (mask inside lens)
- make defocus patterns different from natural images and easier to discriminate
Natural
Unnatural
Notes: To address these challenges we use two main ideas. The first is the fact that typical images we observe around us are not just white noise and we can place strong image priors which will guide our search.
The second idea is to replace the conventional lens with a coded one. This allows us to change the defocus pattern and make it more discriminative to depth variations.

## Slide 40
Defocus as local convolution
Input defocused image
Calibrated blur kernels at different depths
Notes: Now let’s define the problem mathematically. Our input is a single defocused image. In addition, we can calibrate and pre-store the lens blur at different depths.

## Slide 41
Defocus as local convolution
Depth k=1:
Depth k=2:
Depth k=3:
Input defocused image
Local sub-window
Calibrated blur kernels at depth
Sharp sub-window
Notes: If we consider local windows whose depth is constant, the observed image y can be modeled as a convolution of a sharp image x with one of the defocus filters. The exact scale of the defocus filter is a function of depth.
There are 2 elements in this equation that we don’t know- first we don’t know the sharp image x, and second we don’t know the scale of the filter with which it was blurred since we don’t know the depth.

## Slide 42
Overview
Correct scale
Smaller scale
Larger scale
Try deconvolving local input windows with different scaled filters:
Somehow: select best scale.
?
?
?
Notes: So here is the high level strategy that we use in our work.
We try to deconvolve the image with all scales of defocus kernels, and we somehow choose the best explanation. And if we manage to identify the correct scale of defocus we will have the depth.
However, the two steps of this strategy are quite challenging.

## Slide 43
Challenges
Hard to identify correct scale:
Hard to deconvolve even when kernel is known
Input
Ringing with the traditional Richardson-Lucy deconvolution algorithm
?
?
Correct scale
Smaller scale
?
Larger scale
Hard to deconvolve even when kernel is known
Notes: First, deconvolution is known to be difficult, and existing algorithms result in significant ringing artifacts.
The second challenge is that if there was a simple good criterion to identify the correct defocus scale, we could probably solve depth from defocus 20 years ago.
If we check this example we can see that the larger scale indeed looks very wrong. The correct scale is ok, but the smallest scale explanation is also not that bad, so it’s not easy to decide which of these two explanations to keep.
In fact this is the same ambiguity we mentioned in the beginning: do we observe the blurry image of a sharp object or the sharp image of a blurry scene.

## Slide 44
?
=
Deconvolution is ill posed
Notes: The deconvolution problem can be defined as finding an image x, such that convolved with a filter f, will be equal to the input y.
Convolution is a linear operation and therefore we have here linear constraints on x.
However, in many cases the blur filter kills some of the image information and we don’t have a full rank system, which means that there may not be a unique solution.

## Slide 45
Deconvolution is ill posed
?
=
=
?
Solution 1:
Solution 2:
Notes: For example, here are 2 possible solutions, and believe it or not, but convolving these to image with the filter f, gives *exactly* the same image.
Yet, when you look at these two solutions it’s very clear to you which of them is good and which of them isn’t, and this is because you know that the original signal was an image and you have in mind a very strong prior on what an image should look like.

## Slide 46
Idea 1: Natural images prior
Image
gradient
put a penalty on gradients
Natural images have sparse gradients
Natural
Unnatural
What makes images special?
Notes: If we could computationally characterize typical images, we can bias algorithms to output 2D arrays that are more likely to look natural. This is a very powerful idea that is becoming popular for a number of problems in computer vision and image processing.
One way to characterize images is to observe that the gradients are rare, and the normal image on this slide has much fewer gradients comparing to the bad ones.
We can exploit this fact by penalizing potential outputs that have high gradients.

## Slide 47
Deconvolution with prior
_
2
+
_
+
2
?
?
Convolution error
Derivatives prior
High
Low
Equal convolution error
Notes: Therefore we say that we want to find an image x that will minimize the convolution error, but also add the request that it will have fewer gradients.
Or in other words, we try to minimize the sum of a gradient measure over all image pixels.
Therefore despite the fact that the 2 solutions have equal convolution error, we can prefer the good one because it has fewer gradients.

## Slide 48
Comparing deconvolution algorithms
Input
Richardson-Lucy
(Non blind) deconvolution code available online: http://groups.csail.mit.edu/graphics/CodedAperture/
Gaussian prior
“spread” gradients
Sparse prior
“localizes” gradients
Notes: Here is an input blurry image.
A traditional 30 years old way to do deconvolution, is the Richardson Lucy algorithm, which usually produces an image full of ringing.
Instead we can minimize the energy in the previous slide.
The simplest way to penalize the gradients is with the squared norm, which is equivalent to a Gaussian prior. The squared norm is smaller when many small gradients are distributed evenly over many pixels- so this strategy generates some ringing.
A better thing to do is to use a robust norm, or a sparse prior. This prior prefers that only a small number of pixels will suffer- so it generates a small number of sharp transitions and keep the rest of the image clean and smooth.

## Slide 49
Comparing deconvolution algorithms
Input
Richardson-Lucy
(Non blind) deconvolution code available online: http://groups.csail.mit.edu/graphics/CodedAperture/
Gaussian prior
“spread” gradients
Sparse prior
“localizes” gradients

## Slide 50
?
?
Correct scale
Smaller scale
?
Larger scale
Try deconvolving local input windows with different scaled filters:
Recall: Overview
Challenge: smaller scale not so different than correct
Somehow: select best scale.
Notes: This was about deconvolution, and we now that we know how to deconvolve, we return to our main algorithm.
Recall that we said we would like to try to deblur local input windows with different defocus scales and somehow keep the best explanation.
But the challenge is that the smaller scale is not so different from the correct one.

## Slide 51
Idea 2: Coded Aperture
Mask (code) in aperture plane
- make defocus patterns different from natural images and easier to discriminate
Conventional aperture
Our coded aperture
Notes: To reduce this uncertainty we reach our main idea- the coded aperture. The coded aperture is a simple change to conventional lenses- inserting into the aperture an occluding pattern.

## Slide 52: Solution: lens with occluder
Lens
Camera sensor
Point spread function
Object
Focal plane
Notes: To understand what happens let’s return to the rays diagram.

## Slide 53: Solution: lens with occluder
Lens with coded aperture
Camera sensor
Point spread function
Image of a defocused point light source
Aperture pattern
Object
Focal plane
Notes: Since the occluder blocks part of the light rays the scene point isn’t spread uniformly, but in a way proportional to the aperture pattern.

## Slide 54: Solution: lens with occluder
Lens with coded aperture
Camera sensor
Point spread function
Image of a defocused point light source
Aperture pattern
Object
Focal plane
Notes: And like the conventional aperture-
If we move the point light source closer to the focus plane, we get a smaller scale of the same pattern, and the exact scale is a function of depth.

## Slide 55: Solution: lens with occluder
Lens with coded aperture
Camera sensor
Point spread function
Image of a defocused point light source
Aperture pattern
Object
Focal plane

## Slide 56: Solution: lens with occluder
Lens with coded aperture
Camera sensor
Point spread function
Image of a defocused point light source
Aperture pattern
Object
Focal plane

## Slide 57: Solution: lens with occluder
Lens with coded aperture
Camera sensor
Point spread function
Image of a defocused point light source
Aperture pattern
Object
Focal plane

## Slide 58
Coded aperture reduces uncertainty in scale identification
Conventional
Coded
Correct scale
Smaller scale
Larger scale
Notes: So why a coded aperture does actually helps us to estimate depth?
We captured the same image with both a conventional and a coded lens.
And let’s try again to deconvolve our local image window with different scales of the defocus filter. With a conventional aperture we have uncertainty between the correct scale and the smaller one, but with the coded aperture, both the smaller and the larger scales are making mess, so the uncertainty is reduced.
This uncertainty demonstrates the major idea behind the coded aperture, and for those of you who want to understand better what happens, we make a short transition into the frequency domain.

## Slide 59
Convolution- frequency domain representation
=
=
Sharp Image
Sharp Image
Spatial convolution frequency multiplication
Frequency
spectrum
Frequency
spectrum
Frequency
spectrum
Frequency
spectrum
Frequency
spectrum
Frequency
spectrum
Filter, 1st scale
Filter, 2nd scale
Output spectrum has zeros where filter spectrum has zeros
2nd observed image
1st observed image
Notes: Here we have a Fourier transform of a 1D filter at 2 different scales.
We can apply the 2 filters on an image signal. In the frequency domain convolution is just multiplication, and we obtain output signals.
The outputs maintain some of the filters structure and in particular they will be zeros at the same frequencies in which the filters are zeros.

## Slide 60
?
?
Coded aperture: Scale estimation and division by zero
=
=
Frequency
spectrum
Frequency
spectrum
Frequency
spectrum
Frequency
spectrum
Frequency
spectrum
Estimated image
spatial ringing
Large magnitude in image to compensate for tiny magnitude in filter
Estimated image
Filter, wrong scale
Filter, correct scale
Observed image
Notes: Now let’s do the opposite thing- suppose we are given an input signal and we would like to determine by which scale of the filter it was generated.
So we can try to explain it with the first scale, and in this case there is a simple solution- the original image signal.
Now we also try to explain the observed signal with the second scale.
Since convolution is multiplication in the frequency domain, theoretically we just need to divide.
However, at the frequency omega we end up dividing by zero. Since the value of the observed signal is bigger than zero while the value of the filter is zero, no meter which value we place in the recovered image we can never get a non-zero value at the output.
Even for the frequencies in which the filter response is close to zero but not exactly zero we need very high spectrum values in order to explain the observation, and such high values are uncommon in natural images, and they are translated into ringing in the spatial domain.

## Slide 61
?
?
=
Frequency
spectrum
Frequency
spectrum
Frequency
spectrum
Frequency
spectrum
Frequency
spectrum
Estimated image
Estimated image
Division by zero with a conventional aperture?
Filter, wrong scale
Filter, correct scale
Observed image
no spatial ringing
=
Notes: So we see that the division by zero prevents us from explaining the observation with the wrong scale. But why does the zeros trick *not* work with a conventional aperture?
To explain this we got here two scales of the conventional aperture.
And at a first glance we can find a zero value in the wrong scale. However, the corresponding value in the true scale is close enough to zero, and as a result the observed signal value is tiny as well. This means that we now need to divide only a tiny number by zero, and this is not as bad anymore. In fact, any reasonable deconvolution algorithm will explain this tiny value as just noise in the observed signal.
Therefore, we don’t get huge spectrum values in the estimated signal and we don’t get spatial ringing.
As a result, with a conventional aperture the wrong scale explanation is not significantly different than the correct one.

## Slide 62
Filter Design
Sampled aperture patterns
Conventional aperture
More discrimination between scales
Score
Less discrimination between scales
Analytically search for a pattern maximizing discrimination between images at different defocus scales (KL-divergence)
Account for image prior and physical constraints
Notes: In order to design a good aperture filter in a principled way, we propose in the paper an analytical measure for the statistical distance between different scales of a filter.
Using this measure we can search over aperture filters, and evaluate their discrimination score, and we select a filter with a high score.
On the other hand, our measure indeed predicts that a conventional aperture Gaussian filter will have a poor discrimination.
And for further details about this, please see the paper..

## Slide 63
Depth results

## Slide 64
Input
Local depth estimation
Regularized depth
Regularizing depth estimation
_
2
+
Convolution error
Derivatives prior
Try deblurring with 10 different aperture scales
Keep minimal error scale in each local window
+ regularization
Notes: To obtain depth for the full image, we consider each sub-window independently, trying a range of defocus scales and picking the one which minimizes the deconvolution error. However, this can be noisy.
Also, like most passive depth estimation methods, our approach requires texture, so has trouble with uniform areas of the image.
Therefore, we use a markov random field to regularize the local depth map. This prefers the depth to be piece-wise constant and that depth discontinuities should align with image discontinuities. This gives the improved depth map on the right.
The colors correspond to depth from the camera, red being closer and blue being further away.

## Slide 65
Input
Local depth estimation
Regularized depth
Regularizing depth estimation

## Slide 66
All focused results

## Slide 67
Input

## Slide 68
All-focused (deconvolved)
Notes: Unlike conventional plenoptic cameras, our approach produces images at full resolution, which in this case
exceeds that of the projector, so we need to zoom in to see better.

## Slide 69: Close-up
Original image
All-focus image

## Slide 70: Comparison- conventional aperture result
Ringing due to wrong scale estimation
Notes: To show the power of the coded aperture, we used exactly the same
calibration and depth estimation pipelines with a conventional
aperture. The resulting all-focused image contains ringing due to
incorrect estimation of the depth.

## Slide 71: Comparison- coded aperture result
Notes: By contrast, if we use a coded aperture we get a clean result.

## Slide 72
Input

## Slide 73
All-focused (deconvolved)

## Slide 74: Close-up
Original image
All-focus image
Naïve sharpening
Notes: Zooming in, we can see the original and deblurred output. For comparison, we also try a naive edge sharpening operation in Photoshop, but it simply increases the artifacts in the image.

## Slide 75
Application: Digital refocusing from a single image
Notes: Using the all-focused image and the layered depth map, one application
is post-exposure refocusing.

## Slide 76
Application: Digital refocusing from a single image
Notes: and we can refocus on different individuals.

## Slide 77
Application: Digital refocusing from a single image

## Slide 78
Application: Digital refocusing from a single image

## Slide 79
Application: Digital refocusing from a single image

## Slide 80
Application: Digital refocusing from a single image

## Slide 81
Application: Digital refocusing from a single image

## Slide 82
Image AND depth at a single shot
No loss of image resolution
Simple modification to lens
Depth is coarse
But depth is a pure bonus
Lose some light
But deconvolution increases depth of field
Coded aperture: pros and cons
unable to get depth at untextured areas, might need manual corrections.
-
+
+
+
-
+
+
Notes: Let's summarize the pros and cons of the method.
We obtain a high-resolution image and depth
information from a single shot. This requires a simple modification to
a conventional lens.
Like most passive depth acquisition methods our technique relies on the fact that the scene will include texture.
Our depth estimation is not perfect and for some images we need user
help to correct the depth map.
However, since users can continue to use a conventional camera and capture high resolution images the depth information is a pure bonus.
Another limitation is that by blocking parts of the aperture we loose about 50% of the incoming light and we will require longer exposure time. But on the other hand the deconvolution allows us to increase depth of field.

## Slide 83
Depth acquisition:
priceless
$1
Cardboard:
$79.95
50mm f/1.8:
Tape:
$1
Notes: In summary, our coded aperture is a very simple modification of a
conventional lens. It's a low budget project: the lens is $80, the
cardboard is cheap and the tape is virtually free and for this you get
get back depth.

## Slide 84: Some more quick examples

## Slide 85
Quickly move camera in a parabola when taking a picture
A motion at any speed in the direction of the parabola will give the same blur kernel

## Slide 86: Results
Static Camera
Parabolic Camera

## Slide 87: Results
Motion in wrong direction
Static Camera
Parabolic Camera

## Slide 89: RGBW Sensors
2007: Kodak ‘Panchromatic’ Pixels
Outperforms Bayer Grid
  2X-4X sensitivity (W: no filter loss)
  May improve dynamic range (W >> RGB sensitivity)
http://www.dpreview.com/news/2007/6/14/kodakhighsens

## Slide 90: Computational Approaches to Display
3D TV without glasses
  20”, $2900, available in Japan (2010)
  You see different images from different angles
http://news.cnet.com/8301-13506_3-20018421-17.html
Newer version: http://www.pcmag.com/article2/0,2817,2392380,00.asp
http://reviews.cnet.com/3dtv-buying-guide/
Toshiba

## Slide 91: Recap of questions
How can we represent all of the information contained in light?
What are the fundamental limitations of cameras?
What sacrifices have we made in conventional cameras? For what benefits?
How else can we design cameras for better focus, deblurring, multiple views, depth, etc.?
Notes: Answers:
1) Plenoptic function
2) Amount of light
3) Limit light and get depth of field effects; sharp images that are easy to display
4) Lots of ways

## Slide 92: Next class
Exam review
But first, have a good Thanksgiving break!