## Slide 1
11/13/19
How the Kinect Works
Computational Photography
Derek Hoiem, University of Illinois
Photo frame-grabbed from: http://www.blisteredthumbs.net/2010/11/dance-central-angry-review
T2

## Slide 2: Incomplete list of excellent projects
Rendered image looks really good: https://liwenwu2.web.illinois.edu/cs445/proj4/
Contains GIF rendering: https://yilinma3.web.illinois.edu/cs445/proj4/
Quality shadow rendering: https://anbangy2.web.illinois.edu/cs445/proj4/
Pokemon meshes: https://wyang52.web.illinois.edu/cs445/proj4/

## Slide 3
Liwen Wu
Yilin Ma Kexiang Wang

## Slide 4
Anbang Ye
Wanxian Yang
Ruicheng Xian

## Slide 5
How the Kinect Works
Computational Photography
Derek Hoiem, University of Illinois
Photo frame-grabbed from: http://www.blisteredthumbs.net/2010/11/dance-central-angry-review
T2

## Slide 6: Kinect Device

## Slide 7: Kinect Device
illustration source: primesense.com

## Slide 8: What the Kinect does
Get Depth Image
Estimate Body Pose
Application (e.g., game)

## Slide 9: How Kinect Works: Overview
IR Projector
IR Sensor
Projected Light Pattern
Depth Image
Stereo Algorithm
Segmentation,
Part Prediction
Body Pose

## Slide 10: Part 1: Stereo from projected dots
IR Projector
IR Sensor
Projected Light Pattern
Depth Image
Stereo Algorithm
Segmentation,
Part Prediction
Body Pose

## Slide 11: Part 1: Stereo from projected dots
Overview of depth from stereo
How it works for a projector/sensor pair
Stereo algorithm used by Primesense (Kinect)

## Slide 12: Depth from Stereo Images
image 1
image 2
Dense depth map
Some of following slides adapted from Steve Seitz and Lana Lazebnik

## Slide 13: Depth from Stereo Images
Goal: recover depth by finding image coordinate x’ that corresponds to x
f
x
x’
Baseline B
z
O
O’
X
f
X
x
x'

## Slide 14: Stereo and the Epipolar constraint
Potential matches for x have to lie on the corresponding line l’.
Potential matches for x’ have to lie on the corresponding line l.
x
x’
X
x’
X
x’
X

## Slide 15: Simplest Case: Parallel images
Image planes of cameras are parallel to each other and to the baseline
Camera centers are at same height
Focal lengths are the same
Then, epipolar lines fall along the horizontal scan lines of the images

## Slide 16: Depth from disparity
f
x’
Baseline B
z
O
O’
X
f
Disparity is inversely proportional to depth.
x

## Slide 17: Basic stereo matching algorithm
For each pixel in the first image
  Find corresponding epipolar line in the right image
  Examine all pixels on the epipolar line and pick the best match
  Triangulate the matches to get depth information

## Slide 18: Basic stereo matching algorithm
If necessary, rectify the two stereo images to transform epipolar lines into scanlines
For each pixel x in the first image
  Find corresponding epipolar scanline in the right image
  Examine all pixels on the scanline and pick the best match x’
  Compute disparity x-x’ and set depth(x) = fB/(x-x’)

## Slide 19: Correspondence search
Matching cost
disparity
Left
Right
scanline
Slide a window along the right scanline and compare contents of that window with the reference window in the left image
Matching cost: SSD or normalized correlation

## Slide 20: Correspondence search
Left
Right
scanline
SSD

## Slide 21: Correspondence search
Left
Right
scanline
Norm. corr

## Slide 22: Results with window search
Window-based matching
Ground truth
Data

## Slide 23: Add constraints and solve with graph cuts
Graph cuts
Ground truth
    For the latest and greatest: http://www.middlebury.edu/stereo/
  Y. Boykov, O. Veksler, and R. Zabih, Fast Approximate Energy Minimization via Graph Cuts, PAMI 2001
Before

## Slide 24: Failures of correspondence search
Textureless surfaces
Occlusions, repetition
Non-Lambertian surfaces, specularities

## Slide 25: Dot Projections
http://www.youtube.com/watch?v=28JwgxbQx8w

## Slide 26: Depth from Projector-Sensor
Only one image: How is it possible to get depth?
Projector
Sensor
Scene Surface

## Slide 27: Same stereo algorithms apply
Projector
Sensor

## Slide 28: Example: Book vs. No Book
Source: http://www.futurepicture.org/?p=97

## Slide 29: Example: Book vs. No Book
Source: http://www.futurepicture.org/?p=97

## Slide 30: Region-growing Random Dot Matching
Detect dots (“speckles”) and label them unknown
Randomly select a region anchor, a dot with unknown depth
  Windowed search via normalized cross correlation along scanline
    Check that best match score is greater than threshold; if not, mark as “invalid” and go to 2
  Region growing
    Neighboring pixels are added to a queue
    For each pixel in queue, initialize by anchor’s shift; then search small local neighborhood; if matched, add neighbors to queue
    Stop when no pixels are left in the queue
Repeat until all dots have known depth or are marked “invalid”
http://www.wipo.int/patentscope/search/en/WO2007043036

## Slide 31: Projected IR vs. Natural Light Stereo
What are the advantages of IR?
  Works in low light conditions
  Does not rely on having textured objects
  Not confused by repeated scene textures
  Can tailor algorithm to produced pattern
What are advantages of natural light?
  Works outside, anywhere with sufficient light
  Uses less energy
  Resolution limited only by sensors, not projector
Difficulties with both
  Very dark surfaces may not reflect enough light
  Specular reflection in mirrors or metal causes trouble

## Slide 32: Uses of Kinect (part 1)
3D Scanner: http://www.youtube.com/watch?v=V7LthXRoESw
IllumiRoom: http://research.microsoft.com/apps/video/default.aspx?id=191304
https://www.youtube.com/watch?v=nGGMv9RnJIA

## Slide 33: To learn more
Warning: lots of wrong info on web
Great site by Daniel Reetz: http://www.futurepicture.org/?p=97
Kinect patents: http://www.faqs.org/patents/app/20100118123 http://www.faqs.org/patents/app/20100020078 http://www.faqs.org/patents/app/20100007717

## Slide 34: How does the Kinect v2 work?
Time of flight sensor
  Turn on and off two co-located pixels in alternation very quickly (e.g., 10 GHz)
  Pulse laser just as quickly
  Ratio of light achieved by the two pixels tells travel time (i.e., distance) of laser
  By modifying the pulse frequency, you get a low-res and high-res estimate of travel time
http://www.gamasutra.com/blogs/DanielLau/20131127/205820/The_Science_Behind_Kinects_or_Kinect_10_versus_20.php

## Slide 35: Part 2: Pose from depth
IR Projector
IR Sensor
Projected Light Pattern
Depth Image
Stereo Algorithm
Segmentation,
Part Prediction
Body Pose

## Slide 36: Goal: estimate pose from depth image
Real-Time Human Pose Recognition in Parts from a Single Depth Image
Jamie Shotton, Andrew Fitzgibbon, Mat Cook, Toby Sharp, Mark Finocchio, Richard Moore, Alex Kipman, and Andrew Blake CVPR 2011

## Slide 37: Goal: estimate pose from depth image
RGB
Depth
Part Label Map
Joint Positions
http://research.microsoft.com/apps/video/default.aspx?id=144455

## Slide 38: Challenges
Lots of variation in bodies, orientation, poses
Needs to be very fast (their algorithm runs at 200 FPS on the Xbox 360 GPU)
Pose Examples
Examples of one part

## Slide 39: Extract body pixels by thresholding depth

## Slide 40: Basic learning approach
Very simple features
Lots of data
Flexible classifier

## Slide 41: Features
Difference of depth at two offsets
  Offset is scaled by depth at center

## Slide 42: Get lots of training data
Capture and sample 500K mocap frames of people kicking, driving, dancing, etc.
Get 3D models for 15 bodies with a variety of weight, height, etc.
Synthesize mocap data for all 15 body types

## Slide 43: Body models

## Slide 44: Part prediction with random forests
Randomized decision forests: collection of independently trained trees
Each tree is a classifier that predicts the likelihood of a pixel belonging to each part
  Node corresponds to a thresholded feature
  The leaf node that an example falls into corresponds to a conjunction of several features
  In training, at each node, a subset of features is chosen randomly, and the most discriminative is selected

## Slide 45: Joint estimation
Joints are estimated using mean-shift (a fast mode-finding algorithm)
Observed part center is offset by pre-estimated value

## Slide 46: Results
Ground Truth

## Slide 47: More results

## Slide 48: Accuracy vs. Number of Training Examples

## Slide 49: Uses of Kinect (part 2)
Mario: http://www.youtube.com/watch?v=8CTJL5lUjHg
Robot Control: https://www.youtube.com/watch?v=7vq-1TiXi3g
Capture for holography: http://www.youtube.com/watch?v=4LW8wgmfpTE
Virtual dressing room: http://www.youtube.com/watch?v=1jbvnk1T4vQ
Fly wall: http://vimeo.com/user3445108/kiwibankinteractivewall

## Slide 50: Note: pose from rgb video works amazingly well now
https://www.youtube.com/watch?v=pW6nZXeWlGM&t=77s
OpenPose: https://github.com/CMU-Perceptual-Computing-Lab/openpose

## Slide 51: Coming up
Computational approaches to cameras