## Slide 1
Moving Forward
Computational Photography
Derek Hoiem, University of Illinois

## Slide 2: Today
Requested topics
  iPhone LiDAR
  VR
  Holographic displays
  Transformers
Other topics
  Light transport
  Event cameras
Beyond this class…

## Slide 3: This course has provided fundamentals
How photographs are captured from and relate to the 3D scene
How to think of an image as: a signal to be processed, a graph to be searched, an equation to be solved
How to manipulate photographs: cutting, growing, compositing, morphing, stitching
Basic principles of computer vision: filtering, correspondence, alignment

## Slide 4
What else is out there?
Lots!
Machine learning
Videos and motion
3D reconstruction
Scene understanding
Better/cheaper devices
…

## Slide 5: iPhone/iPad LiDAR
Collection using Scaniverse by Asher Mai
https://apps.apple.com/us/app/scaniverse-3d-scanner/id1541433223
Support for iPhone/iPad without LiDAR added in Sept 2022

## Slide 6: iPhone/iPad LiDAR
Works by “time of flight” – the time it takes for a laser to bounce back
  Sends out light using an array of vertical cavity surface-emitting lasers (VCSELs) made by Lumentum
  Detects the return flash using an array of sensors called single-photon avalanche diodes (SPADs) supplied by Sony
Hardware advances
  Vertical cavity surface emitting laser (VCSEL)
    Recently made more powerful, catching up to more expensive edge-emitting lasers
    One chip can hold thousands of lasers and be produced for a few dollars at scale
  Single photon avalanche diode (SPAD)
    Can detect single photons but noisy, so requires complex post-processing
    Thousands can be packed on a chip
  Result: cheap devices, no moving parts
Source: Arstechnica article

## Slide 7: Creating 3D models
LiDAR provides a depth map per image
  May need to refine and increase resolution based on image cues, e.g. iPad Pro 2020 gets only 24x24 depth values per frame
Device also tracks its pose in the scene using SLAM
Depth maps can be fused together based on pose information, and pose can be refined to improve alignment
Dense point cloud can be converted into a mesh that is textured from images, e.g. with Poisson surface reconstruction and texrecon texturing
https://blog.scaniverse.com/scaniverse-high-detail-3d-scans-353d5f42de6b

## Slide 8: VR – Oculus Quest 2
Hardware
  Two 1823x1920 screens w/ 72Hz refresh
  Four front-facing cameras
  IMUs, microphone
Software
  Track head position using SLAM
  Track controllers using IR LEDs
  Track fingers using deep networks (computer vision)

## Slide 9: VR: SLAM-based pose estimation of the head
IMU at 1000Hz
Track points (visual)
Map and update pose
https://techcrunch.com/2019/08/22/how-oculus-squeezed-sophisticated-tracking-into-pipsqueak-hardware/

## Slide 10: Tracking controllers
https://www.mechatech.co.uk/journal/how-do-common-virtual-reality-tracking-systems-work
Controllers have infra-red LEDs
Oculus has 4 cameras that can see the LEDs
Estimate controller pose relative to headset based on LED positions

## Slide 11: Tracking hands
Deep networks for hand pose estimation
  Likely related to existing algorithms such as open pose but taking advantage of multiple cameras and making it extremely efficient
https://www.youtube.com/watch?v=uztFcEA6Rf0

## Slide 12: Holographic displays
Key idea
Generate a light field (i.e. different pictures are sent in different directions, simulating the light that would be cast from a 3D object)
Some versions
Project light onto a glass surface
Screen that scatters light in controlled ways
Laser plasma: powerful lasers excite molecules to create images in thin air without any screen
  Bright, opaque but low-res and limited quality
Micromagnetic (MEMs) piston
  Tiny fast-changing mirrors control light reflections to create view-dependent images; still in prototype
https://www.realfiction.com/how-it-works
https://en.wikipedia.org/wiki/Holographic_display
https://www.youtube.com/watch?v=f7fffZ_k9ow

## Slide 13: Example patent from The Looking Glass Factory
https://patentimages.storage.googleapis.com/70/97/72/a60d4163a0a784/US20170078655A1.pdf
https://www.youtube.com/watch?v=EMUdmE0lKIU
$400-$20K+

## Slide 14: Transformers: multimodal data processors
Input tokens can represent anything: image patches, text tokens, audio, controls, etc.
Transformer encoder: self-attention + MLP
Self-attention: linear project + soft cluster + linear project
  Input: tokens z w/ D dimensions
  Linear projections into query, key, value: [q, k, v] = z*U
  Aggregate values according to key/query similarity
  A = softmax(qk/sqrt(D)) SA(z) = Av
  Multihead attention: project into several lower-dim vectors, aggregate on each set, concatenate and apply linear projection
Invariant to order of tokens: positional embeddings and type embeddings are used to distinguish pos/type of input
Key papers: An image is worth 16x16, Attention is all you need

## Slide 15: GPT-3: large scale <text>-to-<text>, prompting
Process up to 2048 tokens (text to text)
Network of standard (mostly) transformer blocks with 96 layers, 175 billion parameters
Trained on web corpora (400B, 19B tokens), books (12B, 55B tokens), and Wikipedia (3B tokens) to predict the next word
  Estimated cost to train: $12M for one training run
Zero-shot: task description + test input  test output
Few shot task: task description + multiple input/output examples + test input  test output
Used in many applications, e.g. code generation, search, summarization, writing aids
Key papers: “Language Models are Few-Shot Learners” (2020)
Notes: GPT stands for generative pretrained transformer

## Slide 16: Unified-IO: <text, image> to <text, image>
3B parameters
Pre-train on masked text and image completion for text, images, and image/caption pairs
Multitask training on 80 datasets
Unified-IO (June 2022)

## Slide 17
Vision tasks
Image synthesis from text / inpainting / segmentation
Image/object classification
Object detection, segmentation, keypoint estimation
Depth/normal estimation
Vision-language tasks
VQA, image/region captioning, referring expressions comprehension, relationship detection
NLP tasks
Question answering
Text classification

## Slide 18: Blind Inverse Light Transport Problem Predict the light pattern by factorizing observed scene into lighting (projected image) and scene reflectance
Observed
True image projected on screen (out of view)
Recovered image

## Slide 19
Surprising result: A randomly initialized decoder network, when trained to reproduce a corrupted image, fixes the noise, holes, etc.
The network structure acts as a prior!
CVPR 2018

## Slide 20: Magic or math? Gradient descent on encoder network to reproduce Original produces a cleaner image. Even better than recent methods designed to solve this problem.

## Slide 21
NIPS 2019
Now take it a step further. If you have the matrix product of two images, you can recover the factors.
Note: there are practically infinitely many useless solutions to this problem.

## Slide 23
Each “pixel” of light on the projector lights the scene, producing an image
The total image is the sum of images from each pixel
Observed image can be factorized into surface colors and projected image (assuming no ambient light)
https://www.youtube.com/watch?v=bzsfREU2dDM

## Slide 24: Event cameras
First commercially produced in 2008
Respond only when individual pixels change intensity
  Corresponds to camera or scene motion
1 micro-second latency
High dynamic range
100x less power than standard camera
Overview: https://www.youtube.com/watch?v=LauQ6LWTkxM
3D Reconstruction: https://www.youtube.com/watch?v=fA4MiSzYHWA

## Slide 25: Two more
Handwriting beautification (Zitnick SG’13)
  Example of user assistance
Semantic image synthesis (Park et al. CVPR 2019)

## Slide 26: Trends and Future of Computational Photography
Camera phones continue to serve as a platform for latest advances in hardware and software
  E.g. multiple cameras and depth is often available
VR / AR blend graphics with tracking and understanding of environment
  Killer app outside of games and teleconferencing?
Photorealistic content creation from prompts
  Impact outside wow factor still unclear
Design smart programs that work together with people
  This is #1 from Harry Shum, Exec VP of AI and Research at Microsoft

## Slide 27: How can you learn more?
Relevant courses
  Production graphics (CS 419)
  Machine learning (CS 446 and others)
  Deep learning (CS 444)
  Computer vision (CS 543)
  Optimization methods (CS 544)
  Parallel processing / GPU
  HCI, data mining, NLP, robotics

## Slide 28: How can you learn more?
Conference proceedings
  Vision: CVPR, ICCV, ECCV, NIPS
  Computational photography: ICCP
  Graphics: SIGGRAPH, SIGGRAPH Asia

## Slide 29: Computer Vision (CS 543)
Similar stuff to CP
Camera models, filtering, single-view geometry, light and capture
New stuff
Mid-level vision
  Edge detection, clustering, segmentation
Machine learning
Recognition
  Image features and classifiers
  Object category recognition
  Action/activity recognition
Videos
  Tracking, optical flow
  Structure from motion
Multi-view geometry

## Slide 30: Deep Learning for Vision (CS 444)
Linear classifiers
Neural networks
Convolutional networks
Object detection
Dense labeling
Self-supervised learning
GANs
Recurrent networks
Transformers
Reinforcement learning

## Slide 31: How do you learn more?
Explore and fiddle!

## Slide 32: Thank you for a great semester!
Don’t forget to complete your ICES forms

## Slide 34: Image  Light Field
https://www.youtube.com/watch?v=yLCvWoQLnms

## Slide 35: Superresolution
E: Optimize least squares objective with upsampling network
PAT: Optimize “perceptual” (VGG features) loss, adversarial loss, texture corr loss
Pretty similar to above, more limited domain

## Slide 36: De-beautification
Network regresses principal components of discrepancy map

## Slide 37: LDR --> HDR
Regress HDR from one LDR image
Train on synthetic data
Limited to outdoor scenes, rotated so that sun is on top

## Slide 38: Smarter user assistance
Handwriting beautification (Zitnick SG’13)
3D object modeling (Chen et al. SGA’13)
3D object modeling (Kholgade et al. SG’14)

## Slide 39: Video and motion
Video = sequence of images
  Track points  optical flow, tracked objects, 3D reconstruction
  Find coherent space-time regions  segmentation
  Recognizing actions and events
Examples:
  Point tracking for structure-from-motion
    Boujou 1
  Facial transfer: Xu et al. SG2014
Notes: Match move

## Slide 40: Scene understanding
Interpret image in terms of scene categories, objects, surfaces, interactions, goals, etc.
Remove the guy lying down (Alyosha)
Make the woman dance or the guy get up
Fill in the window with bricks
Find me images with only Alyosha and Piotro

## Slide 41: Scene understanding
Mostly unsolved, but we’re getting there (especially for graphics purposes)
Examples
  “From Image Parsing to Painterly Rendering” (Zeng et al. 2010)
  “Sketch2Photo: Internet Image Montage” (Chen et al. 2009)
  Editing via scene attributes (Laffont et al. 2014)

## Slide 42: Image Parsing to Painterly Rendering
Zeng et al. SIGGRAPH 2010

## Slide 43: Image Parsing to Painterly Rendering
Zeng et al. SIGGRAPH 2010
Parse
Sketch
Brush Orientations
Brush Strokes

## Slide 44: Image Parsing to Painterly Rendering
Zeng et al. SIGGRAPH 2010

## Slide 45: Image Parsing to Painterly Rendering

## Slide 46: More examples
Sketch2photo: http://www.youtube.com/watch?v=dW1Epl2LdFM
Animating still photographs
Chen et al. 2009

## Slide 47: Interactive games: Kinect
Object Recognition: http://www.youtube.com/watch?feature=iv&v=fQ59dXOo63o
Mario: http://www.youtube.com/watch?v=8CTJL5lUjHg
3D: http://www.youtube.com/watch?v=7QrnwoO1-8A

## Slide 48: Modeling humans
Estimating pose and shape
  http://clothingparsing.com/
  Parselets (Dong et al., ICCV 2013)
Motion capture
3D face from image (Kemelmacher ICCV’13)

## Slide 49: Better and simpler 3D reconstruction
MobileFusion (2015): https://youtu.be/8M_-lSYqACo

## Slide 50: Questions
How can we simplify editing of photos and videos?
How can we organize photographs and videos?
Can we just capture and store the whole visual world?

## Slide 51: How to create 3D model from multiple images
Solve for camera poses
Propose and verify 3D points by matching
Fit a surface to the points

## Slide 52: Incremental Structure from Motion (SfM)
Goal: Solve for camera poses and 3D points in scene

## Slide 53: Incremental SfM
Compute features
Match images
Reconstruct
  Solve for pose and 3D points in two cameras
  Solve for pose of additional camera(s) that observe reconstructed 3D points
  Solve for new 3D points that are viewed in at least two cameras
  Bundle adjust to minimize reprojection error

## Slide 54: Incremental SFM: detect features
Feature types: SIFT, ORB, Hessian-Laplacian, …
…
Each circle represents a set of detected features
im 1
im 2
im 3
im n

## Slide 55: Incremental SFM: match features and images
For each pair of images:
Match feature descriptors via approximate nearest neighbor and apply Lowe’s ratio test
Solve for F and find inlier feature correspondences
Speed tricks
  Use vocabulary tree to get image match candidates
  Use GPS coordinates to get match candidates, if available
…
Points of same color have been matched to each other

## Slide 56: Incremental SFM: create tracks graph
…
im 1
im 2
im 3
im n
…
tracks graph: bipartite graph between observed 3D points and images

## Slide 57: Incremental SFM: initialize reconstruction
im 1
im 2
im 3
im n
…
Choose two images that are likely to provide a stable estimate of relative pose
  E.g., < 0.7 and many inliers for
Get focal lengths from EXIF, estimate essential matrix using 5-point algorithm, extract pose with
Solve for 3D points given poses
Perform bundle adjustment to refine points and poses
filled circles = “triangulated” points
filled rectangles = “resectioned” images (solved pose)

## Slide 58: Triangulation: Linear Solution
Generally, rays Cx and C’x’ will not exactly intersect
Can solve via SVD, finding a least squares solution to a system of equations
X
x
x'
Further reading: Hartley-Zisserman p. 312-313

## Slide 59: Triangulation: Linear Solution
Given P, P’, x, x’
Precondition points and projection matrices
Create matrix A
[U, S, V] = svd(A)
X = V(:, end)
Pros and Cons
Works for any number of corresponding images
Not projectively invariant
Code: http://www.robots.ox.ac.uk/~vgg/hzbook/code/vgg_multiview/vgg_X_from_xP_lin.m

## Slide 60: Bundle adjustment
Non-linear method for refining structure and motion
Minimizing reprojection error
x1j
x2j
x3j
Xj
P1
P2
P3
P1Xj
P2Xj
P3Xj
Often a robust loss, such as Huber loss is used

## Slide 61: Incremental SFM: grow reconstruction
im 1
im 2
im 3
im n
…
Resection: solve pose for image(s) that have the most triangulated points
Triangulate: solve for any new points that have at least two cameras
Remove 3D points that are outliers
Bundle adjust
  For speed, only do full bundle adjust after some percent of new images are resectioned
Optionally, align with GPS from EXIF or ground control points (GCP)
filled circles = “triangulated” points
filled rectangles = “resectioned” images (solved pose)

## Slide 62: Incremental SFM: grow reconstruction
im 1
im 2
im 3
im n
…
Resection: solve pose for image(s) that have the most triangulated points
Triangulate: solve for any new points that have at least two cameras
Remove 3D points that are outliers
Bundle adjust
  For speed, only do full bundle adjust after some percent of new images are resectioned
Optionally, align with GPS from EXIF or ground control points (GCP)
filled circles = “triangulated” points
filled rectangles = “resectioned” images (solved pose)

## Slide 63: Important recent papers and methods for SfM
Snavely thesis (2008): intro to SfM in Chapter 3
Visual SfM: Visual SfM (Wu 2013)
  Used to be the best incremental SfM software (but not anymore and closed source); paper still very good
COLMAP
  Good open source system based on “Structure-from-motion revisited” (Schonberger Frahm 2016)
OpenSfM:
  Python open-source system, easy to read and modify
Reconstruction of Cornell (Crandall et al. ECCV 2011)

## Slide 64: Multiview Stereo: propose and verify 3D points by matching pixel patches across images
Figure from Furukawa & Hernandez (2015)
Select depth at each pixel that minimizes NCC of patches with other images
Key Assumptions
Enough texture to match
Surface looks the same from each view (non-reflective)

## Slide 65: Multiview Stereo: recommended reading
“Multiview Stereo: a tutorial” by Yasu Furukawa
http://www.cse.wustl.edu/~furukawa/papers/fnt_mvs.pdf
COLMAP:
  Code based on “Pixelwise View Selection for Unstructured Multi-View Stereo” by Schonberger et al. 2016

## Slide 66: Surface Reconstruction
Floating scale surface reconstruction:
http://www.gcc.tu-darmstadt.de/home/proj/fssr/
Constrained Delaunay triangulation
- Create 3D triangulation of dense points and remove faces that conflict with observed points