## Slide 1: Single-view Metrology + More with Pinhole Geometry
Computational Photography
Derek Hoiem, University of Illinois
10/16/12

## Slide 2: Last Tuesday
David Forsyth talked about physically grounded image editing, including inserting 3D objects into photographs

## Slide 3: Last Thursday
Amin Sadeghi talked transforming faces and PCA

## Slide 4: Project 2
Class favorites: vote please
  “Favorites” will be presented next Tues

## Slide 5: Project 3
Due Monday
  http://courses.engr.illinois.edu/cs498dh3/projects/gradient/ComputationalPhotography_ProjectGradient.html
Discussed in lecture 9 (9/25)

## Slide 6: Project 3: Toy Problem
Preserve x-y gradients
Preserve intensity of one pixel
Source pixels: s
Variable pixels: v
minimize (v(x+1,y)-v(x,y) - (s(x+1,y)-s(x,y))^2
minimize (v(x,y+1)-v(x,y) - (s(x,y+1)-s(x,y))^2
minimize (v(1,1)-s(1,1))^2

## Slide 7: Example
Source: Evan Wallace
Gradient Visualization

## Slide 8
+
Specify object region
Source: Evan Wallace

## Slide 9
Label your face

## Slide 11: Review: Pinhole Camera
Camera Center (tx, ty, tz)
.
.
.
f
Z
Y
.
Optical Center (u0, v0)
v
u

## Slide 12: Review: Projection Matrix
Ow
iw
kw
jw
t
R

## Slide 13: Review: Vanishing Points
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)
Slide from Efros, Photo from Criminisi

## Slide 14: This class
How can we calibrate the camera?
How can we measure the size of objects in the world from an image?
What about other camera properties: focal length, field of view, depth of field, aperture, f-number?
How to do “focus stacking” to get a sharp picture of a nearby object
How the “vertigo effect” works

## Slide 15: How to calibrate the camera?

## Slide 16: Calibrating the Camera
Method 1: Use an object (calibration grid) with known geometry
  Correspond image points to 3d points
  Get least squares solution (or non-linear solution)

## Slide 17: Calibrating the Camera
Method 2: Use vanishing points
  Find vanishing points corresponding to orthogonal directions
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)

## Slide 18: Take-home question
Suppose you have estimated three vanishing points corresponding to orthogonal directions. How can you recover the rotation matrix that is aligned with the 3D axes defined by these points?
  Assume that intrinsic matrix K has three parameters
  Remember, in homogeneous coordinates, we can write a 3d point at infinity as (X, Y, Z, 0)
10/16/2012
Photo from online Tate collection
VPx
VPz
.
VPy

## Slide 19: How can we measure the size of 3D objects from an image?
Slide by Steve Seitz

## Slide 20: Perspective cues
Slide by Steve Seitz

## Slide 21: Perspective cues
Slide by Steve Seitz

## Slide 22: Perspective cues
Slide by Steve Seitz

## Slide 23: Ames Room

## Slide 24: Comparing heights
Vanishing
Point
Slide by Steve Seitz

## Slide 25: Measuring height
1
2
3
4
5
5.4
2.8
3.3
Camera height
Slide by Steve Seitz

## Slide 26
Which is higher – the camera or the parachute?

## Slide 27: Computing vanishing points (from lines)
q1
Intersect p1q1 with p2q2
v
p1
p2
q2
Least squares version
  Better to use more than two lines and compute the “closest” point of intersection
  See notes by Bob Collins for one good way of doing this:
    http://www-2.cs.cmu.edu/~ph/869/www/notes/vanishing.txt

## Slide 28: Measuring height without a giant ruler
C
ground plane
Compute Z from image measurements
  Need a reference object
Z
Slide by Steve Seitz

## Slide 29: The cross ratio
A Projective Invariant
  Something that does not change under projective transformations (including perspective projection)
P1
P2
P3
P4
The cross-ratio of 4 collinear points
Can permute the point ordering
  4! = 24 different orders (but only 6 distinct values)
This is the fundamental invariant of projective geometry
Slide by Steve Seitz

## Slide 30: Measuring height
vZ
r
t
b
image cross ratio
B (bottom of object)
T (top of object)
R (reference point)
ground plane
H
C
scene cross ratio

scene points represented as
image points as
R
Slide by Steve Seitz

## Slide 31: Measuring height
R
H
vz
r
b
t
H
b0
t0
v
vx
vy
vanishing line (horizon)
image cross ratio
Slide by Steve Seitz

## Slide 32: Measuring height
vz
r
b
t0
vx
vy
vanishing line (horizon)
v
t0
m0
What if the point on the ground plane b0 is not known?
  Here the guy is standing on the box, height of box is known
  Use one side of the box to help find b0 as shown above
b0
t1
b1
Slide by Steve Seitz

## Slide 33: Take-home question
Assume that the camera height is 5 ft.
  What is the height of the man?
  What is the height of the building?

## Slide 34: Beyond the pinhole: What about focus, aperture, DOF, FOV, etc?
Camera Center (tx, ty, tz)
.
.
.
f
Z
Y
.
Optical Center (u0, v0)
v
u

## Slide 35: Adding a lens
A lens focuses light onto the film
  There is a specific distance at which objects are “in focus”
    other points project to a “circle of confusion” in the image
  Changing the shape of the lens changes this distance
“circle of
confusion”

## Slide 36: Focal length, aperture, depth of field
A lens focuses parallel rays onto a single focal point
  focal point at a distance f beyond the plane of the lens
  Aperture of diameter D restricts the range of rays
focal point
F
optical center
(Center Of Projection)
Slide source: Seitz

## Slide 37: The eye
The human eye is a camera
  Iris - colored annulus with radial muscles
  Pupil - the hole (aperture) whose size is controlled by the iris
Notes: Note that the retina is curved

## Slide 38: Focus with lenses
Lens focal length
Distance to sensor
Distance to object
Equation for objects in focus
Source: http://en.wikipedia.org/wiki/File:Lens3.svg

## Slide 39: The aperture and depth of field
Changing the aperture size or focusing distance affects depth of field
  f-number (f/#) =focal_length / aperture_diameter (e.g., f/16 means that the focal length is 16 times the diameter)
  When you change the f-number, you are changing the aperture
f / 5.6
f / 32
Flower images from Wikipedia http://en.wikipedia.org/wiki/Depth_of_field
Slide source: Seitz

## Slide 40: Varying the aperture
Large aperture = small DOF
Small aperture = large DOF
Slide from Efros

## Slide 41: Shrinking the aperture
Why not make the aperture as small as possible?
  Less light gets through
  Diffraction effects
Slide by Steve Seitz

## Slide 42: Shrinking the aperture
Slide by Steve Seitz

## Slide 43: The Photographer’s Great Compromise
What we want
More spatial resolution
Broader field of view
More depth of field
More temporal resolution
More light
How we get it
Increase focal length
Decrease aperture
Shorten exposure
Lengthen exposure
Increase aperture
Decrease focal length
Cost
Light, FOV
DOF
Light
DOF
Light
Temporal Res

## Slide 44: Difficulty in macro (close-up) photography
For close objects, we have a small relative DOF
Can only shrink aperture so far
How to get both bugs in focus?

## Slide 45: Solution: Focus stacking
Take pictures with varying focal length
http://www.wonderfulphotos.com/articles/macro/focus_stacking/
Example from

## Slide 46: Solution: Focus stacking
Take pictures with varying focal length
Combine

## Slide 47: Focus stacking
http://www.wonderfulphotos.com/articles/macro/focus_stacking/

## Slide 48: Focus stacking
How to combine?
Web answer: With software (Photoshop, CombineZM)
How to do it automatically?

## Slide 49: Focus stacking
How to combine?
Align images (e.g., using corresponding points)
Two ideas
  Mask regions by hand and combine with pyramid blend
  Gradient domain fusion (mixed gradient) without masking
http://www.zen20934.zen.co.uk/photography/Workflow.htm#Focus%20Stacking
Automatic solution would make a very interesting final project
http://www.digital-photography-school.com/an-introduction-to-focus-stacking
Recommended Reading:

## Slide 50: Relation between field of view and focal length
Field of view (angle width)
Film/Sensor Width
Focal length

## Slide 51: Dolly Zoom or “Vertigo Effect”
http://www.youtube.com/watch?v=NB4bikrNzMk
http://en.wikipedia.org/wiki/Focal_length
Zoom in while moving away
How is this done?

## Slide 52: Dolly zoom (or “Vertigo effect”)
Distance between object and camera
width of object
Field of view (angle width)
Film/Sensor Width
Focal length

## Slide 53: Things to remember
Can calibrate using grid or VP
Can measure relative sizes using VP
Effects of focal length, aperture + tricks
1
2
3
4
5

## Slide 54: Next class
Go over take-home questions from today
Single-view 3D Reconstruction