## Slide 1: Light and Color
Computational Photography
Derek Hoiem, University of Illinois
09/10/13
“Empire of Light”, Magritte

## Slide 2: Outline
Light and wavelengths
The eye
  Physiology (rods and cones)
  Receptivity, non-linear response
  Trichromacity
The camera and display
  Bayer filter revisited
  RGB display
Physics of light and reflection
  Direct light: spectrum of wavelengths
  Reflection: influence of albedo, orientation, reflectivity, BRDF
  Inter-reflection: light may be influenced by multiple surfaces
  Illusions, ambiguity of albedo and illumination color, color constancy
  Light sources and shadows
Color spaces
  RGB, HSV, YCrCb, XYZ, Lab

## Slide 3: Announcements
Project 1 due next Mon (9/16), 11:59pm
  Choosing cutoff: sigma > 1
  Remember to convert images to double
  Don’t use built-in code for pyramids, contrast equalization etc., ask if not sure

## Slide 4: Today’s class
How is incoming light measured by the eye or camera?
Incoming Light
Sensors/Retina
Lens

## Slide 5: Today’s class
How is incoming light measured by the eye or camera?
How is light reflected from a surface?
Light source
Sensors/Retina
Lens
Reflected Light
Incoming Light
Notes: Basis for vision, graphics

## Slide 6: Today’s class
How is incoming light measured by the eye or camera?
How is light reflected from a surface?
How can we represent color?

## Slide 7
Photo by nickwheeleroz, Flickr
Slide: Forsyth

## Slide 8: The Eye
The human eye is a camera!
  Iris - colored annulus with radial muscles
  Pupil - the hole (aperture) whose size is controlled by the iris
  What’s the “film”?
    photoreceptor cells (rods and cones) in the retina
Slide by Steve Seitz

## Slide 9: Retina up-close
Light
Notes: Floaty things in your vision are white blood cells in capillaries. Some animals have two foveas (some birds) and some have none (cats and dogs). 100x sensors than nerve fibers: much processing (e.g., center surround) in retina itself

## Slide 10
© Stephen E. Palmer, 2002
Cones
cone-shaped
less sensitive
operate in high light
color vision
Two types of light-sensitive receptors
Rods
rod-shaped
highly sensitive
operate at night
gray-scale vision
slower to respond
Slide Credit: Efros

## Slide 11: Rod / Cone sensitivity
Slide Credit: Efros
Notes: Sock matching in dark is difficult

## Slide 12
© Stephen E. Palmer, 2002
Distribution of Rods and Cones
Night Sky: why are there more stars off-center?
Slide Credit: Efros

## Slide 13: Electromagnetic Spectrum
http://www.yorku.ca/eye/photopik.htm
Human Luminance Sensitivity Function
Slide Credit: Efros
Notes: At least 3 spectral bands required (e.g. R,G,B)

## Slide 14
Why do we see light of these wavelengths?
© Stephen E. Palmer, 2002
…because that’s where the
Sun radiates EM energy
Visible Light

## Slide 15
The Physics of Light
Any patch of light can be completely described
physically by its spectrum: the number of photons
(per time unit) at each wavelength 400 - 700 nm.
© Stephen E. Palmer, 2002

## Slide 16
The Physics of Light
Some examples of the spectra of light sources
© Stephen E. Palmer, 2002

## Slide 17
The Physics of Light
Some examples of the reflectance spectra of surfaces
Wavelength (nm)
% Photons Reflected
Red
400 700
Yellow
400 700
Blue
400 700
Purple
400 700
© Stephen E. Palmer, 2002

## Slide 18: More Spectra
metamers

## Slide 19
© Stephen E. Palmer, 2002
Three kinds of cones:
Physiology of Color Vision
Why are M and L cones so close?
Why are there 3?
Notes: Dogs have 2, birds and butterflies have 4

## Slide 20: 3 is better than 2…
“M” and “L” on the X-chromosome
  Why men are more likely to be color blind (see what it’s like: http://www.vischeck.com/vischeck/vischeckURL.php)
“L” has high variation, so some women are tetrachromatic
Some animals have 1 (night animals), 2 (e.g., dogs), 4 (fish, birds), 5 (pigeons, some reptiles/amphibians), or even 12 (mantis shrimp)
http://en.wikipedia.org/wiki/Color_vision

## Slide 21: We don’t perceive a spectrum
We perceive
  Hue: mean wavelength, color
  Saturation: variance, vividness
  Intensity: total amount of light
Same perceived color can be recreated with combinations of three primary colors (“trichromacy”)

## Slide 22: Trichromacy and CIE-XYZ
Perceptual equivalents with RGB
Perceptual equivalents with CIE-XYZ

## Slide 23: CIE-XYZ
RGB portion is in triangle

## Slide 24
The Psychophysical Correspondence
There is no simple functional description for the perceived
color of all lights under all viewing conditions, but …...
A helpful constraint:
Consider only physical spectra with normal distributions
area
mean
variance
© Stephen E. Palmer, 2002

## Slide 25
The Psychophysical Correspondence
Mean
Hue
# Photons
Wavelength
© Stephen E. Palmer, 2002

## Slide 26
The Psychophysical Correspondence
Variance
Saturation
Wavelength
# Photons
© Stephen E. Palmer, 2002

## Slide 27
The Psychophysical Correspondence
Area
Brightness
# Photons
Wavelength
© Stephen E. Palmer, 2002

## Slide 28: Color Sensing: Bayer Grid
Estimate RGB at each cell from neighboring values
http://en.wikipedia.org/wiki/Bayer_filter
Slide by Steve Seitz

## Slide 29: Alternative to Bayer: RGB+W
Kodak 2007

## Slide 30: How is light reflected from a surface?
Depends on
Illumination properties: wavelength, orientation, intensity
Surface properties: material, surface orientation, roughness, etc.
λ
light source
?

## Slide 31: Lambertian surface
Some light is absorbed (function of albedo)
Remaining light is reflected in all directions (diffuse reflection)
Examples: soft cloth, concrete, matte paints
λ
light source
λ
light source
absorption
diffuse reflection

## Slide 32: Diffuse reflection
Intensity does depend on illumination angle because less light comes in at oblique angles.
albedo
directional source
surface normal
image intensity
Slide: Forsyth

## Slide 33
1
2

## Slide 34
Diffuse reflection
Perceived intensity does not depend on viewer angle.
  Amount of reflected light proportional to cos(theta)
  Visible solid angle also proportional to cos(theta)
http://en.wikipedia.org/wiki/Lambert%27s_cosine_law

## Slide 35: Specular Reflection
Reflected direction depends on light orientation and surface normal
E.g., mirrors are fully specular
λ
light source
specular reflection
Flickr, by suzysputnik
Flickr, by piratejohnny

## Slide 36: Many surfaces have both specular and diffuse components
Specularity = spot where specular reflection dominates (typically reflects light source)
Photo: northcountryhardwoodfloors.com

## Slide 37: BRDF: Bidirectional Reflectance Distribution Function
surface normal
Slide credit: S. Savarese
Model of local reflection that tells how bright a surface appears when viewed from one direction when light falls on it from another

## Slide 38: More complicated effects
λ
light source
transparency
λ
light source
refraction

## Slide 39
λ1
light source
λ2
fluorescence
t=1
light source
t>1
phosphorescence

## Slide 40
λ
light source
subsurface scattering
λ
light source
interreflection

## Slide 41: Inter-reflection is a major source of light

## Slide 42: Inter-reflection affects the apparent color of objects
From Koenderink slides on image texture and the flow of light

## Slide 43: The color of objects
Colored light arriving at the camera involves two effects
  The color of the light source (illumination + inter-reflections)
  The color of the surface
Slide: Forsyth

## Slide 44: Color constancy
Interpret surface in terms of albedo or “true color”, rather than observed intensity
  Humans are good at it
  Computers are not nearly as good

## Slide 45: Color illusions

## Slide 46: Color illusions

## Slide 47: Color illusions

## Slide 48: Color illusions

## Slide 49: Color illusions

## Slide 50: Color illusions
http://www.echalk.co.uk/amusements/OpticalIllusions/colourPerception/colourPerception.html

## Slide 51: Shadows cast by a point source
A point that can’t see the source is in shadow
For point sources, the geometry is simple
Slide: Forsyth

## Slide 52: Area sources
Examples: diffuser boxes, white walls
The energy received at a point due to an area source is obtained by adding up the contribution of small elements over the whole source
Slide: Forsyth

## Slide 53: Area Source Shadows
Slide: Forsyth

## Slide 54: Shading and shadows are major cues to shape and position
From Koenderink slides on image texture and the flow of light
Slide: Forsyth

## Slide 55: Recap
1
2
3
4
5
6
1. Why is (2) brighter than (1)? Each points to the asphault.
2. Why is (4) darker than (3)? 4 points to the marking.
3. Why is (5) brighter than (3)? Each points to the side of the wooden block.
4. Why isn’t (6) black, given that there is no direct path from it to the sun?

## Slide 56: Things to remember
Light has a spectrum of wavelengths
  Humans (and RGB cameras) have color sensors sensitive to three ranges
Observed light depends on: illumination intensities, surface orientation, material (albedo, specular component, diffuse component), etc.
Every object is an indirect light source for every other
Shading and shadows are informative about shape and position

## Slide 57: Take-home questions
09/10/13
Possible factors: albedo, shadows, texture, specularities, curvature, lighting direction