## Slide 1: Directed Diffusion: A Scalable and Robust Communication Paradigm for Sensor Networks
Chalermek Ramesh Deborah
Intanagonwiwat Govindan Estrin
Mobicom 2000

## Slide 2: Capability of Sensor Nodes
Small cheap nodes.
Wireless communication .
Significant computation.
Caching
Notes: This paper was written in 2000 keeping in mind that sensor nodes will be evolving rapidly in the future and will have significant computation power.

## Slide 3: General Background
Sensor node
Sensor node
How many pedestrians do
u observe in geographical
region x ?
Sensor node
Sensor node
Sensor node
Result
Notes: User sends a query to the network of sensor nodes and get back the result.

## Slide 4: Motivation
Sending data over long distances requires more energy.
Aim :
Scalability
Fault tolerance
Minimize energy usage
Suitable for dynamic network
Notes: This paper was written in 2000 keeping in mind that sensor nodes will be evolving rapidly in the future and will have significant computation power.

## Slide 5: Traditional Approach
Sensor node
Central
Node
Sensor node
Sensor node
Sensor node
Long Range Communication
Looses Battery
Sensor node
Notes: As we can see from the marked red communication line, in this approach we have long distance of communication as the nodes because far away nodes have to send data directly to the central server.

## Slide 6
Sensor node
Sensor node
Sensor node
Sensor node
Sensor node
Proposed Approach
Intermediate node can :-
  Cache data
  Transform Data
  Direct interest towards previously cached data
Notes: Short range hop to hop communication is better than long range comm, Saves battery

## Slide 7: Interest and Event Naming
Query/interest/Task Description:
  Type=four-legged animal
  Interval=20ms //send back events every 20ms
  Duration=10 seconds //for the rest 10s
  Rect=[-100, 100, 200, 400] // location
Reply:
  Type=four-legged animal
  Instance = elephant
  Location = [125, 220]
  Intensity = 0.6
  Confidence = 0.85
  Timestamp = 01:20:40
Notes: Task known at the time of deployment.
Sensors collects events and check with the locally stores library. If the signals a 4 legged animal it generates events description once is every 20ms. .
When a node in region X receives the interest it activates the sensors
Attribute value based interest and data naming scheme.

## Slide 8: Interest Propagation
Source
Sink
Initial Interest
  Type=four-legged animal
  Interval= 1s
  Rect=[-100, 100, 200, 400]
  Timestamp =01:20:40
  ExpiresAt =01:30:40
Tries to determine which sensor data has the source
Interest
Data
Gradient
Notes: One who initiates the query –Sink
The source / origin of data
Flood the query across the network.
Get the data.
Aim : 1) the location of the source of interest
2) Part 2 : Select the best path from the sink to source
Interest are monotically refershed.

## Slide 9
Summary of the protocol
A
B
C
Carried out by each node
Reinforcement
Notes: Data matching the interest is drawn towards the node/
It reinforces a small number of paths

## Slide 10
Source
Sink
Interest
Data
Reinforcement

## Slide 11: Reinforcement
Source
Sink
Initial Interest
  Type=four-legged animal
  Interval= 10ms
  Rect=[-100, 100, 200, 400]
  Timestamp =01:20:40
  ExpiresAt =01:30:40
Increase gradient
Notes: Show with marker that there is a path where the data reaches fastest. The we will increase the gradient of that path.

## Slide 12: Gradient Types
Binary Value
Probabilistic forwarding –load balancing

## Slide 13: Interest Cache/Data Propagation
Type | Rect | Timestamp | Gradient
Four-legged animal Instance-elephant | [-100, 100, 200, 400] | 01:20:40 Last received matching interest | Neighbor 1- Data rate, duration Neighbor 2- Data rate, duration
Local
Interaction
Notes: Sensors match signature waveforms from codebook against observations
Sensors match data against interest cache, compute highest event rate request from all gradients, and (re) sample events at this rate
Receiving node:
  Find matching entry in interest cache
    If no match, silently drop
  Check and update data cache (loop prevention, aggregation)
  Resend message along all the active gradients, adjusting the frequency if necessary

## Slide 14
Negative Reinforcement Option 1
B
C
A
Wait for it to time out.
Gradient = 1s
Gradient = 1s
Gradient = 10ms
Notes: Emperically select the low delay path

## Slide 15
Negative Reinforcement Option 2
B
C
A
Decrease the gradient.
Gradient = 10ms
Gradient = 2s
Notes: Used in this paper

## Slide 16: Average Dissipated Energy
0
0.002
0.004
0.006
0.008
0.01
0.012
0.014
0.016
0.018
0
50
100
150
200
250
300
Average Dissipated Energy
(Joules/Node/Received Event)
Network Size
Diffusion
Omniscient Multicast
Flooding
Notes: 5 sources and 5 sinks. Uniformly spread.
AVg-dissipated energy : total energy dissipated per node/ total distinct events seen by sinks.
Omniscient Multicast : each source transmits it sevts along the shortest path multucast tree. To all sinks.
No tree formation
in network aggregtion
They claim diffusion can outperform omniscient multicast due to in-network processing & suppression. For example, multiple sources can detect a four-legged animal in one area.

## Slide 17: Impact of In-network Processing
0
0.005
0.01
0.015
0.02
0.025
0
50
100
150
200
250
300
Average Dissipated Energy
(Joules/Node/Received Event)
Network Size
Diffusion With Suppression
Diffusion Without Suppression
Notes: Aggregation strategy : Node suppresses identical interest recv from various sources.

## Slide 18: Impact of Negative Reinforcement
0
0.002
0.004
0.006
0.008
0.01
0.012
0
50
100
150
200
250
300
Average Dissipated Energy
(Joules/Node/Received Event)
Network Size
Diffusion With Negative Reinforcement
Diffusion Without Negative Reinforcement

## Slide 19: Pros :
Reinforcement maintains adequate number of high quality paths.
It favors the best path.
Energy efficiency improves.
Resilient to Failures.
Not a centralized approach.
Caching helps improve response times.

## Slide 20: Pros :Interest Cache/Data Propagation
Type | Rect | Timestamp | Gradient
 |  | Last received matching interest | Neighbor 1- Data rate, duration Neighbor 2- Data rate, duration
Local
Interaction
All interactions are localized. Thus it is more robust and scalable.
Notes: Sensors match signature waveforms from codebook against observations
Sensors match data against interest cache, compute highest event rate request from all gradients, and (re) sample events at this rate
Receiving node:
  Find matching entry in interest cache
    If no match, silently drop
  Check and update data cache (loop prevention, aggregation)
  Resend message along all the active gradients, adjusting the frequency if necessary

## Slide 21: Cons 1- Interest and Event Naming
Query/interest/Task Description:
  Type=four-legged animal
  Interval=20ms //send back events every 20ms
  Duration=10 seconds //for the rest 10s
  Rect=[-100, 100, 200, 400] // location
Reply:
  Type=four-legged animal
  Instance = elephant
  Location = [125, 220]
  Intensity = 0.6
  Confidence = 0.85
  Timestamp = 01:20:40
Cons :
The sensor nodes should be application aware before deployment.
The algorithm is limited by the size of the dataset Type
Notes: Sensor networks are task specific – tasks are known prior to deployment of the sensor nodes.
Extent choice or granularity of the naming scheme can affect performance.
Tasks like “ Count the

## Slide 22
Query like “count the number of animals” cannot take leverage of the event data rate.
Reinforcement rule can lead to waste of resources
ex: if a node send data better then more load on that node.
Capacity of other nodes are wasted
Cons 2

## Slide 23
B
Y
Source 1
Cons 3 - Multiple Sources
C
A
D
Source 2
B’s events
A’s events
Notes: Source Y will reinforce both YD and YC. Loss of energy

## Slide 24
B
Y
Cons 4 - Multiple Sinks
C
A
X
Sink
B’s events
A’s events
Source
Sink
Notes: Source Y will reinforce both YD and YC. Loss of energy

## Slide 25: Discussions –Piazza 1:30pm
In case of emergencies, there might be a lot of broadcasting that will take place. Congestion ? Effect on energy-efficiency ?
2) What happens if there is a malicious node in the network?
3) Tests were performed in simulation.
4) Unreliable transmission ? Use of acknowledgements.
Notes: 3) Tests were performed in simulation., so hard to say how wireless performance would really be in real world
4) Use of acknowledgements. can be a huge plus here.

## Slide 26: Discussions
5) What is the location is not rectangular ?
6) Global Optima ?
Notes: 3) Tests were performed in simulation., so hard to say how wireless performance would really be in real world
4) Use of acknowledgements. can be a huge plus here.