## Slide 1: Pelican: A Building Block for Exascale Cold Data Storage
Shobana Balakrishnan, Richard Black, Austin Donnelly, Paul England, Adam Glass,
Dave Harper, and Sergey Legtchenko, Aaron Ogus, Eric Peterson and Antony Rowstron
Microsoft Research

## Slide 2: Data in the cloud

## Slide 3: The Problem
A significant portion of the data in the cloud is rarely accessed and known as cold data.
Pelican tries to address the need for cost-effective storage of cold data and serves as a basic building block for exabyte scale storage for cold data.

## Slide 4: Price versus Latency

## Slide 5: Price versus Latency

## Slide 6: Right Provisioning
Provision resources just for the cold data workload:
Disks:
  Archival and SMR instead of commodity drives
Power
Cooling
Bandwidth
Servers
  Enough for data management instead of 1 server/ 40 disks
Enough for the required workload
Not to keep all disks spinning

## Slide 7: Advantages
Benefits of removing unnecessary resources:
High density of storage
Low hardware cost
Low operating cost (capped performance)

## Slide 8: Pelican

## Slide 9: The Pelican Rack
Mechanical, hardware and storage software stack co-designed.
Right-provisioned for cold data workload:
52U rack with 1152 archival class 3.5” SATA disks.
Average size of 4.55 TB to provide a total of 5 PB of storage
It uses 2 servers and no top of the rack switch
Only 8% of the disks are spinning concurrently.
Designed to store blobs which are infrequently accessed.
Notes: Advantages
• Total cost of ownership comparable to tape
• Lower latency than tape
The challenges of resource limitations managed in software

## Slide 10: Resource Domain
Each domain is only provisioned to supply its resource to a subset of disks
Each disk uses resources from a set of resource domains
Domain-conflicting - Disks that are in the same resource domain.
Domain-disjoint - Disks that share no common resource domains.
Pelican domains
  Cooling, Power, Vibration Bandwidth
Notes: domain disjoint disks can move between disk states independently
whereas domain conflicting ones cannot do so as it could lead to over commitment
Resource Domains to be: the categories of things that are being managed

## Slide 11: Handling Right-Provisioning
Constraints over sets of active disks:
  Hard: power, cooling, failure domains
  Soft: bandwidth, vibration
  Constraints in Pelican
  2 active out of 16 per power domain
  1 active out of 12 per cooling domain
  1 active out of 2 per vibration domain

## Slide 12: Schematic representation
12
6
16
Notes: 6 8U chassis
each has 12 trays
each tray has 16 disks

## Slide 13: Data Layout
Objective - maximize number of requests that can be concurrently serviced while operating within constraints.
Each blob is stored over a set of disks.
It is split into a sequence of 128kB fragments. For each “k” fragments, additional “r” fragments are generated.
The k+r fragments form a stripe
In Pelican they statically partition disks into groups and disks within a group can be concurrently active. Thus they concentrate all conflicts over a few sets of disks.
Notes: additional fragments contain redundancy information using Cauchy Reed Solomon erasure code
systematic code to allow the input to be regenerated by simple concatenating these fragments

## Slide 14: Data Placement

## Slide 15
Group Property:
  Either fully conflicting
  Or fully independent
In Pelican - 48 groups of 24 disks
  4 classes of 12 fully-conflicting groups
Blob is stored in one group - Blob is stored over 18 disks (15+3)
Off-Rack metadata called “catalog” holds information about the blob placement

## Slide 16: Advantages
Groups encapsulate the constraints and also reduce time to recover from a failed disk.
Since blob is within a group, rebuild operation use disks spinning concurrently.
Simplifies the IO schedulers task.
Probability of conflict is O(n) which is an improvement from random placement O(n2)

## Slide 17: IO Scheduler
Traditional disks are optimized to reorder IOs to minimize seek latency.
Pelican - reorder requests in order to minimize the impact of spin up latency.
Four independent schedulers. Each scheduler services requests for its class and reordering happens at a class level.
Each Scheduler uses two queues – one for rebuild operations and one for other operations.
Reordering is done to amortize the group spin up latency over the set of operations.
Rate limiting is done to manage the interference between rebuild and other operations.

## Slide 18: Implementation Considerations

## Slide 19
Power Up in Standby is used to ensure disks do not spin without the Pelican storage stack managing the constraints.
Group abstraction is exploited to parallelize the boot process.
  Initialization is done on the group level.
  If there are no user requests then all 4 groups are concurrently initialized
  Takes around 3 minutes to initialize the entire rack.
Unexpected spin up disks is prevented by adding a special No Access flag to the Windows Server driver stack.
The BIOS on the server is modified to ensure it can handle all 72 HBA’s.

## Slide 20: Evaluation
Comparison against a system organized like Pelican but with full provisioning for power and cooling.
The FP uses the same physical internal topology but disks are never spun down.

## Slide 21: Simulator Cross-Validation
• Burst workload, varying burst intensity
Simulator accurately predicts real system behavior for all metrics.

## Slide 22: Performance – Rack Throughput

## Slide 23: Service Time

## Slide 24: Time to first byte

## Slide 25: Power Consumption

## Slide 26: Scheduler Performance
Rebuild Time
Impact on Client Request

## Slide 27: Cost of Fariness
Impact on reject rate
Impact on throughput and latency

## Slide 28: Disk Lifetime
Disk statistics as a function of the workload

## Slide 29: Pros Cons
Reduced
  Cost
  Power Consumption
Erasure codes for fault tolerance
Hardware abstraction simplifies IO schedulers work.
Tight constraints – less flexible to changes
Sensitive to hardware changes
No Justification to some of the configuration decisions made.
Not sure if it is an optimal design

## Slide 30: Discussion
They claim the values they chose to being a sweet spot in the hardware. How is the performance affected by any changes to this??
More importantly how do we handle for systems of different configurations and hardware.
Automate synthesizing of the Data layout – thoughts?