## Slide 1: Synopsis diffusion
For Robust Aggregation in Sensor Networks
Suman Nath, Phillip B. Gibbons,
Srinivasan Seshan, Zachary R. Anderson
Presented by Xander Masotto

## Slide 2: Motivation
  Our goal is to aggregate data collected from sensor nodes
    i.e. Count, Sum, Average, Rank
  We prefer solutions with:
    Low memory usage
    Low power consumption
    Tolerance of node and communication failures
  Aggregating data points in-the-network significantly reduces size of messages, thus saves power

## Slide 3: Tree-based Aggregation
Constructs a spanning tree
Provides low power consumption
Avoids double counting

## Slide 4: Tree-based Aggregation
Constructs a spanning tree
Provides low power consumption
Avoids double counting
Not fault tolerant; if a node fails, we lose its entire subtree

## Slide 5: DAG-based Aggregation
Instead of a tree, let each node have k parents, and send each parent (1/K)th of the sensor information
Reduces the expected error by a factor of K

## Slide 6: DAG-based Aggregation
Instead of a tree, let each node have k parents, and send each parent (1/K)th of the sensor information
Reduces the expected error by a factor of K
Can we do better than this?
Every message contributes to the final answer, which means every node/communication failure increases error in the final answer

## Slide 7: Synopsis Diffusion
Allows sensor readings to have multiple paths to the querying node
This is achieved by using duplicate-tolerant aggregation algorithms

## Slide 8: Outline
Definition and analysis of ODI Synopses
Examples of ODI-correct Algorithms
Multi-path Aggregation Topologies
Evaluation

## Slide 9: Synopses
Synopses are partially aggregated results that give a summary of the data
Synopses are generated by sensors, then passed between nodes and merged together. At the querying node, a synopsis is translated into a final answer.
SG(sensor) = Synopsis generation
SF(s1, s2) = Synopsis fusion
SE(s) = Synopsis Generation

## Slide 10: Synopses
SG(sensor) = {(sensor.id, sensor.value)}
SG(s1, s2) = union(s1, s2)
SG(s) = sum over all values in s
A
B
C
{(A, 1)}
{(B, 2)}
{(C, 3)}
{(A,1), (B,2)}
{(B,2), (C,3)}
{(A,1), (B,2), (C,3)}
Answer: 6

## Slide 11: Synopses
SG(sensor) = {(sensor.id, sensor.value)}
SF(s1, s2) = union(s1, s2)
SE(s) = sum over all values in s
A
B
C
{(A, 1)}
{(B, 2)}
{(C, 3)}
{(A,1), (B,2)}
{(C,3)}
{(A,1), (B,2), (C,3)}
Answer: 6

## Slide 12: ODI-Correctness
Order and Duplicate Insensitivity
SF(SG*(X), SG*(Y)) = SF(SG*(X), SG*(Y \ X))
  Where X and Y are sets of sensors
  SG*(X) = SF(SG(x1), SF(SG(x2), …))
An aggregation algorithm is ODI-correct if and only if:
  SG() preserves duplicates (same sensor, same synopsis)
  SF() is Commutative: SF(s1, s2) = SF(s2, s1)
  SF() is Associative: SF(s1, SF(s2, s3)) = SF(SF(s1, s2), s3)
  SF() is Idempotent: SF(s, s) = s

## Slide 13: ODI-Correct Count
We want to count the number of distinct elements in a multiset M
With each element x, let h(x, j) be the jth bit of its hash
Let SG(sensor) = S({sensor.id})
Let SF(s1, s2) = s1 | s2
ODI-Correct

## Slide 14: ODI-Correct Count
What does S(M) tell us about M?
  For a given h(x), Pr[min{h(x, j)=1} = i] = (½)^(i+1)
  It’s less probable for S(M)[i] to be set when i is large
  The more distinct elements, the more hashed values contribute to S(M), and so the more likely that *some* element has a prefix with a lot of zeros

## Slide 15: ODI-Correct Count
Fast, since number of iterations follows geometric series with p=1/2, so the expected value is 2
When implemented on a sensor node, additional computation cycles compared to ordinary count are negligible

## Slide 16: ODI-Correct Sum
We can easily extend our Count algorithm into summation over integers
Let Expand(id, value) = {(id, 1), (id, 2) … (id, value)}
Let SG(sensor) = S(Expand(sensor.id, sensor.value))
Let SF(s1, s2) = s1 | s2
In practice this is optimized, but basic idea is the same
Can approximate real numbers by using a fixed-point numerical representation

## Slide 17: Other Examples
Mean (combine Sum and Count)
Variance (E[X^2] – E[X]^2)
Sampling K elements uniformly
  Associate a random number with every distinct value, collect the K largest numbers
Ranking by Frequency
  Each synopsis keeps track of top K estimated counts
  Counts are estimated using ODI count synopses

## Slide 18: Rings Topology
Sensor nodes are divided into Rings
The querying node is exclusively in Ring 0
A node is in Ring i+1 if it first hears about the query from a nodes in Ring i

## Slide 19: Rings Topology
Sensor nodes are loosely time synchronized
Divided into epochs, answer produced after each one
Each Ring i is given an allotted time, outer rings first
For a leaf node:
  Let s = SG(self)
  Broadcast s
For an internal node at Ring i:
  Let s = SG(self)
  Listen for messages:
    If received synopsis s’ from Ring (i+1)
      Set s = SF(s, s’)
  Broadcast s

## Slide 20: Implicit Acks
ODI-correctness provides a mechanism for acknowledgements without actually sending ack messages
X
Y
Z
sx

## Slide 21: Implicit Acks
ODI-correctness provides a mechanism for acknowledgements without actually sending ack messages
X
Y
Z
sy
sy
Check whether SF(sx, sy) = sy
If true, then Y effectively received sx

## Slide 22: Adaptive Rings Topology
Use implicit acks in order to adjust the topology in order to improve message reliability
Count the number of messages heard from nodes in rings i, i+1, and i+2 over the last W epochs
Count the number of implicit acknowledgements heard from nodes in rings i-1 and i-2 over the last W epochs
If n(i-1) < n(i+1) and n(i-1) < n(i) < n(i+2) then assign itself to ring i+1 with probability p
If n(i+1) < n(i-1) and n(i+1) < n(i) < n(i-2) then assign itself to ring i-1 with probability p

## Slide 23: Evaluation
Tested the Sum aggregate on a deployment of 600 sensors randomly placed in a 20ft x 20ft grid
Simulated over 500 epochs:
  TAG
  TAG2 (value splitting between 2 parents)
  RINGS
  ADAPTIVE RINGS
  FLOOD
    Every node broadcasts to all neighbors, run for D+1 steps where D is the max-distance from the query node
Calculate the RMS error:

## Slide 29: Thoughts
Would be interesting to find ODI-Correct algorithms that work well for floating point data
Replaced communication error with approximation error
  Replacing equipment, buying better transmitters, or strategically placing sensors won’t help fundamental limit of accuracy
Was it fair to place nodes randomly?
Is 0.13 an acceptable percent error?
  For calculating average, error in numerator and denominator can combine: 1.13 / 0.87 = 1.30
Distribution of error instead of just RMS?
Are there algorithms that can be calculated in single-path topologies that can’t be approximated in multi-path?