## Slide 1: Alibi Routing
Dave Levin, Youndo Lee, Luke Valenta, Zhihao Li, Victoria Lai, Cristian Lumezanu, Brendan Rowen, Neil Spring, Bobby Bhattacharjee
Presented by Kirill Varshavskiy

## Slide 2: Sniff sniff
State agencies censor and log citizens’ internet traffic
Abundant in certain regions
  China
  Syria
  North Korea
  Saudi Arabia
  Bahrain
  Iran
  Vietnam
Notes: This is a very short list, it’s not actually that short. There is a report by Reporters Without Borders about enemies of the internet as well as nations that are known to engage in traffic surveillance. Most nations are on that list in different ways

## Slide 3: Censor-avoidance
Censorship and Surveillance
  Dropping packets
  Injecting data into packets
  Logging packets
Routing protocols often don’t consider intermediate nodes
  Traffic can route through geographic region which might inject data into packet
Data integrity
  Nations may log routing info + drop packets

## Slide 4: Past Approaches
BGP Poisoning (avoidance)
  Failure prone regions blacklisted in BGP
Tor (other overlay systems)
  Anonymized internet usage
  May pass through censored region when going between hops
Geographical routing
  Greedy routing, no avoidance
Some systems provide means to monitor regions visited, but no insurance/proof that certain places were not visited
Notes: Alibi and Tor are complimentary

## Slide 5: What Alibi routing is and what it isn’t
Provides
  Overlay P2P network for data routing
  Proof that sent packet did not enter forbidden region after packet has completed its RTT
  Proof per packet as routing can traverse various paths due to packet switching/routing decisions
Does not Provide
  Guarantee that data is not delivered to forbidden region
    Malicious nodes not in forbidden region might copy and send it elsewhere
  Assurance of reliable communication, just a proof that it didn’t enter the region AFTER transmission

## Slide 6: Terminology and definitions
Forbidden Region
  Geographical location that should not be entered
  Represented by a list of <lat, long> coordinates depicting a geo-polygon
Alibi
  Relay that can be safely used to divert traffic around forbidden region
  Picked such that passing through Alibi AND forbidden region will cause noticeable delay increase
Target regions
  Regions in which Alibis might reside
  Aid in locating Alibi
δ (delta)
  Coefficient to ensure safety under latency fluctuations
  Used to determine target regions

## Slide 7: Proof of avoidance
Proving something did not happen is difficult
Proving something related cannot possibly happen is less difficult
How do you prove packet did not go through forbidden region?
  Consider event x depicting a situation in which a packet traverses through a forbidden region
  Consider event A depicting a situation where a packet does not traverse through a forbidden region
A and x are mutually exclusive
Showing x is impossible, authors show A is true

## Slide 8: Assumptions
All non-forbidden nodes are trustworthy
Nodes cannot lie about smaller RTTs
Based on various signing schemes, returned packet will show all (trustworthy) nodes it traversed

## Slide 9: Relay Guarantees
s
T
f
f
r
d
F
Given path s -> r -> d with an RTT rtt_time
  Calculate RTT through s, r, and d AND the closest possible f to be rtt_forbidden
  If rtt_time is a factor of delta smaller than rtt_forbidden, initial path could not have possibly traversed f
Notes: Before I show you hot to find the relay, let me convince you that once I find it, I will be able to avoid the forbidden region

## Slide 10: Targeting the target region
s
T
f
f
g
d
F
Alibi Routing consists of an overlay network of P2P nodes, each with coarse GPS coords
Target region contains Alibi node
Authors partition world into grid of points
  For each point, consider it as g, calculate δ threshold
All calculations based on greater-circle distance

## Slide 11: Target region based on δ

## Slide 12: Alibi, where art thou?
s
T
f
f
d
F
Each node keeps an active peer list and a neighbor list
  Occasionally sends out random nonces to get neighbors’ GPS coords
  Ping responses come with correct RTT as nonce is random and thus response cannot be pre-constructed
Each hop from source tries to minimize distance to target region

## Slide 13: Security Concerns
Time/distance calculations prevent underselling of RTT from malicious nodes
Eclipse attack: surround node with all malicious nodes
  Requires attack nodes to be physically close to trustworthy nodes
  Algorithm should route hops away from forbidden regions
Sending data copies to attackers
  End to end encryption can solve this, otherwise, nothing would effectively prevent this
Laundering traffic: using relays to attack hosts
  Similar approach as to other systems, whitelisting, solutions exist

## Slide 14: Evaluation
Authors simulated deployment of 20,000 nodes and PlanetLab simulation of 245 hosts
“Enemies of the Internet” labeled as forbidden regions + countries with most Internet users (USA, India, Japan)
Most source-destination pairs successful

## Slide 15: Evaluation
Protocol success using simulation and PlanetLab deployment showed almost 100% success in most δ value cases
Due to limited PlanetLab deployment, at most 2 hops were needed to find relay. Around 40 in simulation.

## Slide 16: Conclusion and Comments
Alibi routing can be used as an intelligent P2P network that bypasses unwanted territories in an efficient manner
Current implementation has to be manually configured. Would be interesting to see how system works in a practical deployment with backoff techniques
Does not tackle various downsides of the algorithm, for example being surrounded by forbidden region or having several forbidden regions, or failure cases where alibis incur too much of a latency to be effective
Authors mention Alibi routing can be used in tandem with Tor, which should be very beneficial to both technologies
P2P design requires lots of nodes to be online/active

## Slide 17: References
https://en.wikipedia.org/wiki/Internet_censorship
http://conferences.sigcomm.org/sigcomm/2015/pdf/papers/p611.pdf
http://alibi.cs.umd.edu/
https://firemon-firemon.netdna-ssl.com/wp-content/uploads/2014/11/firewall.lgo_.jpg
http://archive.cone.informatik.uni-freiburg.de/people/ruehrup/georouting.png

## Slide 18: Discussion
Would you use Alibi routing for your Internet use? (show of hands)
What other cases has Alibi routing not considered?
How does this system handle Internet hubs? If hub for lots of the world’s internet traffic is relayed through a forbidden region, how will the system adapt?
Should this P2P network consider congestion of relay nodes as potential bottleneck?

## Slide 19: Questions?