## Slide 1: Photo Stitching Panoramas from Multiple Images
Computer Vision
CS 543 / ECE 549
University of Illinois
Derek Hoiem
03/3/15
Notes: How does image stitching in a camera work?

## Slide 2: What about focus, aperture, DOF, FOV, etc?

## Slide 3: Adding a lens
A lens focuses light onto the film
  There is a specific distance at which objects are “in focus”
    other points project to a “circle of confusion” in the image
  Changing the shape of the lens changes this distance
“circle of
confusion”

## Slide 4: Focal length, aperture, depth of field
A lens focuses parallel rays onto a single focal point
  focal point at a distance f beyond the plane of the lens
  Aperture of diameter D restricts the range of rays
focal point
F
optical center
(Center Of Projection)
Slide source: Seitz

## Slide 5: The eye
The human eye is a camera
  Iris - colored annulus with radial muscles
  Pupil (aperture) - the hole whose size is controlled by the iris
  Retina (film): photoreceptor cells (rods and cones)
Slide source: Seitz
Notes: Note that the retina is curved

## Slide 6: Depth of field
Changing the aperture size or focal length affects depth of field
f / 5.6
f / 32
Flower images from Wikipedia http://en.wikipedia.org/wiki/Depth_of_field
Slide source: Seitz

## Slide 7: Varying the aperture
Large aperture = small DOF
Small aperture = large DOF
Slide from Efros

## Slide 8: Shrinking the aperture
Why not make the aperture as small as possible?
  Less light gets through
  Diffraction effects
Slide by Steve Seitz

## Slide 9: Shrinking the aperture
Slide by Steve Seitz

## Slide 10: Relation between field of view and focal length
Field of view (angle width)
Film/Sensor Width
Focal length

## Slide 11: Today: Image Stitching
Combine two or more overlapping images to make one larger image
Add example
Slide credit: Vaibhav Vaish

## Slide 12: Concepts introduced/reviewed in today’s lecture
Camera model
Homographies
Solving homogeneous systems of linear equations
Keypoint-based alignment
RANSAC
Blending
How the iphone stitcher works

## Slide 13: Photo stitching
Camera Center
P
Q

## Slide 14: Illustration
Camera Center

## Slide 15: Problem set-up
x = K [R t] X
x' = K' [R' t'] X
t=t'=0
x'=Hx where H = K' R' R-1 K-1
Typically only R and f will change (4 parameters), but, in general, H has 8 parameters
f
f'
.
x
x'
X

## Slide 16: Homography
Definition
  General mathematics:
  homography = projective linear transformation
  Vision (most common usage):
  homography = linear transformation between two image planes
Examples
  Project 3D surface into frontal view
  Relate two views that differ only by rotation

## Slide 17: Homography example: Image rectification
To unwarp (rectify) an image solve for homography H given p and p’: wp’=Hp
p
p’
Notes: 15 min

## Slide 18: Image Stitching Algorithm Overview
Detect keypoints (e.g., SIFT)
Match keypoints (e.g., 1st/2nd NN < thresh)
Estimate homography with four matched keypoints (using RANSAC)
Combine images

## Slide 19: Computing homography
Assume we have four matched points: How do we compute homography H?
Direct Linear Transformation (DLT)

## Slide 20: Computing homography
Direct Linear Transform
Apply SVD: UDVT = A
h = Vsmallest (column of V corr. to smallest singular value)
Matlab
[U, S, V] = svd(A);
h = V(:, end);
Explanations of SVD and solving homogeneous linear systems
Notes: SVD gives the homogeneous least squares solution constrained to have a norm of 1

## Slide 21: Computing homography
Assume we have four matched points: How do we compute homography H?
Normalized DLT
Normalize coordinates for each image
  Translate for zero mean
  Scale so that average distance to origin is ~sqrt(2)
  This makes problem better behaved numerically (see HZ p. 107-108)
Compute using DLT in normalized coordinates
Unnormalize:

## Slide 22: Computing homography
Assume we have matched points with outliers: How do we compute homography H?
Automatic Homography Estimation with RANSAC
Choose number of samples N
HZ Tutorial ‘99

## Slide 23: Computing homography
Assume we have matched points with outliers: How do we compute homography H?
Automatic Homography Estimation with RANSAC
Choose number of samples N
Choose 4 random potential matches
Compute H using normalized DLT
Project points from x to x’ for each potentially matching pair:
Count points with projected distance < t
  E.g., t = 3 pixels
Repeat steps 2-5 N times
  Choose H with most inliers
HZ Tutorial ‘99

## Slide 24: Automatic Image Stitching
Compute interest points on each image
Find candidate matches
Estimate homography H using matched points and RANSAC with normalized DLT
Project each image onto the same surface and blend
  Matlab: maketform, imtransform

## Slide 25: RANSAC for Homography
Initial Matched Points

## Slide 26: RANSAC for Homography
Final Matched Points

## Slide 27: Verification

## Slide 28: RANSAC for Homography

## Slide 29: Choosing a Projection Surface
Many to choose: planar, cylindrical, spherical, cubic, etc.

## Slide 30: Planar Mapping
f
f
x
x
For red image: pixels are already on the planar surface
For green image: map to first image plane

## Slide 31: Planar Projection
Planar
Photos by Russ Hewett

## Slide 32: Planar Projection
Planar

## Slide 33: Cylindrical Mapping
f
f
x
x
For red image: compute h, theta on cylindrical surface from (u, v)
For green image: map to first image plane, than map to cylindrical surface

## Slide 34: Cylindrical Projection
Cylindrical

## Slide 35: Cylindrical Projection
Cylindrical

## Slide 36
Planar
Cylindrical

## Slide 37: Recognizing Panoramas
Brown and Lowe 2003, 2007
Some of following material from Brown and Lowe 2003 talk

## Slide 38: Recognizing Panoramas
Input: N images
Extract SIFT points, descriptors from all images
Find K-nearest neighbors for each point (K=4)
For each image
  Select M candidate matching images by counting matched keypoints (m=6)
  Solve homography Hij for each matched image

## Slide 39: Recognizing Panoramas
Input: N images
Extract SIFT points, descriptors from all images
Find K-nearest neighbors for each point (K=4)
For each image
  Select M candidate matching images by counting matched keypoints (m=6)
  Solve homography Hij for each matched image
  Decide if match is valid (ni > 8 + 0.3 nf )
# inliers
# keypoints in overlapping area

## Slide 40: Recognizing Panoramas (cont.)
(now we have matched pairs of images)
Find connected components

## Slide 41: Finding the panoramas

## Slide 42: Finding the panoramas

## Slide 43: Finding the panoramas

## Slide 44: Recognizing Panoramas (cont.)
(now we have matched pairs of images)
Find connected components
For each connected component
  Perform bundle adjustment to solve for rotation (θ1, θ2, θ3) and focal length f of all cameras
  Project to a surface (plane, cylinder, or sphere)
  Render with multiband blending

## Slide 45: Bundle adjustment for stitching
Non-linear minimization of re-projection error
where H = K’ R’ R-1 K-1
Solve non-linear least squares (Levenberg-Marquardt algorithm)
  See paper for details

## Slide 46: Bundle Adjustment
New images initialised with rotation, focal length of best matching image

## Slide 47: Bundle Adjustment
New images initialised with rotation, focal length of best matching image

## Slide 48: Straightening
Rectify images so that “up” is vertical

## Slide 49: Details to make it look good
Choosing seams
Blending

## Slide 50: Choosing seams
Image 1
Image 2
x
x
im1
im2
Easy method
  Assign each pixel to image with nearest center

## Slide 51: Choosing seams
Easy method
  Assign each pixel to image with nearest center
  Create a mask:
    mask(y, x) = 1 iff pixel should come from im1
  Smooth boundaries (called “feathering”):
    mask_sm = imfilter(mask, gausfil);
  Composite
    imblend = im1_c.*mask + im2_c.*(1-mask);
Image 1
Image 2
x
x
im1
im2

## Slide 52: Choosing seams
Better method: dynamic program to find seam along well-matched regions
Illustration: http://en.wikipedia.org/wiki/File:Rochester_NY.jpg

## Slide 53: Gain compensation
Simple gain adjustment
  Compute average RGB intensity of each image in overlapping region
  Normalize intensities by ratio of averages

## Slide 54: Multi-band Blending
Burt & Adelson 1983
  Blend frequency bands over range  l

## Slide 55: Multiband Blending with Laplacian Pyramid
0
1
0
1
0
1
Left pyramid
Right pyramid
blend
At low frequencies, blend slowly
At high frequencies, blend quickly

## Slide 56: Multiband blending
Compute Laplacian pyramid of images and mask
Create blended image at each level of pyramid
Reconstruct complete image
Laplacian pyramids

## Slide 57: Blending comparison (IJCV 2007)

## Slide 58: Blending Comparison

## Slide 59: Further reading
DLT algorithm: HZ p. 91 (alg 4.2), p. 585
Normalization: HZ p. 107-109 (alg 4.2)
RANSAC: HZ Sec 4.7, p. 123, alg 4.6
Rick Szeliski’s alignment/stitching tutorial
Recognising Panoramas: Brown and Lowe, IJCV 2007 (also bundle adjustment)

## Slide 60: How does iphone panoramic stitching work?
Capture images at 30 fps
Stitch the central 1/8 of a selection of images
  Select which images to stitch using the accelerometer and frame-to-frame matching
  Faster and avoids radial distortion that often occurs towards corners of images
Alignment
  Initially, perform cross-correlation of small patches aided by accelerometer to find good regions for matching
  Register by matching points (KLT tracking or RANSAC with FAST (similar to SIFT) points) or correlational matching
Blending
  Linear (or similar) blending, using a face detector to avoid blurring face regions and choose good face shots (not blinking, etc)
http://www.patentlyapple.com/patently-apple/2012/11/apples-cool-iphone-5-panorama-app-revealed-in-5-patents.html

## Slide 61: Things to remember
Homography relates rotating cameras
Recover homography using RANSAC and normalized DLT
Bundle adjustment minimizes reprojection error for set of related images
Details to make it look nice (e.g., blending)

## Slide 62: Next class
Stereo and epipolar geometry