## Slide 1: Light and Shading
Computer Vision
Derek Hoiem, University of Illinois
01/19/17
“Empire of Light”, Magritte

## Slide 2: FAQ
Final project: see guidelines here https://courses.engr.illinois.edu/cs543/Project_Guidelines.pdf
Waitlist
  80 students on the list so far
  Sign up by Friday (link on course page)
Note other highly related courses
  ECE 418: Image & Video Processing
  ECE 547: Topics in Image Processing

## Slide 3: Today’s class
What determines a pixel’s brightness?
  How is light reflected?
  How is light measured?
What can be inferred about the world from those brightness values?

## Slide 4: How light is recorded

## Slide 5: Digital camera
A digital camera replaces film with a sensor array
Each cell in the array is light-sensitive diode that converts photons to electrons
Two common types: Charge Coupled Device (CCD) and CMOS
http://electronics.howstuffworks.com/digital-camera.htm
Slide by Steve Seitz

## Slide 6: Sensor Array
CMOS sensor
Each sensor cell records amount of light coming in at a small range of orientations

## Slide 7: The raster image (pixel matrix)

## Slide 8: The raster image (pixel matrix)
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93

## Slide 9: Today’s class: Light and Shading
What determines a pixel’s intensity?
What can we infer about the scene from pixel intensities?

## Slide 10: How does a pixel get its value?
Light emitted
Sensor
Lens
Fraction of light reflects into camera

## Slide 11: How does a pixel get its value?
Major factors
  Illumination strength and direction
  Surface geometry
  Surface material
  Nearby surfaces
  Camera gain/exposure
Light emitted
Sensor
Light reflected to camera

## Slide 12: Basic models of reflection
Specular: light bounces off at the incident angle
  E.g., mirror
Diffuse: light scatters in all directions
  E.g., brick, cloth, rough wood
incoming light
specular reflection
incoming light
diffuse reflection

## Slide 13: Lambertian reflectance model
Some light is absorbed (function of albedo)
Remaining light is scattered (diffuse reflection)
Examples: soft cloth, concrete, matte paints
light source
light source
absorption
diffuse reflection
Notes: albedo is the fraction of light reflected

## Slide 14
Diffuse reflection: Lambert’s cosine law
Intensity does not depend on viewer angle.
  Amount of reflected light proportional to
  Visible solid angle also proportional to
http://en.wikipedia.org/wiki/Lambert%27s_cosine_law

## Slide 15: Specular Reflection
Reflected direction depends on light orientation and surface normal
  E.g., mirrors are fully specular
  Most surfaces can be modeled with a mixture of diffuse and specular components
light source
specular reflection
Flickr, by suzysputnik
Flickr, by piratejohnny

## Slide 16: Most surfaces have both specular and diffuse components
Specularity = spot where specular reflection dominates (typically reflects light source)
Photo: northcountryhardwoodfloors.com
Typically, specular component is small

## Slide 17: Intensity and Surface Orientation
Intensity depends on illumination angle because less light comes in at oblique angles.
albedo
directional source
surface normal
reflected intensity
Slide: Forsyth

## Slide 18
1
2

## Slide 19: Recap
When light hits a typical surface
  Some light is absorbed (1-)
    More absorbed for low albedos
  Some light is reflected diffusely
    Independent of viewing direction
  Some light is reflected specularly
    Light bounces off (like a mirror), depends on viewing direction
specular reflection
diffuse reflection
absorption

## Slide 20: Other possible effects
light source
transparency
light source
refraction

## Slide 21
λ
light source
subsurface scattering

## Slide 22
λ1
light source
λ2
fluorescence
t=1
light source
t>1
phosphorescence

## Slide 23: BRDF: Bidirectional Reflectance Distribution Function
surface normal
Slide credit: S. Savarese
Model of local reflection that tells how bright a surface appears when viewed from one direction when light falls on it from another

## Slide 24: Application: photometric stereo
Assume:
  a set of point sources that are infinitely distant
  a set of pictures of an object, obtained in exactly the same camera/object configuration but using different sources
  a Lambertian object (or the specular component has been identified and removed)
Photometric stereo slides by Forsyth

## Slide 25
Each image is:
So if we have enough images with known sources, we can solve for
albedo times 3D normal vector
Source direction and strength
Intensity for pixel

## Slide 26
And the albedo (shown here) is given by:
(the normal is a unit vector)

## Slide 29: Dynamic range and camera response
Typical scenes have a huge dynamic range
Camera response is roughly linear in the mid range (15 to 240) but non-linear at the extremes
  called saturation or undersaturation

## Slide 30: Color
http://www.yorku.ca/eye/photopik.htm
Human Luminance Sensitivity Function
Slide Credit: Efros
Light is composed of a spectrum of wavelengths

## Slide 31
Some examples of the spectra of light sources
© Stephen E. Palmer, 2002

## Slide 32
Some examples of the reflectance spectra of surfaces
Wavelength (nm)
% Photons Reflected
Red
400 700
Yellow
400 700
Blue
400 700
Purple
400 700
© Stephen E. Palmer, 2002

## Slide 33: More spectra
metamers

## Slide 34: The color of objects
Colored light arriving at the camera involves two effects
  The color of the light source (illumination + inter-reflections)
  The color of the surface
Slide: Forsyth

## Slide 35: Color Sensing: Bayer Grid
Estimate RGB at each cell from neighboring values
http://en.wikipedia.org/wiki/Bayer_filter
Slide by Steve Seitz

## Slide 36: Color Image
R
G
B

## Slide 37: Why RGB?
If light is a spectrum, why are images RGB?

## Slide 38: Human color receptors
Long (red), Medium (green), and Short (blue) cones, plus intensity rods
Fun facts
  “M” and “L” on the X-chromosome
    That’s why men are more likely to be color blind (see what it’s like: http://www.vischeck.com/vischeck/vischeckImage.php)
  “L” has high variation, so some women are tetrachromatic
  Some animals have 1 (night animals), 2 (e.g., dogs), 4 (fish, birds), 5 (pigeons, some reptiles/amphibians), or even 12 (mantis shrimp) types of cones
http://en.wikipedia.org/wiki/Color_vision

## Slide 39: So far: lightsurfacecamera
Called a local illumination model
But much light comes from surrounding surfaces
From Koenderink slides on image texture and the flow of light

## Slide 40: Inter-reflection is a major source of light

## Slide 41: Inter-reflection affects the apparent color of objects
From Koenderink slides on image texture and the flow of light

## Slide 42: Scene surfaces also cause shadows
Shadow: reduction in intensity due to a blocked source

## Slide 43: Shadows

## Slide 44: Models of light sources
Distant point source
  One illumination direction
  E.g., sun
Area source
  E.g., white walls, diffuser lamps, sky
Ambient light
  Substitute for dealing with interreflections
Global illumination model
  Account for interreflections in modeled scene

## Slide 45: Recap
Possible factors: albedo, shadows, texture, specularities, curvature, lighting direction
1
2
3
4

## Slide 46: Area sources
A point receives light as the summation of contributions of small elements over the whole source
Slide: Forsyth

## Slide 47: What does the intensity of a pixel tell us?
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
im(234, 452) = 0.58

## Slide 48: The plight of the poor pixel
A pixel’s brightness is determined by
  Light source (strength, direction, color)
  Surface orientation
  Surface material and albedo
  Reflected light and shadows from surrounding surfaces
  Gain on the sensor
A pixel’s brightness tells us nothing by itself

## Slide 50
Photo by nickwheeleroz, Flickr
Slide: Forsyth

## Slide 51: And yet we can interpret images…
Key idea: for nearby scene points, most factors do not change much
The information is mainly contained in local differences of brightness

## Slide 52: Darkness = Large Difference in Neighboring Pixels

## Slide 53: What is this?

## Slide 55: What differences in intensity tell us about shape
Changes in surface normal
Texture
Proximity
Indents and bumps
Grooves and creases
Photos Koenderink slides on image texture and the flow of light
Notes: So far, most people have gotten away with just knowing that differences are important and designing features that measure differences.

## Slide 56: Shadows as cues
From Koenderink slides on image texture and the flow of light
Slide: Forsyth

## Slide 57: Color constancy
Interpret surface in terms of albedo or “true color”, rather than observed intensity
  Humans are good at it
  Computers are not nearly as good

## Slide 58: One source of constancy: local comparisons

## Slide 59
http://www.echalk.co.uk/amusements/OpticalIllusions/colourPerception/colourPerception.html

## Slide 60: Perception of Intensity
from Ted Adelson

## Slide 61: Perception of Intensity
from Ted Adelson

## Slide 62: Color Correction
Simple idea: multiply R, G, and B values by separate constants
=
How to choose the constants?
  “White world” assumption: brightest pixel is white
    Divide by largest value
  “Gray world” assumption: average value should be gray
    E.g., multiply r channel by avg(r) /avg((r+g+b)/3)
  White balancing: choose a reference as the white or gray color

## Slide 63: Things to remember
Important terms: diffuse/specular reflectance, albedo, umbra/penumbra
Observed intensity depends on light sources, geometry/material of reflecting surface, surrounding objects, camera settings
Objects cast light and shadows on each other
Differences in intensity are primary cues for shape

## Slide 64: Thank you
Next class: Image Filters