## Slide 1: Pixels and Image Filtering
Computer Vision
Derek Hoiem, University of Illinois
01/24/17
Graphic: http://www.notcot.org/post/4068/

## Slide 2: Today’s Class: Pixels and Linear Filters
Review of lighting
  Reflection and absorption
What is image filtering and how do we do it?
Color models

## Slide 3: Reflection models
Albedo: fraction of light that is reflected
  Determines color (amount reflected at each wavelength)
Very low albedo (hard to see shape)
Higher albedo

## Slide 4: Reflection models
Specular reflection: mirror-like
  Light reflects at incident angle
  Reflection color = incoming light color

## Slide 5: Reflection models
Diffuse reflection
  Light scatters in all directions (proportional to cosine between light source and surface normal)
  Observed intensity is independent of viewing direction
  Reflection color depends on light color and albedo

## Slide 6: Surface orientation and light intensity
Amount of light that hits surface from distant point source depends on angle between surface normal and source
1
2
proportional to cosine of relative angle

## Slide 7: Reflection models
Lambertian: reflection all diffuse
Mirrored: reflection all specular
Glossy: reflection mostly diffuse, some specular
Specularities

## Slide 8: Questions
How many light sources are in the scene?
How could I estimate the color of the camera’s flash?
Notes: im = imread('billiards.png');
figure(1), imagesc(im), axis image, axis off
figure(1), hold on, plot([0 size(im, 2)], [76 76], 'k', 'linewidth', 1.5)
figure(2), hold off, subplot(3, 1, 1), plot(1:size(im, 2), squeeze(im(76, :, 1)), 'r', 'linewidth', 1.5)
figure(2), hold off, subplot(3, 1, 2), plot(1:size(im, 2), squeeze(im(76, :, 2)), 'g', 'linewidth', 1.5)
figure(2), hold off, subplot(3, 1, 3), plot(1:size(im, 2), squeeze(im(76, :, 3)), 'b', 'linewidth', 1.5)

## Slide 9: The plight of the poor pixel
A pixel’s brightness is determined by
  Light source (strength, direction, color)
  Surface orientation
  Surface material and albedo
  Reflected light and shadows from surrounding surfaces
  Gain on the sensor
A pixel’s brightness tells us nothing by itself

## Slide 10: Basis for interpreting intensity images
Key idea: for nearby scene points, most factors do not change much
The information is mainly contained in local differences of brightness

## Slide 11: Darkness = Large Difference in Neighboring Pixels

## Slide 12: Next three classes: three views of filtering
Image filters in spatial domain
  Filter is a mathematical operation on values of each patch
  Smoothing, sharpening, measuring texture
Image filters in the frequency domain
  Filtering is a way to modify the frequencies of images
  Denoising, sampling, image compression
Templates and Image Pyramids
  Filtering is a way to match a template to the image
  Detection, coarse-to-fine registration

## Slide 13: The raster image (pixel matrix)
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93

## Slide 14: Image filtering
Image filtering: for each pixel, compute function of local neighborhood and output a new value
  Same function applied at each position
  Output and input image are typically the same size

## Slide 15: Image filtering
Linear filtering: function is a weighted sum/difference of pixel values
Really important!
  Enhance images
    Denoise, smooth, increase contrast, etc.
  Extract information from images
    Texture, edges, distinctive points, etc.
  Detect patterns
    Template matching

## Slide 16
1
1
1
1
1
1
1
1
1
Slide credit: David Lowe (UBC)
Example: box filter

## Slide 17
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 |  |  |  |  |  |  |  | 
Credit: S. Seitz
Image filtering
1
1
1
1
1
1
1
1
1
Notes: ones, divide by 9

## Slide 18
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 19
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 20
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 | 30 |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 21
 | 0 | 10 | 20 | 30 | 30 |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 22
 | 0 | 10 | 20 | 30 | 30 |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
?
Notes: ones, divide by 9

## Slide 23
 | 0 | 10 | 20 | 30 | 30 |  |  |  | 
 |  |  |  | 50 |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
?
Notes: ones, divide by 9

## Slide 24
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 | 30 | 30 | 30 | 20 | 10 | 
 | 0 | 20 | 40 | 60 | 60 | 60 | 40 | 20 | 
 | 0 | 30 | 60 | 90 | 90 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 20 | 30 | 50 | 50 | 60 | 40 | 20 | 
 | 10 | 20 | 30 | 30 | 30 | 30 | 20 | 10 | 
 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 0 | 
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz

## Slide 25
What does it do?
Replaces each pixel with an average of its neighborhood
Achieve smoothing effect (remove sharp features)
1
1
1
1
1
1
1
1
1
Slide credit: David Lowe (UBC)
Box Filter

## Slide 26
Smoothing with box filter

## Slide 27: Practice with linear filters
0
0
0
0
1
0
0
0
0
Original
?
Source: D. Lowe

## Slide 28: Practice with linear filters
0
0
0
0
1
0
0
0
0
Original
Filtered
(no change)
Source: D. Lowe

## Slide 29: Practice with linear filters
0
0
0
1
0
0
0
0
0
Original
?
Source: D. Lowe

## Slide 30: Practice with linear filters
0
0
0
1
0
0
0
0
0
Original
Shifted left
By 1 pixel
Source: D. Lowe

## Slide 31: Practice with linear filters
Original
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
?
(Note that filter sums to 1)
Source: D. Lowe

## Slide 32: Practice with linear filters
Original
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
Sharpening filter
  Accentuates differences with local average
Source: D. Lowe

## Slide 33: Sharpening
Source: D. Lowe

## Slide 34: Other filters
-1
0
1
-2
0
2
-1
0
1
Vertical Edge
(absolute value)
Sobel

## Slide 35: Other filters
-1
-2
-1
0
0
0
1
2
1
Horizontal Edge
(absolute value)
Sobel

## Slide 36: Basic gradient filters
0
0
0
1
0
-1
0
0
0
0
1
0
0
0
0
0
-1
0
1
0
-1
or
Horizontal Gradient
Vertical Gradient
1
0
-1
or

## Slide 37: Examples
Write as filtering operations, plus some elementwise operations: +, -, .*,>
Sum of four adjacent neighbors plus 1
Sum of squared values of 3x3 windows around each pixel:
Center pixel value is larger than the average of the pixel values to the left and right:

## Slide 38: How could we synthesize motion blur?
theta = 30; len = 20;
fil = imrotate(ones(1, len), theta, 'bilinear');
fil = fil / sum(fil(:));
figure(2), imshow(imfilter(im, fil));

## Slide 39: Filtering vs. Convolution
2d filtering
  h=filter2(g,f); or h=imfilter(f,g);
2d convolution
  h=conv2(g,f);
f=image
g=filter

## Slide 40: Key properties of linear filters
Linearity:
filter(f1 + f2) = filter(f1) + filter(f2)
Shift invariance: same behavior regardless of pixel location
filter(shift(f)) = shift(filter(f))
Any linear, shift-invariant operator can be represented as a convolution
Source: S. Lazebnik

## Slide 41: More properties
Commutative: a * b = b * a
  Conceptually no difference between filter and signal
Associative: a * (b * c) = (a * b) * c
  Often apply several filters one after another: (((a * b1) * b2) * b3)
  This is equivalent to applying one filter: a * (b1 * b2 * b3)
Distributes over addition: a * (b + c) = (a * b) + (a * c)
Scalars factor out: ka * b = a * kb = k (a * b)
Identity: unit impulse e = [0, 0, 1, 0, 0], a * e = a
Source: S. Lazebnik

## Slide 42
Spatially-weighted average
0.003 0.013 0.022 0.013 0.003
0.013 0.059 0.097 0.059 0.013
0.022 0.097 0.159 0.097 0.022
0.013 0.059 0.097 0.059 0.013
0.003 0.013 0.022 0.013 0.003
5 x 5,  = 1
Slide credit: Christopher Rasmussen
Important filter: Gaussian

## Slide 43
Smoothing with Gaussian filter

## Slide 44
Smoothing with box filter

## Slide 45: Gaussian filters
Remove “high-frequency” components from the image (low-pass filter)
  Images become more smooth
Convolution with self is another Gaussian
  So can smooth with small-width kernel, repeat, and get same result as larger-width kernel would have
  Convolving two times with Gaussian kernel of width σ is same as convolving once with kernel of width
Separable kernel
  Factors into product of two 1D Gaussians
Source: K. Grauman
Notes: Linear vs. quadratic in mask size

## Slide 46: Separability of the Gaussian filter
Source: D. Lowe

## Slide 47: Separability example
*
*
=
=
2D filtering (center location only)
Source: K. Grauman
The filter factors into a product of 1D filters:
Perform filtering along rows:
Followed by filtering along the remaining column:

## Slide 48: Separability
Why is separability useful in practice?

## Slide 49: Some practical matters

## Slide 50: Practical matters
How big should the filter be?
Values at edges should be near zero  important!
Rule of thumb for Gaussian: set filter half-width to about 3 σ

## Slide 51: Practical matters
What about near the edge?
  the filter window falls off the edge of the image
  need to extrapolate
  methods:
    clip filter (black)
    wrap around
    copy edge
    reflect across edge
Source: S. Marschner

## Slide 52: Practical matters
  methods (MATLAB):
    clip filter (black): imfilter(f, g, 0)
    wrap around: imfilter(f, g, ‘circular’)
    copy edge: imfilter(f, g, ‘replicate’)
    reflect across edge: imfilter(f, g, ‘symmetric’)
Source: S. Marschner

## Slide 53: Practical matters
What is the size of the output?
MATLAB: filter2(g, f, shape)
  shape = ‘full’: output size is sum of sizes of f and g
  shape = ‘same’: output size is same as f
  shape = ‘valid’: output size is difference of sizes of f and g
f
g
g
g
g
f
g
g
g
g
f
g
g
g
g
full
same
valid
Source: S. Lazebnik

## Slide 54: A little more about color…

## Slide 55: Digital Color Images
CMOS sensor
Bayer Filter

## Slide 56: Color Image
R
G
B

## Slide 57: Images in Matlab
Images represented as a matrix
Suppose we have a NxM RGB image called “im”
  im(1,1,1) = top-left pixel value in R-channel
  im(y, x, b) = y pixels down, x pixels to right in the bth channel
  im(N, M, 3) = bottom-right pixel in B-channel
imread(filename) returns a uint8 image (values 0 to 255)
  Convert to double format (values 0 to 1) with im2double
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
R
G
B
row
column

## Slide 58: Color spaces
How can we represent color?
http://en.wikipedia.org/wiki/File:RGB_illumination.jpg

## Slide 59: Color spaces: RGB
0,1,0
0,0,1
1,0,0
Image from: http://en.wikipedia.org/wiki/File:RGB_color_solid_cube.png
Some drawbacks
Strongly correlated channels
Non-perceptual
Default color space
R
(G=0,B=0)
G
(R=0,B=0)
B
(R=0,G=0)

## Slide 60: Color spaces: HSV
Intuitive color space
H
(S=1,V=1)
S
(H=1,V=1)
V
(H=1,S=0)

## Slide 61: Color spaces: YCbCr
Y
(Cb=0.5,Cr=0.5)
Cb
(Y=0.5,Cr=0.5)
Cr
(Y=0.5,Cb=05)
Y=0
Y=0.5
Y=1
Cb
Cr
Fast to compute, good for compression, used by TV

## Slide 62: Color spaces: CIE L*a*b*
“Perceptually uniform” color space
L
(a=0,b=0)
a
(L=65,b=0)
b
(L=65,a=0)
Luminance = brightness
Chrominance = color

## Slide 63: Which contains more information? (a) intensity (1 channel) (b) chrominance (2 channels)

## Slide 64: If you had to choose, would you rather go without luminance or chrominance?

## Slide 65: Most information in intensity
Only color shown – constant intensity

## Slide 66: Most information in intensity
Only intensity shown – constant color

## Slide 67: Most information in intensity
Original image

## Slide 68: Take-home messages
Image is a matrix of numbers (light intensities at different orientations)
  Interpreted mainly through local comparisons
Linear filtering is sum of dot product at each position
  Can smooth, sharpen, translate (among many other uses)
Attend to details: filter size, extrapolation, cropping
Color spaces beyond RGB sometimes useful
1
1
1
1
1
1
1
1
1
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
=