## Slide 1: Projective Geometry and Camera Models
Computer Vision
CS 543 / ECE 549
University of Illinois
Derek Hoiem
02/21/17

## Slide 2: HWs
HW 1 back yesterday
  Solutions are posted
  Shadow on specular surface
HW 2 due next Mon night
HW 3 should be out by next Tuesday

## Slide 3: Top-scoring edge methods
Lengyue Chen (Overall: 0.681):
  RGB to LAB
  Smooth each channel (L by sigma=2.8, others by 3)
  Average gradient magnitudes
  No non-max suppression
Anusri Papari (0.669):
  HSV + RGB gradient mags, sigma=2.5
Max Feinberg (0.662)
  HSV + smoothing + gradient
L. Chen Result

## Slide 4: Think about your final projects
Strongly encouraged to work in groups of 3-4 (but if you have a good reason to work by self, could be ok)
Projects don’t need to be of publishable originality but should evince independent effort to learn about a new topic, try something new, or apply to an application of interest
Proposals will be due after Spring Break

## Slide 5: Last notes on registration
Thin-plate splines: combines global affine warp with smooth local deformation
Diff of predicted vs. actual position
Smoothness cost for local warps
Affine warp
Local deformation according to distance from control points
There is a closed form solution for parameter estimation and warping

## Slide 6
Robust non-rigid point matching: http://noodle.med.yale.edu/~chui/tps-rpm.html (includes code, demo, paper)
  Thin-plate spline registration with robustness to outliers

## Slide 7: Next two classes: Single-view Geometry
How tall is this woman?
Which ball is closer?
How high is the camera?
What is the camera rotation?
What is the focal length of the camera?

## Slide 8: Today’s class
Mapping between image and world coordinates
  Pinhole camera model
  Projective geometry
    Vanishing points and lines
  Projection matrix

## Slide 9: Image formation
Let’s design a camera
  Idea 1: put a piece of film in front of an object
  Do we get a reasonable image?
Slide source: Seitz

## Slide 10: Pinhole camera
Idea 2: add a barrier to block off most of the rays
  This reduces blurring
  The opening known as the aperture
Slide source: Seitz
Notes: Q: How does this transform the image? A: It gets inverted

## Slide 11: Pinhole camera
Figure from Forsyth
f
f = focal length
c = center of the camera
c

## Slide 12: Camera obscura: the pre-camera
First idea: Mo-Ti, China (470BC to 390BC)
First built: Alhazen, Iraq/Egypt (965 to 1039AD)
Illustration of Camera Obscura
Freestanding camera obscura at UNC Chapel Hill
Photo by Seth Ilys
Notes: Alhazen was born in Basra, moved to Egypt. Proposed to the king to control the Nile with a dam. Realized he couldn’t do it and feigned madness until the king died. During that time, he wrote the book of optics.

## Slide 13: Camera Obscura used for Tracing
Lens Based Camera Obscura, 1568

## Slide 14: First Photograph
Oldest surviving photograph
  Took 8 hours on pewter plate
Joseph Niepce, 1826
Photograph of the first photograph
Stored at UT Austin
Niepce later teamed up with Daguerre, who eventually created Daguerrotypes

## Slide 15: Dimensionality Reduction Machine (3D to 2D)
Figures © Stephen E. Palmer, 2002
3D world
2D image

## Slide 16: Projection can be tricky…
Slide source: Seitz

## Slide 17: Projection can be tricky…
Slide source: Seitz
Making of 3D sidewalk art: http://www.youtube.com/watch?v=3SNYtd0Ayt0

## Slide 18: Projective Geometry
What is lost?
Length
Which is closer?
Who is taller?

## Slide 19: Length is not preserved
Figure by David Forsyth
B’
C’
A’

## Slide 20: Projective Geometry
What is lost?
Length
Angles
Perpendicular?
Parallel?

## Slide 21: Projective Geometry
What is preserved?
Straight lines are still straight

## Slide 22: Vanishing points and lines
Parallel lines in the world intersect in the image at a “vanishing point”
Notes: Go to board, sketch out various properties of vanishing points/lines

## Slide 23: Vanishing points and lines
o
Vanishing Point
o
Vanishing Point
Vanishing Line
The projections of parallel 3D lines intersect at a vanishing point
The projection of parallel 3D planes intersect at a vanishing line
If a set of parallel 3D lines are also parallel to a particular plane, their vanishing point will lie on the vanishing line of the plane
Not all lines that intersect are parallel
Vanishing point <-> 3D direction of a line
Vanishing line <-> 3D orientation of a surface
Notes: Go to board, sketch out various properties of vanishing points/lines
Parallel lines intersect at a point
The intersection of red lines and blue lines form a parallelogram
Sets of parallel lines on the same plane form a vanishing line
Sets of parallel planes form a vanishing line
Not all lines that intersect are parallel

## Slide 24: Vanishing points and lines
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)
Slide from Efros, Photo from Criminisi

## Slide 25: Vanishing points and lines
Photo from online Tate collection
Notes: Where are the vanishing points? Do buildings on left and buildings on right have the same vanishing line? Which way is the camera tilted?

## Slide 26: Note on estimating vanishing points
Use multiple lines for better accuracy
… but lines will not intersect at exactly the same point in practice
One solution: take mean of intersecting pairs
… bad idea!
Instead, minimize angular differences
Notes: Go to board, sketch out various properties of vanishing points/lines

## Slide 27: Vanishing objects

## Slide 28: Projection: world coordinatesimage coordinates
Camera Center (tx, ty, tz)
.
.
.
f
Z
Y
.
Principal point (u0, v0)
v
u
X

## Slide 29: Homogeneous coordinates
Conversion
Converting to homogeneous coordinates
homogeneous image
coordinates
homogeneous scene
coordinates
Converting from homogeneous coordinates
Notes: Append coordinate with value 1; proportional coordinate system

## Slide 30: Homogeneous coordinates
Invariant to scaling
Point in Cartesian is ray in Homogeneous
Homogeneous Coordinates
Cartesian Coordinates
Notes: Q: Suppose we have a point in Cartesian coordinates. What is that in homogeneous coordinates? A: a ray

## Slide 31: Basic geometry in homogeneous coordinates
Line equation: ax + by + c = 0
Append 1 to pixel coordinate to get homogeneous coordinate
Line given by cross product of two points
Intersection of two lines given by cross product of the lines

## Slide 32: Another problem solved by homogeneous coordinates
  Cartesian: (Inf, Inf)
  Homogeneous: (1, 1, 0)
Intersection of parallel lines
  Cartesian: (Inf, Inf)
Homogeneous: (1, 2, 0)
Notes: Parallel lines intersect at different infinities

## Slide 33
Slide Credit: Saverese
Projection matrix
x: Image Coordinates: (u,v,1)
K: Intrinsic Matrix (3x3)
R: Rotation (3x3)
t: Translation (3x1)
X: World Coordinates: (X,Y,Z,1)
Ow
iw
kw
jw
R,T
Notes: We can use homogeneous coordinates to write camera matrix in linear form.

## Slide 34: Interlude: when have I used this stuff?

## Slide 35: When have I used this stuff?
Object Recognition (CVPR 2006)

## Slide 36: When have I used this stuff?
Single-view reconstruction (SIGGRAPH 2005)

## Slide 37: When have I used this stuff?
Getting spatial layout in indoor scenes (ICCV 2009)

## Slide 38: When have I used this stuff?
Inserting synthetic objects into images: http://vimeo.com/28962540

## Slide 39: When have I used this stuff?
Creating detailed and complete 3D scene models from a single view

## Slide 40: When have I used this stuff?
Multiview 3D reconstruction at Reconstruct

## Slide 41
K
Slide Credit: Saverese
Projection matrix
Intrinsic Assumptions
Unit aspect ratio
Principal point at (0,0)
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)
Notes: Work through equations for u and v on board

## Slide 42: Remove assumption: known principal point
Intrinsic Assumptions
Unit aspect ratio
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)

## Slide 43: Remove assumption: square pixels
Intrinsic Assumptions
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)

## Slide 44: Remove assumption: non-skewed pixels
Extrinsic Assumptions
No rotation
Camera at (0,0,0)
Note: different books use different notation for parameters
Intrinsic Assumptions
Pinhole camera model

## Slide 45: Oriented and Translated Camera
Ow
iw
kw
jw
t
R

## Slide 46: Allow camera translation
Extrinsic Assumptions
No rotation
Intrinsic Assumptions
Pinhole camera model

## Slide 47: 3D Rotation of Points
Rotation around the coordinate axes, counter-clockwise:
p
p’
g
y
z
Slide Credit: Saverese

## Slide 48: Allow camera rotation

## Slide 49: Degrees of freedom
5
6
Notes: How many known points are needed to estimate this?

## Slide 50: Vanishing Point = Projection from Infinity

## Slide 51: Orthographic Projection
Special case of perspective projection
  Distance from the COP to the image plane is infinite
  Also called “parallel projection”
  What’s the projection matrix?
Image
World
Slide by Steve Seitz

## Slide 52: Scaled Orthographic Projection
Special case of perspective projection
  Object dimensions are small compared to distance to camera
  Also called “weak perspective”
Image
World
Slide by Steve Seitz

## Slide 53: Example
Near field: object appearance changes as objects translate
Far field: object appearance doesn’t change as objects translate

## Slide 54: Beyond Pinholes: Radial Distortion
Common in wide-angle lenses or for special applications (e.g., security)
Creates non-linear terms in projection
Usually handled by through solving for non-linear terms and then correcting image
Image from Martin Habbecke
Corrected Barrel Distortion

## Slide 55: Things to remember
Vanishing points and vanishing lines
Pinhole camera model and camera projection matrix
Homogeneous coordinates
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)

## Slide 56: Next class
Applications of camera model and projective geometry
  Recovering the camera intrinsic and extrinsic parameters from an image
  Recovering size in the world
  Projecting from one plane to another