## Slide 1: Single-view Metrology and Camera Calibration
Computer Vision
Derek Hoiem, University of Illinois
02/23/17

## Slide 2: Last Class: Pinhole Camera
Camera Center (tx, ty, tz)
.
.
.
f
Z
Y
.
Principal Point (u0, v0)
v
u

## Slide 3: Last Class: Projection Matrix
Ow
iw
kw
jw
t
R
Notes: As review:
1) Example of my eye and their eye, where both coordinate frames are known. Suppose that I know a 3D point on the board in relation to me, and I want to figure out where that point will appear on their retina. First, I translate and rotate my eye so that it aligns with theirs. Then, I project from 3D onto the 2D visual field.
2) Suppose I know x, K, R, and t. Can I compute X? What can I know about X?

## Slide 4: Last class: Vanishing Points
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)
Slide from Efros, Photo from Criminisi

## Slide 5: This class
How can we calibrate the camera?
How can we measure the size of objects in the world from an image?
What about other camera properties: focal length, field of view, depth of field, aperture, f-number?

## Slide 6: How to calibrate the camera?

## Slide 7: Calibrating the Camera
Method 1: Use an object (calibration grid) with known geometry
  Correspond image points to 3d points
  Get least squares solution (or non-linear solution)

## Slide 8: Linear method
Solve using linear least squares
Ax=0 form

## Slide 9: Calibration with linear method
Advantages
  Easy to formulate and solve
  Provides initialization for non-linear methods
Disadvantages
  Doesn’t directly give you camera parameters
  Doesn’t model radial distortion
  Can’t impose constraints, such as known focal length
  Doesn’t minimize projection error
Non-linear methods are preferred
  Define error as difference between projected points and measured points
  Minimize error using Newton’s method or other non-linear optimization
Can solve for explicit camera parameters:
http://ksimek.github.io/2012/08/14/decompose/

## Slide 10: Calibrating the Camera
Method 2: Use vanishing points
  Find vanishing points corresponding to orthogonal directions
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)

## Slide 11: Calibration by orthogonal vanishing points
Intrinsic camera matrix
  Use orthogonality as a constraint
  Model K with only f, u0, v0
What if you don’t have three finite vanishing points?
  Two finite VP: solve f, get valid u0, v0 closest to image center
  One finite VP: u0, v0 is at vanishing point; can’t solve for f
For vanishing points

## Slide 12: Calibration by vanishing points
Intrinsic camera matrix
Rotation matrix
  Set directions of vanishing points
    e.g., X1 = [1, 0, 0]
  Each VP provides one column of R
  Special properties of R
    inv(R)=RT
    Each row and column of R has unit length

## Slide 13: How can we measure the size of 3D objects from an image?
Slide by Steve Seitz

## Slide 14: Perspective cues
Slide by Steve Seitz

## Slide 15: Perspective cues
Slide by Steve Seitz

## Slide 16: Perspective cues
Slide by Steve Seitz

## Slide 17: Ames Room

## Slide 18: Comparing heights
Vanishing
Point
Slide by Steve Seitz

## Slide 19: Measuring height
1
2
3
4
5
5.3
2.8
3.3
Camera height
Slide by Steve Seitz

## Slide 20
Which is higher – the camera or the man in the parachute?

## Slide 21: Measuring height without a ruler
C
ground plane
Compute Z from image measurements
Z
Slide by Steve Seitz

## Slide 22: The cross ratio
A Projective Invariant
  Something that does not change under projective transformations (including perspective projection)
P1
P2
P3
P4
The cross-ratio of 4 collinear points
Can permute the point ordering
  4! = 24 different orders (but only 6 distinct values)
This is the fundamental invariant of projective geometry
Slide by Steve Seitz

## Slide 23: Measuring height
vZ
r
t
b
image cross ratio
B (bottom of object)
T (top of object)
R (reference point)
ground plane
H
C
scene cross ratio

scene points represented as
image points as
R
Slide by Steve Seitz

## Slide 24: Measuring height
R
H
vz
r
b
t
H
b0
t0
v
vx
vy
vanishing line (horizon)
image cross ratio
Slide by Steve Seitz

## Slide 25: Measuring height
vz
r
b
t0
vx
vy
vanishing line (horizon)
v
t0
m0
What if the point on the ground plane b0 is not known?
  Here the guy is standing on the box, height of box is known
  Use one side of the box to help find b0 as shown above
b0
t1
b1
Slide by Steve Seitz

## Slide 26: Review
How tall is this woman?
Which ball is closer?
How high is the camera?
What is the camera rotation?
What is the focal length of the camera?
Notes: Find orthogonal vanishing points
Rotate image so that horizontal axis is in X direction
Draw horizon
Estimate camera height based on the standard size of Bocce balls (107 mm)
Estimate woman’s height based on camera height
Solve for intrinsic parameters and camera rotation from vanishing points

## Slide 27: What about focus, aperture, DOF, FOV, etc?

## Slide 28: Adding a lens
A lens focuses light onto the film
  There is a specific distance at which objects are “in focus”
    other points project to a “circle of confusion” in the image
  Changing the shape of the lens changes this distance
“circle of
confusion”

## Slide 29: Focal length, aperture, depth of field
A lens focuses parallel rays onto a single focal point
  focal point at a distance f beyond the plane of the lens
  Aperture of diameter D restricts the range of rays
focal point
F
optical center
(Center Of Projection)
Slide source: Seitz

## Slide 30: The eye
The human eye is a camera
  Iris - colored annulus with radial muscles
  Pupil (aperture) - the hole whose size is controlled by the iris
  Retina (film): photoreceptor cells (rods and cones)
Slide source: Seitz
Notes: Note that the retina is curved

## Slide 31: Depth of field
Changing the aperture size or focal length affects depth of field
f / 5.6
f / 32
Flower images from Wikipedia http://en.wikipedia.org/wiki/Depth_of_field
Slide source: Seitz

## Slide 32: Varying the aperture
Large aperture = small DOF
Small aperture = large DOF
Slide from Efros

## Slide 33: Shrinking the aperture
Why not make the aperture as small as possible?
  Less light gets through
  Diffraction effects
Slide by Steve Seitz

## Slide 34: Shrinking the aperture
Slide by Steve Seitz

## Slide 35: Relation between field of view and focal length
Field of view (angle width)
Film/Sensor Width
Focal length

## Slide 36: Dolly Zoom or “Vertigo Effect”
http://www.youtube.com/watch?v=NB4bikrNzMk
http://en.wikipedia.org/wiki/Focal_length
Zoom in while moving away
How is this done?

## Slide 37: Review
How tall is this woman?
Which ball is closer?
How high is the camera?
What is the camera rotation?
What is the focal length of the camera?
Notes: Find orthogonal vanishing points
Rotate image so that horizontal axis is in X direction
Draw horizon
Estimate camera height based on the standard size of Bocce balls (107 mm)
Estimate woman’s height based on camera height
Solve for intrinsic parameters and camera rotation from vanishing points
Calculate the position of the balls given that their height is 0

## Slide 38: Next class
Image stitching
Camera Center
P
Q