## Slide 1: ECE411: Computer Organization and Design Lecture 3: Performance, Energy, and Power Metrics
Rakesh Kumar

## Slide 2: Computer Performance: time!, time!, time!
latency (response time)
  how long does it take to execute a task?
  how long must i wait for the database query?
  high-percentile response time (SLO, SLA, etc. at datacenters)
throughput
  how many jobs can the machine complete in a minute?
  what is the average execution rate?
  how much work is getting done?
Notes: Have them raise their hands when answering questions

## Slide 3: Computer Performance: time!, time!, time!
Source: Latency vs. Throughput (DEV Community)
Notes: Have them raise their hands when answering questions

## Slide 4: How Do We Quantify CPU Performance?
CPU execution time = seconds / program
  time the CPU spends working on a task
  does not include time waiting for I/O or running other programs
programmer
algorithms
ISA
compilers
microarchitecture
system architecture
microarchitecture, pipeline depth
circuit design
Semiconductor technology

## Slide 5: CISC vs. RISC
Design difference between CISC vs. RISC
Share the same goal of improving program performance, but
  RISC: focuses on reducing the cycles per instruction
  CISC: focuses on reducing the number of instructions per program

## Slide 6: Performance Metric
Metric #1: time to complete a task (Texe)
  execution time, response time, latency
    X is N time faster than Y means Texe(Y)/Texe(X) = N
  example:
    machine A runs a program in 20 seconds
    machine B runs the same program in 25 seconds
    A is _______ times faster than B?

## Slide 7: Performance Metric
Metric #2: # of tasks per day, hour, seconds,
  throughput or bandwidth
  not the same as latency
    Multi-core processors improve throughput but not latency
Examples of other metrics
  millions instructions per second (MIPS)
  millions floating-point operations per second (MFLOPS)
  Trillions (1012) of operations per second (TOPS)

## Slide 8: How to Improve Performance
to improve performance (everything else being equal) you can either ________ the # of required cycles for a program, or ________ the clock cycle time or, said another way, ________ the clock rate.
An example: if a computer has a clock cycle time of 5 ns, the clock rate is: 1/(5 x 10-9 sec) = 200 MHz

## Slide 9: Performance Related Metrics
an execution of a given program will require
  some number of instructions (machine instructions)
  some number of cycles
  some number of seconds
we have a vocabulary of metrics that relate these quantities:
  cycle time (seconds per cycle)
  clock rate (cycles per second)
  CPI (cycles per instruction)
instruction set metrics
  Q: if two machines have the same ISA and run the same program
  which of our quantities (e.g., clock rate, CPI, execution time, # of instructions, MIPS) will likely be identical during a comparison?

## Slide 10: Performance Examples
Suppose we have two implementations of the same ISA, what machine is faster for a given program, and by how much?
  machine A w/ a clock cycle time of 10ns and a CPI of 2.5
  machine B w/ a clock cycle time of 20ns and a CPI of 1
Notes:   First: 2*1 + 1*2 + 2*3 = 10 cycles Second: 4*1 + 1*2 + 1*3 = 9 cycles
Which sequence will be faster according to execution time?
  First: 5M*1+1M*2+1M*3 = 10M cycles
  Second: 10M*1+1M*2+1M*3 = 15M cycles

## Slide 11: Performance Examples
2. Consider two code sequences for a given machine w/ 3 different classes of instructions: class A, B, and C requiring 1, 2, and 3 cycles per instruction, which sequence will be faster?
  first code sequence w/ 5 instructions (2 of A, 1 of B, and 2 of C)
  second code sequence w/ 6 instructions (4 of A, 1 of B, and 1 of C)
Notes:   First: 2*1 + 1*2 + 2*3 = 10 cycles Second: 4*1 + 1*2 + 1*3 = 9 cycles
Which sequence will be faster according to execution time?
  First: 5M*1+1M*2+1M*3 = 10M cycles
  Second: 10M*1+1M*2+1M*3 = 15M cycles

## Slide 12: Performance Examples
3. Consider two compilers and a machine operating at 100MHz w/ 3 classes of instructions: class A, B, and C requiring 1, 2, and 3 cycles per instruction, which compiler generates faster running code?
  first compiler's code uses 5M Class A instructions, 1M Class B instructions, and 1M Class C instructions
  second compiler's code uses 10M Class A instructions, 1M Class B instructions, and 1M Class C instructions
Notes: Which sequence will be faster according to execution time?
  First: 5M*1+1M*2+1M*3 = 10M cycles
  Second: 10M*1+1M*2+1M*3 = 15M cycles

## Slide 13: Effective CPI
computing the overall effective CPI is done by looking at the different types of instructions and their individual cycle counts and averaging
  where ICi is the count (percentage) of the number of instructions of class i executed
  CPIi is the (average) number of clock cycles per instruction for that instruction class
  n is the number of instruction classes
Overall effective CPI =  (CPIi x ICi)
i = 1
n

## Slide 14: Effective CPI: Exercise
how much faster would the machine be if a better data cache reduced the average load time to 2 cycles?
how much faster, as we use branch prediction to shave a cycle off the branch time?
what if two ALU instructions could be executed at once?
op | freq | CPIi | freq x CPIi
ALU | 50% | 1 | 
load | 20% | 5 | 
store | 10% | 3 | 
branch | 20% | 2 | 
overall effective CPI |  |  |  =

## Slide 15
Processor A:
  CPI_CORE= 1, CPIMEM = 1, proc. clock = 500 MHz (2ns)
What is the speedup if we double processor clock frequency?
What about an infinite clock frequency?

## Slide 16: Review: Single Cycle vs. Multiple Cycle Timing
clk
cycle 1
multiple cycle implementation:
IFetch
Dec
Exec
Mem
WB
cycle 2
cycle 3
cycle 4
cycle 5
cycle 6
cycle 7
cycle 8
cycle 9
cycle 10
IFetch
Dec
Exec
Mem
lw
sw
IFetch
R-type
clk
single cycle implementation:
lw
sw
waste
cycle 1
cycle 2
multicycle clock slower than 1/5th of single cycle clock due to state register overhead
Notes: Here are the timing diagrams showing the differences between the single cycle and multiple cycle.
In the multiple clock cycle implementation, we cannot start executing the store until Cycle 6 because we must wait for the load instruction to complete.
Similarly, we cannot start the execution of the R-type instruction until the store instruction has completed its execution in Cycle 9.
In the Single Cycle implementation, the cycle time is set to accommodate the longest instruction, the Load instruction.
Consequently, the cycle time for the Single Cycle implementation can be five times longer than the multiple cycle implementation.

## Slide 17: Review: Will multicycle design be faster?
let’s assume tsetup + tcq time for registers = 0.1 ns
  single cycle design:
    clock cycle time = 4.7 + 0.1 = 4.8 ns
    time/inst = 1 cycle/inst × 4.8 ns/cycle = 4.8 ns/inst
  multicycle design:
    clock cycle time = 1.0 + 0.1 = 1.1
    time/inst = CPI × 1.1 ns/cycle (depends on the types or mixture of instructions!)
 | I Fetch | Decode, R-Read | ALU | PC update | D Memory | R-Write | Total (ns)
Add | 1 | 1 | .9 | - | - | .8 | 3.7
Load | 1 | 1 | .9 | - | 1 | .8 | 4.7
Store | 1 | 1 | .9 | - | 1 | - | 3.9
beq | 1 | 1 | .9 | .1 | - | - | 3.0

## Slide 18: Will multicycle design be faster?
 | Cycles needed | Instruction frequency
R-type | 4 | 60%
Load | 5 | 20%
Store | 4 | 10%
beq | 3 | 10%
Let’s assume setup + hold time = 0.1 ns
Single cycle design:
  Clock cycle time = 4.7 + 0.1 = 4.8 ns
  time/inst = 1 cycle/inst * 4.8 ns/cycle = 4.8 ns/inst
Multicycle design:
  Clock cycle time = 1.0 + 0.1 = 1.1
  time/inst = CPI * 1.1 ns/cycle = ???
What is CPI assuming
this instruction mix???

## Slide 19
Calculation assumptions:
  Most instructions take 10 nanoseconds (ns)
  But multiply instruction takes 40ns
  Multiplies are 10% of all instructions
  How much faster is a Multi-cycle Datapath over a single-cycle datapath (setup=hold=0)?

## Slide 20
Assumptions
  30% loads, 5ns
  10% stores, 5ns
  50% adds, 4ns
  10% multiplies, 20ns
  How much faster is a Multi-cycle Datapath over a single-cycle datapath (setup=hold=0)?

## Slide 21: Evaluating ISAs (ISA Design Tradeoffs)
Design-time metrics:
  can it be implemented, in how long, at what cost?
  can it be programmed? ease of compilation?
Static Metrics:
  how many bytes does the program occupy in memory?
Dynamic metrics:
  how many instructions are executed? how many bytes does the processor fetch to execute the program?
  how many clocks are required per instruction?
Best metric: time to execute the program!
CPI
Inst. Count
Cycle Time
Depends on the instructions set, the processor organization, and compilation techniques.

## Slide 22: Benchmarks
Which program to choose?
Real programs
  porting problem, complexity, not easy to understand the cause of results
Kernels
  computationally intense piece of real programs
Toy benchmarks
  QuickSort
Synthetic benchmarks
Benchmark suites
  SPEC for scientific, engineering, and general purpose
  TPC benchmarks for commercial systems
  EEMBC (Embedded Microprocessor Benchmark Consortium) for embedded systems

## Slide 23: SPEC Benchmarks
Integer benchmarks |  | FP benchmarks | 
gzip | compression | wupwise | Quantum chromodynamics
vpr | FPGA place & route | swim | shallow water model
gcc | GNU C compiler | mgrid | multigrid solver in 3D fields
mcf | combinatorial optimization | applu | parabolic/elliptic pde
crafty | chess program | mesa | 3D graphics library
parser | word processing program | galgel | computational fluid dynamics
eon | computer visualization | art | image recognition (NN)
perlbmk | perl application | equake | seismic wave propagation simulation
gap | group theory interpreter | facerec | facial image recognition
vortex | object oriented database | ammp | computational chemistry
bzip2 | compression | lucas | primality testing
twolf | circuit place & route | fma3d | crash simulation fem
 |  | sixtrack | nuclear physics accel
 |  | apsi | pollutant distribution

## Slide 24: Reporting Performance
How do we summarize performance for benchmark set w/ a single number?
let Ti be the execution time of program i:
Arithmetic mean
  Average execution time
  Gives more weight to longer-running programs
(weighted) arithmetic mean of execution times:
  programs w/ the longest execution time will dominate the result
Weighted arithmetic mean
  More important programs can be emphasized
  But what do we use as weights?
  Different weight will make different machines look better

## Slide 25: Issues with Arithmetic Mean
What is the speedup of A compared to B on Program 1?
What is the speedup of A compared to B on Program 2?
What is the average speedup of A compared to B?
What is the speedup of B compared to A? (0.5+2)/2=1.25
 | Machine A | Machine B
Program 1 | 1 sec | 2 sec
Program 2 | 2 sec | 1 sec
2/1
1/2
(2.0+0.5)/2 = 1.25

## Slide 26: Normalizing and Geometric Mean
Dealing w/ speedup (normalized execution time)
Neat property of the geometric mean: Consistent whatever the reference machine

## Slide 27: Normalizing and Geometric Mean
Do not use the arithmetic mean for normalized execution times
  Want to understand why, check this paper

## Slide 28: Reporting Performance (An Example)
 | program a | program b | arithmetic mean | speedup (ref 1) | speedup (ref 2)
machine 1 | 10 sec | 100 sec | 55 sec | 91.8 | 10
machine 2 | 1 sec | 200 sec | 100.5 sec | 50.2 | 5.5
reference 1 | 100 sec | 10000 sec | 5050 sec |  | 
reference 2 | 100 sec | 1000 sec | 550 sec |  | 
 |  | a | b | gm
wrt reference 1 | machine 1 | 10 | 100 | 31.6
 | machine 2 | 100 | 50 | 70.7
wrt reference 2 | machine 1 | 10 | 10 | 10
 | machine 2 | 100 | 5 | 22.4

## Slide 29: Takeaways
CPU Performance
Amdahl’s Law
Power/Energy Metrics
How should we report performance: Arithmetic Mean vs. Geometric Mean

## Slide 30: Announcement
lecture 2 in text book
  Appendix A (HP2), Ch. 2.16 – 2.18 (HP1)
lecture 3 in text book
  Ch. 1.6 – 1.7 (HP1) Ch. 1.8 (HP2)