## Slide 1: Cache Memories

## Slide 2: Write-through Policy
0x1234
0x1234
0x1234
Processor
Cache
Memory
0x1234
0x5678
0x5678

## Slide 3: Write-back Policy
0x1234
0x1234
0x1234
Processor
Cache
Memory
0x1234
0x5678
0x5678
0x5678
0x9ABC
?????
Write miss

## Slide 4: On Write Miss
Write allocate
  The line is allocated on a write miss, followed by the write hit actions above.
  Write misses first act like read misses
  Better performance if data referenced again
No write allocate
  Write misses do not interfere cache
  Line is only modified in the lower level memory
  Mostly use with write-through cache
  Simpler write hardware
  May be better for small caches if written data won’t be read again soon

## Slide 5: Another Question
Consider a 128 byte 2-way set associative write-back cache with 16 byte blocks. Assume LRU replacement and that dirty bits are used to avoid writing back clean blocks. Complete the table below for a sequence of memory references (occurring from left to right).
Address (in decimal): 064 032 064 000 112 064 128 048 240 000 read/write: r r r r w w r r r w
Assume that cache starts empty

## Slide 6: You should complete the answer
Block Addr. | 4 | 2 | 4 | 0 | 7 | 4 | 8 |  |  | 
R/W | R | R | R | R | W | W | R | R | R | W
Set# | 0 | 2 | 0 | 0 | 3 | 0 |  |  |  | 
Tag | 1 | 0 | 1 | 0 | 1 | 1 |  |  |  | 
H/M | M | M | H | M |  |  |  |  |  | 
Writeback? | N | N |  |  |  |  |  |  |  | 
16 byte blocks, 4 LSB byte offset
064 032 064 000 112 064 128 048 240 000
There are 4 sets with 2 blocks each
V D Tag Data
V D Tag Data

## Slide 7: Reducing Miss Rate
Enlarge cache
If cache size is fixed
  Increase associativity and/or line size (does this always work?)
2
5
6
4
0
%
3
5
%
3
0
%
2
5
%
2
0
%
1
5
%
1
0
%
5
%
0
%
M
i
s
s
r
a
t
e
6
4
1
6
4
B
l
o
c
k
s
i
z
e
(
b
y
t
e
s
)
1
K
B
8
K
B
1
6
K
B
6
4
K
B
2
5
6
K
B
Increasing cache pollution

## Slide 8: Instruction and Data Caches

## Slide 9: Why Do We Do This?
Bandwidth: lets us access instructions and data in parallel
Most programs don’t modify their instructions
I-Cache can be simpler than D-Cache, since instruction references are never writes
Instruction stream has high locality of reference, can get higher hit rates with small cache
  Data references never interfere with instruction references

## Slide 10: Cache Performance Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Miss penalty = 100 cycles
  Base CPI (ideal cache) = 2
  Load & stores are 36% of instructions
What is the actual CPI?

## Slide 11: 3-Level Cache Organization
 | Intel Nehalem | AMD Opteron X4
L1 caches (per core) | L1 I-cache: 32KB, 64-byte blocks, 4-way, approx LRU replacement, hit time n/a L1 D-cache: 32KB, 64-byte blocks, 8-way, approx LRU replacement, write-back/allocate, hit time n/a | L1 I-cache: 32KB, 64-byte blocks, 2-way, LRU replacement, hit time 3 cycles L1 D-cache: 32KB, 64-byte blocks, 2-way, LRU replacement, write-back/allocate, hit time 9 cycles
L2 unified cache (per core) | 256KB, 64-byte blocks, 8-way, approx LRU replacement, write-back/allocate, hit time n/a | 512KB, 64-byte blocks, 16-way, approx LRU replacement, write-back/allocate, hit time n/a
L3 unified cache (shared) | 8MB, 64-byte blocks, 16-way, replacement n/a, write-back/allocate, hit time n/a | 2MB, 64-byte blocks, 32-way, replace block shared by fewest cores, write-back/allocate, hit time 32 cycles
n/a: data not available |  | 

## Slide 12: Microarchitecture of Cache Memories
Tag
Set
Offset
Hit?
Address
Hit?
Tag Array
Data Array

## Slide 13: Why This Organization?
Allows tag array to be faster than data array
  Tag array is smaller
Don’t really need output of data array until hit/miss detection complete
Overlap some of data array access time with hit/miss detection
Also integrates well with virtual memory, as we’ll see

## Slide 14: Virtual Memory
Virtual memory – separation of logical memory from physical memory.
  Only a part of the program needs to be in memory for execution. Hence, logical address space can be much larger than physical address space.
  Allows address spaces to be shared by several processes (or threads).
  Allows more efficient process creation.
Virtual memory can be implemented via:
  Demand paging
  Demand segmentation
Main memory is like a cache to the hard disc!

## Slide 15: Virtual Address
The concept of a virtual (or logical) address space that is bound to a separate physical address space is central to memory management
  Virtual address: generated by the CPU
  Physical address: seen by the memory
Virtual and physical addresses are the same in compile-time and load-time address-binding schemes; virtual and physical addresses differ in execution-time address-binding schemes

## Slide 16: Advantages of Virtual Memory
Translation:
  Program can be given consistent view of memory, even though physical memory is scrambled
  Only the most important part of program (“Working Set”) must be in physical memory
  Contiguous structures (like stacks) use only as much physical memory as necessary yet grow later

## Slide 17: Advantages of Virtual Memory
Protection:
  Different threads (or processes) protected from each other.
  Different pages can be given special behavior
    (Read Only, Invisible to user programs, etc).
  Kernel data protected from User programs
  Very important for protection from malicious programs => Far more “viruses” under Microsoft Windows
Sharing:
  Can map same physical page to multiple users (“Shared memory”)

## Slide 18: Use of Virtual Memory
stack
Shared Libs
heap
Static data
code
stack
Shared Libs
heap
Static data
code
Shared
page
Process A
Process B

## Slide 19: Virtual vs. Physical Address Space
A
B
C
D
0
4k
8k
12k
Virtual
Address
C
A
B
0
4k
8k
12k
16k
20k
24k
28k
D
Physical
Address
Virtual
Memory
Main
Memory
Disk
.
.
.
.
.
.
.
4G

## Slide 20: Mapping Virtual to Physical Address
Virtual Page Number
Page Offset
Page Offset
Physical Page Number
Translation
31 30 29 28 27 .………………….12 11 10
29 28 27 .………………….12 11 10
9 8 ……..……. 3 2 1 0
Virtual Address
Physical Address
9 8 ……..……. 3 2 1 0
1KB page size

## Slide 21: Details
The page size is 210 = 1KB
The number of physical pages allowed in memory is 220 (1M pages) - 1GB
VM address space is 4GB
So, it is possible for a virtual page to be absent from main memory and not be mapped to a physical address
  The page resides on disk
Physical pages can be shared by having two virtual addresses point to the same physical address
  Allow two different programs to share data or code

## Slide 22: Design considerations
Main memory is about 100,000× faster than disk
  Pages should be large enough to try to amortize the high access time
    4KB to 16MB in real systems
  Reduce page fault rate!
    Allow fully associative placement of pages in memory
  Page faults can be handled in software
    Can use clever algorithms for choosing how to place pages
  Write-through will not work well for VM
    Use write-back

## Slide 23: Question
How to search the fully associative pages?
  A full search is impractical
  Use a table, page table, that indexes the memory
Page table
  The page table is indexed with the page number from the virtual address to find the corresponding physical page number
  To indicate the location of the page table, the page table register points to the start of the page table
  Each program has its own page table
    Provide protection of one program from another

## Slide 24: Translation w/ Single-Level Page Table
PTBR page table base register
PTE page table entry
VPN virtual page number
PPN physical page number

## Slide 25: Page table
Page table drawing
The page table has an entry for every virtual page
Size of page table in the example

## Slide 26: Page Table Structure Examples
One-to-one mapping, space?
  Large pages  Internal fragmentation (similar to having large line sizes in caches)
  Small pages  Page table size issues
Example:
64 bit address space, 4 KB pages (12 bits), 512 MB (29 bits) RAM
Number of pages = 264/212 = 252
(The page table has as many entrees)
Each entry is ~4 bytes, the size of the Page table is 254 Bytes = 16 Petabytes!
Can’t fit the page table in the 512 MB RAM!

## Slide 27: TLB – a Cache for Page Table Entries
VPN
Offset
TLB
V
D
VPN
PPN
Hit?
PPN
Offset
Yes
No
Use Page Table
Virtual Address
Physical Address

## Slide 28: Typical values for a TLB
TLB size: 16-512 entries
Block size: 1-2 page table entries (4-8 bytes each)
Hit time: 0.5-1 clock cycle
Miss penalty: 10-100 clock cycles
Miss rate: 0.01-1%

## Slide 29: Caches and Virtual Memory
Do we send virtual or physical addresses to the cache?
  Virtual  faster, because don’t have to translate
    Issue: Different programs can reference the same virtual address, either creates security/correctness hole or requires flushing the cache every time you context switch
  Physical  slower, but no security issue
Actually, there are four possibilities
  VIVT: Virtually-indexed Virtually-tagged Cache
  PIPT: Physically-indexed Physically-tagged Cache
  VIPT: Virtually-indexed Physically-tagged Cache
  PIVT: Physically-indexed Virtually-tagged Cache

## Slide 30: Virtually Indexed, Virtually Tagged
Fast cache access
  Only require address translation upon miss
Issues
  Homonym
    Same VA maps to different PAs upon context switch
  Synonym (also a problem in VIPT)
    Different VAs map to the same PA when data is shared by multiple processes
TLB
Processor
Core
VIVT
Cache
Main Memory
VA
hit
miss
cache line return