## Slide 1: Cache/VM interaction

## Slide 2: Microarchitecture of Cache Memories
Tag
Set
Offset
Hit?
Address
Hit?
Tag Array
Data Array

## Slide 3: Why This Organization?
Allows tag array to be faster than data array
  Tag array is smaller
Don’t really need output of data array until hit/miss detection complete
Overlap some of data array access time with hit/miss detection
Also integrates well with virtual memory, as we’ll see

## Slide 4: TLB – a Cache for Page Table Entries
VPN
Offset
TLB
V
D
VPN
PPN
Hit?
PPN
Offset
Yes
No
Use Page Table
Virtual Address
Physical Address

## Slide 5: Typical values for a TLB
TLB size: 16-512 entries
Block size: 1-2 page table entries (4-8 bytes each)
Hit time: 0.5-1 clock cycle
Miss penalty: 10-100 clock cycles
Miss rate: 0.01-1%

## Slide 6: Caches and Virtual Memory
Do we send virtual or physical addresses to the cache?
  Virtual  faster, because don’t have to translate
    Issue: Different programs can reference the same virtual address, either creates security/correctness hole or requires flushing the cache every time you context switch
  Physical  slower, but no security issue
Actually, there are four possibilities
  VIVT: Virtually-indexed Virtually-tagged Cache
  PIPT: Physically-indexed Physically-tagged Cache
  VIPT: Virtually-indexed Physically-tagged Cache
  PIVT: Physically-indexed Virtually-tagged Cache

## Slide 7: Virtually Indexed, Virtually Tagged
Fast cache access
  Only require address translation upon miss
Issues
  Homonym
    Same VA maps to different PAs upon context switch
  Synonym (also a problem in VIPT)
    Different VAs map to the same PA when data is shared by multiple processes
TLB
Processor
Core
VIVT
Cache
Main Memory
VA
hit
miss
cache line return

## Slide 8: Physically-Indexed Physically-Tagged
Slower, always translate address before accessing memory
Simpler for data coherence
TLB
Processor
Core
PIPT
Cache
Main Memory
VA
hit
miss
cache line return
PA

## Slide 9: Virtually-Indexed Physically-Tagged
Gain benefit of a VIVT and PIPT
  Very common in commercial processors
  Parallel Access to TLB and VIPT cache
Issues
  Synonym as VIVT; no homonym
TLB
Processor
Core
VIPT
Cache
Main Memory
VA
hit
miss
cache line return
PA

## Slide 10: Deal w/ Synonym in VIPT Cache
VPN A
process a
VPN B
process b
point to the same
location within a page
tag array
data array
index
index
VPN A != VPN B
how to eliminate duplication?
make cache index a == index b ?

## Slide 11: Synonym in VIPT Cache
if two VPNs do not differ in a then there is no synonym problem, since they will be indexed to the same set of a VIPT cache
imply # of sets cannot be too big
max number of sets = page size / cache line size
  ex: 4KB page, 32B line, max set = 128
a complicated solution in MIPS R10000
VPN
page offset
cache tag
set index
line offset
a

## Slide 12: R10000’s Solution to Synonym
32KB 2-Way virtually-indexed L1
direct-mapped physical L2
  L2 is Inclusive of L1
  VPN[1:0] is appended to the “tag” of L2
given two virtual addresses VA1 and VA2 that differs in VPN[1:0] and both map to the same physical address PA
  suppose VA1 is accessed first so blocks are allocated in L1&L2
  what happens when VA2 is referenced?
    1 VA2 indexes to a different block in L1 and misses
    2 VA2 translates to PA and goes to the same block as VA1 in L2
    3. tag comparison fails (since VA1[1:0]VA2[1:0])
    4. treated just like as a L2 conflict miss  VA1’s entry in L1 is ejected (or dirty-written back if needed) due to inclusion policy
VPN 12 bit
10 bit 4-bit
a= VPN[1:0] stored as part of L2 cache Tag

## Slide 13: Deal w/ Synonym in MIPS R10000
L2 PIPT
cache
a1
phy. tag
data
index
a1
page offset
VA1
index
a2
page offset
VA2
1
0
TLB
miss
physical index ||
a2
a2 !=a1
L1 VIPT cache

## Slide 14: Deal w/ Synonym in MIPS R10000
L2 PIPT
cache
a2
phy. tag
data
index
a1
page offset
VA1
index
a2
page offset
VA2
0
1
TLB
data return
only one copy is
present in L1
L1 VIPT cache

## Slide 15
V
a
l
i
d
T
a
g
D
a
t
a
P
a
g
e
o
f
f
s
e
t
P
a
g
e
o
f
f
s
e
t
V
i
r
t
u
a
l
p
a
g
e
n
u
m
b
e
r
P
h
y
s
i
c
a
l
p
a
g
e
n
u
m
b
e
r
V
a
l
i
d
1
2
2
0
2
0
1
6
1
4
C
a
c
h
e
i
n
d
e
x
3
2
D
a
t
a
C
a
c
h
e
h
i
t
2
B
y
t
e
o
f
f
s
e
t
D
i
r
t
y
T
a
g
T
L
B
h
i
t
P
h
y
s
i
c
a
l
p
a
g
e
n
u
m
b
e
r
P
h
y
s
i
c
a
l
a
d
d
r
e
s
s
t
a
g
3
1
3
0
2
9
1
5
1
4
1
3
1
2
1
1
1
0
9
8
3
2
1
0
DECStation 3100/ MIPS R2000
Virtual Address
TLB
Cache
64 entries, fully associative
Physical Address
16K entries, direct mapped

## Slide 16: Putting it all together

## Slide 17: Another example
Virtual Memory Address width:32 bits Page size:1 K bytes Single level page table Physical Memory 32 bit physical address space Cache Block size:16 bytes Cache size:1 K bytes Associativity:Direct mapped Translation Lookaside Buffer Number of translations:64 Associativity:Direct mapped

## Slide 18: 2-Level TLB Organization
 | Intel Nehalem | AMD Opteron X4
Virtual addr | 48 bits | 48 bits
Physical addr | 44 bits | 48 bits
Page size | 4KB, 2/4MB | 4KB, 2/4MB
L1 TLB (per core) | L1 I-TLB: 128 entries for small pages, 7 per thread (2×) for large pages L1 D-TLB: 64 entries for small pages, 32 for large pages Both 4-way, LRU replacement | L1 I-TLB: 48 entries L1 D-TLB: 48 entries Both fully associative, LRU replacement
L2 TLB (per core) | Single L2 TLB: 512 entries 4-way, LRU replacement | L2 I-TLB: 512 entries L2 D-TLB: 512 entries Both 4-way, round-robin LRU
TLB misses | Handled in hardware | Handled in hardware

## Slide 19: 3-Level Cache Organization
 | Intel Nehalem | AMD Opteron X4
L1 caches (per core) | L1 I-cache: 32KB, 64-byte blocks, 4-way, approx LRU replacement, hit time n/a L1 D-cache: 32KB, 64-byte blocks, 8-way, approx LRU replacement, write-back/allocate, hit time n/a | L1 I-cache: 32KB, 64-byte blocks, 2-way, LRU replacement, hit time 3 cycles L1 D-cache: 32KB, 64-byte blocks, 2-way, LRU replacement, write-back/allocate, hit time 9 cycles
L2 unified cache (per core) | 256KB, 64-byte blocks, 8-way, approx LRU replacement, write-back/allocate, hit time n/a | 512KB, 64-byte blocks, 16-way, approx LRU replacement, write-back/allocate, hit time n/a
L3 unified cache (shared) | 8MB, 64-byte blocks, 16-way, replacement n/a, write-back/allocate, hit time n/a | 2MB, 64-byte blocks, 32-way, replace block shared by fewest cores, write-back/allocate, hit time 32 cycles
n/a: data not available |  |