## Slide 1: Pipelining

## Slide 2: 2-Level TLB Organization
 | Intel Nehalem | AMD Opteron X4
Virtual addr | 48 bits | 48 bits
Physical addr | 44 bits | 48 bits
Page size | 4KB, 2/4MB | 4KB, 2/4MB
L1 TLB (per core) | L1 I-TLB: 128 entries for small pages, 7 per thread (2×) for large pages L1 D-TLB: 64 entries for small pages, 32 for large pages Both 4-way, LRU replacement | L1 I-TLB: 48 entries L1 D-TLB: 48 entries Both fully associative, LRU replacement
L2 TLB (per core) | Single L2 TLB: 512 entries 4-way, LRU replacement | L2 I-TLB: 512 entries L2 D-TLB: 512 entries Both 4-way, round-robin LRU
TLB misses | Handled in hardware | Handled in hardware

## Slide 3: 3-Level Cache Organization
 | Intel Nehalem | AMD Opteron X4
L1 caches (per core) | L1 I-cache: 32KB, 64-byte blocks, 4-way, approx LRU replacement, hit time n/a L1 D-cache: 32KB, 64-byte blocks, 8-way, approx LRU replacement, write-back/allocate, hit time n/a | L1 I-cache: 32KB, 64-byte blocks, 2-way, LRU replacement, hit time 3 cycles L1 D-cache: 32KB, 64-byte blocks, 2-way, LRU replacement, write-back/allocate, hit time 9 cycles
L2 unified cache (per core) | 256KB, 64-byte blocks, 8-way, approx LRU replacement, write-back/allocate, hit time n/a | 512KB, 64-byte blocks, 16-way, approx LRU replacement, write-back/allocate, hit time n/a
L3 unified cache (shared) | 8MB, 64-byte blocks, 16-way, replacement n/a, write-back/allocate, hit time n/a | 2MB, 64-byte blocks, 32-way, replace block shared by fewest cores, write-back/allocate, hit time 32 cycles
n/a: data not available |  | 

## Slide 4: Pipelining: Natural Phenomenon
Laundry Example:
  Ann, Brian, Ming, Ashok each has one load of clothes to wash, dry, and fold
  Washer takes 30 minutes
  Dryer takes 40 minutes
  “Folder” takes 20 minutes
A
B
C
D

## Slide 5: Sequential Laundry
Sequential laundry takes 6 hours for 4 loads
A
B
C
D
30
40
20
30
40
20
30
40
20
30
40
20
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time

## Slide 6: Pipelined Laundry -- Start work ASAP
A
B
C
D
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20

## Slide 7
Pipelined laundry takes 3.5 hours for 4 loads
Total time to wash longer or shorter?
Total wait time longer or shorter?
What’s the utilization of the dryer?
What’s the utilization of the folding table?
What determines the throughput?
A
B
C
D
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20
Pipelined Laundry -- Start work ASAP

## Slide 8: Pipelining Lessons
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Pipeline rate limited by slowest pipeline stage
Multiple tasks operating simultaneously
Potential speedup = Number of pipe stages
Unbalanced lengths of pipe stages reduces speedup
Time to “fill” pipeline and time to “drain” it reduces speedup
A
B
C
D
6 PM
7
8
9
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20

## Slide 9: Review -- Instruction Latencies
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
Single-Cycle CPU
Multiple Cycle CPU
Ifetch
Reg/Dec
Exec
Wr
Add

## Slide 10: Instruction Latencies and Throughput
Single-Cycle CPU
Multiple Cycle CPU
Pipelined CPU
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
Ifetch
Reg/Dec
Exec
Mem
Wr
Load

## Slide 11: Execution in a Pipelined Datapath
IM
Reg
ALU
DM
Reg
IM
Reg
ALU
DM
Reg
IM
Reg
ALU
DM
Reg
IM
Reg
ALU
DM
Reg
IM
Reg
ALU
DM
Reg
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8
CC9
lw
lw
lw
lw
lw
steady
state
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB

## Slide 12: Speed up calculation
Assuming the stages are perfectly balanced
Time between instructions (pipelined) =
Time between instructions (nonpipelined) /
Number of pipe stages

## Slide 13: Pipelining Example 1
A processor that takes 5ns to execute an instruction is pipelined into 5 equal stages. The latch between each stage has a delay of 0.25 ns.
  What is the minimum clock cycle time of the pipelined processor?
  What is the maximum speedup that can be achieved by this pipelined processor? (compared to the original processor)
  Can we have much deeper pipelining?

## Slide 14: Pipelining Example 2
A. A non-pipelined processor takes 5ns to execute an instruction. If I want the processor to be clockable at 2GHz, how many stages should I pipeline this processor into if each latch has a 0.25ns delay?
B. How many stages if I want to clock the processor at 5GHz?
C. What is the maximum speedup that can be achieved by the pipelined processor running at 2GHz? (Compared to the original single cycle processor)
D. What is the average latency of an instruction (belonging to a 23-instruction program) for the pipelined processor?
E. What is the best case speedup and what is the worst case slowdown?

## Slide 15: Hazards
Situations that prevent starting the next instruction in the next cycle
Structure hazards
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Deciding on control action depends on previous instruction

## Slide 16: Data Hazards
When a result is needed in the pipeline before it is available, a “data hazard” occurs.
IM
Reg
ALU
DM
Reg
IM
Reg
ALU
DM
IM
Reg
ALU
DM
Reg
IM
Reg
ALU
DM
Reg
IM
Reg
ALU
DM
Reg
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8
sub $2, $1, $3
and $12, $2, $5
or $13, $6, $2
add $14, $2, $2
sw $15, 100($2)
R2 Available
R2 Needed
Time: 1 2 3 4 5 6 7 8
No hazard here
Hazards! Value in register
hasn’t been updated

## Slide 17: The Pipeline in Execution
add $10, $1, $2
add $11, $8, $7
lw $8, 52($3)
  add $3, $10, $11
Write Back
16
50
16
14
66
And this should be value
from memory (which hasn’t
even been loaded yet).
This should
have been “92”
42

## Slide 18: Branch Hazards
IM
Reg
ALU
DM
Reg
IM
Reg
ALU
DM
IM
Reg
ALU
DM
Reg
IM
Reg
ALU
DM
Reg
IM
Reg
ALU
DM
Reg
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8
beq $2, $1, here
here: lw ...
sub ...
lw ...
add ...
These instructions
shouldn’t be executed!
Finally, the right instruction

## Slide 19: Dealing With Data Hazards
Transparent register file eliminates one hazard.
  Use latches rather than flip-flops in Reg file
    First half-cycle of cycle 5: register 2 loaded
    Second half-cycle: new value is read into pipeline state
IM
Reg
ALU
DM
Reg
IM
Reg
ALU
DM
Reg
IM
Reg
ALU
DM
Reg
IM
Reg
ALU
DM
Reg
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8
sub $2, $1, $3
and $12, $6, $5
or $13, $6, $8
add $14, $2, $2
R2 Available

## Slide 20: Dealing with Data Hazards in Software
IM
Reg
ALU
DM
Reg
IM
Reg
ALU
DM
Reg
IM
Reg
ALU
DM
Reg
IM
Reg
ALU
DM
Reg
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8
sub $2, $1, $3
nop
add $12, $2, $5
nop
Insert enough no-ops (or other instructions that don’t
use register 2) so that data hazard doesn’t occur,

## Slide 21: Handling Data Hazards in Hardware Stall the pipeline
sub $2, $1, $3
and $12, $2, $5
or $13, $6, $2
add $14, $2, $2
IM
Reg
DM
Reg
IM
Reg
DM
IM
Reg
DM
Reg
IM
Reg
DM
Reg
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8
Bubble
Bubble

## Slide 22: Pipeline Stalls
To insure proper pipeline execution in light of register dependences, we must:
  Detect the hazard
  Stall the pipeline
    prevent the IF and ID stages from making progress
    insert“no-ops” into later stages