## Slide 1: Pipelining

## Slide 2: Branch Hazards
IM
Reg
ALU
DM
Reg
IM
Reg
ALU
DM
IM
Reg
ALU
DM
Reg
IM
Reg
ALU
DM
Reg
IM
Reg
ALU
DM
Reg
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8
beq $2, $1, here
here: lw ...
sub ...
lw ...
add ...
These instructions
shouldn’t be executed!
Finally, the right instruction

## Slide 3: Stalling for Branch Hazards
beq $4, $0, there
and $12, $2, $5
or ...
add ...
sw ...
IM
Reg
DM
Reg
IM
Reg
IM
Reg
DM
IM
Reg
DM
Reg
IM
Reg
DM
Reg
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8
Bubble
Bubble
Bubble

## Slide 4: Reducing the Branch Delay
it’s easy to reduce stall to 2-cycles

## Slide 5: Reducing the Branch Delay
it’s easy to reduce stall to 2-cycles

## Slide 6: Stalling for Branch Hazards
beq $4, $0, there
and $12, $2, $5
or ...
add ...
sw ...
IM
Reg
DM
Reg
IM
Reg
IM
Reg
DM
IM
Reg
DM
Reg
IM
Reg
DM
Reg
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8
Bubble
Bubble

## Slide 7: One-cycle branch misprediction penalty
Target computation & equality check in ID phase.
  This figure also shows flushing hardware (will talk about flushing later).

## Slide 8: Stalling for Branch Hazards
beq $4, $0, there
and $12, $2, $5
or ...
add ...
sw ...
IM
Reg
DM
Reg
IM
Reg
IM
Reg
DM
IM
Reg
DM
Reg
IM
Reg
DM
Reg
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8
Bubble

## Slide 9: Data Hazards for Branches
If a comparison register is a destination of 2nd or 3rd preceding ALU instruction
…
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
add $4, $5, $6
add $1, $2, $3
beq $1, $4, target
Can resolve using forwarding

## Slide 10: Data Hazards for Branches
If a comparison register is a destination of preceding ALU instruction or 2nd preceding load instruction
  Need 1 stall cycle
beq stalled
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
ID
EX
MEM
WB
add $4, $5, $6
lw $1, addr
beq $1, $4, target

## Slide 11: Data Hazards for Branches
If a comparison register is a destination of immediately preceding load instruction
  Need 2 stall cycles
beq stalled
IF
ID
EX
MEM
WB
IF
ID
ID
ID
EX
MEM
WB
beq stalled
lw $1, addr
beq $1, $0, target

## Slide 12: Stalling for Branch Hazards
beq $4, $0, there
and $12, $2, $5
or ...
add ...
sw ...
IM
Reg
DM
Reg
IM
Reg
IM
Reg
DM
IM
Reg
DM
Reg
IM
Reg
DM
Reg
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8
Bubble

## Slide 13: Types of Branches

## Slide 14: Branch Prediction
Predicting the outcome of a branch
  Direction:
    Taken / Not Taken
    Direction predictors
  Target Address
    PC+offset (Taken)/ PC+4 (Not Taken)
    Target address predictors
      Branch Target Address Cache (BTAC) or Branch Target Buffer (BTB)

## Slide 15: Branch Prediction Strategies
Static
  Decided before runtime
  Examples:
    Always-Not Taken
    Always-Taken
    Backwards Taken, Forward Not Taken (BTFNT)
    Profile-driven prediction
Dynamic
  Prediction decisions may change during the execution of the program

## Slide 16: What happens when a branch is predicted?
On mispredict:
  No speculative state may commit
    Squash instructions in the pipeline
    Must not allow stores in the pipeline to occur
      Cannot allow stores which would not have happened to commit
    Need to handle exceptions appropriately

## Slide 17: Bimodal Prediction
Table of 2-bit saturating counters
  Predict the most common direction
  Advantages: simple, cheap, “good”
  accuracy

## Slide 18: 2-Bit Predictor
Only change prediction on two successive mispredictions

## Slide 19: Correlation
B1: if (x)
...
B2: if (y)
...
z=x&&y
B3: if (z)
...
B3 can be predicted with 100% accuracy based on the outcomes of B1 and B2

## Slide 20: Two-Level Prediction
Uses two levels of information to make a direction prediction
  Branch History Table (BHT)
  PHT
Captures patterned behavior of branches
  Groups of branches are correlated
  Particular branches have particular behavior

## Slide 21: Two-level Predictor Classification
Yeh and Patt 3-letter naming scheme
  Type of history collected
    G (global), P (per branch), S (per set)
    M (merge?)
      added by Skadron, Martonosi, Clark
  PHT type
    A (adaptive), S (static)
  PHT organization
    g (global), p (per branch), s (per set)

## Slide 22: Some Two-level Predictors
GAs Predictor
PAs Predictor

## Slide 23: Hybrid Prediction
Two or more predictor components combined
Different
branches benefit
from different types
of history

## Slide 24: Special Branches
Procedure calls and returns
  Calls are always taken
  Return address almost always known
Return Address Stack (RAS)
  On a procedure call, push the address of the instruction after the call onto the stack

## Slide 25: Issues Affecting Accurate Branch Prediction
Aliasing
  More than one branch may use the same BHT/PHT entry
    Constructive
      Prediction that would have been incorrect, predicted correctly
    Destructive
      Prediction that would have been correct, predicted incorrectly
    Neutral
      No change in the accuracy

## Slide 26: More Issues
Training time
  Need to see enough branches to uncover pattern
  Need enough time to reach steady state
“Wrong” history
  Incorrect type of history for the branch
Stale state
  Predictor is updated after information is needed
Operating system context switches
  More aliasing caused by branches in different programs

## Slide 27: “Real” Branch Predictors
Alpha 21264
  8-stage pipeline, mispredict penalty 7 cycles
  64 KB, 2-way instruction cache with line and way prediction bits (Fetch)
    Each 4-instruction fetch block contains a prediction for the next fetch block
  Hybrid predictor (Fetch)
    12-bit GAg (4K-entry PHT, 2 bit counters)
    10-bit PAg (1K-entry BHT, 1K-entry PHT, 3-bit counters)

## Slide 28: UltraSPARC-III
14-stage pipeline, bpred accessed in instruction fetch stages 2-3
16K-entry 2-bit counter Gshare predictor
  Bimodal predictor which XOR’s PC bits with global history register (except 3 lower order bits) to reduce aliasing
Miss queue
  Halves mispredict penalty by providing instructions for immediate use

## Slide 29: Pentium III
Dynamic branch prediction
  512-entry BTB predicts direction and target, 4-bit history used with PC to derive direction
Static branch predictor for BTB misses
Return Address Stack (RAS), 4/8 entries
Branch Penalties:
  Not Taken: no penalty
  Correctly predicted taken: 1 cycle
  Mispredicted: at least 9 cycles, as many as 26, average 10-15 cycles

## Slide 30: AMD Athlon K7
10-stage integer, 15-stage fp pipeline, predictor accessed in fetch
2K-entry bimodal, 2K-entry BTAC
12-entry RAS
Branch Penalties:
  Correct Predict Taken: 1 cycle
  Mispredict penalty: at least 10 cycles

## Slide 31: Branch Target Buffers
predict the location of branches in the instruction stream
predict the destination of branches

## Slide 32: BTB Operation
use PC (all bits) for lookup
  match implies this is a branch
if match and predict bits => taken, set PC to predicted PC
if branch predict wrong, must recover (same as branch hazards we’ve already seen)
if decode indicates branch when no BTB match, two choices:
  look up prediction now and act on it
  just predict not taken
when branch resolved, update BTB (at least prediction bits, maybe more)

## Slide 33: BTB Performance
Two things that can go wrong
  didn’t predict the branch (misfetch)
  mispredicted a branch (mispredict)
Suppose BTB hit rate of 85% and predict accuracy of 90%, misfetch penalty of 2 cycles and mispredict penalty of 10 cycles, what is average branch penalty?
Can use both BTB and branch predictor
  have no prediction bits in BTB (why is that a good idea?)
  presence of PC in BTB indicates a lookup in branch predictor to predict whether the branch will go to destination address in BTB.

## Slide 34: What about indirect jumps/returns?
Branch predictor does really well with conditional jumps
BTB does really well with unconditional jumps (jump, jal, etc.)
Indirect jumps often jump to different destinations, even from the same instruction. Indirect jumps most often used for return instructions.
Return easily handled by a stack.
  jal -> push PC+4
  return -> predict jump to address on top of stack, pop stack

## Slide 35: Go through the following document carefully
http://www.cs.utah.edu/~rajeev/cs7810/papers/mcfarling93.pdf

## Slide 36: Next lecture
Instruction-level parallelism
References of the current lecture
  Chapters 4.5, 4.8
  http://www.cs.utah.edu/~rajeev/cs7810/papers/mcfarling93.pdf