## Slide 1: Instruction-level Parallelism

## Slide 2: Tomasulo’s Algorithm
Developed for architecture of IBM 360/91 (1967)
  360/91 system’s goal was to significantly improve performance (especially floating-point) without requiring people to change their code
    Sound familiar?
16MHz
2MB Mem
50X faster
Than SOA

## Slide 3: Tomasulo Organization

## Slide 4: Tomasulo Algorithm
Consider three input instructions
Common Data Bus broadcasts results to all FUs
  RS’s (FU’s), registers, etc. responsible for collecting own data off CDB
Load and Store Queues treated as FUs as well

## Slide 5: Reservation Station Components
Op—Operation to perform in the unit (e.g., + or –)
Qj, Qk—Reservation stations producing source registers
Vj, Vk—Value of Source operands
Rj, Rk—Flags indicating when Vj, Vk are ready
Busy—Indicates reservation station is busy
Register result status—Indicates which functional unit will write each register, if one exists. Blank when no pending instructions that will write that register.
Notes: What you might have thought
1. 4 stages of instruction executino
2.Status of FU: Normal things to keep track of (RAW & structura for busyl):
Fi from instruction format of the mahine (Fi is dest)
Add unit can Add or Sub
Rj, Rk - status of registers (Yes means ready)
Qj,Qk - If a no in Rj, Rk, means waiting for a FU to write result; Qj, Qk means wihch FU waiting for it
3.Status of register result (WAW &WAR)s:
which FU is going to write into registers
Scoreboard on 6600 = size of FU
6.7, 6.8, 6.9, 6.12, 6.13, 6.16, 6.17
FU latencies: Add 2, Mult 10, Div 40 clocks

## Slide 6: Three Stages of Tomasulo Algorithm
1. Issue—get instruction from FP Op Queue
  If reservation station free, the scoreboard issues instr & sends operands (renames registers).
2. Execution—operate on operands (EX)
  When both operands ready then execute; if not ready, watch CDB for result
3. Write result—finish execution (WB)
  Write on Common Data Bus to all waiting units; mark reservation station available.

## Slide 7: Tomasulo Example
ADDD F4, F2, F0
MULD F8, F4, F2
ADDD F6, F8, F6
SUBD F8, F2, F0
ADDD F2, F8, F0
Multiply takes 10 clocks, add/sub take 4

## Slide 8: Tomasulo – cycle 0
ADDD F4, F2, F0
ADDD F4, F2, F0
MULD F8, F4, F2
ADDD F6, F8, F6
SUBD F8, F2, F0
ADDD F2, F8, F0
ADDD F6, F8, F6
MULD F8, F4, F2
ADDD F2, F8, F0
SUBD F8, F2, F0
Instruction Queue
F0
F2
F4
F6
F8
0.0
2.0
4.0
6.0
8.0
FP adders
FP mult’s
1
2
3
1
2
Notes: First instruction
-issue to RS
-read operands
-mark register

## Slide 9: Tomasulo – cycle 1
ADDD F4, F2, F0
MULD F8, F4, F2
ADDD F6, F8, F6
SUBD F8, F2, F0
ADDD F2, F8, F0
ADDD F6, F8, F6
MULD F8, F4, F2
ADDD F2, F8, F0
SUBD F8, F2, F0
Instruction Queue
F0
F2
F4
F6
F8
0.0
2.0
4.0
add1
6.0
8.0
ADDD
2.0
0.0
FP adders
FP mult’s
1
2
3
1
2
Notes: Add will begin execute, Blow up next, because this
One is a little more interesting

## Slide 10: Tomasulo – cycle 2
ADDD F4, F2, F0
MULD F8, F4, F2
ADDD F6, F8, F6
SUBD F8, F2, F0
ADDD F2, F8, F0
ADDD F6, F8, F6
SUBD F8, F2, F0
Instruction Queue
F0
F2
F4
F6
F8
0.0
2.0
4.0
add1
6.0
8.0
mult1
ADDD
2.0
0.0
FP adders
MULD
add1
2.0
FP mult’s
1
2
3
1
2
ADDD F2, F8, F0
MULD add1 - - 2.0 Y
Op Qj Qk Vj Vk Busy

## Slide 11: Tomasulo – cycle 2
ADDD F4, F2, F0
MULD F8, F4, F2
ADDD F6, F8, F6
SUBD F8, F2, F0
ADDD F2, F8, F0
ADDD F6, F8, F6
SUBD F8, F2, F0
Instruction Queue
F0
F2
F4
F6
F8
0.0
2.0
4.0
add1
6.0
8.0
mult1
ADDD
2.0
0.0
FP adders
MULD
add1
2.0
FP mult’s
1
2
3
1
2
ADDD F2, F8, F0

## Slide 12: Tomasulo – cycle 3
ADDD F4, F2, F0
MULD F8, F4, F2
ADDD F6, F8, F6
SUBD F8, F2, F0
ADDD F2, F8, F0
ADDD F2, F8, F0
SUBD F8, F2, F0
Instruction Queue
F0
F2
F4
F6
F8
0.0
2.0
4.0
add1
6.0
add2
8.0
mult1
ADDD
2.0
0.0
ADDD
mult1
6.0
FP adders
MULD
add1
2.0
FP mult’s
1
2
3
1
2

## Slide 13: Tomasulo – cycle 4
ADDD F4, F2, F0
MULD F8, F4, F2
ADDD F6, F8, F6
SUBD F8, F2, F0
ADDD F2, F8, F0
ADDD F2, F8, F0
Instruction Queue
F0
F2
F4
F6
F8
0.0
2.0
4.0
add1
6.0
add2
8.0
add3
ADDD
2.0
0.0
ADDD
mult1
6.0
SUBD
2.0
0.0
FP adders
MULD
add1
2.0
FP mult’s
1
2
3
1
2

## Slide 14: Tomasulo – cycle 5
ADDD F4, F2, F0
MULD F8, F4, F2
ADDD F6, F8, F6
SUBD F8, F2, F0
ADDD F2, F8, F0
ADDD F2, F8, F0
Instruction Queue
F0
F2
F4
F6
F8
0.0
2.0
2.0
-
6.0
add2
8.0
add3
ADDD
2.0
0.0
ADDD
mult1
6.0
SUBD
2.0
0.0
FP adders
MULD
2.0
2.0
FP mult’s
1
2
3
1
2
2.0 (add1 result)

## Slide 15: Tomasulo – cycle 6
ADDD F4, F2, F0
MULD F8, F4, F2
ADDD F6, F8, F6
SUBD F8, F2, F0
ADDD F2, F8, F0
Instruction Queue
F0
F2
F4
F6
F8
0.0
2.0
add1
2.0
-
6.0
add2
8.0
add3
ADDD
add3
0.0
ADDD
mult1
6.0
SUBD
2.0
0.0
FP adders
MULD
2.0
2.0
FP mult’s
1
2
3
1
2

## Slide 16: Tomasulo – cycle 8
ADDD F4, F2, F0
MULD F8, F4, F2
ADDD F6, F8, F6
SUBD F8, F2, F0
ADDD F2, F8, F0
Instruction Queue
F0
F2
F4
F6
F8
0.0
2.0
add1
2.0
-
6.0
add2
2.0
-
ADDD
2.0
0.0
ADDD
mult1
6.0
SUBD
2.0
0.0
FP adders
MULD
2.0
2.0
FP mult’s
1
2
3
1
2
2.0 (add3 result)

## Slide 17: Tomasulo – cycle 9
ADDD F4, F2, F0
MULD F8, F4, F2
ADDD F6, F8, F6
SUBD F8, F2, F0
ADDD F2, F8, F0
Instruction Queue
F0
F2
F4
F6
F8
0.0
2.0
add1
2.0
6.0
add2
2.0
ADDD
2.0
0.0
ADDD
mult1
6.0
FP adders
MULD
2.0
2.0
FP mult’s
1
2
3
1
2
Notes: Skip to cycle 12, where the add will complete

## Slide 18: Tomasulo – cycle 12
ADDD F4, F2, F0
MULD F8, F4, F2
ADDD F6, F8, F6
SUBD F8, F2, F0
ADDD F2, F8, F0
Instruction Queue
F0
F2
F4
F6
F8
0.0
2.0
-
2.0
6.0
add2
2.0
ADDD
2.0
0.0
ADDD
mult1
6.0
FP adders
MULD
2.0
2.0
FP mult’s
1
2
3
1
2
2.0 (add1 result)
Notes: Skip to 15, when the multiply will complete

## Slide 19: Tomasulo – cycle 15
ADDD F4, F2, F0
MULD F8, F4, F2
ADDD F6, F8, F6
SUBD F8, F2, F0
ADDD F2, F8, F0
Instruction Queue
F0
F2
F4
F6
F8
0.0
2.0
-
2.0
6.0
add2
2.0
ADDD
4.0
6.0
FP adders
MULD
2.0
2.0
FP mult’s
1
2
3
1
2
4.0 (mult1 result)

## Slide 20: Tomasulo – cycle 16
ADDD F4, F2, F0
MULD F8, F4, F2
ADDD F6, F8, F6
SUBD F8, F2, F0
ADDD F2, F8, F0
Instruction Queue
F0
F2
F4
F6
F8
0.0
2.0
-
2.0
6.0
add2
2.0
ADDD
4.0
6.0
FP adders
FP mult’s
1
2
3
1
2

## Slide 21: Tomasulo – cycle 19
ADDD F4, F2, F0
MULD F8, F4, F2
ADDD F6, F8, F6
SUBD F8, F2, F0
ADDD F2, F8, F0
Instruction Queue
F0
F2
F4
F6
F8
0.0
2.0
2.0
10.0
-
2.0
ADDD
4.0
6.0
FP adders
FP mult’s
1
2
3
1
2
10.0 (add2 result)

## Slide 22: Tomasulo Summary
Prevents Register as bottleneck
Avoids WAR, WAW hazards
Lasting Contributions
  Dynamic scheduling
  Register renaming (in what way does the register name change?)
  Load/store disambiguation
Notes: Can dispatch multiple insts in 1 cycle, because all
Reading locally

## Slide 23: Limitations
Exceptions/interrupts
  Can’t identify a particular point in the program at which an interrupt/exception occurs
  How do you know where to go back to after an interrupt handler completes?
  OOO completion???
Interaction with pipelined ALUs
  Reservation station couldn’t be released until instruction completes, would need many reservation stations.