## Slide 1: Superscalar Complexity

## Slide 2: View of Superscalar Execution

## Slide 3: Generic Superscalar Processor Models
Fetch
Rename
Wakeup
select
Regfile
FU
FU
bypass
D-cache
execute
commit
Fetch
Rename
ROB
FU
FU
bypass
D-cache
execute
commit
Reg
Wakeup select
Issue queue based
Reservation based
schedule
schedule

## Slide 4: Register Renaming

## Slide 5: Register Renaming
Alpha 21264+, MIPS R10K+, Pentium 4 use explicit register renaming
  Registers are not read until instruction dispatches (begins execution)
  Register renaming ensures no conflicts
R1 PR23
R3 PR17
R4 PR45
R5 PR13
R6 PR20
R7 PR30
…
RAT
DIV R5, R4, R2
ADD R7, R5, R1
SUB R5, R3, R2
LW R7, 1000(R5)
R2 PR2

## Slide 6: Register Renaming
R1 PR23
R3 PR17
R4 PR45
R5 PR13
R6 PR20
R7 PR30
…
RAT
DIV PR37, PR45, PR2
Assume that PR37 is free and allocated to DIV’s destination register R5
PR37
DIV R5, R4, R2
ADD R7, R5, R1
SUB R5, R3, R2
LW R7, 1000(R5)
R2 PR2

## Slide 7: Register Renaming
R1 PR23
R3 PR17
R4 PR45
R5 PR37
R6 PR20
R7 PR30
…
RAT
DIV PR37, PR45, PR2
Assume that PR37 is free and allocated to DIV’s destination register R5
DIV R5, R4, R2
ADD R7, R5, R1
SUB R5, R3, R2
LW R7, 1000(R5)
R2 PR2

## Slide 8: Register Renaming
R1 PR23
R3 PR17
R4 PR45
R5 PR37
R6 PR20
R7 PR30
…
RAT
DIV PR37, PR45, PR2
ADD PR4 , PR37, PR23
Assume that PR4 is free and allocated to ADD’s destination register R7
PR4
DIV R5, R4, R2
ADD R7, R5, R1
SUB R5, R3, R2
LW R7, 1000(R5)
R2 PR2

## Slide 9: Register Renaming
R1 PR23
R3 PR17
R4 PR45
R5 PR37
R6 PR20
R7 PR4
…
RAT
DIV PR37, PR45, PR2
ADD PR4 , PR37, PR23
SUB PR42, PR17, PR2
PR42
DIV R5, R4, R2
ADD R7, R5, R1
SUB R5, R3, R2
LW R7, 1000(R5)
R2 PR2

## Slide 10: Register Renaming
DIV R5, R4, R2
ADD R7, R5, R1
SUB R5, R3, R2
LW R7, 1000(R5)
R2 PR2
R1 PR23
R3 PR17
R4 PR45
R5 PR42
R6 PR20
R7 PR4
…
RAT
DIV PR37, PR45, PR2
ADD PR4 , PR37, PR23
SUB PR42, PR17, PR2
LW PR19, 1000(PR42)
PR19

## Slide 11: MIPS R10000, Recycling Physical Registers
I1:DIV R5, R4, R2
I2:ADD R7, R5, R1
I3:SUB R5, R3, R2
I4:LW R7, 1000(R5)
R2 PR2
R1 PR23
R3 PR17
R4 PR45
R5 PR13
R6 PR20
R7 PR30
…
Register Map
PR37, PR4, PR42, PR19, …
Instruction Queue
(Reservation Stations)
…
Active List
Register Free List
Head
Tail
Commit

## Slide 12: MIPS R10000, Recycling Physical Registers
I1:DIV R5, R4, R2
I2:ADD R7, R5, R1
I3:SUB R5, R3, R2
I4:LW R7, 1000(R5)
R2 PR2
R1 PR23
R3 PR17
R4 PR45
R5 PR13
R6 PR20
R7 PR30
…
Register Map
PR37, PR4, PR42, PR19, …
Instruction Queue
(Reservation Stations)
…
Active List
Register Free List
Head
Tail
Commit

## Slide 13: MIPS R10000, Recycling Physical Registers
I1:DIV R5, R4, R2
I2:ADD R7, R5, R1
I3:SUB R5, R3, R2
I4:LW R7, 1000(R5)
R2 PR2
R1 PR23
R3 PR17
R4 PR45
R5 PR37
R6 PR20
R7 PR30
…
Register Map
PR4, PR42, PR19, …
Instruction Queue
(Reservation Stations)
…
Active List
Register Free List
Head
Commit
DIV PR37,
PR45, PR2
I1: PR13
Tail

## Slide 14: MIPS R10000, Recycling Physical Registers
I1:DIV R5, R4, R2
I2:ADD R7, R5, R1
I3:SUB R5, R3, R2
I4:LW R7, 1000(R5)
R2 PR2
R1 PR23
R3 PR17
R4 PR45
R5 PR37
R6 PR20
…
Register Map
PR42, PR19, …
DIV 2,45:37
Instruction Queue
(Reservation Stations)
…
Active List
I2: PR30
I1: PR13
Register Free List
Head
Commit
ADD PR4,
PR37, PR23
R7 PR4
Tail

## Slide 15: MIPS R10000, Recycling Physical Registers
I1:DIV R5, R4, R2
I2:ADD R7, R5, R1
I3:SUB R5, R3, R2
I4:LW R7, 1000(R5)
R2 PR2
R1 PR23
R3 PR17
R4 PR45
R5 PR42
R6 PR20
…
Register Map
PR19, …
DIV 2,45:37
Instruction Queue
(Reservation Stations)
…
Active List
ADD 37,23: 4
I3: PR37
I2: PR30
I1: PR13
Register Free List
Head
Commit
SUB PR42,
PR17, PR2
R7 PR4
Tail

## Slide 16: MIPS R10000, Recycling Physical Registers
I1:DIV R5, R4, R2
I2:ADD R7, R5, R1
I3:SUB R5, R3, R2
I4:LW R7, 1000(R5)
R2 PR2
R1 PR23
R7 PR19
R4 PR45
R5 PR42
R6 PR20
…
Register Map
…
Instruction Queue
(Reservation Stations)
…
Active List
SUB 17, 2:42
I4: PR4
I3: PR37
I2: PR30
I1: PR13
Register Free List
Head
Commit
LW PR19,
1000(PR2)
Tail
R3 PR17
DIV 2,45:37
ADD 37,23: 4

## Slide 17: MIPS R10000, Recycling Physical Registers
I1:DIV R5, R4, R2
I2:ADD R7, R5, R1
I3:SUB R5, R3, R2
I4:LW R7, 1000(R5)
R2 PR2
R1 PR23
R7 PR19
R4 PR45
R5 PR42
R6 PR20
…
Register Map
…
Instruction Queue
(Reservation Stations)
…
Active List
SUB 17, 2:42
LW 42 :19
I4: PR4
I3: PR37
I2: PR30
I1: PR13
Register Free List
Head
Commit
Tail
R3 PR17
DIV 2,45:37
ADD 37,23: 4

## Slide 18: MIPS R10000, Recycling Physical Registers
I1:DIV R5, R4, R2
I2:ADD R7, R5, R1
I3:SUB R5, R3, R2
I4:LW R7, 1000(R5)
R2 PR2
R1 PR23
R7 PR19
R4 PR45
R5 PR42
R6 PR20
…
Register Map
…
Instruction Queue
(Reservation Stations)
…
Active List
I4: PR4
I3: PR37
I2: PR30
I1: PR13
Register Free List
Head
Commit
Tail
R3 PR17
ADD 37,23: 4
I4, producing register 19, completes, broadcasts a completion signal to IQ

## Slide 19: MIPS R10000, Recycling Physical Registers
I1:DIV R5, R4, R2
I2:ADD R7, R5, R1
I3:SUB R5, R3, R2
I4:LW R7, 1000(R5)
R2 PR2
R1 PR23
R7 PR19
R4 PR45
R5 PR42
R6 PR20
…
Register Map
…
Instruction Queue
(Reservation Stations)
…
Active List
I4: PR4
I3: PR37
I2: PR30
I1: PR13
Register Free List
Head
Commit
Tail
R3 PR17
ADD 37,23: 4
I1, producing register 37, completes, broadcasts a completion signal to IQ

## Slide 20: MIPS R10000, Recycling Physical Registers
I1:DIV R5, R4, R2
I2:ADD R7, R5, R1
I3:SUB R5, R3, R2
I4:LW R7, 1000(R5)
R2 PR2
R1 PR23
R7 PR19
R4 PR45
R5 PR42
R6 PR20
…
Register Map
…, PR13
Instruction Queue
(Reservation Stations)
…
Active List
I4: PR4
I3: PR37
I2: PR30
I1: PR13
Register Free List
Head
Commit
Tail
R3 PR17
ADD 37,23: 4
I2, producing register 4, completes, broadcasts a completion signal to IQ
I1, commits

## Slide 21
Register Rename Logic
Map
Table
Dependence
Check
Logic
Mux
Logical
Source
Regs
Logical
Dest
Regs
Logical
Source Reg
Physical
Source
Regs
Physical
Dest
Regs
Free Pool

## Slide 22: Instr Scheduling: Wakeup & Select
Wakeup Logic
  To notify the resolution of data dependency of input operands
  Wake up instructions with zero input dependency
Select Logic
  Choose and fire ready instructions
  Deal with structure hazard
Wakeup-select is likely on the critical path
  Associative match

## Slide 23
Wakeup Logic
rdyL
rdyR
tagR
tagL
or
=
=
or
tag1
tagIW
…
rdyL
rdyR
tagR
tagL
.
.
.
.
.
.

## Slide 24: Scalar Scheduler (Issue Width = 1)
T14
T16
T39
T6
T17
T39
T15
T39
=
=
=
=
=
=
=
=
T39
T8
T17
T42
Select Logic
To Execute Logic
Tag Broadcast Bus
From Prof. G. Loh’s Slide

## Slide 25: Superscalar Scheduler (Width = 4)
T39
T8
T17
T42
Select Logic
To Execute Logic
Tag Broadcast Bus [3..0]
Adapted from Prof. G. Loh’s Slide
T14
=
=
=
=
T16
=
=
=
=
T39
=
=
=
=
T6
=
=
=
=
T17
=
=
=
=
T39
=
=
=
=
T15
=
=
=
=
T39
=
=
=
=
Snapshot of RS (only 4 entries shown)

## Slide 26
Selection Logic
Issue window
req
grant
anyreq
enable
enable
Arbiter cell

## Slide 27: Simple (?) Select Logic Implementation
Reservation Station
[Palarchala ISCA’97]
Req0
Grant0
Req1
Grant1
Req2
Grant02
Req3
Grant3
Enable
AnyQueue
Req0
Grant0
Req1
Grant1
Req2
Grant02
Req3
Grant3
Enable
AnyQueue
Req0
Grant0
Req1
Grant1
Req2
Grant02
Req3
Grant3
Enable
AnyQueue
Req0
Grant0
Req1
Grant1
Req2
Grant02
Req3
Grant3
Enable
AnyQueue
Tree-like
Arbitrated
Selection
Logic
1

## Slide 28: Simple Select Logic Implementation
Reservation Station
[Palarchala ISCA’97]
Req0
Grant0
Req1
Grant1
Req2
Grant02
Req3
Grant3
Enable
AnyQueue
Req0
Grant0
Req1
Grant1
Req2
Grant02
Req3
Grant3
Enable
AnyQueue
Req0
Grant0
Req1
Grant1
Req2
Grant02
Req3
Grant3
Enable
AnyQueue
Req0
Grant0
Req1
Grant1
Req2
Grant02
Req3
Grant3
Enable
AnyQueue
Priority
Decoder
Enable
AnyQueue
Req0
Req1
Req2
Req3
Grt0
Grt1
Grt2
Grt3
1

## Slide 29: Simple Select Logic Implementation
Reservation Station
[Palarchala ISCA’97]
Req0
Grant0
Req1
Grant1
Req2
Grant02
Req3
Grant3
Enable
AnyQueue
Req0
Grant0
Req1
Grant1
Req2
Grant02
Req3
Grant3
Enable
AnyQueue
Req0
Grant0
Req1
Grant1
Req2
Grant02
Req3
Grant3
Enable
AnyQueue
Req0
Grant0
Req1
Grant1
Req2
Grant02
Req3
Grant3
Enable
AnyQueue
1

## Slide 30: Simple Select Logic Implementation
Reservation Station
Req0
Grant0
Req1
Grant1
Req2
Grant02
Req3
Grant3
Enable
AnyQueue
Req0
Grant0
Req1
Grant1
Req2
Grant02
Req3
Grant3
Enable
AnyQueue
Req0
Grant0
Req1
Grant1
Req2
Grant02
Req3
Grant3
Enable
AnyQueue
Req0
Grant0
Req1
Grant1
Req2
Grant02
Req3
Grant3
Enable
AnyQueue

## Slide 31: Issues to Distinctive Functional Units
Reservation Station
Distributed Instruction Windows (e.g., MIPS R1000 or Alpha 21264)
Faster to have separate instruction schedulers for different instruction types

## Slide 32: Dual Issues to Multiple Units
Grant0
[Palarchala Dissertation]
Req0
Grant1
Req1
Grant2
Req2
Grant3
Req3
Req0
Grant0
Req1
Grant1
Req2
Grant2
Req3
Grant3

## Slide 33
Bypass Delay
The number of bypass paths equals 2xIW2xS
(S is the number of pipeline stages)
Wire length ~ IW, hence, delay ~ IW2
The layout and pipeline depth (capacitive load)
also matter

## Slide 34: Other structures
Registers
Caches

## Slide 35: Limitations of ILP
Assume an ideal processor model
  Register renaming
    Infinite number of virtual registers
    All WAW and WAR hazards can be removed
  Branch prediction
    Perfect branch prediction
  Jump prediction
    All jumps are perfectly predicted
  Memory address alias analysis
    All memory addresses are known exactly
  Perfect caches
    All memory accesses take 1 clock cycle

## Slide 36: Impact of Window Size

## Slide 37: Impact of Branch Prediction
2K window
Max. 64 instruction issues per cycle

## Slide 38: Impact of Finite Registers
2K window
Max. 64 instruction issues per cycle
8K entry tournament predictors
2K jump and return predictors

## Slide 39: Impact of Imperfect Alias Analysis
2K window
Max. 64 instruction issues per cycle
8K entry tournament predictors
2K jump and return predictors
256 integer and 256 FP registers

## Slide 40: Limits of Multiple-Issue Processors: Revisited
Doubling the issue rate above the current 3-6 issue, i.e. 6-12 issue requires
  Issue 3-4 data memory accesses per cycle
  Resolve two or three branches per cycle
  Rename and access more than 20 registers per cycle
  Fetch 12-24 instructions per cycle
   The complexity of implementing these capabilities would sacrifice the maximum clock rate
Another issue is power!
  Modern microprocessors are primarily power limited.
    Static power grows proportionally to the transistor count
    Dynamic power is proportional to the product of the number of switching transistors and the switching rate
  Microprocessors trying to achieve both a high IPC and a high CR must switch more transistors and switch them faster!

## Slide 41: Limits of Multiple-Issue Processors
Energy inefficiency of multiple-issue processors
  Multiple instruction issue incurs overhead in logic that grows faster than the issue rate increase
    Dependence checking, register renaming, wakeup and select, etc.
    Without voltage reduction, higher IPC will lead to lower performance/watt!
  Growing gap between peak issue rate and sustained performance
    The number of transistor switching is proportional to the peak issue rate
    The performance is proportional to the sustained rate
    Thus, growing gap translates to increasing energy per unit performance!
For example, speculation is inherently inefficient
  It can never be perfect, thus there is inherently waste in executing computations before we know that whether the path is taken or not
Increasing clock rate is also not energy efficient
  Increasing clock rate will increase transistor switching frequency
  Faster clock rate need deeper pipeline, but it will increase the overhead of pipelining

## Slide 42: Example: Pentium 4 A Superscalar CISC Machine

## Slide 43: Pentium 4 alternate view

## Slide 44: Pentium 4 pipeline
20 stages !

## Slide 45: HP PA-RISC 8000

## Slide 46: Processor Performance with Time
Year of introduction
Notes: Log scale->growing exponentially
Specint = classic benchmark for integer performance
Moore’s law says: # transistors on chip doubles every 18 months-2years => ideally, performance double stoo
Pretty good prediction for this benchmark.

## Slide 47: Price being paid
Notes: Price paid == power
Greater power -> greater performance on benchmark
At top end (RHS)
Performance on spec = 100
Watts / spec = .1
.6*1000 = 10W (~1997)
2000s – high performance Intel server cores – 150W! :-(
Too hot! In 2001 – Intel VP says chips in 10 years (now) will be hotter than the surface of the sun. Yikes.

## Slide 48: MIPS-X (1988)
ftp://reports.stanford.edu/pub/cstr/reports/csl/tr/86/289/CSL-TR-86-289.pdf
Notes: MIPS-X out of Stanford – caught on fire on command.