## Slide 1: lecture

## Slide 2: Midterm 2: Distribution (Out of 85)

## Slide 3: Midterm 2: Statistics (% out of 100)
 | Mean | Median | Std Dev | Maximum
Question 1 (Control) | 50% | 52% | 20% | 100%
Question 2 (Data) | 42% | 42% | 24% | 100%
Question 3 (DRAM) | 55% | 57% | 27% | 100%
Question 4 (Tomasulo) | 72% | 72% | 16% | 100%
Question 5 (MP3) | 71% | 58% | 22% | 100%
Question 6 (Potpourri) | 69.5% | 69% | 16% | 100%
Total | 60.3% | 63.8% | 13.5% | 

## Slide 4: Design for Low Power

## Slide 5: A Long Time Ago
In a building far away
A man made a prediction
On surprisingly little data
That has defined an industry

## Slide 6: Moore’s Law

## Slide 7: Moore’s Original Issues
Design cost
Power dissipation
What to do with all the functionality possible
ftp://download.intel.com/research/silicon/moorespaper.pdf

## Slide 8: Problems of Power Dissipation
Continuously increasing performance demands
Increasing power dissipation of technical devices
Today: power dissipation is a main problem
High Power dissipation leads to:
High efforts for cooling
Increasing operational costs
Reduced reliability
Reduced time of operation
Higher weight (batteries)
Reduced mobility

## Slide 9: Outline
What is the problem?
Power Components
Historical Context
Solutions

## Slide 10: Dynamic Energy Consumption
Energy/transition = CL * VDD2 * P 0/11/0
Power = CL * VDD2 * f
Vin
Vout
CL
Vdd
Transition Power

## Slide 11: Dynamic Energy Consumption
Energy/transition = tsc * VDD * Ipeak * P 0/11/0
Power = tsc * VDD * Ipeak * f
Vin
Vout
CL
Vdd
Short-circuit Power

## Slide 12: Leakage Energy
Vout
Independent of switching
Sub-threshold current
Drain junction leakage
OFF
Gate leakage

## Slide 13: Power Equations in CMOS
P = α f CL VDD2 + VDD Ipeak (P01 + P10 ) + VDD Ileak
Dynamic power
(≈ 40 - 70% today and decreasing relatively)
Short-circuit power
(≈ 10 % today and decreasing absolutely)
Leakage power
(≈ 20 – 50 % today and increasing)
Notes: f0->1 represents the energy consuming transition

## Slide 14: Dynamic vs Static Power
Source: Leon Stok, DAC 42©

## Slide 15: The 80’s Power Problem
Until mid 80s technology was mixed
  nMOS, bipolar, some CMOS
Supply voltage was not scaling / power was rising
  nMOS, bipolar gates dissipate static power
From Roger Schmidt, IBM Corp

## Slide 16: Solution: Move to CMOS
And then scale Vdd

## Slide 17: Scaling MOS Devices
In this ideal scaling
  V scales to aV, L scales to aL
  So C scales to aC, i scales to ai (i/m is stable)
  Delay = CV/I scales as a
  Energy = CV2 scales as a3
JSSC Oct 74, pg 256

## Slide 18: Processor Power
Continued to grow, even when Vdd was scaled

## Slide 19: Why Power Increased
Growing die size, fast frequency scaling

## Slide 20: Good News
Die growth & super frequency scaling have stopped

## Slide 21: Bad News
Voltage scaling has stopped as well
  kT/q does not scale
  Vth scaling has power consequences
If Vdd does not scale
  Energy scales slowly
Ed Nowak, IBM

## Slide 22: ISSCC, Feb. 2001, Keynote
“Ten years from now, microprocessors will run at 10GHz to 30GHz and be capable of processing 1 trillion operations per second – about the same number of calculations that the world's fastest supercomputer can perform now.
“Unfortunately, if nothing changes these chips will produce as much heat, for their proportional size, as a nuclear reactor. . . .”
Patrick P. Gelsinger
Senior Vice President General Manager
Digital Enterprise Group INTEL CORP.

## Slide 23: Low Power Design Techniques
Three main classes of methods to reduce energy:
Cheating
  Reducing the performance of the design
Reducing waste
  Stop using energy for stuff that does not produce results
  Stop waiting for stuff that you don’t need (parallelism)
Problem reformulation
  Reduce work (less energy and less delay)

## Slide 24: Cheating
Many low-power papers talk only about energy
  Don’t consider performance
Reducing performance can always reduce energy
  But there are many ways to reduce performance
Good technique must lower the optimal curve
  “Sensitivity” of technique
    Must be better than current curve
    This depends on location on the curve

## Slide 25: Reducing Energy Waste
Clock gating
  If a section is idle, remove clock
  Removes clock power
  Prevents any internal node from transitioning
Create system power states
  Turn on subsystems only when they are needed
  Can have different “off” states
    Power vs. wakeup time
    Disk (do you stop it from spinning?)

## Slide 26: Embedded Power Gating
Since transistors still leak when power is off
Can reduce leakage
  250x reported
But costs
  Performance
  Drop in Vdd, Gnd
Embedded
Power Switches
Rows of
Standard Cells
Power Switch
Control Signals
Royannez, et al, 90nm Low Leakage SoC Design Techniques
for Wireless Applications, ISSCC 2005

## Slide 27: Parallelism
If the application has data parallelism
Parallelism is a way to improve performance
  With low additional energy cost

## Slide 28: Existing Processors
10 processors working in parallel

## Slide 29: Problem Reformulation
Best way to save energy is to do less work
  Energy directly reduced by the reduction in work
  But required time for the function decreases as well
    Convert this into extra power gains
  Shifts the optimal curve down and to the right
User Performance
Energy/op

## Slide 30: Saving power using multi-cores
No dynamic power, no static power
Little core, little power
Functional block
Wire
Resources
being used
Processor
Die
[Kumar et al]
Notes: If there is an application that uses only a fraction of execution resources, what we really want is that we be able execute this code on a different simpler, smaller
processor that has exactly the execution resources needed. This processor will dissipate no unnecessary power and will result in highly power-efficient computation.. What we can do is we can put both
of these processors (and maybe more) on the same die. When we are
running an application which is not going to use the large processor
well, we run it on the smaller low-power processor. And while the smaller processor is being used, we turn the larger processor
off completely so that it uses no static or
dynamic power.
And this will lead to very significant power savings.

## Slide 31: Constant Power Scaling
Foxton controller on Itanium II
  Raises Vdd/boosts F when most units idle
  Lowers Vdd for parallel code to stay in budget

## Slide 32: Exploit Specialization
Optimize execution units for different applications
  Reformulate the hardware to reduce needed work
  Can improve energy efficiency for a class of applications
Stream / Vector processing is a current example
  Exploit locality, reuse
  High compute density
μ-controller
Clusters
SRF
Memory System
HISC
NI
Bill Dally et al, Stanford Imagine

## Slide 33: Exploit Integration
Moving units onto one chip
  Reduces the number of I/Os on system
  I/O can take significant power today
  Allows even larger integration

## Slide 34: TI - OMAP2420
Specialization
And power domains
  Most units are off
OMAP 2420
  5 Power Domains
  #1: MCU Core
  #2: DSP Core
  #3: Graphic Accelerator
  #4: Core + Periph.
  #5: Always On logic
Royannez, et al, 90nm Low Leakage SoC Design Techniques
for Wireless Applications, ISSCC 2005

## Slide 35: Low-Power PowerPC
Nowka et al., Low-power PowerPC, ISSCC

## Slide 36: Low Power Design
Reduce dynamic power
  a:
  C:
  VDD:
  f:
Reduce static power

## Slide 37: Low Power Design
Reduce dynamic power
  a: clock gating, sleep mode
  C: small transistors (esp. on clock), short wires
  VDD: lowest suitable voltage
  f: lowest suitable frequency
Reduce static power

## Slide 38: Low Power Design
Reduce dynamic power
  a: clock gating, sleep mode
  C: small transistors (esp. on clock), short wires
  VDD: lowest suitable voltage
  f: lowest suitable frequency
Reduce static power
  Selectively use low Vt devices
  Leakage reduction:
  stacked devices, body bias, low temperature

## Slide 39: Power Saving Opportunities
System
High-level
RT-level
Logic
Physical
> 70%
40 - 70%
25 - 40%
15 - 25%
10 - 15%
Savings
HW/SW Co-design, Custom ISA, Algorithm Design, Communication Synthesis
Scheduling, Binding, Pipelining, Behavioral Transformation
Clock gating, Power gating, Precomputation, Operand Isolation, State Assignment, Retiming
Logic Restructuring, Technology Mapping, Rewiring, Pin Ordering & Phase Assignment
Fanout Optimization, Buffering, Transistor Sizing, Placement, Partitioning, Clock Tree Design, Glitch Elimination
A power-conscious design methodology addresses power at every level of the design hierarchy
Source: Pedram, 1999
Notes: Here is a chart for us to understand the power saving potentials during each design level: system, high-level, RT-level, logic and physical level. On the right side, we have the techniques available in each design level. We can see that the higher the design level, the larger power savings we can achieve. Nonetheless, lower-level design techniques are still needed because these techniques can be orthogonal to one another and applied cumulatively to achieve larger power reductions overall. That is exactly our goal in this research.

## Slide 40: Conclusions
Power is the ultimate limiter for technology scaling.
  Besides the physical limits
Dynamic power has been dominating until about five years ago
  Leakage power catches up due to Vt and Tox scaling
Power optimization has changed the semiconductor industry
Need to optimize power in each design stage
Early and accurate power analysis is essential