## Slide 1: ECE 417 Lecture 8: Speech Production
Mark Hasegawa-Johnson, 9/2017

## Slide 2: Speech (Slide: Scharenborg, 2017)
Specific to humans
Allows us to convey information very fast
Central role in many other language-related processes
One of the most complex skills humans perform:
  https://www.youtube.com/watch?v=DcNMCB-Gsn8
  https://www.youtube.com/watch?v=KtN-FCOeWjI

## Slide 3: Evolution of the vocal tract (Slide: Scharenborg, 2017)
Lowering of the tongue into the pharynx  lowering of the larynx
Lengthening of the neck
At the cost of an increase in the risk of choking on food
Neanderthals were not capable of human speech
Modern human vocal tract: since 50,000 years
Notes: How did humans learn to produce sounds?

## Slide 4: The anatomy and physiology of speech (Slide: Scharenborg, 2017)
Vocal tract
Area between vocal cords and lips
Pharynx + nasal cavity
+ oral cavity
and lungs

## Slide 5: 3 steps to produce sounds (Slide: Scharenborg, 2017)
step 3: articulation =
distortion of air
time-varying formant-frequency
pattern
= speech
step 2: phonation
step 1: initiation
Source
Filter
Notes: Step 1: air from the lungs is pushed past the vocal cords
If they start to vibrate it is called phonation
Step 3: the air, whether vibrating or not, travels through the oral and nasal cavity. Here the air is distorted/changed depending on the shape of the lips, teeth, tongue.

## Slide 6: The Source-Filter Model of Speech Production (Chiba & Kajiyama, 1940)
Sources: there are only three, all of them have wideband spectrum
  Voicing: vibration of the vocal folds, same type of aerodynamic mechanism as a flag flapping in the wind.
  Frication or Aspiration: turbulence created when air passes through a narrow aperture
  Burst: the “pop” that occurs when high air pressure is suddenly released
Filter:
  Vocal tract = the air cavity between glottis and lips
  Just like a flute or a shower stall, it has resonances
  The excitation has energy at all frequencies; excitation at the resonant frequencies is enhanced

## Slide 7: 3 steps to produce sounds
step 3: articulation =
distortion of air
time-varying formant-frequency
pattern
= speech
step 2: phonation
step 1: initiation
Source
Filter
Notes: Step 1: air from the lungs is pushed past the vocal cords
If they start to vibrate it is called phonation
Step 3: the air, whether vibrating or not, travels through the oral and nasal cavity. Here the air is distorted/changed depending on the shape of the lips, teeth, tongue.

## Slide 8: The Source-Filter Model of Speech Production A picture from Martin Rothenberg’s website
Notes: Step 1: air from the lungs is pushed past the vocal cords
If they start to vibrate it is called phonation
Step 3: the air, whether vibrating or not, travels through the oral and nasal cavity. Here the air is distorted/changed depending on the shape of the lips, teeth, tongue.

## Slide 9: The Source-Filter Model
The speech signal, , is created by convolving () an excitation signal through a vocal tract transfer function
The Fourier transform of speech is therefore the product of excitation times transfer function:
...engineers usually compute Fourier transform using rather than . You can get one from the other if you remember that .
Excitation includes all of the information about voicing, frication, or burst. Transfer function includes all of the information about the vocal tract resonances, which are called “formants.”

## Slide 10: The Source-Filter Model
Transfer Function log|H(f)|
Voice Source Spectrum log|E(f)|
Speech Spectrum log|S(f)|=log|H(f)|+log|E(f)|

## Slide 11: Source-Filter Model: Voice Source
The most important thing about voiced excitation is that it is periodic, with a period called the “pitch period,”
It’s reasonable to model voiced excitation as a simple sequence of impulses, one impulse every seconds:
The Fourier transform of an impulse train is an impulse train (to prove this: use Fourier series):
...where is the pitch frequency. It’s the number of times per second that the vocal folds slap together.

## Slide 12: Source-Filter Model: Filter
The vocal tract is just a tube. At most frequencies, it just passes the excitation signal with no modification at all ().
The important exception: the vocal tract has resonances, like a clarinet or a shower stall. These resonances are called “formant frequencies,” numbered in order: . Typically Hz and so on, but there are some exceptions.
At the resonant frequencies, the resonance enhances the energy of the excitation, so the transfer function is large at those frequencies, and small at other frequencies.

## Slide 13: Speech signal: Time domain
=8ms
=2ms
/k/ burst
/k/ aspiration
voicing

## Slide 14: Speech signal: Magnitude Fourier Transform
spacing between
adjacent pitch harmonics =
125Hz
freq of first peak =
500Hz
Aliasing artifacts:
Spectra at should really
be plotted at (negative
frequency components). DFT
puts it at instead.
freq of second peak = 1500Hz

## Slide 15: Speech signal: Log Magnitude Transform
spacing between
harmonics =125Hz
freq of first peak =
500Hz
Aliasing artifacts:
Spectra at should really
be plotted at (negative
frequency components). DFT
puts it at instead.
freq of second peak = 1500Hz

## Slide 16: Part 2: Linguistic units
Speech signal
Linguistic units are:
Phone(me)s
Words
Scharenborg, 2017
Notes: In the context of this project:
Linguistics units are sounds, sound sequences, partial words, words, multi-word sequences

## Slide 17: Linguistic units
Speech = sound
Sound = differences in air pressure
Air pressure waves perceived as different phone(me)s, phone(me) sequences, and (partial or multi) words
Via eardrum, cochlea, and auditory nerve to brain
speech signal
Scharenborg, 2017
Notes: In the context of this project:
Linguistics units are sounds, sound sequences, partial words, words, multi-word sequences

## Slide 18: Some terminology
Phoneme: the smallest contrastive linguistic unit that distinguishes meaning, e.g., tip vs. dip
Allophone: a variation of a phoneme, eg., phot vs. spot
Phone: a distinct speech sound
Word: the smallest distinct unit that can be uttered in isolation which has meaning
Scharenborg, 2017

## Slide 19: Speech sounds
Vowels: unblocked air stream
Consonants: constricted or blocked air stream
Scharenborg, 2017
Notes: Speech sounds can be divided into two types

## Slide 20: Different sounds: Vowels
Tongue height:
  Low: e.g., /a/
  Mid: e.g., /e/
  High: e.g., /i/
Tongue advancement:
  Front : e.g., /i/
  Central : e.g., /ə/
  Back : e.g., /u/
Lip rounding:
  Unrounded: e.g., /ɪ, ɛ, e, ǝ/
  Rounded: e.g., /u, o, ɔ/
Tense/lax:
  Tense: e.g., /i, e, u, o, ɔ, ɑ/
  Lax: e.g., /ɪ, ɛ, æ, ə/
Scharenborg, 2017
heed
hid
hayed
head
had
hod
hawed
hoed
hood
who’d
Notes: In producing vowels the tongue and lips are important for shaping the vocal tract
Tense vowels are typically produced with a narrower mouth than lax vowels, less centralization, and longer duration

## Slide 21: Different sounds: Vowels
Tongue height:
  Low: e.g., /a/
  Mid: e.g., /e/
  High: e.g., /i/
Tongue advancement:
  Front : e.g., /i/
  Central : e.g., /ə/
  Back : e.g., /u/
Lip rounding:
  Unrounded: e.g., /ɪ, ɛ, e, ǝ/
  Rounded: e.g., /u, o, ɔ/
Tense/lax:
  Tense: e.g., /i, e, u, o, ɔ, ɑ/
  Lax: e.g., /ɪ, ɛ, æ, ə/
Scharenborg, 2017
heed
hid
hayed
head
had
hod
hawed
hoed
hood
who’d
F2
2000
800
900
F1
300
Notes: In producing vowels the tongue and lips are important for shaping the vocal tract
Tense vowels are typically produced with a narrower mouth than lax vowels, less centralization, and longer duration

## Slide 22: Different sounds: Consonants
Place of articulation
  Where is the constriction/blocking of the air stream?
Manner of articulation
  Stops: /p, t, k, b, d, g/
  Fricatives: /f, s, S, v, z, Z/
  Affricates: /tS, dZ/
  Approximants/Liquids: /l, r, w, j/
  Nasals: /m, n, ng/
Voicing
Scharenborg, 2017
Notes: The type of consonant or sound that is produced depends on three factors: the place of articulation, the manner of articulation and whether the vocal cords vibrate
Manner of articulation: is it a full blockage or a constriction and how much of a constriction is there?
Plosion
Bit of noise
Combination
Air through the nasal cavity
Fairly open

## Slide 23: Speech sound production
https://www.youtube.com/watch?v=DcNMCB-Gsn8
Recorded in 1962, Ken Stevens
Source: YouTube
Scharenborg, 2017
Notes: We all know what speech sounds like, and now we know how they are produced, but what does it look like when we produce speech?

## Slide 24: Quiz 1: How many words are there?
Each picture shows a waveform of a short stretch of speech:
C
D
A: Electromagnetically (1)
B: Emma loves her mum’s yellow marmelade (6)
C: See you in the evening (5)
D: Attachment (1)
Scharenborg, 2017
Notes: Finding the ‘linguistic units’ in speech

## Slide 25: Electromagnetically
Why is it so hard to determine the number of words?
/i l ɛ kt romæ g nɛ t ɪ k ǝ l i/
silence ≠ word boundary
Scharenborg, 2017

## Slide 26: Quiz 2: Can you spot the odd one out?
Below are three waveforms each containing a single word:
Every time you produce a word it sounds differently
A3 (brother, brother, mother)
Scharenborg, 2017
Notes: Every

## Slide 27: Enormous variability
Speaker differences, e.g., gender, vocal tract length, age
Speaker idiosyncracies , e.g., lisp, creaky voice
Accent: dialects, non-nativeness
Coarticulation: production of a speech sound becomes more like that of a preceding/following speech sound
Speaking style  reductions
Scharenborg, 2017

## Slide 28: Time domain signal: Hard to tell what he was saying

## Slide 29: Magnitude spectrum: A little easier
Easier to measure formants→easier to guess what he’s saying.
Still easy to measure F0→can still guess who he is.
(Formants≈phone-dependent, F0≈person-dependent, though there’s a lot of cross-talk)

## Slide 30: Log magnitude spectrum: A lot easier
Easier to measure formants→easier to guess what he’s saying.
Still easy to measure F0→can still guess who he is.
(Formants≈phone-dependent, F0≈person-dependent, though there’s a lot of cross-talk)

## Slide 31: Log spectrum = log filter + log excitation
But how can we separate the speech spectrum into the transfer function part, and the excitation part?
Bogert, Healy & Tukey:
  Excitation is high “quefrency” (varies rapidly as a function of frequency)
  Transfer function is low “quefrency” (varies slowly as a function of frequency)

## Slide 32: Cepstrum = inverse FFT of the log spectrum (Bogert, Healy & Tukey, 1962)
=quefrency. It has units of time.
IFFT is linear, so since
=+
…the transfer function and excitation are added together. All we need to do is separate two added signals.
Transfer function and Excitation are separated into low-quefrency (ms) and high-quefrency (ms) parts.

## Slide 33: Liftering = filter(spectrum) = window(cepstrum) (Bogert, Healy & Tukey, 1962)
Transfer function and Excitation are separated into low-quefrency (ms) and high-quefrency (ms) parts. So we can recover them by just windowing:

## Slide 34: Liftering = filter(spectrum) = window(cepstrum) (Bogert, Healy & Tukey, 1962)
Then we estimate the transfer function and excitation spectrum using the FFT:

## Slide 35: Inverse Discrete Cosine Transform
Log magnitude spectrum is symmetric: .
In the IFFT definition, the real part is symmetric, and the imaginary part is antisymmetric. Suppose we define , then the definition of IFFT is
…but since is real, so
This is called the “inverse discrete cosine transform” or IDCT. It’s half of the real symmetric IFFT of a real symmetric signal. (note M=N/2).

## Slide 36: Type I DCT, IDCT, and Parseval’s Theorem

## Slide 37: Type II Discrete Cosine Transform
Suppose we define , and . Then
…but now so
This is called the “Type II DCT,” and it’s a lot more common than the Type I DCT because it eliminates the special handling of the k=0 and k=M terms.

## Slide 38: Type II DCT, IDCT, and Parseval’s Theorem

## Slide 39: Details about type II DCT
It was defined as , but in practice we usually just use the FFT coefficients, . This approximation has no real impact on automatic speech recognition, but it might have some impact on pitch tracking – if you’re trying to find out exactly what is the pitch frequency, then shifting by might matter.
The DCT and IDCT formulas are now easy, but Parseval’s theorem still has a funny extra term for c[0]. But it doesn’t matter because…
Remember is the average log magnitude of the spectrum, i.e., a measure of the loudness. Loudness can be increased by just turning up the volume on the microphone, so we probably want to treat differently from all of the other .

## Slide 40: Discrete Cosine Transform = Half of the real symmetric IFFT of a real symmetric signal

## Slide 41: Lifter = window the IFFT (left) or DCT (right) cepstrum

## Slide 42: Both kinds of liftering give the same transfer function and excitation estimates

## Slide 43: Spectrogram: ln(energy(frequency,time))
bu t o nM o n d a y
Scharenborg, 2017
Spectrum lets you measure formants, so it gives some information about vowels.
Timing is important to know about consonants.
Spectrogram = time on the horizontal axis, frequency on vertical axis.
Notes: Explain about amplitude (energy) and frequency ranges, voiced sounds, formants and formant transitions, differences in spectral shape
Each sound has its own spectral pattern depending on the shape of the vocal tract
Differences in formant transitions between the o after t and the o after M
Plosion of the d
Difference in formant tracks between o and a
Diphtong ay

## Slide 44: Summary
Source-filter model:
  Voiced excitation is an impulse train in time (with period = the pitch period ), whose Fourier transform is an impulse train in frequency (with inter-harmonic spacing equal to the pitch frequency )
  Transfer function is nearly at most frequencies, but with big peaks near the resonant frequencies, which are called formants
Phones, phonemes, and allophones
Estimating the transfer function and excitation
  The transfer function is low-quefrency, excitation is high-quefrency
  Cepstrum = =
  Liftering = windowing the cepstrum
  DCT = half of the real symmetric IFFT of a real symmetric signal