## Slide 1: ECE 417, Lecture 11: MFCC
Mark Hasegawa-Johnson
10/2/2018

## Slide 2: Content
What spectrum do people hear? The basilar membrane
Frequency scales for hearing: mel scale
Mel-filter spectral coefficients (also called “filterbank features”)
Speech Production: Consonants and Vowels
Parseval’s Theorem: Cepstral Distance = Spectral Distance

## Slide 3: What spectrum do people hear? Basilar membrane

## Slide 4: Inner ear

## Slide 5: Basilar membrane of the cochlea = a bank of mechanical bandpass filters

## Slide 6: Frequency scales for hearing: mel scale

## Slide 7: Mel-scale
The experiment:
  Play tones A, B, C
  Let the user adjust tone D until pitch(D)-pitch(C) sounds the same as pitch(B)-pitch(A)
Analysis: create a frequency scale m(f) such that m(D)-m(C) = m(B)-m(A)
Result:

## Slide 8: Mel Frequency Spectral Coefficients (Filterbank Coefficients)

## Slide 9: Mel filterbank coefficients: convert the spectrum from Hertz-frequency to mel-frequency
Goal: instead of computing
We want
Where the frequencies are uniformly spaced on a mel-scale, i.e., is a constant across all k.
The problem with that idea: we don’t want to just sample the spectrum. We want to summarize everything that’s happening within a frequency band.

## Slide 10: Mel filterbank coefficients: convert the spectrum from Hertz-frequency to mel-frequency
The solution:
Where

## Slide 11: Mel filterbank coefficients: convert the spectrum from Hertz-frequency to mel-frequency

## Slide 12: Speech Production

## Slide 13: The Source-Filter Model of Speech Production (Chiba & Kajiyama, 1940)
Sources: there are only three, all of them have wideband spectrum
  Voicing: vibration of the vocal folds, same type of aerodynamic mechanism as a flag flapping in the wind.
  Frication or Aspiration: turbulence created when air passes through a narrow aperture
  Burst: the “pop” that occurs when high air pressure is suddenly released
Filter:
  Vocal tract = the air cavity between glottis and lips
  Just like a flute or a shower stall, it has resonances
  The excitation has energy at all frequencies; excitation at the resonant frequencies is enhanced

## Slide 14: Different sounds: Consonants
Place of articulation
  Where is the constriction/blocking of the air stream?
Manner of articulation
  Stops: /p, t, k, b, d, g/
  Fricatives: /f, s, S, v, z, Z/
  Affricates: /tS, dZ/
  Approximants/Liquids: /l, r, w, j/
  Nasals: /m, n, ng/
Voicing
Scharenborg, 2017
Notes: The type of consonant or sound that is produced depends on three factors: the place of articulation, the manner of articulation and whether the vocal cords vibrate
Manner of articulation: is it a full blockage or a constriction and how much of a constriction is there?
Plosion
Bit of noise
Combination
Air through the nasal cavity
Fairly open

## Slide 15: Speech signal: Time domain
=8ms
/k/ burst
/k/ aspiration
voicing

## Slide 16: Speech sound production
https://www.youtube.com/watch?v=DcNMCB-Gsn8
Recorded in 1962, Ken Stevens
Source: YouTube
Scharenborg, 2017
Notes: We all know what speech sounds like, and now we know how they are produced, but what does it look like when we produce speech?

## Slide 17: The Source-Filter Model
The speech signal, , is created by convolving () an excitation signal through a vocal tract filter
The Fourier transform of speech is therefore the product of excitation times filter:
Excitation includes all of the information about voicing, frication, or burst.
Filter includes all of the information about the vocal tract resonances, which are called “formants.”

## Slide 18: Source: V/UV,
The most important thing about voiced excitation is that it is periodic, with a period called the “pitch period,”
It’s reasonable to model voiced excitation as a simple sequence of impulses, one impulse every seconds:
The Fourier transform of an impulse train is an impulse train (to prove this: use Fourier series):
...where is the pitch frequency. It’s the number of times per second that the vocal folds slap together.

## Slide 19: The Source-Filter Model
Transfer Function log|H(f)|
Voice Source Spectrum log|E(f)|
Speech Spectrum log|S(f)|=log|H(f)|+log|E(f)|
spacing between
adjacent pitch harmonics =
125Hz

## Slide 20: Filter:
The vocal tract is just a tube. At most frequencies, it just passes the excitation signal with no modification at all ().
The important exception: the vocal tract has resonances, like a clarinet or a shower stall. These resonances are called “formant frequencies,” numbered in order: . Typically Hz and so on, but there are some exceptions.
At the resonant frequencies, the resonance enhances the energy of the excitation, so the transfer function is large at those frequencies, and small at other frequencies.

## Slide 21: The Source-Filter Model
Transfer Function log|H(f)|
Voice Source Spectrum log|E(f)|
Speech Spectrum log|S(f)|=log|H(f)|+log|E(f)|

## Slide 22: Different sounds: Vowels
Tongue height:
  Low: e.g., /a/
  Mid: e.g., /e/
  High: e.g., /i/
Tongue advancement:
  Front : e.g., /i/
  Central : e.g., /ə/
  Back : e.g., /u/
Lip rounding:
  Unrounded: e.g., /ɪ, ɛ, e, ǝ/
  Rounded: e.g., /u, o, ɔ/
Tense/lax:
  Tense: e.g., /i, e, u, o, ɔ, ɑ/
  Lax: e.g., /ɪ, ɛ, æ, ə/
Scharenborg, 2017
heed
hid
hayed
head
had
hod
hawed
hoed
hood
who’d
F2
2000
800
900
F1
300
huggable
Notes: In producing vowels the tongue and lips are important for shaping the vocal tract
Tense vowels are typically produced with a narrower mouth than lax vowels, less centralization, and longer duration

## Slide 23: Time domain signal: Hard to tell what he was saying

## Slide 24: Magnitude spectrum: A little easier
spacing between
adjacent pitch harmonics =
125Hz
freq of first peak =
500Hz
Aliasing artifacts:
Spectra at should really
be plotted at (negative
frequency components). DFT
puts it at instead.
freq of second peak = 1500Hz

## Slide 25: Log magnitude spectrum: A lot easier
spacing between
harmonics =125Hz
freq of first peak =
500Hz
Aliasing artifacts:
Spectra at should really
be plotted at (negative
frequency components). DFT
puts it at instead.
freq of second peak = 1500Hz

## Slide 26: Different sounds: Vowels
Tongue height:
  Low: e.g., /a/
  Mid: e.g., /e/
  High: e.g., /i/
Tongue advancement:
  Front : e.g., /i/
  Central : e.g., /ə/
  Back : e.g., /u/
Lip rounding:
  Unrounded: e.g., /ɪ, ɛ, e, ǝ/
  Rounded: e.g., /u, o, ɔ/
Tense/lax:
  Tense: e.g., /i, e, u, o, ɔ, ɑ/
  Lax: e.g., /ɪ, ɛ, æ, ə/
Scharenborg, 2017
heed
hid
hayed
head
had
hod
hawed
hoed
hood
who’d
F2
2000
800
900
F1
300
huggable
Notes: In producing vowels the tongue and lips are important for shaping the vocal tract
Tense vowels are typically produced with a narrower mouth than lax vowels, less centralization, and longer duration

## Slide 27: Log spectrum = log filter + log excitation
But how can we separate the speech spectrum into the transfer function part, and the excitation part?
Bogert, Healy & Tukey:
  Excitation is high “quefrency” (varies rapidly as a function of frequency)
  Transfer function is low “quefrency” (varies slowly as a function of frequency)

## Slide 28: Cepstrum = inverse FFT of the log spectrum (Bogert, Healy & Tukey, 1962)
=quefrency. It has units of time.
IFFT is linear, so since
=+
…the transfer function and excitation are added together. All we need to do is separate two added signals.
Transfer function and Excitation are separated into low-quefrency (ms) and high-quefrency (ms) parts.

## Slide 29: Inverse Discrete Cosine Transform
Log magnitude spectrum is symmetric: . Suppose we assume that and , then
This is called the “inverse discrete cosine transform” or IDCT. It’s half of the real symmetric IFFT of a real symmetric signal. (note M=N/2).

## Slide 30: Liftering = filter(spectrum) = window(cepstrum) (Bogert, Healy & Tukey, 1962)
Transfer function and Excitation are separated into low-quefrency (ms) and high-quefrency (ms) parts. So we can recover them by just windowing:

## Slide 31: Liftering = filter(spectrum) = window(cepstrum) (Bogert, Healy & Tukey, 1962)
Then we estimate the transfer function and excitation spectrum using the FFT:

## Slide 32: Parseval’s Theorem
L2 norm of a signal equals the L2 norm of its Fourier transform.

## Slide 33: Parseval’s Theorem: Examples
Fourier Series:
DTFT:
DFT:

## Slide 34: Parseval’s Theorem: Vector Formulation
Suppose we define the vectors and as the cepstrum and the log spectrum, thus

## Slide 35: Parseval’s Theorem: Vector Formulation
That way Parseval’s theorem can be written very simply as
…or even more simply as…
i.e., the L2 norm of the cepstrum equals the L2 norm of the log spectrum.

## Slide 36: What it means for Gaussian classifiers
Suppose we have two acoustic signals and , and we want to find out how different they sound. If they have static spectra, then a good measure of their difference is the distance between their log spectra:

## Slide 37: Low-pass liftering smooths the spectrum

## Slide 38: Low-pass liftered L2 norm
If you want to know whether two signals are the same vowel, then you want to know how different their smoothed spectra are. Let H(k) be your liftering function. You lifter the log spectrum = windowing the cepstrum, then find the distance:

## Slide 39: Low-pass liftered L2 norm
In particular, suppose
Then

## Slide 40: MFCC: mel-frequency cepstral coefficients
Divide the acoustic signal into frames
Compute the magnitude FFT of each frame
Filterbank coefficients:
MFCC:
Liftering: keep only the first 12-15 MFCC coefficients, set the rest to zero.