## Slide 1
Heat Exhaustion Detection Device
Electrical & Computer Engineering
Team: 12
Zackary Haycraft
Danny Schaub
Tongli Zhou
May 1, 2023

## Slide 2
Preventing Heat Related Illnesses
Heat related illnesses such as heat stress, heat exhaustion and heat stroke are a serious problem for everyone but especially individuals who perform hard labor in harsh environments.
People in less fortunate areas do not always have access to expensive smart watches. There is no alternative for monitoring the condition of one's body.
With global temperatures rising early estimates from the Center for Disease Control and Prevention have estimates that heat related deaths have increased by 56% between 2012 and 2018 [1].
GRAINGER ENGINEERING
The Problem
ELECTRICAL & COMPUTER ENGINEERING

## Slide 3
IMAGE / GRAPHIC
IMAGE / GRAPHIC
Monitor the Wearers Chloride level
According to a study in the Journal of Taiba University Medical Sciences patients experiencing one of these heat-related illnesses showed a marked decrease in the sweat chloride concentration as the illness got worse [2]
Monitor the Heat Index of the Environment
The Heat index chart provides a danger level as well as likely effects the heat index level will have on the body
Use temperature and humidity sensor to monitor the heat index level
GRAINGER ENGINEERING
The Solution
ELECTRICAL & COMPUTER ENGINEERING

## Slide 4
Design
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
The goal was to create a wearable device to monitor the chloride concentration in a person's sweat.
We created a method of measuring chloride from a solution.

## Slide 5
Arduino Uno
Microcontroller board based on the ATmega328P
User-friendly, built in Arduino IDE support
Provided power and control to our project
Enabled easier debugging capabilities
GRAINGER ENGINEERING
Power and Control
ELECTRICAL & COMPUTER ENGINEERING

## Slide 6
Conductivity Sensor
Utilized relaxation oscillator to generate 1 kHz AC square wave.
Conductivity measurements based on average voltage across electrodes.
Developed salt water samples for testing verification.
Temperature and Humidity Sensor
DHT22 temperature and humidity sensor used
Resulting measurements used in heat index calculations
Results verified with heat index chart
GRAINGER ENGINEERING
Sensors
ELECTRICAL & COMPUTER ENGINEERING

## Slide 7
programming issues with PCB
Measuring inaccuracies of conductivity sensors
Parts order incompatible with current design.
Getting parts too small for breadboard testing
GRAINGER ENGINEERING
Issues and obstacles
ELECTRICAL & COMPUTER ENGINEERING

## Slide 8
It is important to do advanced research on the parts you order - make sure parts are compatible with each other
Small components which don't fit on breadboards often have similar breadboard sized equivalents
Time spent waiting for parts to arrive can still be productive
Test parts on breadboard before trying on a PCB
Programing can be simplified by using online APIs
GRAINGER ENGINEERING
In the Future... (What we learned the hard way)
ELECTRICAL & COMPUTER ENGINEERING

## Slide 9
Thank You!
Questions?
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 10
[1] M. Davis, “Heat-Related Deaths Up 56% Between 2018 and 2021, Provisional Data Shows,”
ValuePenguin, Jun. 06, 2022. https://www.valuepenguin.com/heat-related-deaths-study
(accessed Feb. 02, 2023).
[2] A. H. Alzeer and H. A. K. Al Otair, “Sweat chloride concentration in patients with heat stroke,” Journal of Taibah University Medical Sciences, vol. 9, no. 1, pp. 50–53, Mar. 2014, doi: 10.1016/j.jtumed.2013.06.004.
[3] N. US Department of Commerce, “What is the heat index?,” www.weather.gov. https://www.weather.gov/ama/heatindex#:~:text=For%20example%2C%20if%20the%20air (accessed Apr. 29, 2023).
GRAINGER ENGINEERING
Refrences
ELECTRICAL & COMPUTER ENGINEERING