## Slide 1
Easy Bake PCBs
Electrical & Computer Engineering
Team 51
ECE 445 – SP 23
May 02, 2023

## Slide 2
Introduction
Team Introduction
Problem
Solution
High-Level Requirements
Block Diagram
Final Product Clip
ELECTRICAL & COMPUTER ENGINEERING
GRAINGER ENGINEERING

## Slide 3
GRAINGER ENGINEERING
Introduction
ELECTRICAL & COMPUTER ENGINEERING
Bhaven Shah
Computer Engineering
Raghav Narasimhan
Computer Engineering
Zak Kaminski
Electrical Engineering

## Slide 4
GRAINGER ENGINEERING
Introduction
ELECTRICAL & COMPUTER ENGINEERING
Problem:
Soldering is time consuming and requires technical skill
Hand soldering requires larger pads for Surface Mount Devices(SMD) increasing PCB size
Need for increased efficiency of soldering for testing and production
Reflow ovens exist, but are expensive ($250 minimum)

## Slide 5
GRAINGER ENGINEERING
Introduction
ELECTRICAL & COMPUTER ENGINEERING
Solution:
Toaster Oven based Reflow Oven
Breakout board to control the reflow process following the JEDEC recommendation
Camera to watch process and stop from any failures occurring

## Slide 6
GRAINGER ENGINEERING
Introduction
ELECTRICAL & COMPUTER ENGINEERING
High-Level Requirements:
Solder PCBs with a margin of error of 10%
Detect when a component covers less than 50% of the pad
Reach temperatures of up to 270°C with a tolerance of ± 10°C

## Slide 7
GRAINGER ENGINEERING
Introduction
ELECTRICAL & COMPUTER ENGINEERING
Block Diagram (Original):

## Slide 8
GRAINGER ENGINEERING
Introduction
ELECTRICAL & COMPUTER ENGINEERING
Block Diagram (Updated):

## Slide 9
GRAINGER ENGINEERING
Introduction
ELECTRICAL & COMPUTER ENGINEERING
Demo Clip:

## Slide 10
Subsystem Designs
Power
Sensors
HVAC
User Interface
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 11
GRAINGER ENGINEERING
Power Subsystem
ELECTRICAL & COMPUTER ENGINEERING

## Slide 12
GRAINGER ENGINEERING
Design – Power
ELECTRICAL & COMPUTER ENGINEERING
Power Supply R&V:
Requirements | Verified?
5V regulator circuit outputs 5V ± 10% for a 120V AC power supply. | Yes
3.3V regulator outputs 3.3V ± 0.3V given a 5V ±10% input. | Yes

## Slide 13
Results:
Had to switch from the Link Switch 120 VAC to 5 VDC circuit to an off-the-shelf power supply
  Original circuit was too complex and difficult to debug
  The power supply is much easier to use and understand
GRAINGER ENGINEERING
Design – Power
ELECTRICAL & COMPUTER ENGINEERING
Notes: https://www.electron.com/12v-dc-switching-power-supply-mean-well-rs-100-12-p53684/

## Slide 14
GRAINGER ENGINEERING
Sensor Subsystem
ELECTRICAL & COMPUTER ENGINEERING

## Slide 15
GRAINGER ENGINEERING
Design – Thermocouple
ELECTRICAL & COMPUTER ENGINEERING
Thermocouple R&V:
Requirements | Verified??
Thermocouple must be accurate within ± 2°C | Yes
Thermocouple must be able to give a temperature every 0.5 ± 0.1 second | Yes
Blue: SPI Signal, Green: Clock Signal, Yellow: Chip Select
Notes: https://courses.engr.illinois.edu/ece445/getfile.asp?id=19638

## Slide 16
GRAINGER ENGINEERING
Design – Thermocouple
ELECTRICAL & COMPUTER ENGINEERING
Results:
Had to use I2C ports on the touchscreen microcontroller in order to read the SPI output of the thermocouple
  Able to do this because the MAX31855 does not receive any serial data (no MOSI port)
  MISO to SDA
  Clocks and chip selects connect together
Notes: https://courses.engr.illinois.edu/ece445/getfile.asp?id=19638

## Slide 17
GRAINGER ENGINEERING
Design – Camera
ELECTRICAL & COMPUTER ENGINEERING
Camera R&V:
Requirements | Verified?
Camera must be able to detect when a component is covering less than 70% of its corresponding pad | Yes
Camera must be able to send a frame once every 0.5 ± 0.1 second | Yes
Notes: https://courses.engr.illinois.edu/ece445/getfile.asp?id=19638

## Slide 18
GRAINGER ENGINEERING
Design – Camera
ELECTRICAL & COMPUTER ENGINEERING
Results:
Used OpenCV along with Image Processing library to determine image similarity
  One photo would be captured in the beginning of the soldering process
  Subsequent pictures would be taken at 0.5-second increments
  The similarity with the most recent picture and the original picture is determined
  A threshold is set stating if the similarity is too low, a 'slip' occurs
Notes: https://courses.engr.illinois.edu/ece445/getfile.asp?id=19638

## Slide 19
GRAINGER ENGINEERING
Camera Algorithm - Results
ELECTRICAL & COMPUTER ENGINEERING
Example:
Notes: https://courses.engr.illinois.edu/ece445/getfile.asp?id=19638

## Slide 20
GRAINGER ENGINEERING
Camera Algorithm - Results
ELECTRICAL & COMPUTER ENGINEERING
Example:
Notes: https://courses.engr.illinois.edu/ece445/getfile.asp?id=19638

## Slide 21
GRAINGER ENGINEERING
Design – Microcontroller
ELECTRICAL & COMPUTER ENGINEERING
Microcontroller R&V:
Requirements | Verified?
Microcontroller digital output pins must correctly output a 1 or 0 for a corresponding voltage of ≥ 3.0V and ≤ 0.2V respectively. | Yes
Microcontroller digital input pins must correctly read a 1 or 0 for a corresponding voltage of ≥ 3.0V and ≤ 0.2V respectively | Yes
Microcontroller can produce a variable PWM signal at a frequency of 100kHz | No
Notes: https://courses.engr.illinois.edu/ece445/getfile.asp?id=19638

## Slide 22
GRAINGER ENGINEERING
Design – Microcontroller
ELECTRICAL & COMPUTER ENGINEERING
Results:
Had to shift away from using a PWM and instead used GPIO pins for the same use
  Solid-state relay worked differently from what we initially thought
  Can use a GPIO for the fan and the heating instead
Changed microcontroller to the one on the touchscreen
  NXP microcontroller was difficult to program and the IDE was difficult to use
  Power traces were not connected to the microcontroller on the PCB
Notes: https://www.digikey.com/en/maker/projects/adafruit-pyportal-iot-for-circuitpython/3a9b824ec105490daff240ba4496ef80
https://courses.engr.illinois.edu/ece445/getfile.asp?id=19638

## Slide 23
GRAINGER ENGINEERING
HVAC Subsystem
ELECTRICAL & COMPUTER ENGINEERING

## Slide 24
GRAINGER ENGINEERING
Design – HVAC
ELECTRICAL & COMPUTER ENGINEERING
Heating R&V:
Requirements | Verified?
When the user begins the reflow process, the coils should begin to heat the chamber and follow the specified profile that was chosen within ±10°C | Yes
When the reflow process reaches ± 10°C peak temperature the fan will turn on at 7600 ± 10% RPM. | No
10 – 30 seconds after reaching the peak temperature ± 5°C the fan will run at 8300 ± 10% RPM. | No
Preheat
Soak
Reflow
Cool

## Slide 25
GRAINGER ENGINEERING
Design – HVAC
ELECTRICAL & COMPUTER ENGINEERING
Results:
  We were able to successfully control the heating of the toaster oven
    Had to use a BJT transistor circuit
  We were unable to get the fan integrated into the circuit, but could integrate it as we have the data
Notes: https://courses.engr.illinois.edu/ece445/getfile.asp?id=19638

## Slide 26
GRAINGER ENGINEERING
User Interface Subsystem
ELECTRICAL & COMPUTER ENGINEERING

## Slide 27
GRAINGER ENGINEERING
Design – User Interface
ELECTRICAL & COMPUTER ENGINEERING
Results:
  Easy to read and responsive touchscreen
    Displayed the reflow profile graph
  Created a new graph that showed the current temperature in the oven with a red line
  Profile selector
    Press profile button and then press save

## Slide 28
Conclusion
Lessons Learned
Future Work
Thank You & Questions
ELECTRICAL & COMPUTER ENGINEERING
GRAINGER ENGINEERING

## Slide 29
GRAINGER ENGINEERING
Lessons Learned
ELECTRICAL & COMPUTER ENGINEERING

## Slide 30
GRAINGER ENGINEERING
Conclusion
ELECTRICAL & COMPUTER ENGINEERING
Lessons Learned
More careful consideration is needed when picking components
GPIO pins on microcontrollers provide very little current and can create issues
Breadboarding is very useful and helps provide confirmation that our circuit works
Dev boards and through-hole components are useful for testing
Order backup components

## Slide 31
GRAINGER ENGINEERING
Future Work
ELECTRICAL & COMPUTER ENGINEERING

## Slide 32
GRAINGER ENGINEERING
Conclusion
ELECTRICAL & COMPUTER ENGINEERING
Future Work
Run full tests to ensure the reflow process is working
Use a PID controller to get more accurate temperature readings
Use a Solid-State Relay with +3.3VDC as a viable input voltage
Integrate the Camera Module with the microcontroller so that it can halt the process

## Slide 33
Thank You
Any questions?
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING