## Slide 1
Automated Frozen Pipe Burst Prevention System
Electrical & Computer Engineering
Group # 22: Neha Vagvala, Benedicta Udeogu, Ethan Zhang
05/02/2023

## Slide 2
Problem
How can we automate the process of preventing pipes from bursting due to the expansion of frozen water within them?
ELECTRICAL & COMPUTER ENGINEERING
GRAINGER ENGINEERING

## Slide 3
The Statistics:
An estimated average of over 250,000 families each year will suffer damage from frozen and burst pipes.
The damage is estimated to be up to $400-500 million each year.
To further highlight the fragility of frozen pipes, even a rupture as small as 1/8th of an inch can release up to 250 gallons of water per day.
When Is This Particularly Useful/Applicable?
The resident has left the household for an extended period and forgets to keep the thermostat set to at least 55 °F
The resident forgets to turn on the tap to let a little trickle run through the pipe before leaving
GRAINGER ENGINEERING
Why Is This Worth Solving?
ELECTRICAL & COMPUTER ENGINEERING

## Slide 4
Solution
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
2 prevention methods automatically triggered upon crossing 55 °F:
A valve system that opens to allow water to flow through the pipe to prevent the water from being stagnant and freezing
A notification sent to the designated resident's smartphone to alert them of the current water temperature and the potential imminent risk of a pipe burst

## Slide 5
Test Results
Successful Implementation of All 3 High-Level Requirements
Demo Video
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 6
System is triggered only when the temperature sensor output reads at or below 13.0 °C/55 °F.
A push notification is sent to the mobile device using Wi-Fi upon Raspberry Pi receiving low temperature reading.
Water is deposited to the pipe over the course of 5 seconds so that the movement from trickling water prevents the pipe from freezing.
GRAINGER ENGINEERING
High Level Requirements
ELECTRICAL & COMPUTER ENGINEERING

## Slide 7
GRAINGER ENGINEERING
VIDEO
LINK
ELECTRICAL & COMPUTER ENGINEERING

## Slide 8
Design Overview
Block Diagram
Major Components
Subsystems
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 9
GRAINGER ENGINEERING
Block Diagram
ELECTRICAL & COMPUTER ENGINEERING

## Slide 10
ATMega328P-PU Microcontroller
Interfaces with digital temperature sensor output, LCD display, and raspberry pi 4
Programmed via USB 3.0 Type A port and the Arduino IDE software
Waterproof DS18B20 Digital Temperature Sensor
Waterproof
Usable temperature range:
  -55°C to 125°C
  -67°F to 257°F
+/- 0.5°C tolerance from –10°C to +85°C
Uses 1-Wire Interface
GRAINGER ENGINEERING
Microcontroller Subsystem
ELECTRICAL & COMPUTER ENGINEERING

## Slide 11
Power
12V DC wall adapter
MCU Connection
Transistor gate pin connected to digital I/O of ATmega328
Switch closes for 5s when temperature was 55 °F or lower
  12V power
  Water flows
GRAINGER ENGINEERING
Valve Control Subsystem
ELECTRICAL & COMPUTER ENGINEERING
Notes: Benedicta

## Slide 12
Raspberry Pi
Also continuously reads the digital output of the temperature sensor via 1-Wire protocol
Connected to wi-fi network of user's home
Sends a push notification to user's mobile phone when temperature drops below threshold and valve system is activated
  User can be anywhere with internet
Python script
  requests and w1thermsensor libraries
  User token stored in yaml for security
GRAINGER ENGINEERING
Notification Subsystem
ELECTRICAL & COMPUTER ENGINEERING
Notes: Benedicta

## Slide 13
IMAGE / GRAPHIC
Complications
Short Circuit
  Different thicknesses of routing nets under MCU
  Did not use backside of PCB
  Lack of knowledge first time around
    Use of SMD rather than THT
    Faulty connections
Flipped pins
Multimeter suggested voltage was dispersing properly across components
  Resistor read correct resistance as well
GRAINGER ENGINEERING
PCB - 1
ELECTRICAL & COMPUTER ENGINEERING
Notes: Benedicta

## Slide 14
Breadboard Prototype
Hardware consisted mostly of I/O with DS18B20 Sensor
  Serial and simple
  No major hardware issues
Software
  OneWire
  DallasTemperature
  LiquidCrystal
GRAINGER ENGINEERING
IMAGE
ELECTRICAL & COMPUTER ENGINEERING

## Slide 15
IMAGE / GRAPHIC
Changes
GRAINGER ENGINEERING
PCB - 2
ELECTRICAL & COMPUTER ENGINEERING
Added test points
  LED
Used both sides of PCB
  Did not route under components
Included more headers
  More flexibility
    5v header could act as input or output depending on how power was connected
    Backup pins if routings were wrong
Minimized SMD parts even more
  THT microcontroller and resistors
Notes: Benedicta

## Slide 16
GRAINGER ENGINEERING
Requirements & Verifications
ELECTRICAL & COMPUTER ENGINEERING
Component | Requirements | Verification
NMOS Transistor & Solenoid Valve | 1. Provide 12 VDC +/- 10% from a 10.8 VDC to 13.2 VDC solenoid valve regulated by a 5 VDC microcontroller. | 1. Using a NMOS transistor, connect a digital I/O pin from the ATmega328p, set as an output, to the "Gate" pin of the transistor and only close (set pin to HIGH) the gate when the temperature reading reaches threshold. Observe the valve open during this time.
DS18B20 Digital Temperature Sensor Probe | 1. The system should only be triggered between a temperature of 13.0 °C and 14.0 °C, accounting for the +/- 0.5 °C tolerance of the DS18B20 Digital Thermometer. 2. Temp sensor conversion takes 750 s. Atmega328p and Raspberry Pi reading the DS18B20 temperature sensor do not cause read failures. | 1. Measure the temperature of the water in the reservoir using an alternate thermometer and compare the result to the output of the DS18B20 digital thermometer on the LCD. 2. Add a delay (2000) after a read of the temperature sensor to see the removal of read failures as the ATmega328p and the Raspberry Pi attempt to read temperature versus when the delay is not there.
ATmega328p Microcontroller | 1. The MCU burn bootloader works and is able to upload any sketch once flashed. Ability to interact with incoming data signals and sensors. | 1. Connect an LED to an analog pin of the microcontroller. Set the LED to blink every second. After proper programming of the board through USBasp, one should see the LED blink in 1 s intervals.

## Slide 17
Challenges
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 18
Sourcing the short in PCB – 1
Dealing with enterprise wifi for notification system
Eliminating interference between the reads of the ATmega328p and the Raspberry Pi
Verifying soldering connections
GRAINGER ENGINEERING
Challenges
ELECTRICAL & COMPUTER ENGINEERING

## Slide 19
Conclusions
ELECTRICAL & COMPUTER ENGINEERING
GRAINGER ENGINEERING

## Slide 20
Fully functional demonstration of all three high-level requirements with working PCB
Acquired Skills:
Figuring out which components to use and best suit the needs of our project
Powering components with different voltage requirements
PCB design
Debugging PCB on breadboard prototype
Programming Waterproof DS18B20 Digital Temperature Sensor
Programming LCD Display
Programming solenoid valve
Programming Raspberry Pi to send notification to smartphone
Learning how to integrate subsystems to operate cohesively and in unison
GRAINGER ENGINEERING
Conclusions
ELECTRICAL & COMPUTER ENGINEERING

## Slide 21
Future Improvements
ELECTRICAL & COMPUTER ENGINEERING
GRAINGER ENGINEERING

## Slide 22
variable rate of water flow dependent on current pipe water temperature
replacing the Raspberry Pi with a more affordable piece of hardware such as an ESP32 Wi-Fi Module
GRAINGER ENGINEERING
Future Improvements
ELECTRICAL & COMPUTER ENGINEERING
smart thermostat integration

## Slide 23
Image Links
best-smart-thermostats-refresh-lead-1663969484.jpg
https://www.controlvalves.com/product/model-127fav-flow-control-and-programmable-solenoid-valve/
ESP32 wifi module
https://www.etechnophiles.com/fqp30n06l-mosfet-pinout-datasheet-arduino-project/
https://core-electronics.com.au/plastic-water-solenoid-valve-12v-1-2-nominal.html
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 24
Thank you for watching!
The floor is open for Q/A 
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING