## Slide 1
RFID Lock
Team 40
By Nich Rogers, David Sullivan, Arely Irra

## Slide 2
Agenda:
1. Introduction
2. Functionality
3. Successes & Failures
4. Conclusions & Further Work
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
2/24

## Slide 3
Why are RFID locks useful?
Examples of uses
  college apartments, visually impaired, health conditions
Rent friendly version
  Do NOT exist
  Replace entire handle, deadbolt
    Security deposit
GRAINGER ENGINEERING
Objective: What are we solving?
ELECTRICAL & COMPUTER ENGINEERING
3/24
Notes: Renter friendly solutions do not exist or is not being made by possible competitors and physical design aspect would allow ours to be a unique entry into the market

## Slide 4
Physical Design
Competitive
Current Infrastructure
  Allow normal use
GRAINGER ENGINEERING
Initial Design
ELECTRICAL & COMPUTER ENGINEERING
4/24
Notes: Initial designs of the product focused on the physical as that is what would set our product apart from competitors. Our product would exist with current infrastructure on apartment doors to allow continued access of current keys for roommates, landlords etc to have access but allow for new RFID access as well.

## Slide 5
Prototype
Machine Shop
  Design discussion
  Torque
  Base plate vs. final
Needs more refinement
GRAINGER ENGINEERING
Design Changes
ELECTRICAL & COMPUTER ENGINEERING
5/24
Top View
Front View
Back View
Notes: The idea itself was workshopped with the machine shop on how to mount a servo motor to effectively rotate the lock. It was recommended that we use a high-torque servo motor mounted to the lock via a custom metal base plate. It ended up almost replacing the inside portion of the deadbolt entirely and needs more refinement to be the rent friendly product we had in mind but at this point the physical aspect was not the main focus anymore.

## Slide 6
IMAGE / GRAPHIC
High Level Overview of block diagram
GRAINGER ENGINEERING
Block Diagram
ELECTRICAL & COMPUTER ENGINEERING
6/24
Notes: Here is a quick overview of the high level subsystems of our design. We had three main subsystems: the power subsystem, the door management subsystem and the user interface subsystem. The power subsystem consists of the wireless power transmitter and receiver that form the heart of the project. The door management subsystem is the controlling component of the project, consisting of the the NFC scanner, microcontroller and servo motor that all interact to unlock/lock the door. Lastly, for user interfacing, we have a button to add a key to the system’s memory.

## Slide 7
Functionality
Test results and data
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
7/24

## Slide 8
Power Circuits
Induction Power
  LC Oscillator
Two separate circuits
  Source and Sink
GRAINGER ENGINEERING
Brief Overview
ELECTRICAL & COMPUTER ENGINEERING
8/24
Notes: Our design was meant to use induction charging. Induction charging uses an alternating current in one inductor to induce an emf in another inductor. Air is the medium this energy is transferred over most commonly and in our circuit.
Since this requires two separate circuits for one circuit will act as the power source and the other as the power sink. The power sink has an output of 5V where there computation and functional components will be connected (microcontroller, motor, RFID reader etc…)

## Slide 9
Operating power source
Induction power supply
  Mosfet
  ~50 ns
GRAINGER ENGINEERING
Power Supply
ELECTRICAL & COMPUTER ENGINEERING
9/24
Notes: Using induction to supply power means we need an alternating current source.
Using a mosfet as a switch we are able to get an AC current through the induction charging coil. This current oscillation reflected by the oscillating voltage swapped at a rate of ~50 nanoseconds with the inductor changing from a voltage of ~11.5 V to ~5.5 V with reference to ground.

## Slide 10
Powersink
EMF
1.7 Volts, at .1 Amps
  Needed 5V at .4745A
  Compensation
  1,500 uses
GRAINGER ENGINEERING
Power Supply
ELECTRICAL & COMPUTER ENGINEERING
10/24
Notes: The alternating current induces an emf in the opposite coil when placed in vicinity
Output
This AC emf induced was converted to a DC voltage. This voltage only managed to hit 1.7V at .1 A. Not close enough to the required 5V, .4745 A.
Adding a 3.6 V battery to boost the voltage allowed the linear voltage regulator to charge to the necessary voltage within a range of ~3.5-30 seconds.
When removing testing outliers this goes down to ~3.5-8 seconds.

## Slide 11
Discharging Trials
GRAINGER ENGINEERING
Circuit Charging Data
ELECTRICAL & COMPUTER ENGINEERING
Charging Trials
11/24

## Slide 12
GRAINGER ENGINEERING
RFID/NFC Implementation
ELECTRICAL & COMPUTER ENGINEERING
12/24
Notes: Unfortunately, we were unable to get our system soldered onto the PCB and so ended up breadboarding the system to get the desired functionality. The circuit itself is relatively simple, with the microcontroller connected to the NFC scanner, servo motor and button. Most of the magic here occurs in the microcontroller where the key is read and stored. The button on the

## Slide 13
GRAINGER ENGINEERING
RFID/NFC Implementation
ELECTRICAL & COMPUTER ENGINEERING
https://youtu.be/UBmJpX4orZQ
13/24
Notes: Here is a quick demonstration of the NFC system working in full. Try to not to read the numbers on my credit card too closely :)

## Slide 14
IMAGE / GRAPHIC
Necessary Considerations
Pros:
  NFC is ubiquitous
  Well documented
  Expandable to Smartphone Applications
Cons:
  NFC is relatively short range
  RF communication protocols are confusing for first time developers
GRAINGER ENGINEERING
RFID Considerations/Concerns
ELECTRICAL & COMPUTER ENGINEERING
14/24

## Slide 15
Power Circuits
GRAINGER ENGINEERING
PCB Designs
ELECTRICAL & COMPUTER ENGINEERING
15/24

## Slide 16
Door Unit PCB P1
GRAINGER ENGINEERING
PCB Designs
ELECTRICAL & COMPUTER ENGINEERING
16/24

## Slide 17
Door Unit PCB P2
GRAINGER ENGINEERING
PCB Designs
ELECTRICAL & COMPUTER ENGINEERING
17/24

## Slide 18
Successes & Failures
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
18/24

## Slide 19
LC Oscillator
Troubleshooting
  Mosfet, and current ratings
Induced emf
Too low
  1.7 V boosted with battery
Solutions
Coil turns, area, B field/current
  Higher rated parts
Capacitors
Voltage
  output times
  discharge times
GRAINGER ENGINEERING
Power circuit
ELECTRICAL & COMPUTER ENGINEERING
19/24
Notes: LC Oscillator
The power source circuit is an LC Oscillator which took more troubleshooting than anticipated. Taking into account current draw we were able to source higher current rated resistors from ECE store and got this working.
Induced emf
While the coupled induction coils produced an emf in the sink, it was not strong enough to hit 5V output at .4745A.
Induced emf is based on:
Coil turns
Change in flux over time
  larger area, higher turn count, or increased B field
    Increased current flow through power source
      New mosfet and resistors with even higher current ratings.
Capacitors
Voltage output times
Voltage discharge times

## Slide 20
RFID Reader
Differentiating between different NFC protocols
NFC has multiple sub protocols, each with different key lengths
Need more data on power requirements
Successfully able to read and decode NFC cards
Microcontroller
Flash Memory
Too many reads and writes
Successfully wrote keys to memory
Keys overwriting each other, could unlock with unadded keys
Like RFID Reader, need accurate power measurement
Servo Motor
Voltage Requirements
Initial measurements incorrect, to run successfully, servo required 5V/3A
GRAINGER ENGINEERING
Lock Management Subsystem
ELECTRICAL & COMPUTER ENGINEERING
20/24
Notes: LC Oscillator
The power source circuit is an LC Oscillator which took more troubleshooting than anticipated. Taking into account current draw we were able to source higher current rated resistors from ECE store and got this working.
Induced emf
While the coupled induction coils produced an emf in the sink, it was not strong enough to hit 5V output at .4745A.
Induced emf is based on:
Coil turns
Change in flux over time
  larger area, higher turn count, or increased B field
    Increased current flow through power source
      New mosfet and resistors with even higher current ratings.
Capacitors
Voltage output times
Voltage discharge times

## Slide 21
Power Transceiver, Receiver and MCU
PCB with power receiver and microcontroller:
last minute changes
cost us PCB delivery time
Late parts delivery
Burning through parts
Instead of waiting for the PCB
Breadboard testing/debugging
dev board simulation
GRAINGER ENGINEERING
PCB
ELECTRICAL & COMPUTER ENGINEERING
21/24
Unit PCB
User PCB

## Slide 22
Conclusion and Further Work
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
22/24

## Slide 23
Further Adjustments
Microcontroller currently boots from cold each time the power brick comes into contact
  Overuse of flash memory
  Could be resolved with small battery
Onboard Flash vs SPI Flash
  Current System utilizes onboard flash
  Frequent reads and writes degrade flash which could eventually corrupt the program
  Move to entirely ram based program or use off-board flash
GRAINGER ENGINEERING
Takeaways
ELECTRICAL & COMPUTER ENGINEERING
23/24

## Slide 24
Power, PCB, and Casing
Further research and testing for power
New PCB designs
Waterproof casing
Testing for user friendliness
Stretch Goal
Develop an application that stores key cards
Use systems like Samsung Reverse wireless charging for powering (Qi standard compliance)
GRAINGER ENGINEERING
Further Work
ELECTRICAL & COMPUTER ENGINEERING
24/24
Notes: Future work includes further research and testing to reach a level of power that’s strong enough to power the motor through wireless charge, as well as printing new PCB designs to reflect these changes.
Additional work includes creating a waterproof renter friendly casing that would mount around the deadbolt, and testing for user friendliness using the speakers and LED’s to indicate when an RFID has been scanned.
A stretch goal that would be beneficial for productization would be to develop an application that can store key cards. Another additional feature would be to utilize a system such as Samsung’s reverse wireless charging to power the system without needing the power brick.