## Slide 1
Team 46: Smart Light Switch
Electrical & Computer Engineering
Christine Chung, Michael Chen, Spencer Robieson
1
Notes: Michael

## Slide 2
GRAINGER ENGINEERING
Agenda
ELECTRICAL & COMPUTER ENGINEERING
Problem/Solution
Project Requirements
Block Diagram and Design Changes
Subsystem Requirements
Detailed Design Description
Successes and Challenges
Key Takeaways
2
Notes: Michael

## Slide 3
GRAINGER ENGINEERING
Objective
ELECTRICAL & COMPUTER ENGINEERING
Problem
Binary switches have no brightness control
No automatic light dimming
~10% of a home’s energy use is used for lighting
Neutral wiring is required for smart switches
3
Notes: CC

## Slide 4
GRAINGER ENGINEERING
Objective
ELECTRICAL & COMPUTER ENGINEERING
Solution
Create a smart switch that can connect to existing light switches and intelligently control lights
Sensors will be able to detect the ambient light and any obstructions
Control system will adjust the power level of the lights to maintain a constant, user set level
No neutral wiring will be required
4
Notes: Michael

## Slide 5
GRAINGER ENGINEERING
Objective
ELECTRICAL & COMPUTER ENGINEERING
High Level Requirements
Be able to connect to any existing light fixtures and switch. No neutral wire will be required. | Maintain a constant light level for the room at desired brightness.
Prevent unintended fluctuations in light from temporary obstructions in front of the switch. | Have an override switch that allows for absolute control of the lights.
5
Notes: Spencer

## Slide 6
GRAINGER ENGINEERING
Original Design
ELECTRICAL & COMPUTER ENGINEERING
Three separate subsystems
5 V converter for power
Microcontroller connected to sensors and user interface
Triac handles AC mains voltage
6
Notes: CC

## Slide 7
GRAINGER ENGINEERING
Design Changes
ELECTRICAL & COMPUTER ENGINEERING
Eliminated AC/DC conversion
Changed luminosity sensor so linear regulator isn't needed
Triac – changed to directly powering using microcontroller
7
Notes: CC

## Slide 8
GRAINGER ENGINEERING
Functional Blocks and Requirements
ELECTRICAL & COMPUTER ENGINEERING
Control Subsystem | Sensor Subsystem | Power Subsystem
Microcontroller interfaces with user interface and light bulb simultaneously | Ultrasonic sensor accurately detects a person between the heights of 5’ and 6’ within 20 cm. | Flyback converter outputs 5V ±10%
Microcontroller siphons power from AC mains, while ensuring the light stays off. | Luminosity sensor detects the typical brightness in a room from 100-4000 lumens. | Flyback converter functions from 5V-120V input
8
Notes: Spencer

## Slide 9
GRAINGER ENGINEERING
PCB Design
ELECTRICAL & COMPUTER ENGINEERING
Front
Back
9
Notes: CC

## Slide 10
GRAINGER ENGINEERING
Project Build – Sensors
ELECTRICAL & COMPUTER ENGINEERING
HC-SR04 ultrasonic sensor to detect distance of obstructions
  Outputs analog voltage
  VEML7700 luminosity sensor to detect room brightness
  Communicates using I2C
Ultrasonic sensor
Luminosity sensor
10
Notes: Spencer

## Slide 11
GRAINGER ENGINEERING
Project Build – Control Subsystem
ELECTRICAL & COMPUTER ENGINEERING
Using ATmega328P
Takes input from user interface and sensors and utilizes PID feedback loop to control dimming
Outputs PWM square wave to LEDs
Tested using an Arduino
Control Flowchart
PID Control Feedback Loop
11
Notes: Spencer / Michael

## Slide 12
GRAINGER ENGINEERING
Project Build - Demo
ELECTRICAL & COMPUTER ENGINEERING
12

## Slide 13
GRAINGER ENGINEERING
Project Build – Control
ELECTRICAL & COMPUTER ENGINEERING
Microcontroller
13
LED array
User light level control
Manual override
Notes: Spencer

## Slide 14
GRAINGER ENGINEERING
Project Build – Triac Dimming
ELECTRICAL & COMPUTER ENGINEERING
Triac Dimming Schematic
Triac
Optoisolator
Expected Waveform
14
Notes: CC

## Slide 15
GRAINGER ENGINEERING
Project Build - Power Conversion
ELECTRICAL & COMPUTER ENGINEERING
Power Conversion Schematic
PCB Testing
Breadboard Testing
15
Notes: CC

## Slide 16
GRAINGER ENGINEERING
Project Build – Power Conversion
ELECTRICAL & COMPUTER ENGINEERING
Power Conversion Schematic
Rectifier
16
Notes: CC

## Slide 17
GRAINGER ENGINEERING
Project Build – Power Conversion
ELECTRICAL & COMPUTER ENGINEERING
Power Conversion Schematic
Transformer w/ Auxiliary Winding
Transformer w/ Auxiliary Winding
Switching Control
Why Flyback?
Buck-boost topology for low-power DC/DC
Isolation through transformer provides safe functionality
Output voltage controlled by switching transistor UCC28720
Design Parameters
Vin (V) | 85-132
Vout (V) | 5
Iout (A) | 0.2
Pout (W) | 1
17
Notes: A flyCCback converter is a type of DC-DC converter that uses a transformer to convert a DC input voltage to a DC output voltage. It is called a "flyback" converter because the energy is stored in the transformer during the first half of the switching cycle and then released or "flyback" during the second half of the cycle.
Here's a simplified explanation of how a flyback converter works:
During the first half of the switching cycle, a transistor (usually a MOSFET) is turned on, allowing current to flow from the input voltage source to the transformer primary winding. At the same time, a diode connected to the transformer secondary winding is reverse-biased, preventing current flow to the output.
Energy is stored in the transformer core and its associated windings as a magnetic field during the first half of the switching cycle. The amount of energy stored is proportional to the voltage and the time that the primary current is flowing.
During the second half of the switching cycle, the transistor is turned off, and the energy stored in the transformer is released into the secondary winding. This causes a voltage to be induced in the secondary winding, which is rectified by the diode and filtered by an output capacitor.
The output voltage is regulated by controlling the duty cycle of the switching transistor. This is usually done using a feedback loop that compares the output voltage to a reference voltage and adjusts the duty cycle to maintain the desired output voltage.
The flyback converter topology allows for the use of a single transformer to provide isolation between the input and output, which is useful in many applications.
Overall, the flyback converter is a simple and efficient way to convert DC voltages in many applications, including power supplies for consumer electronics, LED lighting, and automotive electronics.

## Slide 18
GRAINGER ENGINEERING
Test Results – Sensors
ELECTRICAL & COMPUTER ENGINEERING
Ultrasonic Sensor
Luminosity Sensor
Distance to nearest object in cm
If switch is blocked or not
Light level in lux
Output taken from serial monitor on Arduino
18
Notes: Spencer

## Slide 19
GRAINGER ENGINEERING
Test Results – Sensors/Control
ELECTRICAL & COMPUTER ENGINEERING
Control Loop
Current brightness vs user desired
Difference between current and desired light
Duty cycle of PWM output
Combining microcontroller and sensors using Arduino
Arduino serial monitor output
19
Notes: Michael

## Slide 20
GRAINGER ENGINEERING
Test Results – Power
ELECTRICAL & COMPUTER ENGINEERING
Flyback Converter Test Results
5V output
80V input
17V Auxiliary Voltage
20
Notes: CC

## Slide 21
GRAINGER ENGINEERING
Successes & Challenges
ELECTRICAL & COMPUTER ENGINEERING
Successes | Challenges
Sensor subsystem build and integration | Debugging on PCB
Control subsystem design and integration | Rectifier and triac
Power conversion with flyback | 
Adapted to challenges that came up and modified design as necessary | 
21
Notes: Michael: Success
CC: Challenges
Sensor subsystem build and integration:
With slight changes to sensor parts, we successfully verified operation of sensors and inputs
Communcation between control and sensors verified as well
Control subsystem design and integration:
Able to successfully implement the PID control algorithm and steadily achieve target light level in our test box using the sensors and controls from the sensor subsystem
Power conversion with flyback:
Achieved 5V output from flyback circuit
Challenges
Debugging on PCB:
Had to switch to debugging on a breadboard to shorten the debugging cycle
We were able to get most parts of our design working on the breadboard

## Slide 22
GRAINGER ENGINEERING
Conclusion
ELECTRICAL & COMPUTER ENGINEERING
Key Takeaways:
We learned a lot about:
Designing and testing power systems, especially for high voltage
PCB design and debugging
Planning and executing a project with various subsystems and design phases
If we redesigned our project, we would:
Adjust timeline to allow more time for PCB debugging & reordering
Investigate rectifier principles
Future Work:
Adjust for use with actual light fixtures
Package into a smaller form factor
22
Notes: Spencer
Introduction to your team and your project.
Objective. What problem are you solving?
Brief review of original design, statement on areas of design that changed, and overview of each functional block's requirements.
Description of project build and functional test results. You can choose to include a short (30s) video of your project here.
Discussion of successes and challenges, as well as explanations of any failed verifications demonstrating and understanding of the engineering reason behind the failure
Conclusions from the project: what did you learn, what would you do differently if you redesigned your project, etc.
Recommendations for further work.

## Slide 23
23