## Slide 1
Scanning Bluetooth to FM Transmitter
Team 18
Electrical & Computer Engineering
2 May 2023

## Slide 2
IMAGE / GRAPHIC
Existing Devices
Current products stream user’s audio from their phone to the car radio via FM
Problem
Devices can only transmit
Require user input to change the frequency
GRAINGER ENGINEERING
Bluetooth to FM Transmitters
ELECTRICAL & COMPUTER ENGINEERING
Product currently for sale
Notes: Madigan

## Slide 3
Device out of enclosure
Add FM Reception Functionality
Device will scan for empty stations
Takes less driver focus off of road
High-Level Requirements
Device will connect and receive audio data via Bluetooth.
Device will transmit audio via FM.
Device will scan FM stations and automatically select one with minimal interference.
GRAINGER ENGINEERING
Solution
ELECTRICAL & COMPUTER ENGINEERING
3
Device in enclosure
Notes: Dan

## Slide 4
GRAINGER ENGINEERING
Block Diagram
ELECTRICAL & COMPUTER ENGINEERING
4
Notes: James

## Slide 5
Back side of PCB
ESP32-WROOM-32
Provides built-in Bluetooth, communication protocols, and GPIO
Changed microcontroller to older model for proper Bluetooth support
Bluetooth
Built off of template provided by Espressif Audio Development Framework
Used Bluetooth A2D and AVRC profiles and interrupts for front panel I/O
GRAINGER ENGINEERING
Microcontroller & Bluetooth
ELECTRICAL & COMPUTER ENGINEERING
5
Notes: James

## Slide 6
Si4706 and Loop Antenna
Receives FM and outputs audio
Loop antenna designed per the manufacturer’s Antenna Design Guidelines
Signal measurement capability (signal strength measurement)
Our design uses signal strength measurement to find vacant channels
Testing
Injected tone using signal generator, took strength measurement
Observed spectrum using spectrum analyzer, compared to data from IC
Added more loops to antenna
Significant coupling between receiver and transmitter
GRAINGER ENGINEERING
Receiver
ELECTRICAL & COMPUTER ENGINEERING
6
Receiver verification input setup

## Slide 7
GRAINGER ENGINEERING
Receiver
ELECTRICAL & COMPUTER ENGINEERING
7
FM Spectrum
Voltage (dBμV)
Frequency (Hz)
Channel Selection Algorithm
Device continuously scans FM spectrum
Updates rolling average of last 5 measurements
We impose threshold
Sort least to greatest
Finds station with two neighbor stations below threshold on either side

## Slide 8
Si4711 and Loop Antenna
Si4711 takes digital audio input and outputs FM signal
Loop antenna designed per the manufacturer’s Antenna Design Guidelines
Testing
Verified transmission by observing output of IC on a spectrum analyzer
Qualitatively confirmed by listening to transmission on a radio
Verified that transmission is not received past 3m
GRAINGER ENGINEERING
Transmitter
ELECTRICAL & COMPUTER ENGINEERING
8
Transmitted signal strength seen on the spectrum analyzer

## Slide 9
TPS5403
Integrated buck converter capable of outputting 1.7A at 3.3V with input voltage between 4.5-28 V
Testing
Initial configuration unable to support the startup power draw
By raising the switching frequency, the issue was solved
Higher switching frequency raised noise floor of receiver
GRAINGER ENGINEERING
Switching Regulator
ELECTRICAL & COMPUTER ENGINEERING
9
Increased noise floor due to regulator
Noise floor without regulator

## Slide 10
NCP1117
Linear regulator capable of outputting 1A at 3.3V with input voltage between 4.5-20V
Traces and pads were manually cut since PCB was not designed for this device
Testing
Placed on electronic load at 600mA
Ran for 58 seconds before dropping the voltage due to overheating
GRAINGER ENGINEERING
Linear Regulator
ELECTRICAL & COMPUTER ENGINEERING
10
Testing the linear regulator
Cutting the PCB
Notes: James

## Slide 11
Successful Project Despite Challenges
Completed the project based on our initial requirements
Added features not initially planned (e.g., AVRCP and RDS)
Challenges and Learning Opportunities
Avoid placing the transmitter and receiver close to one another to limit coupling
Power supply should be more thoroughly considered and be tested more rigorously
RF circuits have high susceptibility to noise, even at relatively low frequencies
GRAINGER ENGINEERING
Conclusions
ELECTRICAL & COMPUTER ENGINEERING
11

## Slide 12
Higher Audio Fidelity
Transmit digital audio for HD Radio or similar technologies
Refine Form Factor
Smaller display (e.g., a 7-segment display) and microcontroller
ESP32 could serve as a base for other devices in the vehicle
GRAINGER ENGINEERING
Further Work
ELECTRICAL & COMPUTER ENGINEERING
12

## Slide 13
Thank you to our TA and ECE445 course staff
Questions? Comments? Advice?
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
13