## Slide 1
BLUETOOTH SPEAKER WITH MOTION-BASED AUTOMATED VOLUME ADJUSTMENT
ECE 445 - Team 69
Chirag Kikkeri
Raj Pulugurtha
Dhruv Vishwanath
Notes: Raj

## Slide 2
GRAINGER ENGINEERING
Problem
ELECTRICAL & COMPUTER ENGINEERING
Distracted driving is an issue for everyone using the roads
Playing music in the car while driving is a hassle
Notes: Raj

## Slide 3
Speaker that changes volume based on change in speed
Portable with Bluetooth functionality
Fulfills needs for different types of users
Speaker system has a “stationary mode” and a “moving mode”
GRAINGER ENGINEERING
Solution
ELECTRICAL & COMPUTER ENGINEERING
Notes: Raj

## Slide 4
Front and rear images of our final product showing some of the components inside
GRAINGER ENGINEERING
Final Product
ELECTRICAL & COMPUTER ENGINEERING
Notes: Raj

## Slide 5
Video demonstration of our speaker changing volume as speed changes in the car
GRAINGER ENGINEERING
Final Product
ELECTRICAL & COMPUTER ENGINEERING
https://drive.google.com/file/d/1nKspFGlMjxZxkiGdCIF0npBenQMTZHf0/view
Notes: Raj

## Slide 6
High Level Requirements
Speaker volume changes automatically in driving mode at a fixed rate of 3 dB for a change of 15 MPH
In stationary mode the speaker should be controlled manually using buttons
Any Bluetooth device should be able to transmit media continuously to the system at 2.1 Mbps and the system will play media at an audio quality of 80 dB Signal to Noise ratio
GRAINGER ENGINEERING
Design Review Refresher
ELECTRICAL & COMPUTER ENGINEERING
Notes: Dhruv
After making adjustments from the Design Review, we thought our approach would be straightforward, as all we had to do is test our idea on a breadboard, build a PCB with that design, and then implement the same thing on the PCB. Easy, right?

## Slide 7
RN52-I/RM116 has no breakout board
Unable to test the part without PCB
Forced us to change design
Need to change volume with microcontroller
GRAINGER ENGINEERING
Bluetooth Subsystem Changes
ELECTRICAL & COMPUTER ENGINEERING
Notes: Dhruv

## Slide 8
Changed to ESP32
Equipped with Bluetooth functionality
Simplified our design
Volume adjustment capabilities
GRAINGER ENGINEERING
Microcontroller Changes
ELECTRICAL & COMPUTER ENGINEERING
Notes: Dhruv
To compensate for RN 52, we changed to ESP 32

## Slide 9
Modified Bluetooth keyboard library
Wrote code to change volume through ESP32
Used accelerometer data for volume control
Accuracy of values cannot be determined before soldering
GRAINGER ENGINEERING
Software Implementation for ESP32
ELECTRICAL & COMPUTER ENGINEERING
Notes: Chirag
End slide with how our design on breadboard worked bc it produced volume and we got values from accelerometer, but we couldn’t test validity of values without wires soldered in

## Slide 10
PCB schematic design for speaker
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Raj

## Slide 11
GRAINGER ENGINEERING
PCB Footprint and Model
ELECTRICAL & COMPUTER ENGINEERING
Notes: Raj
Followed development board datasheet
Added female connectors for design flexibility
Connected extra GPIO pins for buttons
Successfully receives accelerometer data
Unable to produce speaker output
Time is starting to become a factor

## Slide 12
Retrieves acceleration on three axes
Converted data to velocity using Vf = V0 + at
Required additional thresholds to calibrate
Tested values in the car
Struggled with sensitivity and consistency
GRAINGER ENGINEERING
Accelerometer Subsystem
ELECTRICAL & COMPUTER ENGINEERING
Notes: Dhruv

## Slide 13
Put less focus on audio quality
Unable to implement stereo sound
Pins in design had been swapped
Audio amplifier has DAC capabilities
Used extra female connectors on PCB to connect to speaker
GRAINGER ENGINEERING
Speaker Subsystem
ELECTRICAL & COMPUTER ENGINEERING
Notes: -Dhruv

## Slide 14
Focus on sound output reduced buttons
Unable to show volume and battery levels
Rely on Bluetooth device to adjust music
Successfully added mode button
Able to implement and test debouncing
GRAINGER ENGINEERING
User Interface Subsystem Changes
ELECTRICAL & COMPUTER ENGINEERING
Notes: Chirag

## Slide 15
Used 5-volt battery pack
PCB has voltage regulator
Able to input 3.3 volts via Micro-USB
Checked for consistency by stress-testing
Can be recharged via USB-C
GRAINGER ENGINEERING
Power Subsystem
ELECTRICAL & COMPUTER ENGINEERING
Notes: Chirag

## Slide 16
Sample rate: 300 milliseconds
Window size: 10 samples
GRAINGER ENGINEERING
Moving Average
ELECTRICAL & COMPUTER ENGINEERING
Notes: Chirag

## Slide 17
Volume vs. speed relationship that we implemented for demonstration purposes
GRAINGER ENGINEERING
Testing and Results
ELECTRICAL & COMPUTER ENGINEERING
Speed in MPH | Relative Volume Level on iPhone
20-25 | 95%
15-20 | 90%
10-15 | 75%
5-10 | 60%
<5 | 45%
Notes: Chirag
- Add table with speeds here and discuss how this is what we got from the demo video

## Slide 18
High Level Requirements
Speaker volume changes automatically in driving mode at a relative rate of 15% for a change of 5 MPH
In stationary mode the speaker is controlled manually using buttons
Bluetooth transmits media continuously, resulting in a change of volume based on a moving average
GRAINGER ENGINEERING
Successes
ELECTRICAL & COMPUTER ENGINEERING
Notes: Raj
- Talk about how we made slight changes  Discuss why we made said changes

## Slide 19
Implementing stereo sound
Sensitivity of accelerometer for low speeds
Debugging PCB
Frying development boards for ESP32
GRAINGER ENGINEERING
Challenges
ELECTRICAL & COMPUTER ENGINEERING
Notes: Dhruv

## Slide 20
Improve the user interface of our product
Invest in higher quality parts
Implement stereo sound
Would modify our approach earlier
GRAINGER ENGINEERING
Outlook and Improvements
ELECTRICAL & COMPUTER ENGINEERING
Notes: Chirag
Want to add buttons and LEDs
Would improve accelerometer data and sound quality
Improves sound quality

## Slide 21
Volume stays at appropriate levels
Minimal interface reduces distractions
Mode button keeps user focused on task
GRAINGER ENGINEERING
Ethics
ELECTRICAL & COMPUTER ENGINEERING
Notes: Chirag

## Slide 22
Notes: Give special thanks to Abhisheka and Prof Fliflet