## Slide 1
AUTOMATIC PET DOOR​
Electrical & Computer Engineering
TEAM 27: HAIJIAN WANG​, HAORAN ZHENG​, ZHIHAO XU​

## Slide 2
GRAINGER ENGINEERING
Problem To Solve
ELECTRICAL & COMPUTER ENGINEERING

## Slide 3
For people living near the natural ecosystem, human-wildlife conflicts can frequently happen, and one type of such conflict is intruding wild animals.​
GRAINGER ENGINEERING
PROBLEM TO SOLVE​
ELECTRICAL & COMPUTER ENGINEERING
Hello there~

## Slide 4
A “welcome-all” pet door can cause some problem…
For small to medium-sized wild animals like raccoons and coyotes, the unlocked pet door can be an entrance to people's houses.
https://www.youtube.com/watch?v=yr1OcFafctI​
GRAINGER ENGINEERING
PROBLEM TO SOLVE
ELECTRICAL & COMPUTER ENGINEERING
I am coming…

## Slide 5
A “block-all” pet door also cause problems…
Locking the pet can prevent wildlife from intruding, but it will also keep the house owner's pets out of the door at the same time.
GRAINGER ENGINEERING
PROBLEM TO SOLVE
ELECTRICAL & COMPUTER ENGINEERING
May I come in?

## Slide 6
GRAINGER ENGINEERING
Project Overview
ELECTRICAL & COMPUTER ENGINEERING

## Slide 7
We built a door to welcome pets and prevent wildlife
When an object approaches our pet door, it should be able to execute the following sequential steps without any manual operation:
Detecting the approaching object
Identifying the species of the detected object
Locking/unlocking according to the determined species
GRAINGER ENGINEERING
PROJECT OVERVIEW
ELECTRICAL & COMPUTER ENGINEERING

## Slide 8
GRAINGER ENGINEERING
Concept Picture
ELECTRICAL & COMPUTER ENGINEERING

## Slide 9
GRAINGER ENGINEERING
Block Diagram Overview
ELECTRICAL & COMPUTER ENGINEERING

## Slide 10
GRAINGER ENGINEERING
Design Explanation
ELECTRICAL & COMPUTER ENGINEERING

## Slide 11
Our project can be divided into Five subsystems:​
Camera Subsystem
Motion Sensors Subsystem
Power Subsystem
Microcontroller
Notification Subsystem
GRAINGER ENGINEERING
Design EXPLANATION
ELECTRICAL & COMPUTER ENGINEERING
Design EXPLANATION

## Slide 12
IMAGE / GRAPHIC
IMAGE / GRAPHIC
Camera Subsystem
Requirement: this subsystem consists of a Raspberry Pi Camera Module 3 responsible for detecting the approaching animal and a Raspberry Pi 4 Model B responsible for identifying the approaching animal.​
GRAINGER ENGINEERING
Design EXPLANATION
ELECTRICAL & COMPUTER ENGINEERING

## Slide 13
IMAGE / GRAPHIC
IMAGE / GRAPHIC
Motion Sensor Subsystem
This subsystem consists of an Ultrasonic Distance Sensor to measure the approaching object's distance to our pet door, so the pet door will not unlock if no object is within a certain range.​
Requirement: it should measure the distance between the pet and the door and send a signal to the microcontroller.
GRAINGER ENGINEERING
Design EXPLANATION
ELECTRICAL & COMPUTER ENGINEERING

## Slide 14
IMAGE / GRAPHIC
IMAGE / GRAPHIC
Microcontroller
An ESP32-S3-WROOM-2 microcontroller
Requirement: provides the main control for our latch and speaker once receiving signals from Raspberry Pi and the Ultrasonic Distance Sensor.​
GRAINGER ENGINEERING
Design EXPLANATION
ELECTRICAL & COMPUTER ENGINEERING

## Slide 15
IMAGE / GRAPHIC
IMAGE / GRAPHIC
Notification Subsystem
This subsystem includes a Latch to Lock/unlock the door, and a Speaker to notify the house owner that the door is currently unlocked.
Requirement: After receiving the correct signal from the microcontroller, the speaker should ring, and latch should lock and unlock properly.
GRAINGER ENGINEERING
Design EXPLANATION
ELECTRICAL & COMPUTER ENGINEERING

## Slide 16
IMAGE / GRAPHIC
IMAGE / GRAPHIC
Power Subsystem
This subsystem consists of an HWE 12.8V 7Ah Battery and two RED WOLF Adjust DC Converters
Requirement: provide corresponding voltage and power to our whole system.
GRAINGER ENGINEERING
Design EXPLANATION
ELECTRICAL & COMPUTER ENGINEERING

## Slide 17
GRAINGER ENGINEERING
Concept Picture
ELECTRICAL & COMPUTER ENGINEERING

## Slide 18
GRAINGER ENGINEERING
Our Final Product ...
ELECTRICAL & COMPUTER ENGINEERING

## Slide 19
GRAINGER ENGINEERING
PCB Design and Results
ELECTRICAL & COMPUTER ENGINEERING

## Slide 20
GRAINGER ENGINEERING
PCB Design
ELECTRICAL & COMPUTER ENGINEERING

## Slide 22
GRAINGER ENGINEERING
SUCCESSES...
ELECTRICAL & COMPUTER ENGINEERING
We have a working ESP32 microcontroller on our PCB!

## Slide 23
GRAINGER ENGINEERING
SUCCESSES...
ELECTRICAL & COMPUTER ENGINEERING
AI and Camera:
  high true positive rate, high true negative rate
  Might detect a dog as a person, but it will eventually classify it as a dog
Power:
  Successful 12V, 5V, and 3.3V conversion.
  Using 3.3V microcontroller pin to control a 12V circuit with MOSFETs
Peripherals and Control:
  Control program on ESP32: decode, display, and decide
  Successfully reading from ultrasonic, outputting music from speakers, and unlocking latch.

## Slide 24
GRAINGER ENGINEERING
…AND CHALLENGES
ELECTRICAL & COMPUTER ENGINEERING
“No serial data connection” in Arduino
  Rx/Tx connections for UART
  Boot up the ESP32 with proper strapping pins: both GPIO 0 and EN to ground
ESP32 decided to burn itself and die
  Bad soldering
  Maybe due to the high current from the direct connection with Raspberry Pi

## Slide 25
GRAINGER ENGINEERING
…AND CHALLENGES
ELECTRICAL & COMPUTER ENGINEERING
Cannot get video stream from the camera in Python
  OpenCV build issues
  Raspberry Pi camera driver compatibility issues
Overheating voltage converter? Program not running? Floating signal voltages? ...
  ALL SOLVED

## Slide 26
GRAINGER ENGINEERING
Project Conclusion
ELECTRICAL & COMPUTER ENGINEERING
Sacrifices: 5 ESP32 chips, 6 Ultrasonic Sensors, 7 PCB boards, 10 AMS117-5V, trillions of capacitors and resistors.

## Slide 27
GRAINGER ENGINEERING
PROJECT CONCLUSION
ELECTRICAL & COMPUTER ENGINEERING
Lessons:
  PCB design process
    Pay attention to packaging and dimension
    Always consider the current and voltage limits in every connection
  Always do more
    Ordered excessive parts (Yes, we had thousands of capacitors)
    Designed extra pin connections
    Made multiple spare boards

## Slide 28
GRAINGER ENGINEERING
RECOMMENDED FURTHER WORK​
  Multithreading in Python to speed up the AI model​
  More integrated PCB: buck converter, auto reset, auto boot, USB connection​
  Customized trained AI model for specific pet
  Wireless Communication and Application

## Slide 29
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
In conclusion, we successfully designed the hardware and software that meet our requirements

## Slide 30
Thank You!
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING