## Slide 1: Sensing Instrument for Generating Haptic Touch – SIGHT
Team 30 – John Lee, Dip Patel, Jamiel Abed
ECE 445 Final Presentation – Spring 2023
TA - Dushyant Singh Udawat

## Slide 2: Agenda
Team/Project introduction
Project demonstration
Objectives
Design
Project build
Measurements
Successes
Conclusion

## Slide 3: We are SIGHT
Team Introductions
  Jamiel Abed – Computer Engineering
  Dip Patel – Computer Engineering
  John Lee – Electrical Engineering
What we built
  A modular system that can detect objects, their speeds, their distances, and use that information to deploy a haptic feedback relative to those metrics.
  In layman's terms: We built a device that detects objects and alerts the user of them.
  It alerts them with a haptic feedback of varying intensities depending on how far the object is and how fast it's approaching.

## Slide 4: What does it look like?

## Slide 5: Objective
What are we trying to do?
  Aid those who are visually impaired using ultrasonic detection
  This is not a replacement to walking sticks, this is meant to serve as a supplement
  Can detect further than what a walking stick can reach out to
(source: link.springer.com)

## Slide 6: Design
Figure 1: Block diagram

## Slide 7: Project Build
Physical Design
  Front
    HB100 Doppler Module
    HC-SR04 Ultrasonic Distance Sensor
  Back
    Haptic Pad (Mini Vibration Motor)
  Inside
    Development board containing microcontroller with flashed software
    6V- Battery Pack
Figure 2: Physical design schematic

## Slide 8: Testing Filtering
Median Filter
  We use a median filter to sift through windows of data at a time to minimize noise.
  This gives us more accurate readings by disregarding the extremities in each window.

## Slide 9: Before Filter
Figure 3: Distance plot before filtering

## Slide 10: After Filter
Figure 4: Distance plot after filtering

## Slide 11: Testing Distance
Measuring Distance Readings
  Distance Plot (left)
  Distance Values (right)
Figure 5: Distance test setup

## Slide 12: Distance Test
Within 2% error must be between 196-204 cm
Real average distance was 199.1 cm which is within the 2% error range
Figure 6: 2-meter distance test

## Slide 13: Testing Haptic Intensity
Measuring the intensity of haptic motors
  Records zeroes at the start
  Gradually spikes up to 100 (max intensity)
  Gradually spikes back down to zero (no feedback)
Figure 7: Haptic intensity readings

## Slide 14: Sucesses and Challenges
Successes
  Our project works as intended with good accuracy
  We stayed true to our original design and plan with this project
Challenges
  The Doppler Module does not contribute to the overall system as much as we had envisioned
    The Doppler Module can only provide data when it detects movement
  PCB flashing issues
    We also faced some issues getting our project to function on the PCB

## Slide 15: Conclusion
Things we have learned...
  Working with a microcontroller (STM32)
  How to interface and interconnect different systems together
  Building and planning a project from scratch (schematics, whiteboarding, ordering parts, etc...)
  Making and ordering a custom-built PCB
  Writing formal style documentation that captured the entire process
Things we would do differently...
  Use a bigger microcontroller (STM32F4 series) and not a nucleo development board (better hardware as well as onboard flashing)
  Get better sensors (better ultrasonics or maybe even LIDAR) since sensor reliability was a major obstacle in our project

## Slide 16: Future Work
Ideally would want to get better hardware and rethink the sensing algorithm
Work on extending the range as well as capabilities to work in different environments
Design better enclosure and work on miniaturizing components so that it is more ergonomic for the user
Getting this approved by NIH and FDA for public use

## Slide 17: Questions?