## Slide 1: Automatic Beverage Bottle Sorter
Group #5 Jiajun Huang, Joe Yu, Jingjie He
Dec. 5th, 2023

## Slide 2: Problem
Garbage bins in ECEB don't separate plastic and metal
People may not follow instructions on the garbage bin

## Slide 3
Solution
A garbage bin with an automatic sorting system
Sort metal cans, plastic bottles, or others and sorted into three separate bins
No need for instruction on garbage bins
No need for extra labor for sorting

## Slide 4
High level requirements
The system start sorting process after an object is inserted and finished analysis less than 40 seconds.
Our scaled down model should sort objects that are less than 1 inch in diameter and 3 inch in length.
It should correctly sort plastic bottles, metal cans, and others into three different bins.

## Slide 5
Block Diagram

## Slide 7
PCB
ESP-32
Laser diode
Switch
LDO
Metal Detector
Photo diode
Motors

## Slide 8
PCB Cont.

## Slide 9: Subsystems & Verification

## Slide 10: Power subsystem
Power subsystem consisted of a
7.5V AC to DC converter
5V AC to DC converter
LDO with 5V fixed output
LDO with 3.3V fixed output.
The 7.5V AC to DC converter is used to power two LDO and 5V AC to DC converter is used to power the metal detector

## Slide 11: Power Subsystem Requirements and Verification
Requirements | Testing Results
A 3.3/5 VDC regulator should provide 3.3/5 VDC +/- 0.1 V with at most 0.5A of current to power the microcontroller and the laser diodes | Output Voltage (3.3V LDO) = 3.3 V Output Voltage (5V LDO) = 5 V
AC/DC converter takes120 VAC as input and outputs 5/7.5VDC +/- 0.2V with 3 A current. | Output Voltage = 5 V Output Voltage = 7.5 V

## Slide 12: Challenge of Power subsystem
Why use 2 AC/DC converter?
Operating motor generates noise
Noise affect the performance of metal detector
Future improvements
Use one 7.5 V AC/DC converter with 3 LDOs:
  One 3.3 V
  Two 5V

## Slide 13
Analysis Chamber Design

## Slide 14
Analysis Chamber Design Cont.
Side View
Top View

## Slide 15: Control Subsystem
ESP32-S3 micro-controller
Mini-usb2UART protocol to load our programs.

## Slide 16: Control Subsystem Requirement and Verification
State verification table:
Requirement:
Correctly control the motor with sequential logic

## Slide 17: Motor Subsystem
Gate motor is response to close or release the insertion gate,
Ramp Motor 1&2 are carried with ramp that force the bin roll down to the specified location
Driven by pause wave with frequency of 50 HZ
Angle depends on pulse width
We use the <Deneyap_Servo.h> library to send various degree signal to achieve sequential control.

## Slide 18: Motor Subsystem Requirement and Verification
Angle verification
We expect each motor response to each state with correct angle
The measuring error should stay in requirements ± 1 degree
Requirements

## Slide 19: Sensing Subsystem
.
The sensing subsystem is composed of:
Two photo detector determine the shape of the bottle
The metal detector detect the material of the object
The switch detects the motion of the gate to know something is inserted in

## Slide 20: Sensing Subsystem: Photo Sensor
Reversed biased photo diode
The beam of the laser is aligned with the photo diode. The voltage output decreased when the laser is blocked by inserted object.

## Slide 21: Sensing Subsystem: Photo Sensor (First attempt)
Laser is on | Output voltage
YES | 0.381V
NO | 0.319V

## Slide 22: Photodiode Requirements and Verification
Test condition | Vout1 | Vout2
Directly hit by laser | 1.4V | 1.9V
Block by single layer of transparent plastic | 0.8V | 1.1V
Laser off | 47mV | 205mV
Requirements
Light sensing system should have at least 5mV change in its output voltage when blocked by plastic bottles. The lowest resolution for the ADC of our microcontroller is 0.56mV.

## Slide 23: Sensing Subsystem: Metal detector
.
The metal detector produce a AC singal with DC offset. The output value changed when
metal is inserted in and the frequency of AC singal and DC offset will increase. We
processed the output into a DC value within the measurment range of esp32

## Slide 24: Metal Detector Requirements and Verification
Requirements | Testing Results
Metal detector should have at least 200mV change in its output voltage when metal is inserted. The lowest resolution for the ADC of our microcontroller is 0.56mV. | 

## Slide 25: Sensing Subsystem: Switch
The switch connected 3.3 V to a 4700 ohm resistor
The voltage is high when the gate is open.

## Slide 26: Thank You!
Question?