## Slide 1
Fire and Gas Detection System with Real Time LED Navigation
Abel Garcia, Alex Parafinczuk, Jainam Shah
Electrical & Computer Engineering
5 May 2025

## Slide 2
Introduction
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 3
Problem Statement
Fires, whether accident or natural, can cause severe damages to homes and inhabitants
Modern Fire and Gas systems only trigger alarms and notify emergency services
Emergency response time isn't immediate
Residents may panic or become disoriented during these emergencies
A need exists for systems that both mitigate damage and a guide safe evacuation
Introduction
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Abel

## Slide 4
Our Projects Goals
Detects fires using temperature sensors and a microcontroller
Guides users to nearest exit with LED navigation
Closes vent automatically to suffocate the fire source.
Use Firebase-based web application as the main communication method with ESP-32
Designed for low power, quick response, and ease of use
Introduction
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Abel

## Slide 5
High Level Requirements
Web app for designing floor plan with rooms, doors, sensors, and exits. Algorithm identifies fire-affected zones and selects safest exit route. LED indicators display escape path with perfect accuracy.
Fire alarm triggers at ≥ 90℃; CO alarm at > 20 ppm
Control unit shuts off HVAC and closes vents when a fire is present. System resumes normal HVAC/vent operation after fire clearance
Introduction
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Jainam

## Slide 6
This is our Block Diagram for our Project, in total we have 5 different
subsystems and our communication protocol is GPIO
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Abel

## Slide 7
Ethical Considerations
According to Section I.1 of the IEEE Code of Ethics, we emphasized keeping the safety and wellbeing of the user as our highest priority in our design.
The user's data privacy was upheld in accordance with the ACM Code of Ethics Section 1.6, ensuring the private data they provide for the operation of our project is used responsibly.
Introduction
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Alex

## Slide 8
Design
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 9
CHART / GRAPH
Original PCB Design (First Round)
Design
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Alex

## Slide 10
Final Designs for the Main Control Board
and the Temperature Boards
Design
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Alex

## Slide 11
These two schematics show two subsystems which originally were
Designed this way, but were changed later
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Abel

## Slide 12
CHART / GRAPH
Changes Made in the Power Subsystem
Main Changes
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Abel

## Slide 13
CHART / GRAPH
Changes Made in the Sensor Subsystem
Main Changes
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Abel

## Slide 14
Control Subsystem Responsibilities
The microcontroller (ESP32) will manage all subsystems (except power) via GPIO.
Reads temperature and gas sensor data
Controls alarm, LED colors, digital servo motor, ICs, and gate drivers
Sends sensor data to web app and stores it in Firebase via Wi-Fi
Coordinates real-time system response based on sensor input
Control Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Jainam

## Slide 15
IMAGE / GRAPHIC
IMAGE / GRAPHIC
Control Subsystem Requirements
ESP32 cycles through the 8:1 multiplexer to read temperature data within milliseconds.
Triggers alarm if:
  Temperature > 90°C or
  CO > 100 ppm or CH₄ > 5000 ppm
Uses Wi-Fi to:
  Upload sensor data to Firebase
  Receive app commands and control LEDs, buzzer, and servo with high precision.
Buzzer emits 80dB alarm when hazard is detected
Control Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Jainam

## Slide 16
Power Subsystem Responsibilities
Powers the other four subsystems
Uses three 9V 1500mAh lithium-ion batteries
Supports four voltage levels: 7V, 5V, 3.3V, and 1.5V
Designed for low current draw; max expected current ~500mA
Three separate voltage rails to ensure each regulator has its own current draw
Power Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Alex

## Slide 17
IMAGE / GRAPHIC
IMAGE / GRAPHIC
Power Subsystem Requirements
Provide 3.3V ± 0.3V for ESP32
Supply 5V and 1.5V ± 0.2V for gas sensor heater pins
Deliver 5V ± 0.5V to temperature sensor, buzzer alarm, and 8:1 multiplexer and other relevant ICs.
Provide 7V to motor and support ~300-500 mA current draw during vent operation
Power Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Alex

## Slide 18
Sensor Subsystem Responsibilities
Collects environmental data for processing by ESP32
Includes:
  Gas Sensor(MQ-9B) to measure CO and CH₄ concentrations
  Temperature sensor (LMT84DCKR) with inverse voltage-temperature relationship
The temperature sensor was chosen to prevent ESP32 damage
Includes LEDs to visually indicated hazard detection in real time
Sensor Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Alex

## Slide 19
IMAGE / GRAPHIC
Sensor Subsystem Requirements
Temperature Sensor
  Range: -50°C to 150°C
  Typical accuracy: ±0.4°C
Gas Sensor
  CO detection: 10-500 ppm
  CH₄ detection: 300-1000 ppm
LED Indicators (upon fire detection):
  Red LED: 300 mcd
  Yellow LED: 600 mcd
  Green LED: 700 mcd
Sensor Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Alex

## Slide 20
Vent Subsystem Responsibilities
Automatically Closes Vents and shuts off HVAC during Fire Detection
Prevents fire spread by stopping the flow of oxygen
Vent Controlled by 7V digital servo motor (25kg*cm torque, 180° rotation)
Servo integrated into vent cover via ECE Machine Shop
Controlled by PWM signals from ESP32 for precise, incremental movement
Vent Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Alex

## Slide 21
IMAGE / GRAPHIC
Vent Subsystem Requirements
Motor must close vents after HVAC turns off during fire detection in two seconds.
Vents reopen only after fire is cleared
HVAC must shut off immediately upon fire signal to limit airflow
HVAC must return to normal operation once no hazard is detected
Vent Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Alex

## Slide 22
Notes: Alex

## Slide 23
App Subsystem Responsibilities
React frontend with Firebase backend for floorplan creation
Floorplan converted into a graph structure and stored in Firebase
ESP32 reads/writes sensor data and LED commands via Wi-Fi in real time
Optimal route is updated continuously until the hazard clears
Upon fire detection:
  App uses sensor data to assign hazard cost to each room
  Pathfinding algorithm identifies optimal exit route
  LED configuration for the route is stored in Firebase for ESP32 to display
App Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Jainam

## Slide 24
App Subsystem Requirements
Must display and store user-defined floor plan accurately
Must receive real-time sensor data via Wi-Fi without interruption
Must compute and communicate optimal escape route within five seconds of hazard detection
App Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Jainam

## Slide 25
IMAGE / GRAPHIC
Floor Plan Application
Drag and drop components
Room creation modal
Assign sensors and LEDs to rooms
Save floorplan to Firebase
React Application
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Jainam

## Slide 26
ESP32 Data
Store data from ESP, LED configuration, and floor plan
Upload sensor data in real-time
Update flag 'alarmTriggered' when threshold reached
  Runs pathfinding algorithm
Firebase – ESP32 Side
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Jainam

## Slide 27
Application Data
Store floorplan as graph for pathfinding
Rooms and exits as nodes; doors and stairs as edges
Room nodes updated with sensor data
Pathfinding stores LED configuration
Firebase – Application Side
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Jainam

## Slide 28
LED Configuration Algorithm
Uses A-star to find optimal path to each exit
Sensor data is updated before finding path
Uploads LED configuration to Firebase:
  Optimal path is in green LEDs
  Immediate danger is in red LEDs
  Sub-optimal areas are in yellow LEDs
  No possible path results in all yellow LEDs
Runs every 2 seconds while hazard detected
Starting room defined in code
  a
Pathfinding Algorithm
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Example: Start in Room 1, Fire in Room 3
Notes: Jainam

## Slide 29
Test Results
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 32
Successes and Challenges
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 33
What Went Right
Overall, we were able to complete most of the High-Level Requirements which we had aimed to accomplish for this project
Our schedule that we had planned helped in guiding us to complete the project
We were all excited and passionate to get the project to work
Successes
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Abel

## Slide 34
What Went Wrong
The Gas Sensor was the main challenge of the project
The Power Supply also gave issues that we forgot to account for
Challenges
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Abel, Introduce problems

## Slide 35
IMAGE / GRAPHIC
IMAGE / GRAPHIC
How it Works
Sensing layer: tin dioxide changes resistance in presence of gas
Voltage increases when gas is detected.
Two Power inputs:
  5V for sensor operation
  Heater element across pins 2 & 5 to enable gas detection
Heater cycling required:
  5V for 60s, then 1.5V for 90s to complete detection cycle
Initial Design Issue:
  Used a 2:1 Mux, but it could not handle 200 mA current draw (limited to 50 mA).
  Solution required direct switching or higher-current routing method
Challenges: Gas Sensor Problem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Abel

## Slide 36
IMAGE / GRAPHIC
Going Back to Basics
Mux solution failed due to current limit
Switched to classic PMOS-based switching technique
Two PMOS transistors control by ESP32 GPIOs:
  5V PMOS active for 60s
  1.5V PMOS active for 90s
Includes dead time to prevent both PMOS from turning on simultaneously
Challenges: Gas Sensor Solution
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Abel

## Slide 37
IMAGE / GRAPHIC
IMAGE / GRAPHIC
Dropout Voltage
LM317 dropout voltage (1.5V-2.5V) was too high for stable 1.5V regulation
Daisy-chained setup: 9V -> 5V -> 3.3V -> 1.5V
  LM317 used from 3.3V -> 1.5V
  At ~100 mA load, dropout exceeded safe margin -> output dropped below 1.5V (regulation fails)
Key Issues:
  LDO dropout increased with load
  Inconsistent regulation for 1.5V rail
Challenges: Power Subsystem Problem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Abel

## Slide 38
IMAGE / GRAPHIC
IMAGE / GRAPHIC
New Design
LDO Regulator Upgrade:
  Replaced LM317 with LD1085V (same footprint, 1.5V dropout @ 3A)
  Ensures stable 1.5V output
Voltage Regulation Strategy:
  Separated Rails:
    9V -> 5V (LDO)
    9V -> 3.3V -> 1.5V
  ESP32 gets dedicated power path for reliability
  Replaced 9V -> 3.3V LDO with buck converter to reduce heat and improve efficiency
Challenges: Power Subsystem Solution
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Abel

## Slide 39
Improvements
The 8:1 Mux could be improved upon; our mux has a voltage drop of 0.1V across all temperature sensor inputs.
More time with the Gas Sensor would allow us to fix it
Not all houses are single story; a need exists to improve our model for any house layout.
Adding motion detectors to have real time assistance for each individual at any time.
Adding different methods for guiding residents to safety
The Future
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Abel, Introduce problems

## Slide 40
Thank You
Questions
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Jainam