## Slide 1
AI-Based Transcription Device
Electrical & Computer Engineering
TA: Jiankun Yang
Group 45
Chang Liu Gao Gao Ziyang Huang
5/5/2025
Notes: Z : Hi, we are group 45. Our project is an AI-based transcription device. My name is … major
2. My name is … major
3. My name is … major

## Slide 2: Overview
Project Intro
Design Review
Result
Successes & Challenges
Conclusion
Notes: Z: Our presentation will be separated into the following categories: Project intro, design review, result, successes & challenges, and conclusion.

## Slide 3
Project Intro
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: C. Project intro

## Slide 4
Motivation
Zoom’s live transcription is useful
Miss key points
Misunderstand
Problems
Internet required
Not portable
Extra device needs
Project Intro
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: C. After the pandemic, ZOOM meetings became crucial to our daily study and work. One of ZOOM’s features really caught our eye, and that is live transcription. In an in-person meeting or lecture, we frequently struggle to understand all the points brought by the presenter. The issue can be raised externally, such as through environmental noise and insufficient audio equipment, or internally, such as our lack of attention or accents from the presenter.

## Slide 5
What we want?
Portable
Offline
Easy to use
Single device
Project Intro
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: C: Therefore, we proposed a device that can do the live transcription for us, and we need to make it better. ZOOM’s live transcription requires an internet connection. We want our device can be able to run offline to ensure we can access live transcription anywhere. Similar live transcription software has to be run on a device, such as a laptop or smartphone. We want our transcription device to be an individual system. Besides, we want our device to be portable, so that we can carry it anywhere we want. Moreover, the device has to have sufficient battery capacity, which can last as long as a long lecture or meeting.

## Slide 6
Design Review
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: G: Design review

## Slide 7
Design Review
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Subcomponents
Notes: G: Here is a visual aid of our subcomponents. The microphone captures audio signals and delivers them to the processing unit. Once the processing unit finishes with transcription, it will send the transcribed text messages to the microcontroller. The microcontroller will handle the overall data flow and send commands to the display to visually print text on the screen. The entire system is powered by a bettery.

## Slide 8
Design Review
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Block Diagram
Notes: G: To be specific, here is our final block diagram. We can see our entire system can be separated into four units: Speech processing unit, central controller, power manager, and display module. The microphone is connected to a Raspberry Pi 5, which is a board for processing transcription. The transcription is done by the VOSK model, which is an open-source AI model developed by Meta. The central controller is basically an STM32F4 MCU; it communicates with the speech processing unit via UART and the display module via SPI. Lastly, the power manager provides 5V and 3.3V to our subsystems.

## Slide 9
Design Review
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Subsystem | Requirements | Verification
Speech Processing Unit | Each sentence must be displayed within 3 seconds after finishing speaking. | Use a stopwatch to record the time gap between speaking and displaying.
 | The transcribed accuracy has to be at least 80%. | Speak poems to the device. Calculate the error rate.
Central Controller | The SPI communication speed should be fast enough to avoid noticeable delay. | Compare the sentence displayed time on the screen to the time in the Linux terminal.
Display Module | The displayed text must be readable. | Read a sentence to the device and check if it displays all characters reasonably.
Power Manager | The battery must support ≥3 hours of operation on a full charge. | Fully charge the device, run continuous transcription and measure uptime.
RV Table
Notes: Z: Here is our RV table by different subsystems. The primary factor to achieve the transcription is the transcription speed. We need to ensure that each sentence is displayed within 3 seconds after finishing speaking. Its corresponding verification rubric we set up here uses a stopwatch to record the time gap between speaking and displaying. Meanwhile, the accuracy of transcription determines the usability of our device. Therefore, we need our device to have at least 80% accuracy. This will be tested by speaking poems to the device and calculating the error rate. The central controller handles the data flow. Hence, we must ensure that the SPI communication is fast enough to avoid noticeable delay. We will test this by comparing the sentence display time on the screen to the time in the terminal. The displayed text on our display module needs to be readable, and we can just verify this by checking whether the layout of characters on the screen is reasonable. Finally, our power manager must support the entire system at least 3 hours on a full charge. To verify this, we can just let the device work continuedly after a fully charge to measure the uptime.

## Slide 10
Design Review
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Speech Processing Unit
Raspberry Pi 5
Run VOSK model
Deliver transcribed text to the microcontroller
Notes: C: To achieve our requirements, our speech processing unit must have sufficient performance to run the VOSK model fast enough. Meanwhile, the power consumption has to be reasonable, since our system is powered by a battery. Considering the cost of a normal edge computing platform, we finally chose the Raspberry Pi 5 as our speech processing board. The Raspberry Pi will run the VOSK model to transcribe input audio into text messages. Then, the text messages will be sent to the UART.

## Slide 11
Design Review
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Central Controller
STM32F411RE6
Decode UART packages
Send commands to the display
Notes: G: The central controller is basically a system of STM32F411RE6. This MCU not only provides sufficient I/O for us, but also its large memory ensures our data will not be lost during communication among our subsystems. The MCU will decode UART packages from the Raspberry Pi, and it will command the display module to show the characters on the screen with a specific order.

## Slide 12
Design Review
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Display Module
ILI9341
Receive commends from the central controller
Display characters
Notes: C: The display is driven by ILI9341. We chose this display because of its abundance of online resources. Because of those resources’ support, we could modify the driver to improve its performance in our design. The display module receives commands from the central controller and displays characters readably.

## Slide 13
Design Review
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Power Manager
Power bank
3 hours run
3.3 V for the system
4.5 A for the Raspberry Pi 5
Notes: G: The design of the power manager was the first difficulty we encountered. Though the Raspberry Pi 5 has a decent performance and a good power consumption, it has to be powered by a large current. A normal boost converter can not bear such a high current. Though there are some options with the QFN package, considering their difficulty of soldering, cost, and excessive requirement for battery, we finally decide to use a power bank to power our system. The power bank provide universal USB 5V to the central controller and speech processing unit. On our PCB, there is a regulator to reduce the input 5V to 3.3V that is acceptable for our MCU.

## Slide 14
Design Review
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Reset & Boot
Crystals
Decap
STM32F4
USB-C
Notes: G: Here is the layout of our PCB that is mounted with the minimum system of STM32F4, USB-C port, and necessary protection circuits. Here is our ……. The PCB is small enough to ensure our device is portable.

## Slide 15
Design Review
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Software
Python Scripts
C Scripts
Notes: Z: Our software level is separated into two parts. One is a Python script running on a Raspberry Pi, and the other is the C code that runs on our central controller.

## Slide 16
Design Review
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Python Scripts
VOSK
Audio
for char in transcribed_data:
UART_send(char)
UART
Notes: Z: Here is a visual description of our Python code. We initially deploy the VOSK model on our Raspberry Pi 5. We feed captured audio from the microphone to the model. The model transcribes audio to text strings. Then, we loop through each character of those strings and send them one by one to the UART.

## Slide 17
Design Review
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
C Scripts
main
Enable_Interupt();
HAL
Void CallBack() {
if (!lastChar) {
addToLineBuffer();
}
else {
ILI9341(lineBuffer);
cleanBuffer();
}
}
UART
Triggered
Call
Driver
Void ILI9341(lineBuffer) {
if (printable) {
print(lineBuffer);
}
else {
addNewline();
print(lineBuffer);
}
}
Notes: Z: Here is a visual description of our C code on the STM32. We enable interrupt-triggered UART via the HAL library under our main function. When the UART receives a character, the callback function will be called. The microcontroller will distinguish if the current character is the last one in a sentence. If this is true, the callback function will call the driver to display the sentence. If the current character is not the last in a sentence, it will add the character to a line buffer and keep accepting more characters. Once the driver is called, it will attempt to print the sentence on the display. If the current line is not large enough, it will automatically make newline until the entire sentence is displayed.

## Slide 18
Result &
Verification
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Z: let’s move to result and verification.

## Slide 19
Result & Verification
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Speed
# Trial | Time Delay (s)
1 | 1.61
2 | 1.58
3 | 1.66
4 | 1.61
5 | 1.90
Average | 1.672
Notes: Z: To test the speed of transcription, we measure the time gap between speaking and displaying. Here is a video of verification. After doing 5 trials, we observed the average time delay of transcription is 1.672s, which is much less than our expected value that is 3 seconds.

## Slide 20
Result & Verification
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Accuracy & Readability
Notes: Z: To test the accuracy, we read poems to the device and check how many characters is wrongly transcribed. Here is a video of our verification progress.

## Slide 21
Result & Verification
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Accuracy & Readability
Error Rate: 13%
Notes: Z: Here is the result of the other attempts we made. These poems have 93 characters in total, and there are 12 falsely transcribed characters. Therefore, we can determine our error rate is 13%, which is satisfactory compared to our goal of 80% accuracy that is an error rate of 20%.

## Slide 22
Successes & Challenges
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: C: Success and challenges

## Slide 23
Successes and Challenges
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Successes
Portable somehow
Offline
Easy to use
Single device
Challenges
5 A current supply for Raspberry Pi
Lossless UART communication
Raspberry Pi environment set up
Display layout
Notes: C: We successfully achieved our initial goal, which is building a portable, offline, easy-to-use single live transcription device. During the project implementation, we encountered lots of challenges. The first one, as we mentioned, is the 5 A current supply for Raspberry Pi. Though the final solution is not ideal, we use a power bank to satisfy this current requirement. The second one is lossless UART communication. In our initial UART setup, the communication rate is low, and some characters may be lost due to a long time of waiting. We resolved this issue by using interrupt-triggered UART communication. Moreover, we encounter a problem during the Raspberry Pi environment setup. To deal with this problem, we wrote a shell script to allow the system to automatically open the environment and run the program. Finally, that is the display layout. We encountered a character overlap problem. We solve this issue by modifying its driver.

## Slide 24
Conclusion
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: C: Conclusion

## Slide 25
Conclusion
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
What we learned?
Embedded system with AI
Edge computing devices
Communication protocols
PCB design
Python & C coding
Notes: C: During this project, we learn the following: embedded system with AI, edge computing devices, communication protocols, PCB design, and python C coding.

## Slide 26
Conclusion
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Future Work
Power manager could be integrated on board
Raspberry Pi 5 is not that good
Self-trained AI model
More portable
Notes: G: Here is the future work we can do. The first one is integrating the power manager on our own PCB. This is kind of related to our second future work. That is replaced by Raspberry Pi 5 with another edge computing platform, such as Jetson or FPGA. Since the Pi 5 is a fairly new device, there is not much official support for setting up its environment and I/O. For example, we used to design a microphone connected to the MCU on our PCB. Though the Raspberry Pi 5 supports I2S, which allows us to deliver a digital audio signal from the MCU to the PI, the I2S port can never be initialized. Another work we can do is train our own AI model. We can use the resource on the Media space to train a model to adapt more to normal lectures and meetings. Finally, we could make our device more portable by shrinking the size of the PCB, choosing another computing platform, and making the system more integrated.

## Slide 27
Special Thanks to:
Prof. Arne Fliflet
TA. Jiankun Yang
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 28
Thank you!
Questions ?
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING