## Slide 1
Omnidirectional Drone
ECE445 Final Presentation
Mahir Koseli, Ivan Ren, Dhruv Satish
12/8/2025

## Slide 2
Mahir Koseli
Software Lead
Senior in Electrical Engineering at UIUC
Team
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Ivan Ren
Mechanical and Integration Lead
Senior in Electrical Engineering at UIUC
Dhruv Satish
Electrical Lead
Graduating Senior in EE & Physics at UIUC

## Slide 3
IMAGE / GRAPHIC
Objective
Create an over actuated drone system with decoupled movement in all 6 DOF, allowing for movement at any orientation and in any direction.
High Level Requirements
Individual ESC able to ramp up and down BLDC motor through PWM control
Physical design with optimal motor orientation and mounted electronics/motors
Move (1) vertically upwards 1 meter, hold (2) a fixed altitude ± 0.25 meter
Introduction
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 4
IMAGE / GRAPHIC
Overview
Our overall system can be broken into 3 main parts: the mechanical subsystem, electrical subsystem, and flight control/telemetry subsystem.
The mechanical subsystem provides the frame, the electrical subsystem handles all motor control and power management, and the flight control/telemetry subsystem reads user input and communicates to the electrical subsystem
Original Design
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 5
Overview
The electrical subsystem contains all required electronics to power and control the motors, including the ESCs, motors, current and voltage sensors, BMS, and MCU.
Requirements
12V battery capable of 100A continuous output at 12V nominal
Reverse polarity and overvoltage protection
Stable 3.3V output for MCU
MOSFET Bridge capable of 100 kHz switching
Motor selection has reasonable thrust for takeoff
  Thrust (10A): 427g
  Total from optimal config: 2.3 * 427 = 982.1 grams
Electrical Subsystem - Overview
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 6
MOSFET Bridge
One of the functions our custom PCB handles is providing a triple Half-bridge for a BLDC motor:
Gate drivers PWM input up to 100 KHz
Programmed MOSFET control functionality
Current-sense
Motor breaking energy dissipation
20A continuous output
Custom PCB Requirements
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 7
Power Protection
The secondary function the PCB performs is power protection:
3.3V steady buck-converter output
Overvoltage protection up to 35V
Reverse-polarity protection
Custom PCB Requirements cont.
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 8
Original Concepts
Due to the scope of our project, we had several reference designs that we originally planned to base our design off. In specific, VESC and DeepBlueEmbedded both had reference designs for robust ESCs.
We planned to also develop a custom flight controller board to integrate our IMU, 2.4 GHz receiver, and main microcontroller.
Changes
Timing constraints and delays with our PCB layout due to multiple revisions for trace width meant that we were unable to implement a flight board, deciding to instead use several breakout boards for the sensors we chose and then connecting them to a Nucleo Board.
When verifying our final ESC, 2 of our high-side MOSFETs did not function, making it impossible for us to drive a BLDC motor using our board. We were able to demonstrate half-functionality using a drone battery and several LEDs. We used off-the-shelf 4-in-1 ESCs instead as a fallback.
Electrical Subsystem - Changes
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 9
Overview
The mechanical subsystem provides a stiff frame to keep each motor in its expected orientation, mounting points for all the required electronics, as well as a protective cage during flight testing.
Requirements
Mounting points for each of the motors in an optimal orientation
Stiff frame verified through bending stiffness analysis and physical testing
Safe mounting for electronics, batteries, ESCs
Subsystem 2 – Mechanical Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 10
Mechanical Requirements
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Mechanical Frame
The main skeleton of the frame is formed from carbon fiber and held together by corner joints to give overall structure to the drone. 8 pairs of carbon point towards the center at predefined angles to provide motor mounting locations, and mounting points for the central hub:
420 mm face diagonals, 5 mm ID 3 mm OD
300 mm edges, 5 mm ID 3mm OD
200 mm space diagonals, 3 mm solid
Total estimated weight = 154.4 + 44 = 198.4 g < 250 g allocated
Stiffness estimates Itotal = Icenter + Ad2 = 3.97 + 44.1786 = 48.2 mm -> 2×48.15≈96.3mm, 4 times as stiff as original design

## Slide 11
Mechanical Requirements cont.
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Mechanical Frame
The body of the mechanical frame must have safe mounting points for our MCU, custom PCB, each of the 8 motors in an optimal orientation, battery pack, and 4 in 1 ESCs
Raised mounting holes for Nucleo Board, custom PCB, ESCs
Central location for battery with ample space for heat dispersion
Sufficiently thick arm mounts for each of the motors
Total weight = 8 * 9 + 47 + 33 = 152 g < 200 g allocated

## Slide 12
Original Concepts
The optimization problem for motor orientation has already been solved in the official publication by ETH Zurich. There are also existing CAD files for other designs. We originally planned to use an existing build, including their carbon fiber dimensions to create our frame.
Fabrication-wise, we planned to use primarily SLA 3D printers (resin printers) due to improved resolution and material selection.
Changes
To reduce fabrication cost and time, as well as due to the lack of materials online matching the exact dimensions required, our mechanical lead decided to build a new frame from the ground up using comparable parts. Calculations were done to ensure the alternatives had similar or better stiffness values, weights, and that costs/availability were reasonable.
Due to resolution and curing issues, we were unable to use the SLA printers for several of our parts and opted to use FDM 3D printers at a high-resolution layer height instead.
Mechanical Subsystem - Changes
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 13
Overview
The software subsystem handles collects data from the onboard sensors and remote controller and transforms it into different motor thrust combinations through a control scheme.
Requirements
Read data from IMU and 2.4 GHz remote controller
Execute selected control algorithm using onboard MCU
Output 8 different ESC motor channel outputs
Subsystem 3 – Software Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 14
Telemetry
The main function our software performs is decoding our remote controller signals from the receiver, as well as IMU data, and then outputting 8 PWM channels for each of the 8 motors:
PWM channel output for each of the 8 motors Decode CRSF protocol output from receiver over UART
Decode IMU output over UART
Combine IMU and CRSF input values into 8 channel output
Software Requirements
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 15
Controls
The control system is a cascaded PD controller that hinges on 4 main parts:
Control position depending on current vehicle state and our final setpoints (depending on user input)
Control attitude of the drone to maintain angular position and balance
Control translational and angular movement rate in each dimension
Solve for optimal thrust combination
Software Requirements
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 16
Original Concepts
Robust controls are required to operate and balance the drone in each of the 6 DOF. With 8 motors to operate, the control concept comes down to an 8 by 6 matrix, where each of the motors have an output that produces a known translational acceleration (x, y, z) and a known rotational acceleration (alpha, beta, gamma) depending on its orientation.
Filtered IMU data and CRSF data is transmitted over UART to our STM chip, allowing for our drone to balance itself.
Changes
We were unable to execute a full 6 DOF balancing control schema; to optimize for our high-level requirements, we simplified our system down to an 8 x 4 matrix that only focused on linear movement. This introduces issues with translational drift, but our time constraints meant we focused on hovering first.
Instead of implementing a sensor fusion algorithm to filter raw IMU data using an Extended Kalman filter or Madgwick's Algorithm, we bought an IMU with an onboard M0 processor for built-in sensor fusion.
Software Subsystem - Changes
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 17
Project Build
First successful skeleton frame testing using our custom joints, we ran into several tolerance issues. Our carbon rods measured out to almost exactly 3.00 mm using Mitutoyo Calipers (0.01 mm precision) but our joints took multiple iterations to print due to deformations and imperfect surfaces.
We weighed this portion of the frame with a final value of ~210g, within the expected range of 198g to 250g, most likely due to the glue and print scaling (for tolerance).
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 18
Project Build cont.
We began assembling our main frame, ensuring all components fit properly on the body of the drone. We would eventually switch from this frame to version printed by a Bambu Labs FDM printer due to issues with the alignment of the top and bottom plates that connected to the carbon skeleton. Small adjustments were made due to printing constraints with FDM printers.
Since SLA printers print with 100% infill, this part was heavier than expected at 67 grams, in comparison to our FDM part printed at 60% infill which weighed in at 37 grams.
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 19
Project Build cont.
Testing motors using lab power supply and Nucleo board to verify functionality of off-the-shelf ESCs. We applied different current limits to the power supply and tested each motor and ESC channel to confirm functionality.
We used the oscilloscope to verify the PWM output from the Nucleo board was as expected. Once we could confirm that each motor could be individually ramped up and down from the Nucleo board, we begun assembly.
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 20
Project Build cont.
For our previous breadboard demos, we had confirmed functionality of the IMU and receiver modules, so we began assembly of the drone on a newly printed frame. This included our custom PCB as our power protection unit attached to the battery.
The final weight of all parts came out to ~ 952 grams, which is cutting close to our total 10A motor thrust value of 982 grams.
Unfortunately, during our first test run of our system all connected, something went terribly wrong and our Nucleo board started smoking when the battery terminals were connected. Mahir's laptop also was fried, not booting up anymore.
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 21
Project Build cont.
At this point, we were in complete panic mode. We're very thankful for the course staff giving us another chance here to demo.
We didn't have access to another Nucleo board, so as a last-ditch attempt, we ported over our project to Arduino and began intensive testing to locate our issue.
We knew that since Mahir's laptop was fried, something was sending power through the STM and STLink. We first began testing with a bench top power supply, oscilloscope and function generator to isolate our last MCU from the ESC.
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 22
Project Build cont.
Through careful testing, we also realized there was an issue with the ESC wiring. Two of the ESC outputs are battery terminal monitoring wires to the negative and positive poles. The positive terminal should never have been connected to our MCU without being voltage divided, which fried our board.
After carefully reconnecting our Arduino to the ESC and monitoring oscilloscope and multimeter outputs with a heavily limited current output, we were able to drive the ESC with the Arduino PWM outputs through Servo.h.
We were also able to pinpoint an ESC issue, 2 of the channels on this ESC seemed to have been fried when our Nucleo board was fried. We decided to use the other 4-in-1 ESC for our redemption demo.
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 23
Project Build cont.
We then confirmed IMU and radio receiver functionality using Arduino. Thankfully, existing libraries for CRSF and BNO085 existed for Arduino and we were able to quickly confirm functionality.
We quickly wrote some code to tie the remote controller channel output, IMU angular orientation and motor speed together and demo this to confirm some level of functionality.
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 24
CHART / GRAPH
Short commentary from Ivan showing our Arduino-based system's functionality
Video Demo
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 25
Successes
Wrote custom driver to receive and decode data over UART for our specific ExpressLRS radio receiver/transmitter system that transmits channel data through the CRSF protocol
Built completely custom mechanical design based off available carbon dimensions, within stiffness and weight requirements
Wrote custom cascaded PD controller for linear translational movement utilizing IMU data and current state
Designed and laid out custom 4-layer PCB for high-power BLDC applications, verified robust power protection functionality and half-functionality of triple half-bridge driver
Failures
Project timing issues meant rushed final product and massive integration issues when faced with unexpected setbacks i.e. Dhruv's flight delayed 4 days, IMU model incorrect, frying Nucleo board, several motor delivery delays
Due to rushing, testing and verifications at each step were not as comprehensive as detailed in original schedule leading to fried boards
Only produced and tested one version of the custom PCB due to several revisions, leading to only partial functionality of final board without time to revise
Project management needs improvement, securing dedicated facilities meant for drone flight and buying parts sooner in case of delays
Successes and Failures
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 26
What did we learn
The scope of our project was massive. We were aware of the level of challenge to some degree, which is why Dhruv and Ivan began planning and designing the schematic for our ESCs over the summer. However, during the school semester, it became clear our execution did not match the scope of our project, regardless of what reasons led to this. At some points throughout the semester, we began to realize our performance was differing from the schedule, and though we worked late nights to catch up, this pattern already made it clear that our pacing was unsustainable. We have learned:
For any project of some complexity, proper delegation and ownership over deadlines is vital
Small, consistent steps are significantly better than attempting large scale changes
Making note of all deadlines, including shipping/contacting/manufacturing, and making resilient back up plans to account for delays is extremely important since things will go wrong when you don't expect
Conclusion
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 27
What would we do differently
We are ultimately still proud of the work we were able to finish in the time we had. The root to our final issues was due to rushing and time constraints. We believe that better project management would've fixed the root of our issues, though a few other specifics also stand out to us.
Better parallelize our testing efforts, buy standalone sensors and then write drivers to integrate each sensor system with our MCU while testing our electronics and designing mechanical system
Simulate our systems – a lot of what we did depended on our final product, better simulation would have given us a chance to test our control systems
Improved electronics testing, we should have approached each integration step with the proper measurement tools before hooking up any electronics, which would have prevented us from frying our board
Conclusion
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 28
Our Plans from Here
We were very impressed by the packaging and efficient design for the off-the-shelf 4-in-1 ESCs. Dhruv and Ivan would like to learn from the production quality of a commercial product by redesigning their ESCs to perform at a similar level while reducing the overbuilt-ness of some parts
The current frame can be improved on to improve manufacturability and structural rigidity; the current skeleton performs well, but weight reductions can be made without sacrificing strength
Mahir and Ivan would like to use the existing frame and motors, fix up the current parts and attempt to test Mahir's cascading control system/make tweaks to enable full omnidirectional movement as a controls project
We have seen this project as an amazing learning experience that gave us a very thorough rundown of how to perform in high-stress environments under unforgiving constraints. Learning how to pivot between systems and implement working systems from almost nothing was a humbling and enriching experience that none of us will ever forget as we move on in our learning journey
Future Goals
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 29
Thank You Everyone For Listening!
Questions?
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING