## Slide 1
ECE 445 Final Presentation
Enhanced Golf Rangefinder
Team #14
Peter Maestranzi, Jake Hindenburg, Emma DiBiase
12/09/2025
Notes: All

## Slide 2
Objective
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Jake

## Slide 3
Objective – Problem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Problem: Golf is an extremely difficult and precise sport
  Account for varying distances shot to shot
  Environmental factors (wind, temperature, humidity)
  Devices and applications exist and are common for measuring distance, but do not consider the environment
Notes: Jake
18th hole at augusta national – 464 yards (par 4)

## Slide 4
Objective – Solution
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Our solution: Design a rangefinder device that accounts for external environment factors
Distance measurement from Time-of-Flight sensor
Environmental measurements using several peripheral sensors
Data passed to ESP-32 microcontroller where an adjusted distance is calculated
OLED Display shows all data and provides a golf club recommendation to user
Example of Using a Rangefinder
Enhanced Golf Rangefinder
Notes: Peter

## Slide 5
Design
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Emma

## Slide 6
Design – High Level Requirements
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
High Level Requirements
The rangefinder measures the correct distance from the user to the flag pin when the button is pressed.
When the button is pressed, the environmental sensors collect the correct data and provide the necessary adjustments accordingly.
The user interface recommends a suitable club based on the measured distance.
Notes: Emma

## Slide 7
Design – Block Diagram
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Block Diagram
Notes: Jake – make bigger, bigger text. Along the way show

## Slide 8
Design – Power Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Power Subsystem on Main PCB
Power Subsystem Block Diagram
9V Connection
Notes: Emma
~20-40mA load on Buck Converter (5V)
~190mA load on Linear Voltage Regulator when all sensors are in operation (3.3V)
Primary Power Source: 9V DC Duracell Battery
9V to 5V Buck Converter (LM2596S-5)
                Powers the Wind Speed sensor PCB
Output of Buck Converter connects to 5V to 3.3V Linear Voltage Regulator (LD1117S33TR_SOT223)
  Powers the remaining sensors, ESP32 Microcontroller, OLED Display, and the button
  Schematic: talk about capacitors and inductor smoothing output and preventing ripple/spikes in current or voltage.

## Slide 9
Design – Power Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
3.3V Verification
5V Verification
Power Subsystem Requirements and Verification
Notes: Emma
~20-40mA load on Buck Converter (5V)
~190mA load on Linear Voltage Regulator when all sensors are in operation (3.3V)
Go over requirements that we set, all of them applying to the amount of voltage we are outputting at different points in the circuit within a 5% tolerance. Prove this with the multimeter

## Slide 10
Design – Controller Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Microcontroller – ESP32-S3-WROOM-1-N16
  High processing power
  Low power consumption
  Wide range of sensor support
Microcontroller Pinout
ESP-32 Microcontroller on Main PCB
Programmer pins
Notes: Jake
Microcontroller – ESP32-S3-WROOM-1-N16
  High processing power
    Good for filtering, averaging,compensations
  Low power consumption
    ~20-25mA
  Wide range of sensor support
    Enough GPIO to support themultitude of sensors that make upthe device

## Slide 11
Design – Controller Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Microcontroller Programming Flowchart
Controller Subsystem Requirements and Verification
Notes: Jake

## Slide 12
Design – Peripherals Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
SEN0366 ToF sensor
BME280 temperature and humidity sensor integrated into main PCB
Modern Device wind speed sensor integrated into a separate PCB
Peripheral sensors collect data and send to the microcontroller
SEN0366 ToF Sensor
BME280 Sensor in PCB Schematic
Notes: Peter

## Slide 13
Design – Peripherals Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Wind Sensor PCB Schematic
Wind Sensor PCB
Notes: Peter

## Slide 14
Design – Peripherals Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Temperature Verification
Notes: Peter

## Slide 15
Design – Peripherals Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Distance Verification Showing Tape Measured Distance and Scaled Rangefinder Measurements
Notes: Peter

## Slide 16
Design – Peripherals Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Average Value: 2.403 mph
Average Value: 2.757 mph
Commercial Wind Meter Measurements
Enhanced Rangefinder Measurements
14.7% Variation
Notes: Peter

## Slide 17
Design – Display Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
1.3” OLED Display with SH1106 Driver
Displays Temperature data, Humidity data, Wind Speed data, Distance/Adjusted Distance, and Club Suggestion
Display Subsystem Requirements and Verification
OLED Display
OLED Readings
Notes: Emma
Is being powered by the 3.3V regulator drawing ~ 30mA when the screen is on, and is connected to the microcontroller via serial connection.

## Slide 18
Design – Physical Design
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
3D Model Designed via openSCAD (PLA Filament)
132mm (L) x 76mm (W) x 87mm (H) dimensions
Enclosure 3D Model
Printed Enclosure
Notes: Emma
3D printed rectangular enclosure PLA filament, designed on openSCAD explain dimensions
Includes a removable lid with ventilation holes and airways in the back face to allow for proper airflow for the wind speed sensor and the thermistor.
Also accounts for heat dissipation preventing the inside of the enclosure from becoming too hot.
Finally, includes mounting holes for the PCBs, display, and button as well as a cutout for the tof laser to emit and receive.

## Slide 19
Conclusion
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Peter

## Slide 20
Conclusion – Takeaways
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
What We Could Have Done Better
Early PCB Adjustments
Parts Orders
Takeaways
Collaboration
Documentation
Scheduling/Process
Notes: Peter

## Slide 21
Conclusion – Future Work
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Future Improvements...
Longer range distance sensor
Additional User Interface (Phone App)
New Wind speed sensor design
More compact design
Notes: Jake
Future Improvements...
Replace our 50m ToF sensor with something that islonger range
Design a UI so that users can input how far they hit theirclubs into an application rather than changing theprogram
New way to measure wind speed along with direction
More compact design

## Slide 22
Thank You
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: All