## Slide 1
Autonomous Wi-Fi Mapping Car
Ben Maydan, Avi Winick, Josh Powers
Group 2

## Slide 2
Existing manual signal surveys are extremely expensive, slow, and prone to human error
Technicians charge thousands of dollars for site surveys
The autonomous car offers a low-cost, automated solution for consistent high-resolution mapping
Eliminates the need for expensive technician visits
What problem does this solve?
Gemini Image

## Slide 3
Developing an autonomous mobile robot for Wi-Fi mapping
Uses LIDAR and SLAM to build a 2D map and navigate
Collects and correlates Wi-Fi signal strength with location data
Generates a detailed heat map for network optimization
What is our project?
Gemini Image

## Slide 4
Design

## Slide 5
Base Subsystem

## Slide 6
Host GUI

## Slide 7
Control Subsystem
Gemini Image

## Slide 8
Sensing Subsystem

## Slide 9
Drivetrain and Power Subsystem

## Slide 10
Design - Power
https://www.amazon.com/dp/B0CYPG8NNQ?ref_=ppx_hzod_title_dt_b_fed_asin_title_0_0
2 7.4V Lithium Ion batteries with – 3300mAh / 24.42Wh.
Optimization: Downsized from 5000mAh to meet the 1.5 kg vehicle weight constraint without compromising performance.
Safety Margin:
Capacity: 15C Rating, giving us 49.5A Continuous Discharge if needed.
Load: 2A Peak Stall Current.
Result: stable voltage delivery without overheating.
Energy Available: 24.42 Wh per battery.
Power Draw: ~7.4 W (Nominal).
Calculated Runtime: >2 Hours (Exceeds 15-minute requirement by 13x).

## Slide 11
Design - Power Protection

## Slide 12
Design - Power Budget
Total Peak Load: Calculated at 5A (Motors + LIDAR + Headroom).
Component Selection: Selected P-MOSFETs rated for 15A Continuous, providing a 3x Safety Factor.
Protection Strategy: Fuse limits are set to 10A (Trip) to accommodate temporary motor stall currents while protecting against dead shorts.

## Slide 13
Design – Power Integrity
Brownout Prevention: Motors + LIDAR spin-up created current transients causing 200mV sag
Bulk Electrolytic: Act as energy reservoir need motor drivers and LIDAR
Decoupling Capacitance: Handles fast switching to limit noise

## Slide 14
Dual Controller Architecture:
  ESP32: Handles motor control, Bluetooth, and Wi-Fi scanning.
  Raspberry Pi: Dedicated "brain" for running SLAM algorithm
Design – Software (System Architecture)
Gemini Image

## Slide 15
Chip to Chip Communication:
  We use a special method called COBS encoding with TX and RX wires connected from the ESP32 to the Raspberry Pi.
  This is very useful in preventing packet loss.
Design – Software (System Architecture)
Gemini Image

## Slide 16
Intelligent Path Planning
  Uses BFS Flood Fill to identify the accessible "Island Map".
  Generates a lawnmower pattern using A* algorithm for driving in between Wi-Fi recording points.
Wi-Fi Mapping:
  ESP32 tags every Wi-Fi RSSI sample with (x, y) coordinates.
  Utilizes Bluetooth to transmit heatmap and dataset to GUI.
Design – Software (Autonomous Navigation)

## Slide 17
Prone to segmentation faults
  Difficult to tune the hole-width hyperparameter
We implemented a redundancy layer
  If the algorithm has a segmentation fault we automatically pick it back up from where it started
  If we start the autonomous phase and the timeout phase passes, we use a high-quality list of previous LiDAR points to rebuild the map
Software Challenges – SLAM on Raspberry Pi

## Slide 18
Generated SLAM Map
Map in code is 8 x 8 meters
  This is why white unoccupied area is smaller relative to total map.
Room made with poster boards
  Mostly rectangular but more triangular at the top
Featureless room & black lines
  It's harder to localize; it's possible our redundancy code kicked in here

## Slide 19
Requirements and Verifications

## Slide 20
Results

## Slide 21
Developed a robot which uses a LIDAR sensor to autonomously navigate calculated paths
  Measures Wi-Fi signal strength at various points on this path
Successfully implemented a custom PCB to manage power distribution, ensuring stable operation for motors and sensitive logic components via separate voltage rails.
Conclusion
Gemini Image

## Slide 22
Refine omnidirectional wheels so friction is close to non-existent but also consistent everywhere
Drone to not limit Wi-Fi mapping to a flat plane
Improve the sensing subsystem to address the current limitation where the LiDAR sensor cannot detect obstacles that absorb light rays
Transition from testing in controlled environments to complex spaces to validate the navigation algorithms against unpredictable physical layouts.
Future Work