## Slide 1
Insight: Cardiovascular Screening Device
Team 32
Team: Jay Nathan, Rishab Iyer, Ethan Pereira
Professor: Yu
TA: Weiman Yan

## Slide 2
Purpose
Real-time Physiological Sensing
For
Early, Cost-effective Cardiac Screening
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Ethan

## Slide 3
Issues We Are Addressing
Cardiovascular Disease is the leading global cause of death
Key risks like hypertension, arrhythmias, and sinus bradycardia often go undetected.
Screening today is costly and fragmented.
Consumer devices are incomplete, offering limited, single-sensor data.
Problem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Ethan

## Slide 4
IMAGE / GRAPHIC
What We Have Developed
A low-cost, portable cardiac screening device integrating ECG, PPG, and motion sensing
A Custom ESP32-C3 PCB collects synchronized physiological data with reliable acquisition
3D-printed enclosure ensures PCB stays protected and functional
Provides early detection insights for 3 indicators in a simple, user-friendly display.
Solution
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Jay

## Slide 5
Block Diagram
Design
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Jay

## Slide 6
Schematic
Design
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Jay

## Slide 7
Footprint
Design
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Jay

## Slide 8
Subsystem Function
Provides stable voltage rails for all sensors/components
Power enters through 5 V barrel jack
Poly-fuse prevents voltage shorts
LDOs used to power other sensors
Requirements & Verifications
R: Must provide stable 3.3 & 1.8 V rails under full sensor load
  V: Measure rails using oscilloscope during PPG LED and SPI activity
R: Over-current protection must activate during short on 5 V line
  V: Apply intentional short downstream of polyfuse; observe trip/reset
Power Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: jay

## Slide 9
Subsystem Function
Contains all sensors involved with gathering physiological data
3 sensors: ECG sensor, PPG IR/LED sensor, Triple-Axis Accelerometer
All connected to the ESP32 Microcontroller
Requirements & Verifications
R: 3 sensors must correctly communicate over SPI/I2C
  V: Run enumerations and read device ID registers
R: 3 sensors must produce valid physiological waveforms/data
  V: Collect sample ECG, PPG, and XYZ logs; check for expected patterns
R: PPG-derived heart rate matches reference device by ±7 BPM
  V: Compare PPG HR to pulse oximeter
Sensing Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Jay, Rishab

## Slide 10
Subsystem Function
ESP32 is central hub of sensor communication, timestamping, and data transmission to host PC
USBC connector supports data communication & PCB programmability
Requirements & Verifications
R: The ESP32-C3 must boot reliably, detect sensors, and stream synchronized packets
  V: Inspect boot logs; capture continuous sensor packets for set period of time
R: The system must maintain error-free USB or Wi-Fi communication
  V: Stream data and monitor for dropped frames or packet loss
Microcontroller/Communication Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Rishab

## Slide 11
IMAGE / GRAPHIC
Subsystem Function
Primary Hub for Disease Detection, Noise Filtering, Feature Detection
Live Dashboard for Viewing Status
Requirements & Verifications
R: Sensor data must be cleaned, synchronized, and normalized by the processing pipeline
  V: Inspect raw vs. processed data; confirm time alignment
R: Diagnostic outputs (arrhythmia, hypertension, bradycardia) must be repeatable across five trials
  V: Provide identical input streams; verify consistent classifications
R: Dashboard displays updated diagnostic results in real time
  V: Stream live data and observe interface updates
Disease Detection Subsystem (Software)
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Ethan

## Slide 12
Video of Insight
Video Demo
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Ethan

## Slide 13
Results
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Ethan

## Slide 14
Accomplishments
Fully programmable PCB that utilizes all 3 sensors as expected
Implemented sensor fusion system with relative accuracy
Data reading halting feature when either ECG or PPG sensor doesn’t detect human-sensor interaction
Successes & Challenges
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Challenges We Came Across
Replacing Outdated/Incompatible Parts
  Ex: Replace AD8232 ECG sensor w/ MAX30003 ECG sensor
Grounding Faults
  Correcting footprint grounding issues in between PCB orders
Notes: Rishab

## Slide 15
What We Learned
Working under time constraints
Learning to change/adapt designs based on feedback & circumstances
Learning to temper expectations and ambitions
Future Steps
Fully implement wireless data streaming via Bluetooth/WiFi
Reduce PCB footprint and enclosure size to make device more “portable”
Explore mobile app development
What We Learned & Future Steps
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Rishab

## Slide 16
Thank You
Questions?
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Rishab